## Slide 1
ISOLPHARM project: Development of two preclinical imaging devices for 111Ag β and γ radiation
Alberto Andrighetto - Istituto Nazionale di Fisica Nucleare
Laboratori di Legnaro
PSMR2024, May 23th

## Slide 2: Talk Overview
1) Brief introduction on ISOLPHARM Project
2) Imaging results on PET and SPECT isotopes
3) R&D activities on tailored detectors for 111Ag
4) Conclusions

## Slide 3: Medical radionuclides production @LNL
Proton-rich radionuclides
E.g.: 47Sc, 99mTc, 51Mn/52Mn
MAINLY DIAGNOSTIC
ISOL technique
Tunable energy: 35 – 70 MeV; High output current: up to 500 µA in dual extraction mode
for Fundamental & Applied research
RIB
Neutron-rich radionuclides
E.g., UCx target: 111Ag, 131I, 90Y, 89Sr
MAINLY THERAPEUTIC
Direct activation
technique

## Slide 4: Radiopharmaceutical Frame (small molecules)
Targeting Agent:
At present: PSMA-617
Before: CCK2R
Chelator: 111Ag
Linker: Bifunctional
Scaffold :
Best candidate
Detectors

## Slide 5: The ISOLPHARM Project – 4 pillars
Also…Scientific and training hub
2. Innovative Method
Innovative production @SPES of several (medical)
Carrier Free + High Purity
radionuclides
(111Ag,89Sr,136Cs..)
3. Facility at SPES
An irradiation station,
using the SPES
Low Energy Beams, is
planned in the SPES building
.
4. Activities, INFN Experiments
Financed by CSN5 (physics application): ISOLPHARM_Ag +
ISOLPHARM_EIRA + ADMIRAL
1. National Collaboration
Broad, focused on radio-
pharmaceutical development:
synthesis,characterization
and preclinical tests (vitro/vivo)

## Slide 6
The ISOLPHARM collaboration
Development of a β-imaging
system based on solid-state detector
Development of a γ-imaging scintigraphic system
Radiobiological characterization
Radiopharmaceutical
production

## Slide 7: ISOLPHARM: Innovative Method
The ISOLPHARM method is able to produce and select a
SINGLE RADIO-ISOTOPE
+ high specific activity
+ radionuclidic purity

## Slide 8: 3. ISOLPHARM: the irradiation facilty at SPES
Cyclotron
Front-End
IRIS Beam Collector
Proton beam
Radioactive beam
Starting Point: Some tens of mCi are sufficient to start a R&D on radiopharmaceuticals
low costs, easy set-up

## Slide 9
The ISOLPHARM Facility
IRIS: Detection and quality control station
Secondary Target with isotope deposited (107Ag)

## Slide 10: ISOLPHARM: 10 Years of activity
Simulations and feasibility evaluation
of Ag as radiopharmaceutical precursor
First production of 111Ag in reactor and beginning of in-vitro and in-vivo testing
Providing new tools for preclinical trials on 3D scaffolds
2018 - 2019
2020 - 2022
2023 - 2025
2014 - 2017
Interdisciplinary Study Group on production of medical radioisotopes at SPES
2024 - 2025
Follows the technological aspect for the radionuclide production
INFN experiments
PRIN

## Slide 11: Why doing imaging within ISOLPHARM?
ISOLPHARM project performs imaging:
To improve the existing imaging devices toward innovative radionuclides (tailored SPECT & γ camera )
To study the cellular uptake of radiopharmaceuticals
To track the radiopharmaceutical within a body for preclinical applications

## Slide 12
Imaging results using PET and SPECT
isotopes (quick review..)

## Slide 13: PET vs SPECT ISOLPHARM radioisotopes
111Ag (half-life 7.45d) emits:
γ-rays
  342 keV (7%)
  245 keV (1%)
111In (2.8d) emits:
  245 keV (94%)
  171 keV (91%)
68Ga (half-life 67m) and
64Cu (12h) emit:
positrons
  a pair of collinear 511 keV γ-rays
innovative isotope
M. Ballan, PhD thesis - Uni. Ferrara, 2019

## Slide 14: 64Cu – chelated (2021)
study of the in vivo stability of chelators
~ 10 MBq 64Cu-DO2A2S injected in BALB/c nude mice
biodistribution obtained at 1, 4, 24 h post injection
PET/CT images
1
M. Tosato et al., Molecules, 27 (2022) 4158

## Slide 15: 111In – targeted (2021)
study of the in vivo stability of chelators (DOTA)
~ 7 MBq 111In- DOTA- IP-001 + Z360 (ligand)
biodistribution obtained at 4, 24 h post injection
SPECT/CT images at 4 (left), 24 (right) h p.i.
γ-CUBE mouse/rat SPECT
2
M. Verona et al., Molecules 26 (2021) 918
IP01= Isolpharm Linker
Z360
DOTA

## Slide 16: 68Ga – targeted (2022)
study of the biodistribution of targeting agent Z360 (CCK2R)
~ 6 MBq 68Ga-NODAGA-IP01- Z360
biodistribution obtained for cells expressing the CCK2R
PET/CT images
3
A. M. Pavone et al., Life 14 (2024) 409

## Slide 17
→ 111Ag has dosimetric behavior equal to 186Re, which was recently studied in Phase I / II trials
→ 111Ag exhibits possible ‘theranostic’ properties
similar to 177Lu which was recently approved by FDA.
111Ag properties
β- emitter (average energy 360 keV)
Good half-life (7.45 days)
Average tissue penetration (1.8 mm)
Medium energy γ rays -> SPECT candidate
111 Isobaric chain | Half-Life T½ | Decay | Target Yield
Cadmium-111 | Stable |  | Low yield production
Silver-111 | 7.45 days | β─ | Good yield production
Palladium-111 | 23.4 min | β─ | Bad release, short T1/2
Rhodium-111 | 11 sec. | β─ | No release, very short T1/2
→ No Isobaric 111 contamination in the secondary target (also with LASER off)!
→ 111Ag can be produced @ SPES with high purity & with high production rate
→ No radiopharmaceuticals radiolabeled with 111Ag in the market.
Radiopharmaceutical radiolabeled with 111Ag

## Slide 18: 111Ag versus 177Lu
 | 177Lu |  | 111Ag | 
half-life | 6.64 days |  | 7.45 days | 
β- | 79 % intensity | 149 keV (average) | 92 % intensity | 360 keV (average)
γ | 10 % intensity | 208 keV (average) | 7 % intensity | 342 keV (average)
Is 111Ag a possible alternative to 177Lu?
177Lu
111Ag

## Slide 19
111Ag production & separation

## Slide 20
2 mm
3 mm
5 mm
Can Ag-111 be imaged?
Bruker In-Vivo Xtreme can perform pre-clinical imaging via 111Ag radiopharmaceuticals:
  Used the Direct Radioisotopic Imaging (DRI)
  PMMA Phantoms filled with 111Ag solution
Xtreme will be used to evaluate the targeting efficiency-> Only planar distribution
DRI
Test with 111Ag in phantoms (2023)
4
Nicola Zancopè, M.Sc. thesis - Uni. Padova, 2022

## Slide 21
21
Imaging with free 111Ag (March 2024)
150 mg of 110Pd
irradiated in the LENA
central thimble
Obtained 88 MBq of 111Ag
111Ag
biodistribution
in vivo imaging
5 days after injection
5

## Slide 22
R&D on tailored detectors for 111Ag
111Ag

## Slide 23
ISOLPHARM gamma camera for γ-imaging
3-1 - Detector Design & Electronics
Electronics:
CAEN FERS DT5202
Optical photon detectors (SiPM):
Hamamatsu S14161 8x8 ch 3x3 mm²
Tungsten Collimator:
2 mm holes, 1 mm septa, 30 mm length
Scintillating crystal:
(GAGG) 1x1x26 mm3 matrix
What we are doing
Design/perform a gamma camera tailored to 111Ag
Aim: to localize radiopharmaceutical deposits within mice for pre-clinical experiment

## Slide 24
24
Two tumors 8 mm apart
ISOLPHARM γ-imaging
GEANT4 Simulations: -> Detector performance
MOBY phantom used to generate activity distributions
  Injection of 3 MBq of 111Ag in two spots of the liver
  5 min acquisition
Tumors are detectable according to the simulation
First experiments (April 2024):
Tests are ongoing with sealed sources (137Cs)
At the end of this year tests with 111Ag phantoms are planned

## Slide 25
Beta detector is based on ALPIDE chip. This is a monolithic active pixel sensor (MAPS) designed for the Inner Tracking System of the ALICE experiment at CERN.
The Silicon sensor is segmented into 1024 x 512 sensitive pixels of size 28 μm x 28 μm.
ISOLPHARM Beta detector for β-imaging
What we are doing:
Design/perform a high-resolution and cost-effective beta imaging system
  to generate two-dimensional activity maps for in-vitro test
  Aim: to revealing the localization of radiopharmaceutical deposits within cell cultures (internalization)

## Slide 26
26
ISOLPHARM β-imaging
GEANT4 Simulations -> detector performance
Simulated images in a realistic 2D cell culture with 111Ag: • Radiopharmaceutical deposited in dispersed tumor cell clusters • About 10^6 radiopharmaceutical molecules internalized per cell • 15-minutes acquisition time
First experiments with 111Ag (March 2024):
Dedicated firmware mounted on the detector
A collimated source of 111Ag was imaged
3.5 MBq 111Ag produced at LENA

## Slide 27
111Ag Imaging: preliminary results
3-1 - Detector Design & Electronics
γ ray
optical photons
Scintillation
Image after scintillation
Source:
3 cylinders (5 mm diameter) of 111Ag solution
Beta imaging:
0.2 mm resolution can be obtained → cell culture imaging
Gamma imaging:
~7 mm resolution can be obtained → in-vivo imaging
γ
β

## Slide 28
Conclusion

## Slide 29
ISOLPHARM is also a training hub: good collaboration with Universities
24 Master theses in Pharmacology
13 Master and Bachelor theses in Physics
2 Master theses in Chemistry
4 Master theses in Industrial Engineering
4 PhD theses

## Slide 30
The ISOLPHARM Team
Thank you for your kind attention!
Visit our webpage: https://isolpharm.pd.infn.it/web/
Post-graduate and PhD students:
Alberto Arzenton, Daiyuan Chen, Jessica Delgado, Giorgio Grosso, Omorjit Singh Khwairakpam, Aurora Leso, Davide Serafini, Nicola Zancopè