## Slide 1: TBPIX Pisa activities program
System test
Module Quality test

## Slide 2
Activities strictly related to our commitment of mechanical support for the barrel pixel (TBPIX)
  For this are necessary: engineering (drawings, mechanical part production, manpower from A.T.) and technical support
  Support from physicists for setting up systems, data tacking and analysis
  Can be classified as medium (M) long (L) term activities
1. Simple "system test" setup
  to investigate thermal behaviour of fully equipped ladder (M)
  to check electric flange in Aluminium (M-L)
  Measurement of unwanted layers distortion (twisting, bending,…) with thermal stresses (M-L)
  Equipment: the following “materials” has to be procured
    at least 4 CROC modules,
    port card, multiwire cables, E-links
    CMS large climate chamber to cool down system setup
2. T-cycling and thermal study
  Single module or one ladder in the “best thermal contact configuration” (aluminium plate) (M)
  study electrical and mechanical behaviour of module after T-cycling
  measurements of thermal gradients in the module
    Equipment: climate chamber (possibility at CERN, already exploited, or in Pisa with GLAST equipment (to be re qualified))
  Cooling loop thermal performance study (L)
  measurement of cooling efficiency of pipes with CO2 with/without thermal grease/glue
  Equipment: large CMS climate chamber, LV and HV system test equipment
Program for system tests

## Slide 3
Activity necessary to understand basic module performance
  Do not need engineering/technical support, but physics manpower data taking and analysis
    Almost all are short-medium term activities
Study of Bump bonding effective connection:
    with X-rays, pixel alive map
    with "noise" method (ETH)
    using cross-talk effect (PSI)
  First two methods we have already implemented and used in laboratory. We believe one out of the three will be implemented for module Q.A., i.e. to be used in our case after assembly in a ladder
Xray setup
  Study of VCal calibration: sample based but statistically significant tests during production to extract the mean value to be used during operation
  In case Pisa support will be needed during production
  Xray tests:
    bump bonding quality: sample based at the beginning of production or/and a few modules per every batch
    high hit rate for pixel/column/chip efficiency study vs hit rate, grading(?): to see on a sample of modules whether such test is needed for all modules
    hit efficiency vs time: long term stability
  Academic understanding of module performance
Program for module quality tests