## Slide 1: Sterile Neutrino Dark Matter Searches with the KATRIN Experiment
16th Pisa Meeting on Advanced Detectors
Frank Edzards
May 2024

## Slide 2: Agenda
Motivation
TRISTAN detector system
Conclusions

## Slide 3: Agenda
Motivation
TRISTAN detector system
Conclusions

## Slide 4: Active neutrinos

## Slide 5: Sterile neutrinos
Sterile neutrino: lepton that does not carry any charge
Mass eigenstate not purely sterile, can have any mass

## Slide 6: Sterile neutrinos
Heavy sterile neutrinos (> GeV)
Lightness of neutrinos + Matter/anti-matter asymmetry
Light sterile neutrinos (~1 eV)
Short-baseline neutrino oscillation anomalies
keV-scale sterile neutrinos (~1-50 keV)
Dark matter candidate
arXiv:1901.08330 (2019): C. Giunti and T. Lasserre
arXiv:1906.01739 (2019): S. Böser, C. Buck, C. Giunti, J. Lesgourgues, L. Ludhova, S. Mertens, A. Schukraft, M. Wurm
Prog. Part. Nucl. Phys. 104 (2019): A. Boyarsky, M. Drewes, T. Lasserre, S. Mertens, O. Ruchayskiy
ϕ
L

## Slide 7: Sterile neutrinos in single β-decay
+
Signature: spectral distortion with kink-like feature

## Slide 8: KATRIN - Working principle
70 m long
Tritium source
30 μg of gaseous T2
1011 T2 decays/s
Spectrometer
Electrostatic filter
MAC-E filter principle
Detector
Counts electrons
Rate vs HV

## Slide 9: KATRIN - Data taking overview
1st m𝜈 campaign
m𝜈 < 1.1 eV PRL 123, 221802 (2019) Phys. Rev. D 104, 012005 (2021)
2nd m𝜈 campaign
m𝜈 < 0.8 eV Nat. Phys. 18, 160–166 (2022)
1st to 5th m𝜈 campaign
Unblinded, will be released soon

## Slide 10: KATRIN - Challenge
Signature of
neutrino mass
Vret = -18 kV
1010 e/s
Electron energy
1 e/s
Rate

## Slide 11: KATRIN - Challenge
Signature of
neutrino mass
Signature of
sterile neutrino
Vret = -18 kV
Vret = 0 kV
1 e/s
1010 e/s
Detector:
- Integral
- differential

## Slide 12: Agenda
Motivation
TRISTAN detector system
Conclusions

## Slide 13: KATRIN - New detector (TRISTAN)
Silicon drift detector (SDD) technology
  Handling of high rates (100 kcps/pixel)
  Excellent energy resolution (300 eV at 20 keV)
Novelty: application to β-spectroscopy
3 mm
4 cm
4 cm
S. Mertens et al., J. Phys. G46 (2019) S. Mertens et al., J. Phys. G48 (2020) M. Gugiatti et al., NIM-A 979 (2020) M. Biassoni et al., EPJ. Plus 136 (2021) P. King et al., JINST 16 T07007 (2021)

## Slide 14: TRISTAN Detector
Electrons
Detector module
Monitor spectrometer
Full system
X-rays
Sterile neutrino search

## Slide 15: TRISTAN Detector
Electrons
Detector module
Full system
X-rays
Sterile neutrino search
Monitor spectrometer

## Slide 16: Performance with X-rays
Test of multiple prototype designs
Detector chip,
7 pixels, Ø 3 mm
ETTORE readout ASIC (12 channels)

## Slide 17: Performance with X-rays
Test of multiple prototype designs
Excellent performance demonstrated
  Energy resolution
140 eV FWHM at 6 keV (1 μs shaping)
  S. Mertens et al., J. Phys. G46 (2019)
55Fe
Detector chip,
7 pixels, Ø 3 mm
ETTORE readout ASIC (12 channels)
Measurement with an 55Fe calibration source
  Mn- line at ~5.9 keV
  Mn- line at ~6.5 keV

## Slide 18: Performance with X-rays
Test of multiple prototype designs
Excellent performance demonstrated
  Energy resolution
  Linearity
0.1% linearity (up to 60 keV)
241Am
  S. Mertens et al., J. Phys. G46 (2019)
140 eV FWHM at 6 keV (1 μs shaping)
55Fe

## Slide 19: TRISTAN Detector
Electrons
Detector module
Full system
X-rays
Sterile neutrino search
Monitor spectrometer

## Slide 20: Detector response to electrons
Electron microscope
Precise understanding and modeling of detector electron response required
Silicon escape peak
Main peak
1. Dead layer
2. Charge sharing
3. Backscattering

## Slide 21: Detector response to electrons
Electron microscope
1st effect: Dead layer
Main peak
Silicon escape peak
Low-energy tail
Simulation
charge collection
depth
X-ray
e-
Si 450 μm
sensitive volume
SiO2 ~10 nm
S. Mertens et al., J. Phys. G48 (2020)
Measurement result: < 50 nm

## Slide 22: Detector response to electrons
Electron microscope
2nd effect: Charge sharing of pixels
Main peak
Silicon escape peak
Charge sharing plateau

## Slide 23: Charge sharing
Electron microscope
Investigation of charge sharing with pulsed laser (640 nm, ⌀min~7 μm)
Laser
Detector
Fiber optics
Collimator
xyz-stage
Collimating lens
Entrance window of detector

## Slide 24: Charge sharing
Electron microscope
Investigation of charge sharing with pulsed laser (640 nm, ⌀min~7 μm)
Grid scan in triple point region

## Slide 25: Detector response to electrons
Electron microscope
3rd effect: Backscattering
Main peak
Backscattering continuum
Silicon escape peak
Sensitive volume
Dead layer
e-

## Slide 26: TRISTAN Detector
Electrons
Detector module
Full system
X-rays
Sterile neutrino search
Monitor spectrometer

## Slide 27: Detector module
166 px SDD with integrated JFET
Ettore ASICs
(below cap)
Silicon carbide (CeSiC)
cooling link
Copper cooling and holding structure
Rigid flex PCB (signal and power lines)
40 mm
38 mm

## Slide 28: Detector Module
Largest SDD array operated ever!
All pixels working
Homogeneous performance
Average energy resolution at -35°C:
  ~160 eV FWHM at 5.9 keV

## Slide 29: TRISTAN Detector
Electrons
Detector module
Full system
X-rays
Sterile neutrino search
Monitor spectrometer

## Slide 30: Installation in KATRIN MoS
Test in quasi-realistic environment (B-field, vacuum, etc.) w/ X-rays and electrons
Excellent energy resolution: 147 eV FWHM at 6 keV
Stable long-term operation
83mKr

## Slide 31: TRISTAN Detector
Electrons
Detector module
Full system
X-rays
Sterile neutrino search
Monitor spectrometer

## Slide 32: Towards a detector tower
166 pixels
9 x 166 pixels
TRISTAN tower
(including vacuum shield and cooling structure)
Detector section
7 pixels
Installation in KATRIN beamline planned for 2026

## Slide 33: Agenda
Motivation
TRISTAN detector system
Conclusions

## Slide 34: Summary
TRISTAN will search for sterile neutrinos in the keV mass range with the KATRIN experiment
Excellent spectroscopic performance (electrons and photons) demonstrated in various test stands
Largest SDD array operated ever

## Slide 35
Thanks for your attention!

## Slide 38: Radiation damage test setup
tantalum hot cathode electron source
ceramic insulators
e-
detector
electrically movable shutter
motorized stage with encoder

## Slide 39: Electron interactions in silicon
collision with electrons
elastic
ionization
threshold 1eV
collision with nucleus
elastic
primary knock on atom (PKA)
threshold 25eV
Ekin>255 keV necessary
with up to 50 keV electrons the only degradation of the detector can come from ionization
focus is not on bulk but on insulating 10 nm SiO2 layer

## Slide 40: Detector cross section
SiO2 ca. 10 nm
Si 450 μm
insulator
doped area, conductive, dead layer
depleted area, sensitive volume
ionization cannot lead to any lasting change here, electrons and holes are movable
ionization can lead to trapped charges, etc...
z
electrons
mean deposit charge
photons

## Slide 41: Timeline
 | Jan | Feb | Mar | Apr | May | June | July | Aug | Sep | Oct | Nov | Dec
2024 | R&D, single-component manufacturing |  |  |  |  |  |  | Three modules in replica setup |  |  |  | 
2025 |  |  |  | Full TRISTAN tower in replica setup |  |  |  |  |  |  |  | 
2026 | Integration of TRISTAN tower in beamline & new RW material |  |  |  | Commissioning of TRISTAN tower |  |  | keV sterile neutrino search |  |  |  | 
2027 | Option A: Physics runs |  |  |  | keV sterile neutrino search |  |  |  |  |  |  | 
 | Option B: upgrade RW chamber |  |  |  |  |  |  |  |  |  |  | 

## Slide 42: KATRIN - Latest results
First campaign
  Total statistics: 2 million events
  Best fit: eV² (stat. dom.)
  Limit: eV (90% CL)
Second campaign
  Total statistics: 4 million events
  Best fit: eV² (stat. dom.)
  Limit: eV (90% CL)
Combined result
  eV (90% CL)

## Slide 43: Charge sharing
Fit charge cloud distribution assuming a Gaussian charge cloud to determine the charge cloud size
Charge cloud width: 𝜎 ≲ 16 µm

## Slide 44: Detector backscattering
Measurements with two TRISTAN SDDs in dedicated test setup
  At different electron energies
  At different incident angles
166 px SDD
7 px SDD
Custom e-gun
Steering coils

## Slide 45: Detector backscattering
Good agreement between measurement and simulation
7 px SDD
166 px SDD

## Slide 46: Detector backscattering
Backscattering
  increases with incident angle
  decreases with energy

## Slide 47: Detector module
Challenges:
High density: 400 wire bonds to detector chip
3D design to have readout electronics behind sensor
UHV vacuum and magnetic field compatibility
Cooling to -50°C
...
Cesic
Copper cooling structure
Wire bonds
SDD chip, 38 x 40 mm
200-pin array connector
Flex cable
7x ETTORE ASIC

## Slide 48: Detector module

## Slide 49: KATRIN - Sterile Neutrino Model
Rear wall
Backscattering
Source
Scattering on gas molecules
e
e
e
T2
Detector
Dead layer
Backscattering
Charge sharing
e
Transport
Adiabaticity
Change rear wall material
Adjust gas density
Adjust magnetic field
New detector system

## Slide 50
Backscattering of electrons at rear wall changes spectral shape → limits sensitivity considerably
Possible solutions:
  Change rear wall material, e.g. Au → Be
  Block electrons from rear wall with blocking potential, e.g. -20 kV potential
  Positive rear wall
e
Rear wall

## Slide 51
Maximum allowed detector rate (100 kcps/px):
  defines column density for selected mass range
  defines retarding potential
Possible solution:
  Adjust column density to smaller value
p
n
Electron energy
Counts
Low retarding potential
High mass range
Shorter meas. time
High retarding potential
Low mass range
Longer meas. time
Source section

## Slide 52
Adiabatic transport needs to be assured
Non-adiabaticity:
  Chaotic transmission in spectrometer due to high E and B field gradients
  Energy-dependent transmission loss / gain
Transport section
With existing coils / currents

## Slide 53
<0
>0
Adiabatic transport needs to be assured
Non-adiabaticity:
  Chaotic transmission in spectrometer due to high E and B field gradients
  Energy-dependent transmission loss / gain
Solution:
  Adjust B field settings (Bmax on source side)
  No transmission loss for
  sufficiently large
Transport section

## Slide 54
Replace current detector flange with novel flange holding TRISTAN detector
Upgrade sealings to UHV standard, add cooling option
Chamber for ~4000 connections
Detector section
>> Maximize synergies with current setup

## Slide 55: DAQ System
Custom-developed system
  Higher event rates
  More readout lines
  Operation in strong magnetic field, HV
  Trigger flexibilities, etc.
First successful tests

## Slide 56: Spectrum Modeling
Systematics must be well understood
Complete model currently being developed