## Slide 1
Micromegas detectors at Saclay : Past, Present, and, Future experiments
16th Advanced detector PISA Meeting
Maxence Vandenbroucke for the Saclay MPGD lab
CEA Saclay
maxence,Vandenbroucke@cea.fr

## Slide 2
Micromegas

## Slide 3
Sparks reduction R&D (2010)
Micromegas Timeline at Saclay
HDB
COMPASS (2001)
Future experiments

## Slide 4: The Pixel Micromegas for COMPASS (2011)
What’s new ?
  GEM preamplification
GEM at 2mm
MM alone
Spark probability VS Gain
Notes: Sparks pb

## Slide 5: The Pixel Micromegas for COMPASS
What’s new ?
  GEM preamplification for sparks
  1280 Pixels in beam area for high rate (10 MHz/cm²)
  Bulk Micromegas
Conditions
  10⁷ Muon/s or 108 hadrons/s beam
  APV25 readout
  Ne/C2H6/CF4 (80/10/10)
The 40x40cm2 COMPASS MM
Bulk MM
GEM
Integration
Test

## Slide 6: PMM – Results : Sparks and Efficiency
Sparks
  Every 5-10 min in high rate hadrons
  No consequence on efficiencies
  No ageing
Muons (2015)
Muons (2022)
Hadrons (2015)
(loss of area = APV card issue)
See : Aging effects in the COMPASS hybrid GEM-Micromegas pixelized
Detectors (JINST, 2023) D. Neyret et al.
Notes: Btw 11 years, efficiency increase, it gets better like wine

## Slide 7: PMM – Results : Resolution
Resolution
  Spatial : ~80um (down to 60um in the best conditions)
  Time :
    9ns muons (Ne/C2H6/CF4 80/10/10)
    13ns hadrons (Ne/C2H6/CF4 85/10/5)
See: Performance of large pixelised Micromegas detectors in the COMPASS environment (JINST, 2013) F.Thibault et al.

## Slide 8: CLAS12 - 2017
What’s new ?
  Cylindrical resistive Micromegas
  DREAM electronics
pillar
3mm
-1000V

## Slide 9: CLAS12 – Micromegas tracker
Cylindrical Micromegas
  Strip resistive Micromegas
  6 Layers with different radius (18 det.)
  1D drift C or Z, 3mm drift
  Very light : 0.5% of X0
Forward Disk Micromegas
  20MHz integrate rate
  2 independent resistive zone
  1D strip design rotated at 60 deg
Conditions
  5T Magnetic field, gas Ar/Iso (90/10)
  11GeV e- beam up to 1035 cm-2s-1
Bulk
Resistive
Integration
Test
See: The CLAS12 Micromegas Vertex Tracker (NIMA, 2020) F.Bossu et al.
target
e-

## Slide 10: CLAS12 - Operations
6 Cylindrical layers
Operation issues
Maintenance by zoom since COVID
Multi purposes DREAM readout

## Slide 11: CLAS12 - Efficiencies
Highest intensity e- beam on Cu/Sn target
2019, LH2, 50nA
LH2 target, Efficiencies above 90%
Efficiencies down to 80% due to wrong gas mixture and distribution, now swap with ALERT detector
2022 :
Efficiencies not 99% due to 3mm drift and 5T magnetic field
Notes: All layers works and we will see with fixed gas issues after ALERT

## Slide 12: CLAS12 - Performances
See: Alignment of the CLAS12 central hybrid tracker with a Kalman Filter (NIMA, 2022) M. Arratia et al.
Alignment data with cosmic
  Average cluster size: ~4
  Centroid residuals after alignment:
    Z detectors: 432µm
    C detectors: 258µm
With external tracker at Saclay ~200um
Time resolution of FMT : 15ns (LH2 target, 2018)

## Slide 13: Muon Tomography – 2016
What’s new ?
  Cheap 2D Resistive 50x50cm detectors
  DREAM electronics
See Tuesday Talk : B. Lefevre, 2D and 3D analysis improvements with Machine Learning for Muography Applications
Bulk @ ELVIA
Resistive
Integration
Test @ Saclay

## Slide 14: ATLAS NSW - 2021
What’s new ?
  Large detectors
  VMM electronics
  Floating micromegas
See Friday Talk : S. Rosati, ATLAS New Small Wheel Performance Studies with 2023 (LHC Run3) data
See : The large inner Micromegas modules for the Atlas Muon Spectrometer upgrade: Construction, quality control and characterization, (NIMA, 2022) E. Ferrer et al.

## Slide 15: The TPC Outer Tracker for sPHENIX (2022)
What’s new ?
  Fast design + production at Saclay (1y), 20 MM
  Zigzags readout for 2mm
  Resistive segmentation
  SAMPA FEE from TPC
🔎
First design 09/2021
Installed 02/2023
Bulk MM
Resist
Integration
Test

## Slide 16: The TPC Outer Tracker for sPHENIX
Efficiency in cosmic rays ~99%
Resolution in cosmic rays
  390um for 1mm strips (Phi)
  420um for 2mm zigzag strips (Z)
See : The sPHENIX Micromegas Outer Tracker, (submitted to Elsevier, 2024) H. Pereira Da Costa et al.

## Slide 17: The TPC Outer Tracker for sPHENIX
Now in Au-Au collision
Correlation between MM and Minimum Bias Det.
See : The sPHENIX Micromegas Outer Tracker, (submitted to Elsevier, 2024) H. Pereira Da Costa et al.
Time Distribution of all MM in Au-Au

## Slide 18: Other Micromegas « sparks »
Glass Micromegas, X-Rays
From the HBD, coupling MM with photon convertor => Picosec (2015) (see A. Kallitsopoulou talk)
Glass Micromegas, Neutrons
Glass Micromegas, Beta for medical imaging
From : Optical readout Micromegas for neutron and beta imaging Antoine Cools - 13/12/2023
Starting 2018
2024
2023
Bulk MM
Integration
Test

## Slide 19: Future : P2 (2025-2026)
What’s new ?
  Light metallic micromegas (aim at ~0.2% of an X0) “Sail tracker”
  VMM SRS FEE + custom made backend + Online Trigger
  1280x1cm2 pads per 60o sector, 18 det. Total ~20k channels
Conditions :
  Ebeam = 155 MeV, Ibeam = 150 mA
  Backward scattered electron = Low energy (=xray)
  100MHz signal integrated in backward (100GHz forward …)
<- 60cm ->
Challenging PCB routing
Bulk MM
Integration
Test
e-

## Slide 20: Future : P2 (2025-2026)
“RD4” 10x10cm2 prototypes
  Sail trackers with carbon frame OK
  Rate validated with 800MeV electrons at Mainz OK
  ~5 sparks during data taking (electrons below the hadronic threshold)
Remaining issues
  Sail tracker difficult to bulk in full size
  VMM hybrids are not well protected for sparks
  3mm drift gap with mylar might be challenging
Current Vs Rate
Mylar
Readout Kapton
Mesh
Drift
Mylar

## Slide 21: Future : EIC (2027-2029)
What’s new ?
  Cylindrical resistive bulk MM
  2D strip readout
  SALSA chip
CyMBAL: Cylindrical Micromegas Barrel Inner Layer
  Low material budget: 0.5% of an X0 in the active area
  Spatial resolution of ~150μm
  Timing resolution ~10ns
  Compact design, inside a ~2T magnet
Single tile
Bulk MM
Resist
Integration
Test
See poster : MPGD Trackers in the ePIC Detector at the EIC, Kondo Gnanvo

## Slide 22: Future : EIC (2027-2029)
RD4 Test Beam at Mainz with 880MeV electrons
  2xUrwell to study 2D readout
  2D ”Diamonds” with resistive MM
  2xResistive MM for 2D readout
  Resistive grid patterns in production
Results non conclusive due to multiple scattering
  Next test beam in September 2024 with fixed geometry to get best 2D readout design

## Slide 23: SUMMARY AND OUTLOOK
  All these projects made within large collaborations and thanks RD51 ! And welcome DRD1 !
    GEM + MM for COMPASS
    Cylindrical MM for CLAS12
    Large MM for NSW
    Robust MM for sPHENIX
    And many more : T2K, forfire, ILC, ZZ R&D, ASACUSA, Gbar …
  Next
    Light sail trackers for P2 with fast VMM acquisition
    Cylindrical and new ASIC for EIC