## Slide 1: Attività 2024 WP Acceleratore
Incontro coi referees
Roma, 4 settembre 2023
Manuela Boscolo (INFN-LNF)

## Slide 2: Team italiano FCC Acceleratore: WP2 RD_FCC
Regione di Interazione e Machine-Detector Interface LNF, Pisa, Perugia (FCCIS, AidaInnova)
Collimation studies CERN doctoral student & Sapienza /LNF
Cavita’ SRF LNL (iFAST)
Damping Ring e+ e linee trasferimento vicine al DR LNF (CHART)
Effetti collettivi INFN-Roma1, LNF (FCCIS)
Sorgente ibrida di positroni a cristalli INFN-Ferrara (PRIN)
Ottimizzazione beamline linea di cattura e+ INFN-Milano
Diagnostica per il controllo della corrente bunch-by-bunch via Compton scattering INFN-Milano
Interesse sui magneti SC di FCC-ee INFN-Genova
Magneti ad alto campo FCC-hh [progetto separato dal feasibility study FCC] INFN-Genova, INFN-Mi
FONDI ESTERNI,
PROGETTI EU & SINERGICI
giallo: sezioni nuove
italico: progetti x strategy GE

## Slide 3: Progetti su FCC finanziati dalla giunta INFN per la prossima European Strategy for Particle Physics Update (ESPPU)
IR and MDI full-scale mockup
SRF cavities
Progetti revisionati ed approvati dal MAC, finanziati separatamente dalla Giunta ma senza FTE dedicati, gli FTE sono conteggiati in RD_FCC ma hanno comitati di review (in parte) diversi.
Questi progetti sono stati presentati alla CSN1 di luglio
Esiste anche un progetto non ancora finanziato sui damping rings (vedi dopo).

## Slide 4: Disegno Regione di Interazione e MDI
Progettazione meccanica IR e MDI, parte di FCCIS
  Disegno beam pipes, bellows, BPM, magneti e criostato, supporti
  Integrazione vertex e lumical
R&D sperimentale sul disegno della regione di interazione con un mockup della IR (finanziamento ad hoc GE & CERN)
Disegno ed integrazione vertex detector di IDEA
  layout, cabling & services, simulazioni termo-meccaniche e cooling
Studio dei fondi macchina nel rivelatore
Studio beam losses & collimation design
Final Focus optics – non-local solenoid compensation scheme with P. Raimondi (alternative under study)
Beamstrahlung radiation and handling
LNF: M. Boscolo, G. Broggi, A. Ciarma, E. Di Pasquale, F. Fransesini, S. Lauciani; Pisa: F. Bosi, F. Palla; Perugia: G. Baldinelli, L. Fanò, C. Turrioni

## Slide 5: Mechanical model for the FCC-ee MDI
Inlet/outlet for paraffin cooling (copper)
Two halves AlBeMet pipe
Transition
Bellows
Electron Beam Welding
Thick copper deposition
  Inner radius 10 mm
  Outer radius 11.7 mm
Central Support tube with endcaps
Low impedance vacuum chamber, warm and cooled (prototyping and mockup planned)
M. Boscolo, F. Palla, F. Fransesini, F. Bosi and S. Lauciani, Mechanical model for the FCC-ee MDI, EPJ Techn Instrum 10, 16 (2023)
https://doi.org/10.1140/epjti/s40485-023-00103-7
Presentations at FCC WEEK 23 by
Fabrizio Palla (INFN-Pisa) & Francesco Fransesini (INFN-LNF)
https://indico.cern.ch/event/1202105/
M. Boscolo et al., Status of the IR and MDI of the FCC-ee, IPAC23, 7-12 maggio 2023;
A. Novokhatski, et al. Estimated heat load and proposed cooling system in the FCC-ee IR beam pipe, IPAC23, 7-12/5/2023
To reduce the cooling material, the design provides five channels for each side; in this way is possible to use the needed quantity of coolant and reduce the material, creating a light structure.
Notes: central chamber we are working at the moment

## Slide 6: Vertex integration with accelerator components
Vertex (MAPS) with 3 inner layers supported by the conical chamber and mounted with the beam pipe and LumiCal to the support tube
Vertex outer layers and 6 disks (MAPS) mounted directly on the support tube.

## Slide 7: Mock-up della regione di interazione
Motivi
Validazione della progettazione meccanica dei disegni CAD del MDI
Permette di comprendere meglio i servizi, come i cavi e i tubi
Permette di avere una visione più ampia della sequenza di installazione e dei possibili intoppi.
Può aiutare a prevedere potenziali problemi di accesso all’IR
Outreach
Obiettivi e attivita’ relative al mock-up presentate alla CSN1 di luglio

## Slide 8: Assegnazione temporale delle risorse finanziarie Progetto MDI mockup (estratto dal verbale del MAC)
Per tutti i progetti, il 40% delle risorse allocate (missioni e attrezzature) saranno rese disponibili per consentire lo svolgimento del lavoro dei primi 18 mesi di attività. Il rimanente 60% dei fondi è posto sub-iudice.
I fondi sono assegnati alla CSN1 secondo modalita’ che verranno concordate con il Presidente di Commissione. Il MAC affianchera’ la Commissione nel referaggio. Una sessione ad-hoc per un’analisi dello stato dei progetti potrebbe essere tentativamente fissata nell’autunno del 2024.
Progetto | Strutt. INFN | Attrezzature |  |  | Missioni |  |  | TOT. | AdR(**)
 |  | totale | 1a asseg. | sub iudice | totale | 1a asseg. | sub iudice |  | 
MDI mockup FCCee | LNF et al. | 80 KE | 32 KE | 48 KE | 10 KE | 4 KE | 6 KE | 90 KE | -

## Slide 9: Accordo INFN-FCC CERN (aka Addendum)
In via di approvazione da parte degli uffici legali dell’INFN (ok) e del CERN (nuova versione in approvazione)
INFN
CERN
To be defined
DRAFT

## Slide 10: Thermal simulation started
Full model
Extraction of a radial sector for layer 3
Start from a radial sector of layer 3 (relying on periodic symmetry) and import in ANSYS FEA. Then move to all other layers.
….
Inlets
Outlets
….
Simplification of the solid domain
Sensors
Definition of the fluid volume
FIRST STEPS
INFN Perugia
G. Baldinelli, F. Bianchi, C. Turrioni

## Slide 11: Preliminary results – simulations
TEMPERATURE OF THE SENSORS (SILICON)
Maximum temperature = +66°C
Air velocity drops to 10 m/s inside (from 20 m/s)
Thermal figure of merit:
66-15 = 51°C
Linear behaviour
11
Feeding holes diameter is 2.5 mm too small  next try 6 mm (>5x flux increase)
Air at 15°C – 20 m/s

## Slide 12: Validazione del sistema vertex
Modelli meccanici in scala 1:1 dei rivelatori di vertice (Pisa)
  Utilizzeremo Alluminio per la parte dell’Outer Vertex e dei dischi
  Fibra di carbonio per il rivelatore di vertice
  Studio del routing dei cavi.
Validazione del cooling ad acqua per l’outer vertex e dischi (Pisa)
  Singola stave con tubi di raffreddamento con acqua e fogli riscaldanti (100 ± 20 mW /cm2)
Validazione su piccola scala delle simulazioni termiche sui materiali (Perugia)
Termocriostato per caratterizzazione di piccoli elementi (12kE su Pisa)
Validazione cooling dell’inner vertex (Pisa)
  Realizzazione di un modello del vertex in fibra di carbonio e del supporto conico con i canali
  Fogli riscaldanti per simulare la dissipazione tra 50 ±20 mW/cm2
  Realizzazione di un setup dedicato alla validazione del cooling ad aria (Wind tunnel)
    Parte del setup utilizzerà fondi specifici allocati dalla GE per il mock-up a LNF, e la copertura richiesta su RD_FCC è per le parti specifiche che servono solo per quello ’stand-alone’ a Pisa.
      richiesti a luglio 20kE subj alla stima dei costi, che oggi siamo in grado di quantificare

## Slide 13: Schematic design for the wind cooling tunnel for FCC inner tracker
F. Bosi, M. Massa, F. Palla
Ventilation
Unit 1
Conical Sector 1
Heat exchangers
Refrigeration Unit
Electrical resistance
Inner Tracker tube
Pressure sensor
Temperature sensor
Flow sensor
Return air circuit
Adjustable flow restriction
Camera Vision
Ventilation
Unit 2
Conical sector 2

## Slide 14: Wind tunnel for VTX air cooling

## Slide 15: Total Cost Wind Cooling Tunnel
item | cost for Pisa wind tunnel [Keuro] | used and paid by MDI Mockup project (GE-CSN1) [kEuro] | cost requested to RD_FCC RD_Flavour [kEuro]
Dummy inner vertex | 15 | 15 | 0
Ventilation units | 2 |  | 2
Heat exchanger | 0.3 | 0.3 | 0
Refrigeration unit | 17 | 17 | 0
Electrical resistance | 0.5 | 0 | 0.5
Adj. restrictions | 0.5 | 0 | 0.5
Connecting tubes | 3 | 0 | 3
Support structure | 2.5 | 0 | 2.5
Instrumentation | 8 | 0 | 8
TOTAL | 48.8 | 32.3 | 16.5

## Slide 16: Progetti su FCC finanziati dalla giunta INFN per la prossima European Strategy for Particle Physics Update (ESPPU)
IR and MDI full-scale mockup
SRF cavities
Progetti revisionati ed approvati dal MAC, finanziati separatamente dalla Giunta ma senza FTE dedicati, gli FTE sono conteggiati in RD_FCC ma hanno comitati di review (in parte) diversi.
Questi progetti sono stati presentati alla CSN1 di luglio

## Slide 17: Thin film SRF cavities R&D @LNL
FCC-ee requires higher cavities performances wrt LHC
Mandatory improve all production steps
LNL: Cristian Pira, G. Keppel, F. Stivanello, D. Fonnesu
Deposizione Nb3Sn su Cu. Cavità a 400 MHz di FCCee.
il coating via magnetron sputtering (DC-MS) di film superconduttivi di Nb3Sn su Cu;
il Plasma Electrolytic Polyshing (PEP) di Cu e Nb per la preparazione dei substrati (alternativo ad EP e sostenibile), brevetto INFN. Scaling 6 → 1.3 GHz.
lo spinning per la produzione di cavità seamless in rame.
Vantaggi. Meno Nb, da 2 a 4.2K (energy saving), Ea → più alto. Competitors: Sn vapor diffusion (ma su cavità di Nb!), PVD su Cu (€, rth, cryocooler). Attività high risk high gain, di prospettiva pluriennale.
FCCee: 1364 cavities
In total
Attivita’ in sinergia con iFAST

## Slide 18: SRF cavities project Budget
Finanziamento richiesto (k€) | WP | Item per cui si richiede tale finanziamento
20 | 1,2,3 | Missioni
30 | 1,2 | Consumabili vari
15 | 1 | Target Nb3Sn (4” per test e rettagolare per cavità 1.3 GHz)
10 | 1 | Passante rotante magnetico e motore per rotazione cavità 1.3 GHz
20 | 1 | Sorgente Magnetron rettangolare
120 | 1,2 | Ion Milling
10 | 2 | Adattamento impianto QWR ALPI per PEP
40 | 2 | Modifiche impianto Polishing 1.3 GHz per PEP
40 | 2 | Struttura per Jet-Polishing su 1.3 GHz
10 | 2 | Upgrade corrente alimentatore PEP
50 | 2 | Soluzioni chimiche
30 | 2 | Lastre rame OFE per campioni e cavità spinning
30 | 2 | Lastre Nb per cavità
10 | 2 | Stampo nylon cavità 1.3 GHz
10 | 3 | Stampi materiale bassofondente
25 | 2 | Spinning cavità
ATTREZZATURE |  |  | MISSIONI |  |  | TOT | AdR
TOT | 1a asseg. | 2a asseg. | TOT | 1a asseg. | 2a asseg. |  | 
440 | 180 | 260 | 20 | 8 | 12 | 460 | 50

## Slide 19
WP4 Funded by CHART –Swiss program: Collaboration between PSI and CERN with external partners
FCC-ee Damping Rings
Several injector layout have considered with different TL arrangements, latest FCC-ee injector layout 6 GeV option (since April 2022)
LNF: C. Milardi, A. De Santis, S. Spampinati, E. Ozgur

## Slide 20: Hybrid crystal-based positron source for future e+e- colliders
Main advantages of the hybrid source:
  Enhancement of photon generation in crystals in channeling conditions  enhancement of pair production in the converter target!
  High rate of soft photons  creation of soft e+ easily captured in matching systems
  Decrease of the deposited energy and Peak Energy Deposition Density (PEDD) in the converter target!
→ total energy deposit shared between the two stages ⇒ overall lower energy density
→ very low energy deposit and PEDD in thin radiator (< X0) ⇒ very low heating and thermo-mechanical stress
Idea of R. Chehab, V. Strakhovenko and A. Variola, NIM B 266 (2008) 3868
Conventional
Hybrid scheme
Thin radiator
Thick converter
Activity started in RD-FA and continued in RD-MUCOL for either LEMMA and FCC -> now moving in RD-FCC since is fully focused in the design and test of a possible hybrid source for FCC
Sept 2022: MoU between INFN-Ferrara and IJCLab to develop hybrid crystal based positron sources for future colliders

## Slide 21: Attività Infn Ferrara 2024
  Design, realizzazione di targhette cristalline finalizzate per il test al PSI within ;
  Design e realizzazione di convertitori amorfi – granulari (per diminuire la PEDD nel convertitore);
  Continuazione ed ottimizzazione dei test di irragiamento delle targhette per valutarne la resistenza in condizioni simili a FCC (di recente abbiamo ricevuto contatti dal gruppo STI CERN per possibili test oltre quelli a MAMI);
  Caratterizzazione cristallografica delle targhette prima e dopo l’irragiamento;
  Test di radiatori cristallini con fasci di elettroni di alta energia al CERN PS e design/preparazione del setup con misura dei positroni;
  Finalizzazione del modello MC in Geant4 e implementazione della full simulation della sorgente nell’injector di FCC-ee;
  Definizione della configurazione per il test al PSI mediante Monte Carlo.
The final goal is to be ready with a full hybrid source desing to be directly compared with the conventional one and to be tested within the second phase of CHART@PSI in the full injector
INFN-Ferrara: L. Bandiera, N. Canale, G. Paternò, A. Sytov

## Slide 22: PRIN 2022 e+BOOST
Cofinanzia l’attività, in particolare con assegni di ricerca/dottorandi e parte dell’apparato sperimentale (rivelatori)!
INFN 100 keuro (P.I. L. Bandiera) , UniInsubria 60 keuro (M. Prest) e UniNapoli 40 keuro ( A.O.M. Iorio)
22
Intense positron source Based On Oriented crySTals - e+BOOST (PI L. Bandiera)
Financed by Italian Ministry of University and Research - PRIN project

## Slide 23: Richieste Ferrara 2024
MISSIONI (9.5 keuro)
Missioni a MAMI per test irraggiamenti (3 persone 5 gg) 3.5 keuro
Missioni al CERN PS per test di radiatori cristallini (2 persone 7 gg) 3 keuro
Missioni a IJCLab per simulazioni per CHART Injector (1 persona 15 gg) 3 keuro
CONSUMO (14 keuro)
Nuove targhette circolari e più larghe di W cristallino per minimizzare PEDD, con spessore tra 1 e 2 mm finalizzato dal Monte Carlo e dalla geometria del fascio del PSI (12 keuro)
Convertitori di tungsteno amorfi e granulari 0. 5 keuro
Realizzazione holder per caratterizzazione cristalli al diffrattometro e su fascio 1. keuro
Termocoppie per test irraggiamento 0.5 keuro

## Slide 24: Collective effects activity ongoing 2023 and for 2024
Essential to assess beam current limits and instability thresholds  luminosity
Impedance budget evaluation in longitudinal and transverse planes
for the 4IP layout and for the booster (booster in collab. with DESY)
Single beam collective effects in longitudinal plane: microwave instability
Single beam collective effects in transverse plane: transverse mode coupling instability (TMCI)
    typically not cured in beam-beam collisions. Simulations give us an indication if we can expect problems with the transverse impedance.
Beam-beam interaction including the longitudinal impedance
M. Migliorati (Sapienza & INFN-Roma1)
M. Zobov (LNF), M. Bethouei (LNF)
M. Migliorati et al, Study of Beam-Beam Interaction in FCC-ee Including Updated Transverse and Longitudinal Impedances», for IPAC23
M. Migliorati et al, Studies of FCC-ee Single Bunch Instabilities with an Updated Impedance Model», for IPAC23
Richieste su LNF: Licenza software CST Microwave Studio per calcolo impedenza e wakefields 12 k€

## Slide 25: Beam Dynamics Studi a INFN-Milano
Attivita’ cominciata nel 2023 continuera’ nel 2024
Disegno ed ottimizzazione linea di cattura sorgente positroni con ASTRA e GIOTTO
INFN-Milano: A. Bacci, F. Broggi, M. Rossetti Conti, I. Drebot

## Slide 26: Gran Totale Richieste Acceleratore
MDI
Galleria del vento per dimensionamento raffreddamento vertex, Pisa 16.5 k€ (richiesta a RD_Flavour)
Termocriostato per caratterizzazione di piccoli elementi Perugia, richiesta su Pisa 12k€
Licenza software Autodesk progettazione meccanica Pisa 3 k€
EFFETTI COLLETTIVI
Licenza software CST per calcolo impedenza Roma-1, richiesta su LNF, 12 k€
SORGENTE POSITRONI IBRIDA A CRISTALLI Ferrara
  Missioni 9.5k€
  Consumo 14k€
WP acceleratore Missioni per riunioni, meeting, conferenze

## Slide 27: Conclusioni
Forte spinta di FCC dal CERN e dalla comunità internazionale
Le attivita’ di macchina su FCC sono in crescita, con un aumento degli FTE in RD_FCC WP-Accel
Siamo un gruppo impegnato su diversi item rilevanti.
Quest’anno sono partite anche attività di R&D di validazione sperimentale in vari ambiti
  MDI, SRF con finanziamenti GE (e CERN)
  sorgente positroni (Chart, PRIN, INFN)

## Slide 28: Materiale addizionale

## Slide 29: Attivita’ prevista per Frascati per il mock-up per il 2024-5
Modelli meccanici in scala 1:1 della camera da vuoto centrale e della camera conica inclusi i circuiti di raffreddamento
Test di validazione della thick copper deposition sul AlBeMet
Modello meccanico dei soffietti
Disegno esecutivo struttura di supporto fibra- di carbonio insieme a Pisa
Disegno supporti meccanici
Assemblaggio

## Slide 30: Spazi di assemblaggio e test ai LNF
Identificato un laboratorio con un tavolo di granito sufficiente.
Alcuni lavori di ammodernamento strutturale e di equipaggiamento in fase di discussione.

## Slide 31: MDI – Studio dei fondi nel rivelatore e particelle perse con ottimizzazione collimatori
Studio dell’impatto dei fondi macchina e radiazione di sincrotrone, studio di shielding a protezione del rivelatore e componenti della macchina
Lavoro di modellizzazione della IR nel software di fisica per tracciare primari e secondari
Ottimizzazione delle maschere per la radiazione di sincrotrone, e collimatori per fermare particelle che si perderebbero nella IR
Anagrafica:
A. Ciarma, art.36 fondi esterni FCCIS (LNF), 1FTE
G. Broggi, CERN doct. student & Sapienza, LNF, 1 FTE
Background from SR photons
Andrea Ciarma
Giacomo Broggi

## Slide 32: Alcuni preventivi per il tunnel di raffreddamento
preliminare

## Slide 33: Ventilation Unit
Duct fan Euro 377+IVA
N.3 pezzi Totale Euro 1379,82

## Slide 34: Heat Exchanger
Heat exchanger Euro 219+IVA
N.1 pezzo Totale Euro 267,18

## Slide 35: Refrigeration Unit
Refrigeration Unit Euro 13.628+IVA
N.1 pezzo Totale Euro 16.626

## Slide 36: Electrical Resistance
Electrical Resistance Euro 400+IVA
N.1 pezzo Totale Euro 488

## Slide 37: Adjustable Restriction
Adjustable Restriction Euro 350+IVA
N.1 pezzo Totale Euro 427

## Slide 38: Instrumentation
N.4 Probe warm wire Euro 480+IVA = 2342,4
N.2 Probe Helical Euro 775+IVA = 1891
N.3 Probe Pitot Tube Euro 254+IVA = 929,64
N.3 Humidity probe Euro 674+IVA = 2466,84
Totale Euro 7629,88

## Slide 39: VXD Cooling Study

## Slide 40: Overall Vertex layout
Total power ~120 W – Air cooled
Total weight ~230 grams
3 layers

## Slide 41
15 overlapping staves of 6 modules each
Power budget ~12 W
Total weight ~22 grams
Layer 1

## Slide 42
24 overlapping staves of 10 modules each
P
Power budget
~32 W
Total weight ~63 grams
Layer 2

## Slide 43
18 overlapping staves of double 16 modules each
Total weight ~150 grams
Power budget
~77 W
Layer 3

## Slide 44
APPROACH FOR THERMAL SIMULATIONS
Heat transfer through solid bodies and to the fluid (air) must be taken into account in the thermal model.
The geometric complexity of the structure and the small thickness of the parts are the most challenging aspects: simplifications of the model are needed.
Full model of the three layers

## Slide 45
APPROACH FOR THERMAL SIMULATIONS
Focus on Layer 3

## Slide 46
APPROACH FOR THERMAL SIMULATIONS
Starting from a radial sector of layer 3 to understand the level of detail that can be handled with simulation.
….
Inlets
Outlets
….
Simplification of the solid domain
Sensors
Volume of the fluid

## Slide 47
THERMAL SIMULATIONS
GRID CREATION
13,745,863 nodes
Smallest edge: 0.25 mm
Longest edge: 557 mm
Ratio: 2,228

## Slide 48
THERMAL SIMULATIONS
GRID CREATION
Power generation (8.55 W in the silicon only )
Carbon fiber
Rohacell
Air

## Slide 49
THERMAL SIMULATIONS
MODELS AND BOUNDARY CONDITIONS
Thermal conductivity values
Silicon = 148 W/mK
Rohacell = 0.3 W/mK
Carbon fiber truss = 180 W/mK (isotropic)
Carbon fiber truss = 2 W/mK (isotropic)
Air = 0.025 W/mK
Power generation
Carbon fiber
Rohacell
Air

## Slide 50
THERMAL SIMULATIONS
PRELIMINARY RESULTS
PATHLINES COLOURED BY TEMPERATURE
Inlet
Outlet

## Slide 51
THERMAL SIMULATIONS
PRELIMINARY RESULTS
PATHLINES COLOURED BY TEMPERATURE (INLET)
Inlet air average temperature = 15°C

## Slide 52
THERMAL SIMULATIONS
PRELIMINARY RESULTS
PATHLINES COLOURED BY TEMPERATURE (OUTLET)
Outlet air average temperature = 39°C

## Slide 53
THERMAL SIMULATIONS
PRELIMINARY RESULTS
VELOCITY FIELD IN A PLANE (COLOUR BY VELOCITY)

## Slide 54
THERMAL SIMULATIONS
PRELIMINARY RESULTS
VELOCITY FIELD IN A PLANE (COLOUR BY VELOCITY)
Average velocity in the section = 0.68 m/s

## Slide 55
THERMAL SIMULATIONS
PRELIMINARY RESULTS
TEMPERATURE OF THE SENSORS (SILICON)
Maximum temperature = +66°C
Air temperature at the inlet= +15°C
(at 20 /m/s)
Thermal figure of merit:
66-15 = 51°C
Linear behaviour

## Slide 56
THERMAL SIMULATIONS
CONCLUSIONS AND FUTURE WORK
Preliminary simulations show that the air cooling seems a feasible way for the thermal management of the vertex
The model has to be improved strongly:
  Anisotropy of the materials
  Turbulent model
  Grid independence check
  Refinement of the boundary conditions
Optimisation of the system (on course): speed and temperature of air, proper direction of the inlet flow, materials, connection with the other layers, etc…
Experimental validation of the simulations
A parallel mechanical analysis is needed

## Slide 57: Hybrid Crystal-based e+ source for FCC-ee
Speaker: L. Bandiera - INFN Ferrara
bandiera@fe.infn.it
04/09/2023

## Slide 58: Hybrid crystal-based positron source for the FCC-ee
CHART project at
Crystal radiator
Test foreseen after 2025
CHART project on the FCCee Injection System: Collaboration between PSI and CERN with external partners: CNRS-IJCLab (Orsay), INFN-LNF, INFN-Ferrara, KEK (Japan)
Conventional
Hybrid scheme
Thin radiator
Thick converter

## Slide 59: Measurement of the γ-spectrum of the crystal radiator
Versatile setup adaptable to CERN PS and DESY beam tests
Electron energy of 5-6 GeV – of interest for future e+e- colliders (FCC-ee, ILC, CLIC, LEMMA, CEPC …)
Activity currently on RD-MUCOL
Notes: Nevertheless, W was used in past e+ source experiments and Ir in NA48. We also have an experience with W in collaboration with KLEVER/NA62.

## Slide 60: Measurement of the γ-spectrum and MC validation
⇒ Increase in the average number of high-energy deposit events (i.e. in the average number of events featuring many output photons — more than 2) in case of axial alignment if compared to random.
The active photoconverter gives the average information on the number of radiated photons
L. Bandiera et al., Eur. Phys. J. C 82, 699 (2022)
⇒ larger and peaked energy loss distribution in axial vs. random orientation!
electromagnetic radiation in the BGO calorimeter at different angular configurations
e- @5.6 GeV
Electron beam energy: 5.6 GeV
Crystal target: W <100>, 2.24 mm long
Channeling critical angle ≈ 1 mrad
W crystal X-ray topography @BM05
Notes: Nevertheless, W was used in past e+ source experiments and Ir in NA48. We also have an experience with W in collaboration with KLEVER/NA62.

## Slide 61: Hybrid source optimization for FCC-ee
Collaboration with IJCLab (leader I. Chaikovska)
M. Soldani (INFN-Ferrara)
energy deposit and PEDD in amorphous converter can be reduced by tuning L (while keeping the radiator thickness fixed to maximise EM enhancement) and D
L
D
L. Bandiera et al., EPJC 82, 699 (2022)
E = 6 GeV
σ = 500 μm
σ’ = 100 μrad
Geant4 simulation of the converter stage…
(radiator stage already optimised with dedicated code and experimental data→ dedicated input files)
W <111> 2 mm
Activity currently on RD-MUCOL
Notes: Nevertheless, W was used in past e+ source experiments and Ir in NA48. We also have an experience with W in collaboration with KLEVER/NA62.

## Slide 62
conventional (amorphous)
collimator
magnet
a = 5.5 mm
FCC-ee hybrid vs conventional e+ source
M. Soldani (INFN-Ferrara) in collaboration with I.Chaikovska (IJCLab)
To be tested at PSI
in 2025
Huge reduction of PEDD in the converter!
Same or even higher rate of positrons!
Activity currently on RD-MUCOL
Notes: Irradiation tests to measure the heating/radiation resistance (A past test at SLAC with a thin W crystal (0.3 mm thick) showed no damages up to a fluence of 2x1020 e-/cm2. We would try to get a larger fluence to determine the damage threshold) PEDD, or Peak Energy Deposition Density, refers to the maximum amount of energy deposited per unit volume in a given material or medium during a specific event or process. It is a measure of the energy concentration within a localized region.

## Slide 63
conventional (amorphous)
collimator
magnet
a = 5.5 mm
FCC-ee hybrid vs conventional e+ source
M. Soldani (INFN-Ferrara) in collaboration with I.Chaikovska (IJCLab)
To be tested at PSI
in 2025
Huge reduction of PEDD in the converter!
Same or even higher rate of positrons!
Poster @IPAC2023
Activity currently on RD-MUCOL
Notes: Irradiation tests to measure the heating/radiation resistance (A past test at SLAC with a thin W crystal (0.3 mm thick) showed no damages up to a fluence of 2x1020 e-/cm2. We would try to get a larger fluence to determine the damage threshold) PEDD, or Peak Energy Deposition Density, refers to the maximum amount of energy deposited per unit volume in a given material or medium during a specific event or process. It is a measure of the energy concentration within a localized region.

## Slide 64: Targets irradiation studies @MAMI
IPAC 2022: F. Alharthi ,I. Chaikovska , R. Chehab , S. Ogur , S. Wallon , , A. Ushakov , V. Mytrochenko , Y. Zhao , P. Sievers , L. Bandiera , A. Mazzolari , M. Romagnoni , A. I. Sytov , M. Soldani , W. Lauth , O. Khomyshyn , D. Klekots
The results of this work is based on the collaboration between CNRS, University of paris saclay, INFN- FERRARA and MAINZ.
Courtesy of F. Alharthi (IJCLab)
Activity currently on RD-MUCOL
Joint effort between IJCLab and INFN-FE

## Slide 65: INFN Ferrara activity ongoing – 2023 Currently on RD-MUCOL
Experimental activities
Characterization and test on different material than W (Ir and diamond) as a route the final configuration for the crystal radiator and amorphous converter
Optimized irradiation tests on crystal and converter targets at MAMI (planned for November 2023): we are planning to irradiate a crystal sample already characterized by X-ray and tested on e-beam - Joint effort between IJCLab and INFN-FE
VERY PRELIMINARY
Energy loss spectra of 5.6 GeV electrons in a diamond crystal (2 mm, <110>) in different crystal-to-beam orientation.
The analysis of increase of photon number is ongoing

## Slide 66
Monte Carlo activities
Validate the new G4 model for crystal radiator simulation inside Geant4 -> possibility to change crystal parameters inside Geant4
We are goint to use the current MC setup in Geant4 for the implementation of the hybrid-source in the full pre-injector -> collaboration with people involved in this task (from the CHART project)
A. Sytov (MSCA Individual Fellow)
INFN Ferrara activity ongoing – 2023 Currently on RD-MUCOL
VERY PRELIMINARY

## Slide 67: Feasibility Study Timeline and main activities/milestones

## Slide 68: Detector solenoid & IR magnets
Contributo allo sviluppo del solenoide per il rivelatore IDEA con R&D sul conduttore.
Attualmente i magneti per rivelatori sono avvolti con conduttori basati sulla lega NbTi (Tc=9 K). La stabilità rispetto a eventi che possono provocare il quench è garantita da un rivestimento di allumino puro realizzato per co-estrusione. Al momento non esistono più aziende che forniscono questi conduttori.
Tra le possibili alternative, l’uso di conduttori a base di MgB2 (Tc=39 K) è particolarmente interessante e promettente.
La fase iniziale (2023) riguarda uno studio di principio di magneti avvolti con MgB2. La seconda fase richiederà un R&D specifico sui conduttori .
Contributo alla modellizzazione final focus quads QD0, molto simile a quello di SuperB, e test.
La Sezione di Genova ha il software e le competenze per la modellizzazione nonché le attrezzature per i test funzionali (a 4.2 K) su modelli e prototipi.
R. Musenich (0.05FTE), S. Farinon (0.05 FTE) INFN-Ge

## Slide 69
High Field Magnet development program as long-term separate R&D project
Primary goal: open for high energy hadron colliders: three linked challenges are fields↑, costs↓ and power ↓.
CERN budget for material ~ 200 MCHF over ten years
Goal is ~16 T for Nb3Sn, at least ~20 T for HTS
Production of models and prototypes: to demonstrate material, design and engineering choices, industrialisation and costs (HF and long: contrary to RF systems, such magnets are generally not needed for small accelerators or industry)
For muon collider: performance increases with achievable dipole fields in collider ring
Infrastructure and test stations: for tests up to ~ 20 T and 20-50 kA
HTS: for high field and for power reduction (also for Higgs factories) ← Power (FCC-hh) ~ 560 MW ( ~TWh annually) with Nb3Sn and at 1.9K
FCC-hh and the HFM programme
8.3 T Nb-Ti
12 T Nb3Sn
quadrupole
14.5 T Nb3Sn
Demonstrate Nb3Sn magnet technology for large scale deployment, pushing it to its practical limits
in terms of maximum field and production scale.
Demonstrate the suitability of HTS for accelerator magnet applications providing a proof-of-principle
of HTS magnet technology beyond the reach of Nb3Sn.
Courtesy G. Bisoffi