## Slide 1: An Update on the FOOT Experiment (since CSN3, june 2023)
M. Villa (UNIBO & INFN Bologna)
5 September 2023

## Slide 2
Status update (now)
Calorimeter
Magnets
Table mechanics
Inner tracker (see dedicated presentation)
Emulsion Analysis
Future Programs (later)
External funding requests
Fondi 2023: sblocchi SJ, restituzioni, nuove richieste
Fondi 2024: Richieste e chiarimenti
Outline

## Slide 3: Calorimeter - Last advances
Mechanical pieces:
- support table for calibrations delivered in mid May
(no beam facility will cover all front face of the calorimeter; we need to move it)!
- vertical module holders being redesigned to mount in a 6x6 configuration
            Detectors:
            - last batch delivered at the end of May 2023
            - gluing completed in August 2023

## Slide 4: Calorimeter - Timeline
Modules:
  32 modules (288 crystals) assembled, 26 of them already calibrated in temperature
  23 crystals ready at CERN
  gluing at CERN (last 82 crystals) completed since the beginning of July
Temperature calibration:
  to be completed by September 2023
  System assembly:
  in September/October 2023, in Torino
  installation in CNAO by end of October (20-25)

## Slide 5: CNAO2022 Screensaver Runs: Intercalibration Strategies
How can we equalise crystal response?
By analysing carbon Runs we conceive two strategies revolving around the modified Birks function
P0 Shift Method
Easier to implement in SHOE
Less precise
Not-swept crystals friendly
Crystal Calibration Method
Equalisation done with a single multiplying factor
Harder to implement in SHOE
More precise
Impossible retrieve info from not-swept crystals
Equalisation done by calculate energy response curve for each crystal
06/06/2023

## Slide 6: Intercalibration Strategies: P0 Methods
Calibration curves before P0 calibration
Distance between point varies with energy
How can we equalise with a single number?
Fit reference crystal with free parameter
Fit all other crystals with P1 and P2 fixed
P023/P0cry is the intercalibration factor
Calibration curves after P0 calibration
Residual distribution after P0 calibration

## Slide 7: Intercalibration Strategies: P0 Methods – Integral Resolution
Sum amplitude distribution of all 74 crystal after equalization to esteem the total calorimeter resolution
How can we check how the P0 Methods works?
Already implemented in SHOE

## Slide 8: Intercalibration Strategies: Crystal Calibration Methods
Three Carbon energy screensaver points
For each crystal we obtain p0, p1 and p2
Energy esteemed as inverse modified Birks
How can we improve equalisation?

## Slide 9: Intercalibration Strategies: Crystal Calibration Methods – Integral Resolution
Sum Energy distribution of all 74 crystal after ADC to Energy conversion to esteem the total calorimeter resolution
Does integral resolution improve with this method?
Best strategy for next data taking

## Slide 10: Calorimeter Summary
10
Gluing completed
System Assembly in September / October 2023 in Torino
Temperature Calibration to be completed in September 2023
Energy Calibration can be done with the calorimeter fully mounted (beam in “screensaver” mode), the performance is within the requirement (2%)
Next measurements 27 October - 6 November at CNAO
06/06/2023

## Slide 11
Habemus
magnetes

## Slide 13: Permanent magnets – Next steps
Modules arrived in Frascati on 30th August (2 weeks before expected)
1. Validation of the magnets via magnet measurements in Frascati
Two techniques: Hall probe (pointlike) and wire measurements (integral)
2. Insertion of the magnets in the vertical movement system (Frascati, 18-20 sep)
3. Integration of the assembly on the mechanical table (Pisa, mid October)
4. Installation of the whole system in CNAO (20-25 October)

## Slide 14: Status of mechanics
14
Joint effort among:
Pisa, Frascati, Roma, Bologna, Perugia
Most orders have been placed.
Shop work needed in september/october
Time line:
all material in Pisa by beginning of October
Transfer to CNAO from 20 of October

## Slide 15
Rivelatore a emulsioni nucleari:
Stato dell’arte e prospettive
FOOT: referee meeting
A. Alexandrov, V. Boccia, A. Di Crescenzo, G. De Lellis, G. Galati, A. Iuliano, A. Lauria, M. C. Montesi, V. Tioukov
Università di Napoli “Federico II”, INFN Napoli,
Università di Bari, INFN Bari

## Slide 16
The emulsion spectrometer structure
S1: Vertexing
S2: Charge identification
S3: Momentum - range measurement
and isotope identification
10 cm
12.5 cm
C (C2H4) layer
1000 (2000) μm
Emulsion film
300 μm
Lexan
1000 μm
Tungsten
500 μm
Tungsten
900 μm
Lead
1000/2000 μm
200 MeV/n
16O
400 MeV/n
Same structure for the 2019 and 2020 runs

## Slide 17
Stato dell'Analisi
Completata l’analisi sulla misura della carica, in S2, con 16O a 200 MeV/n su target in C e a 400 MeV/n su target in C e in C2H4: articolo in fase di sottomissione
Completata la ricostruzione delle tracce nell’intero ECC a 200 MeV/n con target in C e in C2H4 e a 400 MeV/n con target in C. Collegamento tra le sezioni ottimizzato rispetto ai primi tentativi del 2022
On going: misura dell’impulso dei frammenti usando tecniche di analisi multivariata
Ottimizzata la misura della sezione d’urto integrata a 200 MeV/n su target in C e in C2H4 (miglioramento della ricostruzione dei vertici, della simulazione MC degli effetti strumentali e di ricostruzione)
Pilot test per misure la sezione d’urto di frammentazione in cinematica diretta grazie a Nano-Imaging-Tracker (NIT): emulsioni nucleari con risoluzione della decina dei nanometri

## Slide 18
Stato dell'Analisi
Completata l’analisi sulla misura della carica, in S2, con 16O a 200 MeV/n su target in C e a 400 MeV/n su target in C e in C2H4: articolo in fase di sottomissione

## Slide 19
Stato dell'Analisi
Completata la ricostruzione delle tracce nell’intero ECC a 200 MeV/n con target in C e in C2H4 e a 400 MeV/n con target in C. Collegamento tra le sezioni ottimizzato rispetto ai primi tentativi del 2022. Rimangono criticità per quanto riguarda la ricostruzione di tracce e vertici negli ECC 400 MeV/n a causa di problemi dei film di emulsione nucleare in S1
ΔY
Residual after corrections (GSI3 data)
Display di tracce con più di 100 segmenti (GSI3 data)
ΔX
ΔθX
ΔθY
ΔX
ΔY
ΔθX
ΔθY

## Slide 20
Stato dell'Analisi
On going: misura dell’impulso dei frammenti usando tecniche di analisi multivariata. Test su MC True per trovare le migliori variabili da utilizzare e l’algoritmo più efficace. Allenamento dell’algoritmo sul MC Reco

## Slide 21
Stato dell'Analisi
Ottimizzata la misura della sezione d’urto integrata a 200 MeV/n su target in C e C2H4 (miglioramento della ricostruzione dei vertici, della simulazione MC degli effetti strumentali e di ricostruzione)
Total reaction cross section
(# of vertices)
Total production cross section
(# of fragments)

## Slide 22
Stato dell'Analisi
Pilot test per misure la sezione d’urto di frammentazione in cinematica diretta grazie a Nano-Imaging-Tracker (NIT): emulsioni nucleari con risoluzione della decina dei nanometri
  Realizzate emulsioni di tipo NIT presso LNGS
  NIT esposte a p@200MeV presso il TIFPA
  Sviluppo NIT effettuato presso LNGS
  In corso: assemblaggio di un nuovo microscopio che supera i limiti della diffrazione ottica per l’analisi delle NIT a Napoli
  TO DO: Scansioni e Analisi dei dati (Napoli+Bari)
Macchina per la produzione del gel che costituisce le NIT
  Pilot test al TIFPA