## Slide 1: Experimental and theoretical development of plasma sources for plasma-based particle accelerators
Candidate: Dott. Lucio Crincoli
Lucio Crincoli | PhD in Accelerator Physics, Sapienza Università di Roma
Supervisor: Prof. Massimo Ferrario
Co-supervisor: Dott. Angelo Biagioni

## Slide 2
Outline
Introduction
Plasma Wakefield acceleration
Experimental and numerical study of capillary geometry
Plasma density measurements with Stark broadening method
Neutral gas dynamics with OpenFOAM
Segmented capillary for m-scale plasma sources
Integrated capillary for staged focusing-acceleration
Plasma discharge capillaries
Conclusions
Future perspectives
Experimental setup for capillary testing at Plasma_Lab (LNF-INFN)
Novel schemes for long sources and staged acceleration
Lucio Crincoli | PhD in Accelerator Physics, Sapienza Università di Roma

## Slide 3: Plasma Wakefield acceleration
Introduction
Lucio Crincoli | PhD in Accelerator Physics, Sapienza Università di Roma
Pre-formed neutral plasma channel
Density modulation excited by a driver beam (laser pulse or particle bunch)
Bubble shaped structure with GV/m accelerating fields in the driver wake
Plasma density dependence
Density uniformity required for witness beam acceleration

## Slide 4: Gas-filled discharge capillaries
Requirements:
Density uniformity
Shot to shot stability
Reproducibility
Longevity
Introduction
Lucio Crincoli | PhD in Accelerator Physics, Sapienza Università di Roma
Design:
Geometry
Plasma formation techniques
Materials

## Slide 5: Plasma_Lab experimental setup
Vacuum chamber
  10-6 mbar, 3 primary scroll pumps, 1 turbo-molecular pump
Gas injection system
  H2, N2, Ar
  10-50 mbar at 1 Hz
Electrical discharge circuit
  HV generator and pulser
  5-20 kV us-short pulses
Delay generator
Diagnostic system
  Optical line
  Imaging spectrometer
  ICCD camera
Introduction
Lucio Crincoli | PhD in Accelerator Physics, Sapienza Università di Roma

## Slide 6: Stark broadening method
The spectrometer acquires hydrogen spectral lines of Balmer series
Stark effect: correlation between plasma density and hydrogen spectral linewidth
Temporal and spatial resolved measurements of plasma density
Position (mm)
λ (nm)
Electrode
shadow
Plasma
channel
Plasma plume
Δλ
Balmer β line
Capillary
Introduction
Lucio Crincoli | PhD in Accelerator Physics, Sapienza Università di Roma

## Slide 7: Geometrical design of capillaries
Experimental and numerical study of capillary geometry
Lucio Crincoli | PhD in Accelerator Physics, Sapienza Università di Roma
3 cm long channel
1 mm diameter
2 inlets:
  Uniform channel
  Different distance between inlets (9, 15 and 24 mm)
1 inlet, various channel shapes:
  Uniform (Ø 1 mm)
  Cigar shape (Ø 1.3 mm inner, Ø 1 mm outer)
  Tapered with conical ends (Ø 1 mm inner, Ø 2 mm outer)

## Slide 8: Plasma density measurements: 2 inlets at various distances
Lucio Crincoli | PhD in Accelerator Physics, Sapienza Università di Roma
Experimental and numerical study of capillary geometry
H2 pulses at 30-50 mbar
Opening valve for 5 ms at 1 Hz
7 kV pulses applied 7 ms after valve closure

## Slide 9: Plasma density measurements: 1 inlet - different channel shapes
Lucio Crincoli | PhD in Accelerator Physics, Sapienza Università di Roma
Experimental and numerical study of capillary geometry
H2 pulses at 30-50 mbar
Opening valve for 5 ms at 1 Hz
9 kV pulses applied 7 ms after valve closure

## Slide 10: Neutral gas dynamics with OpenFOAM
Lucio Crincoli | PhD in Accelerator Physics, Sapienza Università di Roma
SonicFOAM solver
Mesh refinement 100-200 um
Vacuum boxes
p_in 40 mbar
Experimental and numerical study of capillary geometry

## Slide 11: Longitudinal hydrogen density profiles
Lucio Crincoli | PhD in Accelerator Physics, Sapienza Università di Roma
2 inlets:
  Higher uniformity with closer inlets at ionization instant
1 inlet:
  Higher uniformity with cigar shape
  Controlled ramps with conical ends
Experimental and numerical study of capillary geometry

## Slide 12: Segmented capillary
Independent plasma discharges
Parallel HV circuits
Modulation of longitudinal plasma density profile
Cheap and compact m-scale sources
HV
HV
Novel schemes for long sources and staged acceleration
Lucio Crincoli | PhD in Accelerator Physics, Sapienza Università di Roma

## Slide 13
Novel schemes for long sources and staged acceleration
Experimental setup
2 HV generators and pulsers, one for each segment
5-20 kV voltage pulses
H2, N2, Ar neutral gas
10-50 mbar 1 Hz pulsed injection
Delay generator for discharge synchronization
Capillary features
2 segments 8 cm long
2 mm diameter
Common grounded electrode
Lucio Crincoli | PhD in Accelerator Physics, Sapienza Università di Roma

## Slide 14
6 kV
14
Central electrode
6 kV
1st test
Goal
Uniform density profile
Test settings
Left segment: 6 kV
Right segment: 6 kV
Results
Symmetric distribution until 2000 ns
Density gradient after 2000 ns
Hβ Balmer spectral line acquired by ICCD camera
Lucio Crincoli | PhD in Accelerator Physics, Sapienza Università di Roma
Novel schemes for long sources and staged acceleration

## Slide 15
Central electrode
6 kV
7.5 kV
15
2nd test
Goal
Steep density gradient at segments crossing
Test settings
Left segment: 6 kV
Right segment: 7.5 kV
Results
Density gradient at until 2500 ns
Symmetric distribution after 2500 ns
Hβ Balmer spectral line acquired by ICCD camera
Lucio Crincoli | PhD in Accelerator Physics, Sapienza Università di Roma
Novel schemes for long sources and staged acceleration

## Slide 16
16
Vb (V)
16 cm capillary
Single segment
  16 cm, 20 mbar
2 segments
  8 cm, 20 mbar
EuPRAXIA 5 GeV case (1.5 GV/m)
Single segment
  3 m, 20 mbar
7 segments
  40 cm, 20 mbar
3 kV
6 kV
70 kV
8 cm
3 m
40 cm
14 kV
16 cm
m-scale sources:
Continuous vs segmented channels
Lucio Crincoli | PhD in Accelerator Physics, Sapienza Università di Roma
Novel schemes for long sources and staged acceleration

## Slide 17: Integrated capillary for staged focusing and acceleration
Lucio Crincoli | PhD in Accelerator Physics, Sapienza Università di Roma
HV
Mixer
APL1
PWFA
APL2
Novel schemes for long sources and staged acceleration

## Slide 18
Novel schemes for long sources and staged acceleration
Experimental setup
1 High voltage generator
HV mixer feeding 3 parallel pulsers
Alternating polarization
HV generator
Mixer
HV pulser
HV pulser
HV pulser
Design
3 segments, each 3 cm long
  2 active plasma lenses
  1 accelerating stage
5 cm long drifts
2 Inlets in the drifts
2 mm diameter
APL1
APL2
ACC
Lucio Crincoli | PhD in Accelerator Physics, Sapienza Università di Roma

## Slide 19
e-beam
19
Operating properties
Discharges synchronization
  Lenses synchronized with the beam entrance
  Central discharge applied 3 µs before for plasma acceleration
10 kV voltage resulting in:
  500 A on the lenses
  250 A in the accelerator
Internal drifts behave like spacers
Lucio Crincoli | PhD in Accelerator Physics, Sapienza Università di Roma
Novel schemes for long sources and staged acceleration

## Slide 20
20
200 consecutive shots taken with accelerated beam
200 pC driver – 50 pC witness
Plasma density for acceleration: 2x1015 cm-3
133 MV/m accelerating gradient
Stable accelerated beam
Lucio Crincoli | PhD in Accelerator Physics, Sapienza Università di Roma
Novel schemes for long sources and staged acceleration
Electron beam focusing and acceleration at SPARC_LAB

## Slide 21
21
Lucio Crincoli | PhD in Accelerator Physics, Sapienza Università di Roma
Novel schemes for long sources and staged acceleration
Plasma source design for EuPRAXIA Advanced Photon source
Gas jet
Laser ionisation
Conveyor – Roots pump to remove gas of the jet from the interaction chamber
Turbo-molecular and scroll pumps to keep 10-4 mbar
1 Hz operation with helium at 30-40 bar

## Slide 22
22
Future perspectives
Experimental activities:
  High repetition rate sources
  m- scale sources
Numerical analysis developments:
  Simulation codes for electrical discharge and plasma dynamics
Lucio Crincoli | PhD in Accelerator Physics, Sapienza Università di Roma
Conclusions

## Slide 23
23
References
Tajima T and Dawson J M 1979 Phys. Rev. Lett. 43(4) 267–270
Spence D J and Hooker S M 2000 Phys. Rev. E 63(1) 015401
Ferrario M et al. 2013 Nuclear Instruments and Methods in Physics Research Section B: Beam Interactions with Materials and Atoms 309 183–188 ISSN 0168-583X the 5th International Conference ”Channeling 2012”, ”Charged Neutral Particles Channeling Phenomena” September 23-28,2012, Alghero (Sardinia), Italy
Ferrario M et al. 2018 Nuclear Instruments and Methods in Physics Research Section A: Accelerators, Spectrometers, Detectors and Associated Equipment 909 134–138 ISSN 0168-9002 3rd European Advanced Accelerator Concepts workshop (EAAC2017)
Biagioni A et al. 2019 Technical report SPARC-PL-19/001, National Institute of Nuclear Physics – Frascati National Laboratories
Griem H R 1974 Spectral line broadening by plasmas (University of Maryland, College Park, Maryland: Academic Press)
Romeo S et al, 2023 Plasma Phys. Control. Fusion 65 115005
Weller H G, Tabor G, Jasak H and Fureby C 1998 Computer in Physics 12 620–631 ISSN 0894-1866
Pompili R et al, 2018 Phys. Rev. Lett. 121(17) 174801 URL https://link.aps.org/doi/10.1103/PhysRevLett.121.174801
Lucio Crincoli | PhD in Accelerator Physics, Sapienza Università di Roma
Conclusions

## Slide 24: Thank you for the attention
Lucio Crincoli | PhD in Accelerator Physics, Sapienza Università di Roma

## Slide 25: Backup slides
Lucio Crincoli | PhD in Accelerator Physics, Sapienza Università di Roma

## Slide 26: Plasma sources
Gas-filled discharge capillaries
Lithium/rubidium vapor oven
Gas jet plasma sources
Gas cells
Introduction
26
Lucio Crincoli | PhD in Accelerator Physics, Sapienza Università di Roma

## Slide 27
Plasma discharge capillaries R&D
Plasma density profile
Shot-to-shot stability
Very long sources for EuPRAXIA (m-scale)
A Biagioni et al 2021 Plasma Phys. Control. Fusion 63 115013
Lucio Crincoli | PhD in Accelerator Physics, Sapienza Università di Roma
Backup slides

## Slide 28
28
Active plasma lenses
Lucio Crincoli | PhD in Accelerator Physics, Sapienza Università di Roma
Backup slides

## Slide 29
29
Upgraded version
Inlets directly injecting in the stages
Open drifts to reduce electrical conductivity
Tungsten-copper electrodes
Reduced crosstalk
Hβ Balmer spectral line acquired by ICCD camera
Lucio Crincoli | PhD in Accelerator Physics, Sapienza Università di Roma
Backup slides

## Slide 30
Electron beam focusing and acceleration at SPARC_LAB
Plasma capillary
Plasma capillary
Focusing
lens
Acelerating
section
Extraction
lens
Integrated plasma module
Active plasma lens
30
C-band structure
H2 filled capillary
Optical/THz diagnostics
To the FEL
Lucio Crincoli | PhD in Accelerator Physics, Sapienza Università di Roma
Backup slides