## Slide 1
Longitudinal beam coupling impedance mitigation studies for
CERN PS accelerator complex
PhD Accelerator physics – XXXVII cycle
Michela Neroni*
Supervisors
Andrea Mostacci (Sapienza, University of Rome), Christine Vollinger (CERN)
23rd of October 2023
*michela.neroni@uniroma1.it

## Slide 2
Outline
Introduction
        Longitudinal beam coupling impedance and implications on beam dynamics
        Motivation of the study
        The main extraction kickers in the CERN Proton Synchrotron
Electromagnetic calculations
        Wakefield simulations
        Frequency domain and schematic simulations
Radiofrequency measurements
        Stretched wire measurements
Beam impedance mitigation
        Location of the critical resonances
        Mitigation strategy
Impedance of other components in the PS complex
Conclusions and outlook

## Slide 3: Longitudinal beam coupling impedance
When facing cross section variations of the vacuum chamber wall, as well as its finite resistivity, charged particles travelling in the accelerator, induce electromagnetic fields mainly left behind the generating particle  Wakefield  Beam losses and instabilities
Courtesy of M. S. Sullivan
Wake function is the electromagnetic impulse response of any given structure (Green function in time domain):
In frequency domain  Longitudinal beam coupling impedance is the Fourier transform of the longitudinal wake function:

## Slide 4: Beam instabilities and mitigation strategy
Depending on the decay time of the wakefield, we can distinguish two types of impedances:
Narrow-band impedances , impedance bandwidth and bunch length). Wakefield lasts during the passage of many bunches
 coupled bunch instabilities.
Broad-band impedances (). Wakefield created by these impedances decays over one bunch length
 single bunch instabilities.
 Reducing Q factor: introduction of HOM-couplers, broadening methods like insertion of absorbers (e.g. ferrites).
 Reducing R/Q and therefore changing the overall geometry (to be decided in the design phase or mitigated with adding shields in an existing structure)
:
,

## Slide 5: Motivations
Total PS Longitudinal Impedance
RF cavities
Vacuum equipment
Kickers
Kickers are one of the main source of broadband impedance in the PS, with unwanted effects, e.g. loss of Landau damping.
While the LIU target is reached today, tackling critical impedance sources will provide additional margin.
PS Transverse Dipolar vertical impedance
Courtesy of S. Joly
LIU project (LHC Injectors Upgrade) in view of HL-LHC
PS impedance model up-to-date with the most recent geometrical model of each component.
Longitudinal coupled-bunch instabilities is one of the main limitations in the PS for reaching higher intensities in the LIU framework.

## Slide 6
PS fast extraction kickers
KFA71, KFA79 and SMH16 involved in the main extraction from PS towards SPS and experimental areas.
KFA71
KFA79
SMH16
IV
Kickers first installed in the 1970s
Twelve magnet modules foreseen for extraction, split into two different devices
2.45 m
0.89 m

## Slide 7
Model geometry and materials
Highly dispersive behaviour  magnetic permeability of Ferrite 8C11 by Ferroxcube
9-cells magnet
Frame ground/HV plates ground/HV conductors
Aluminum alloys
Plates combs Alumina
KFA79 module unit
High geometrical complexity 
Large computational resources required
3D models built in CST starting from old drawings and CATIA models

## Slide 8
Outline
Introduction
        Longitudinal beam coupling impedance and implications on beam dynamics
        Motivation of the study
        The main extraction kickers in the CERN Proton Synchrotron
Electromagnetic simulations
        Wakefield simulation
        Frequency domain and schematic simulations
Radiofrequency measurements
        Single stretched wire measurements
Beam impedance mitigation
        Location of the critical resonances
        Mitigation strategy
Impedance of other components in the PS complex
Conclusions and outlook

## Slide 9
Induced voltage
Broadband impedance contribution driven by the ferrite
 Intrinsic in the kicker design

Energy loss
Coupled bunch instabilities
To avoid impedance peaks in the low frequency range, up to 150 MHz
** E. Shaposhnikova, “Longitudinal beam parameters during acceleration in the LHC”, Tech. Rep. LHC-PROJECT-NOTE-242, CERN, 2000
Bunch spectrum
By expanding the exponential to the first order *
For low frequencies  low coupled bunch instabilities threshold (cumulative PS longitudinal shunt impedance) **
* J. L. Laclare, “Bunched beam coherent instabilities,” in Proceedings of CAS 1985 Vol. I, pp. 264–326, 1987
Total voltage induced by the bunch on a charge in a time distance :

## Slide 10
Wakefield simulations
Three impedance contributions:
Broadband
Low frequency
Higher frequency
 Ferrite drives the broadband behavior as described by Tsutsui*
* H. Tsutsui, “Some simplified models of ferrite kicker magnet for calculation of longitudinal coupling impedance”, Tech. Rep. CERN-SL-2000-004-AP, CERN, 2000
PEC boundaries along x and y-axis, equivalent to short circuit
Open boundary along beam axis

## Slide 11
Adding cable terminations
KFA79
Input connector  cables terminated on open circuit when the main switch in off-state, i.e. when not extracting from the PS
Output connector 
Connecting cables terminated on 15 Ω
Circuit schematic of a magnet module unit*
* L. Sermeus et al., “The kicker systems for the PS Multi-turn Extraction”, No. CERN-ATS-2010-140, 2010
Each magnet module is connected to the power circuit by means of very long cables  impedance model of the component must include the kicker as it is in the actual configuration in the machine.

## Slide 12
Simulating wire measurement
    Input power connectors always terminated on ideal open transmission line
    Output power connector terminations considered as:
    ideal open transmission line
    short circuit
    15 Ω resistor (actual situation)
Frequency domain simulation (FD) to mimic single stretched wire measurements setup  including in the 3D model matching resistors and copper wire
Treating power connectors as waveguide ports  6 + 2 (kicker input/output) ports component
Combined schematic simulation: lumped element circuit connected to a 3D electromagnetic FD simulation
Three different configurations simulated:

## Slide 13
Effect of cable terminations
The transmission parameter, , is of interest because it directly gives information on the longitudinal beam coupling impedance
Cable terminations highly influence impedance behaviour in the low frequency range

## Slide 14
Outline
Introduction
        Longitudinal beam coupling impedance and implications on beam dynamics
        Motivation of the study
        The main extraction kickers in the CERN Proton Synchrotron
Electromagnetic simulations
        Wakefield simulation
        Frequency domain and schematic simulations
Radiofrequency measurements
        Single stretched wire measurements
Beam impedance mitigation
        Location of the critical resonances
        Mitigation strategy
Impedance of other components in the PS complex
Conclusions and outlook

## Slide 15
Matching resistor
Stretched wire
Wire measurements performed on KFA79 with 15 Ω resistor at the output power connector and input connector undefined open (effect of cable terminations at low frequency confirmed – see spare slides)
Stretched wire measurements
3 peaks in the low frequency range:
    22.3 MHz
    34.9 MHz
    47.8 MHz
High frequency peak at 667 MHz
Notes: appendix

## Slide 16: Wire measurements vs. wakefield simulation
Very good agreement between measured longitudinal impedance and simulated one:
Three low frequency resonances (within 2 MHz from the measured ones)
Main high frequency resonance around 660 MHz
Notes: Different boundary conditions between Wakefield simulations and wire measurements. The wire may detune the resonant peak and it may modify the shunt impedance value. TEM configuration
Discrepancy may be due to different losses in real component and definition of the mesh

## Slide 17
Wire measurements vs. wire simulations

## Slide 18
Outline
Introduction
        Longitudinal beam coupling impedance and implications on beam dynamics
        Motivation of the study
        The main extraction kickers in the CERN Proton Synchrotron
Electromagnetic calculations
        Wakefield simulation
        Frequency domain and schematic simulations
Radiofrequency measurements
        Single stretched wire measurements
Beam impedance mitigation
        Location of the critical resonances
        Mitigation strategy
Impedance of other components in the PS complex
Conclusions and outlook

## Slide 19
Location of the resonances
E-field monitor 19.69 MHz - Side view
E-field monitor 32.29 MHz - Side view

## Slide 20
E-field monitor 45.5 MHz – Side view
Location of the resonances
Idea: to create a conductive path for the induced currents by connecting all the ground contacts (plates of adiacent modules and modules-vacuum tank)
How can we mitigate the unwanted contributions?

## Slide 21: Adding transitions pieces
Copper blocks are placed symmetrically respect to the x-axis (and respect to the center of the beam)
The corners and edges of the blocks must be rounded in the mechanical design
11mm
15mm
25mm
~10mm
130mm
18.5mm
22.5mm
25mm
~12mm
130mm

## Slide 22
Impedance mitigation

## Slide 23
Outline
Introduction
        Longitudinal beam coupling impedance and implications on beam dynamics
        Motivation of the study
        The main extraction kickers in the CERN Proton Synchrotron
Electromagnetic calculations
        Wakefield simulation
        Frequency domain and schematic simulations
Radiofrequency measurements
        Single stretched wire measurements
Beam impedance mitigation
        Location of the critical resonances
        Mitigation strategy
Impedance of other components in the PS complex
Conclusions and outlook

## Slide 24
1-cell model
GOAL: to build an EM model of Finemet cavity + amplifier system, matching with measurements, for further impedance investigations.
Impedance of PSB Finemet cavities
Wire measurements – single cell result

## Slide 25
GOAL: fast frequency shift of about 200 kHz on the fundamental mode, to allow a fast switching between proton and ion frequencies.
EM simulations and RF measurements of upgraded septa magnets to verify their compliance with impedance requirements before installation in the PS.
Simplified SMH16
PS 80 MHz fast ferrite tuner
 Simulations, radiofrequency and material permeability measurements to demonstrate the working principle of the instrument.
The use of the fast tuner can allow the number of cavities to be reduced from three to two in the PS  impedance reduction
Impedance of PS septa magnets
Courtesy of C. Vollinger

## Slide 26
Outline
Introduction
        Longitudinal beam coupling impedance and implications on beam dynamics
        Motivation of the study
        The main extraction kickers in the CERN Proton Synchrotron
Electromagnetic calculations
        Wakefield simulation
        Frequency domain and schematic simulations
Radiofrequency measurements
        Single stretched wire measurements
Beam impedance mitigation
        Location of the critical resonances
        Mitigation strategy
Impedance of other components in the PS complex
Conclusions

## Slide 27
Conclusions
The longitudinal beam coupling impedance results for both PS extraction kickers have been presented and critical resonances were discussed.
New 3D geometry benchmarked by very good agreement between measurements and simulations. The transmission cable terminations highly impacts the beam coupling impedance.
Transition pieces are confirmed to be beneficial in mitigating low frequency resonances  Mechanical implementation of transition pieces soon and measurements can be performed again afterwards.
Impedance model of the kickers and other upgraded PS components will serve to update the PS impedance model  to have reliable beam dynamics simulations and instabilities studies.
If simulations and measurements the fast ferrite tuner would proof its working principle, this would allow a big improvement in the impedance reduction with the elimination of one out of three 80 MHz cavities.
Notes: KFA71 cannot be measured

## Slide 28: Spare slides

## Slide 29
Courtesy of A. Lasheen
Shunt impedance threshold for coupled-bunch instabilities
Coupled-bunch instabilities threshold

## Slide 30
Wire measurements performed before including 15 Ω resistor at HV hookups output – HV hookups undefined open
Wire measurements – HV hookups termination
Notes: appendix

## Slide 31
E-field monitor 654 MHz – Side view

## Slide 32
Mitigation strategy – resonance location
Mitigation strategy: M. Neroni et al., “Characterization of the longitudinal beam coupling impedance and mitigation strategy for the fast extraction kicker KFA79 in the CERN PS”, in Proc. 14th International Particle Accelerators Conference, 2023
E-field monitor at 35.7 MHz
KFA71

## Slide 33
Connecting ground contacts (module-module, module-tank)  copper rods and bars
Adding transition pieces
Notes: Sufficient to see impact on the beam impedance from simulation

## Slide 34
Significant improvement
Adding transition pieces

## Slide 35
Field monitors with transition pieces
E-field monitor 64 MHz - Side view
E-field monitor 712 MHz - Side view

## Slide 36
Implementation of transition pieces
Courtesy of P. Trubacova
Not possible to implement the same transitions which are in the KFA45

## Slide 37
5mm
15 mm
Courtesy of P. Trubacova
Implementation of transition pieces