## Slide 1
PhD Seminars
Terahertz/Infrared Radiation: From the Production with Accelerator Based Sources to the Use in Material Characterization for Accelerator Cavities
PhD Student: Lorenzo Mosesso
PhD Supervisor: Stefano Lupi
PhD Co-Supervisor: Salvatore Macis

## Slide 2: Why THz/IR Radiation?
3
5
4
2
1
Materials
Characterization and control of quantum materials
Security
Can penetrate fabrics and plastics, so it can be used in surveillance
Enviromental science
Can be used for sensing and characterizing airborn pollution and VOCs
Medicine
Imaging technique as a replacement for medical X-rays.
Biology
Non-destructive, non-contact and label-free optical method for biological detection
IR/THz Units:

## Slide 3: Outline: THz/IR Radiation in Accelerator Physics
Particle Accelerators as THz/IR Radiation Sources – Design of optical beamlines
THz/IR Radiation for Material Characterization in Accelerator Technologies
SISSI 2.0 Beamline @ Elettra
SABINA THz/MIR Free Electron Laser @ SPARC_LAB
alloys with different Ag concentrations
Transition Metal Oxide Thin Films on Cu ( coatings)
Notes: The first part of my PhD project deals with the THz/IR radiation intended as the product of particle acceleration.

## Slide 4: Why Sources Based on Particle Accelerators
THz/IR Sources:
Conventional IR Sources (CW operation, low brightness, low collimation)
Quantum Cascade Lasers (work mainly in CW, strict operational temperatures, small frequency tunability…)
Laser-based sources (pulsed radiation, frequency range limited by the non-linear crystals, high energy pulses…)
Particle Accelerator-based sources they can provide radiation with astonishing properties, overcoming the previous limitations
‘THz Gap’: Challenges associated with the generation, manipulation and detection of THz radiation
Pulsed Radiation
Unmatched Brightness
Polarized Light
Frequency Tunability (over a broad range)
Suitable for time-resolved spectroscopy
Broadband Emission
Low angular divergence (suitable for micro-spectroscopy)
Infrared Synchrotron Radiation
(ISRS)
FEL Radiation

## Slide 5: Dedicated THz/IR Facilities in the World (Not Exhaustive List!)
ALS, Berkley (CA)
IRSR for Microspectroscopy
ANSTO, Melbourn
THz-FIR Beamline
DIAMOND, Uk
B22 Miriam Beamline
SISSI and THz TeraFermi @ Elettra, Trieste
DAΦNE – SINBAD
SABINA THz/MIR FEL
@ SPARC_LAB, Frascati (RM)
SOLEIL, Orsay, France
SMIS Beamline
Santa Barbara (CA)
UCSB THz/FIR Free Electron Laser Source
THz @ Phoang Accelerator Laboratory, Korea
ISIR THz FEL @ Osaka University, Japan
CAEP THz FEL facility Peking University, China
ELBE/FELBE High-Power THz Facility, Dresda, Germany
Spring-8, Harima Japan
IRSR for Microspectroscopy
NSLS, BNL, Upton, NY, USA
IRSR for Microspectroscopy
LNSL, Sao Paulo, Brasil
IMBUIA IR Beamline

## Slide 6: Towards the Fourth Generation Light Sources: Upgrade@Elettra
Higher brilliance:
Increased coherence:
Great reduction in transverse emittance (mainly horizontal)
Innovative design in magnetic optic: new modified multi-bend achromats dipoles (with Longitudinal Gradient and Reverse Bendings)
Elettra is a third generation synchrotron light source with:
a storage ring of
operation energy of and
28 beamlines available for external users
Major upgrade towards the realization of a ‘Diffraction Limited SR' light source in the soft X-rays

## Slide 7: SISSI: Present and Future Upgrade
Two branchelines (Material Science and Chemical-Life Science) are provided with a full equipment to perform at different thermodynamics conditions:
IR and Optical Spectroscopy
Microspectroscopy
Imaging
Nanospectroscopy (s-SNOM)
The SISSI (Synchrotron Infrared Source for Spectroscopy and Imaging )infrared beamline at Elettra extracts the IR and visible components of synchrotron radiation generated by bending magnets
Present Elettra Storage Ring with S2BA (9.1 Section)
Future Elettra 2.0 Storage Ring with S6BA-E (9.1 Section)
SISSI 2.0
Design of the new optical beamline for IRSR extraction:
Spatial constraints and new emission properties must be taken into account
6 dipoles
16 quadrupoles
20 sextupoles
4 skew quadrupoles
4 octupoles with correctors
Planned and Developed thorugh the collaboration:
Sapienza University (Stefano Lupi)
CNR-IOM (Michele Zacchigna)

## Slide 8: SISSI 2.0 Beamline Design: Radiation Properties
B80
B80
B64
Observation Screen
Section of the Storage Ring dedicated to SISSI 2.0
Dipolar contribution of the magnetic lattice provided with:
Longitudinal Gradient Bending Dipoles
Reverse Bendings
SRW Simulations to calculate the SR Electric Field in Near Field Regime

## Slide 9: Design of the Optical Beamline: Collecting Mirror
Power Density
Slotted Mirror
Larger slot:
Thinner slot:
from the beam
Downstream B80
X-Rays load:
are unbearable. Required slotted mirrors
The most critical point in the beamline design is the radiation extraction through a collecting mirror. Several issues need to be addressed:
Mirror installation within the machine and space availability
Mirror thermal load induced by SR broadband emission
Photon Flux collection (minimum required for the experimental applications)

## Slide 10: Design of the Optical Beamline: Wavefront Propagation
Toroidal or Parabolic for M2
WORK IN PROGRESS: Beam Propagation through the rest of the optical beamline up to the existing end-station:
Installation of a conical mirror for beam reshaping (beam profile suitable for micro-spectroscopy)
Oral Contribution:
TeraDays 2024 (Federico II, Napoli)
SRI 2024 (DESY, Hamburg)
SILS 2024 (Università della Calabria, Rende)

## Slide 11: SABINA: About the Project
SABINA: Source of Advanced Beam Imaging for Novel Applications
GOAL: Enhancement of the SPARC_LAB research facility – increase of the uptime and improvement of the accelerator performances:
Technological plant renewal
Substitution of the ancillary systems and upgrade of the facility in terms of technology
Creation of two user facilities:
FLAME: High power laser for solid target experiments
THz/IR FEL: radiation source for optical spectroscopy (pump probe), also at cryogenic T
STATUS: kick off Sept. 2019, project finalization: end of 2025
Project co-founded by Regione Lazio within POR-FESR 2014-2020 funds and INFN

## Slide 12: The SABINA THz/IR FEL
SABINA aims to develop a user facility based on a FEL delivering radiation with the following important properties:
monochromatic light with /sub- time duration
Tunable frequency in a large spectral range between - (by tuning the beam energy in the LINAC)
High energy per pulse (up to )
Tunable polarization (from linear, to circular, to elliptical)

## Slide 13: FEL Beamline Layout
RF Photocatode gun
SPARC_LAB LINAC
APPLE X Undulators
Two S-band accelerating RF cavities
One C-band accelerating section
S1 band
S2 band
C band

## Slide 14: PhD Thesis: Extraction Beamline Design
M5 Toroidal Mirror
(EFL1 = 7530 mm)
(EFL2 = 3000 mm)
Extraction optics
An OTR screen separate the electron beam and the THz-IR radiation
Undulator
Here the accelerated electrons generate the FEL radiation in the THz-IR range
M1 OTR Screen
M2 Parabolic Mirror
(EFL = 908 mm)
M3 Plane Mirror
M4 Parabolic Mirror
(EFL = 7530 mm)

## Slide 15: PhD Thesis: Extraction Beamline Design
Extraction optics
An OTR screen separate the electron beam and the THz-IR radiation
Undulator
Here the accelerated electrons generate the FEL radiation in the THz-IR range
Diagnostic
The radiation is focused on a diagnostic setup (alignment, beam characterization)
Diagnostic Hutch

## Slide 16: PhD Thesis: Extraction Beamline Design
Extraction optics
An OTR screen separate the electron beam and the THz-IR radiation
Undulator
Here the accelerated electrons generate the FEL radiation in the THz-IR range
Diagnostic
The radiation is focused on a diagnostic setup (alignment, beam characterization)
Experimental hutch
The radiation is directed inside the experimental hutch where spectroscopy measures are performed
Oral Contributions:
SILS 2023 (Sapienza, Roma)
TeraDays 2024 (Federico II, Napoli)
SRI 2024 (DESY, Hamburg)
SILS 2024 (Università della Calabria, Rende)

## Slide 17: Outline: THz/IR Radiation in Accelerator Physics
Particle Accelerators as THz/IR Radiation Sources – Design of optical beamlines
THz/IR Radiation for Material Characterization in Accelerator Technologies
SISSI 2.0 Beamline @ Elettra
SABINA THz/MIR Free Electron Laser @ SPARC_LAB
alloys with different Ag concentrations
Transition Metal Oxide Thin Films on Cu ( coatings)

## Slide 18: Motivation of the Study: Future Perspectives on RF Cavities
Conventional Accelerating Schemes:
RF Cavities
Technological Improvements required for:
Higher Accelerating Gradients
()
Reduced Costs (compact accelerator)
Existing Limitations:
Dielectric Breakdowns
RF Pulse Heating
Field Emission and Dark Currents
Mechanical and Thermal Stress
Natural Continuation of previous INFN Projects (Gruppo V):
DEMETRA (LNF, SLAC, KEK, UCLA)
TERA (LNF, Sapienza, Federico II, Torino)
NUCLEAAR (LNF, Sapienza, Tor Vergata)
IMPACT (LNF, Sapienza)
Solutions?
Find innovative materials to overcome the proposed limitations

## Slide 19: 1° Case Study: Diluted CuAg Alloys
CuAg alloys with low Ag concentrations (0.028% wt Ag to 0.1% wt Ag)
Complete solid solubility (uniform samples – no microstructures)
Increased mechanical strength
(solution hardening)
High electrical and thermal conductivities (comparable to Cu)

## Slide 20: 2° Case Study: Thin Films on Cu Substrate
Research on has reached some important milestones within the framework of the past INFN projects
Thin film growth procedures
Quality of the deposition (AFM, SEM, Raman, X-Rays)
Transport and mechanical characterization vs. film thickness
Coating of cylindrical RF cavity prototypes
Key Features:
High conductivity at low thickness ():
High work functions
Reduced field emission and dark currents
High thermal stability and mechanical resistance

## Slide 21: Experimental Methodology: Irradiation with High Intensity sub-THz/THz Radiation
New testing protocol to evaluate the damage induced by high electric fields on Cu-based samples
No needs for assembled RF cavities
High intensity THz pulses irradiating the sample with:
Polarization p or s
Tunable incident angle
Tunable energy per pulse
Varying number of pulses
Repetition Rate
Specific properties are being investigated:
Ultrafast thermodynamic evolution
Thermal induced deformations on the surface/thin film removal
Ablation phenomena
Change of surface chemical composition
RF Cavity environment reproduced!

## Slide 22: Theoretical Methodology: N-Temperature Model
We are interested in describing the thermal dynamics of a system when irradiated by ultra-fast pulsed radiation using a complementary theoretical approach:
2 – Temperature Model
Different degrees of freedom of the system are considered as separated interacting thermal reservoirs, each with its own temperature
Different inertia!
Completely implemented for Cu
Some experimental results have been preliminarily reproduced with the numerical simulations
Work in progress: Implementation of the model for the Cu-based materials

## Slide 23: Future Perspectives
Sapienza Terahertz group will be involved in the practical realization of the beamlines, both in the installation and alignment of the optics.
The installation of the optics for SABINA is scheduled for the middle of next year. The group will be involved in the implementation of the equipment for the diagnostic chamber and for the installation of the optical set-up in the experimental chamber

## Slide 24: Acknowledgements
Sapienza Terahertz Group:
Prof. Stefano Lupi (Sapienza University of Rome, INFN)
Salvatore Macis (Sapienza University of Rome, INFN)
Annalisa D’Arco (INFN, Sapienza University of Rome)
Elettra – Sissi Group
Giovanni Birarda
Lisa Vaccari
Michele Zacchigna
INFN – Gruppo V
Augusto Marcelli
Bruno Spataro
Thanks for your attention!!
External Collaborations
Vincenzo Stagno (Sapienza University of Rome, Department of Earth Science)
Andrea Notargiacomo (CNR, Institute of Photonics and Nanotechnologies)
Maria Lilia Pia (CNR, Institute of Photonics and Nanotechnologies)

## Slide 25: Question Time

## Slide 26: Properties of the Radiation: Just the Idea
Interference pattern studied for . The electron trajectory in the simulations is unchanged and the single SR Electric Field contributions from the single magnetic components are disentangled from the total emission
Superposition between the two Edges
The superposition between the two contribution is located along the direction of the straight section
Classical Edge Radiation contribution with the single interference pattern in the direction of the straight section
By superimposing the electric fields to calculate the combined Intensity distribution we get
Superposition Region due to Reverse Bend.
Superposition of two SR contribution in NF regime: strong interference!
Observation Screen

## Slide 27: Magnetic Field Disentanglement: Interference Pattern
Observation Screen
Integration interval to study the contribution from the first three magnetic elements
Edge radiation from BM80#01 and Q24RB#01 (downstream and upstream edges respectively)
Edge Radiation (conventional) given by the two consecutive reverse bending
SR emission from the second reverse bending Q24RB#02
(the interference pattern derives from the superposition with the SR emission from the first bending)
Together with the conventional Synchrotron Radiation emission we need to consider the Edge Radiation contributions, which gets more relevant the more the wavelength is longer
Geloni et al. Theory of the Edge Radiation
This set of Edge contributions overlap with the interference background within the superposition region generated by the Reverse Bendings, providing for the complex spatial intensity distribution in SISSI 2.0

## Slide 28: Backup slide for Elettra

## Slide 29: Question Time: Multiband Achromats with reverse bendings
The new magnetic lattice has 24 arcs, 12 short straights and 12 long straight, and it has a 12-fold symmetry, i.e. 12 equal achromats
Each achromats is composed by two arcs, separated by a short straight section of free space
The achromats are separated by a long free space straight section with length
Each arc of Elettra 2.0 consist in 3 unit cells, i.e.:
3 bending dipoles, of which only one is characterized by a vertical field gradient, while the others two have both transverse and longitudinal field gradients. In other words this is the difference between the B64 and the two B80
8 quadrupoles, four of which are shifted to give the reversed kick (purple element in the picture)
10 combined sextupoles
To get the full understanding of the magnetic structure it is necessary to get some detail on the full magnetic lattice expected in the new Elettra 2.0.
Single Arc
Full Achromat based on two arcs
Reverse bending is introduced through the dipole kick obtained by shifting the quadrupoles!!

## Slide 30: Question Time: ELETTRA 2.0
Let’s start with the description of the single magnetic components. In particular let’s start with the bending dipole B80. Each half achromat has two B80, each one characterized by three sections named BQ, B and BQ respectively
The dipole magnet B80 is composed of three sectors (BQ, B, BQ) with longitudinal symmetry. The central sector (B) has a constant field. The other two (BQ) have a transverse quadrupolar gradient. What does it means for a dipole to have a quadrupolar gradient? The idea is explained by the following figure:
The idea is to imagine a quadrupole centred at a given point and to take the field generated by this quadrupole as the field produced by a dipole located at an off-centred position with respect to the origin of the quadrupole. The more the dipole is located near the origin of the imaginary quadrupole and the more is bigger the transverse gradient in the dipole field
The picture above explain very well the reason why the B80 dipoles have strong magnetic gradients in the transverse direction. These transverse gradients can’t be simulated in SRW, which assume as an important hypothesis that the magnetic field is UNIFORM in the transverse direction.

## Slide 31: Question Time: Dipoles B80
The magnetic field in the figure is reported as a function of the longitudinal position expressed in . The total length of the dipole is but the tails of the field extends for a total length of
220 mm
290 mm
1.459 T
1.01 T

## Slide 32: Question Time: ELETTRA 2.0
Let’s consider now the quadrupoles definition, focusing in particular on the reverse bending. The Elettra 2.0 standard lattice hosts eight quadrupoles for each half-achromat, four of which are used for reverse bending (RB). The RB is obtained by shifting the quadrupoles with respect to their nominal position in order to obtain a dipolar kick.
The table shows the parameters characterizing the quadrupoles. The last four elements, namely - are the reverse bending
All the quadrupoles are grouped in three distinct families, which differs in terms of magnetic length and gap aperture. The three different groups are reported in the picture and are listed below:
Q13 This group includes and , which are long
Q24 This group includes and , which are long
Q24RB This group includes all the reverse bending quadrupoles. In particular they have a magnetic length as for the case of the Q24 quad, with the only difference that the Q24RBs need a larger gap aperture

## Slide 33: Question Time: some Elettra 2.0 parameters
The new magnetic lattice reduces the present horizontal emittance by a factor 49, increasing the brilliance and the coherence of the radiation

## Slide 34: Question Time: SABINA

## Slide 35: SPARC Photoinjector
The SPARC photoinjector consist of:
RF photocatode gun (1.6 cell S-Band RF cavity with high gradients)
LINAC to produce electron bunches with high brilliance and high currents
With the introduction of the last C-band section the electron beam can be accelerated up to -
Just after the RF gun, the electron beam is focalized by a motorized solenoid and then it is injected with the proper matching conditions in the booster.
The entrance of the first accelerating section is placed at 1.5 meters from the cathode, where the local maximum of transverse emittance oscillations is expected

## Slide 36: (1) RF Photocatode Gun
The photocathode is composed by a 1.6 cell RF gun operated at S-band (2.856 GHz, of BNL/UCLA/SLAC type)
Acceleration is obtained by means of high fields in the cavity, with a peak on the cathode (120 MV/m)
Electron beam energy is up to 5.5 MeV at the entrance of the LINAC
The cathode consist of a polycrystalline oxigen-free copper with high quantum efficiency ()
A laser system with tunable properties allows the extraction of electron bunches with the required properties

## Slide 37: (1) Laser System
The photocathode pulses are up-converted via harmonic generation to the 3rd harmonic at , which is the wavelength required for electron extraction out of copper cathode
SPARC_LAB photocathode laser system is based on a Titanium-Sapphire laser at 800 nm of about 150 fs and its harmonics
The laser is synchronized with the RF system and it is based on the Chirped Pulse Amplification (CPA) of the pulse
The laser is used both to extract electrons from the photocathode and to feed the Vis-UV FEL in the seeded mode

## Slide 38: (2) LINAC
SPARC LINAC is based on three SLAC-Type TW (traveling wave) high gradient RF cavities
TW acceleration: the beam is accelerated having the particles standing on the crest of the wave propagating inside the cavity
High gradients:
Max energy reached at the end of the LINAC: -
During the operation time of SABINA, only the first section is used at full capacity:
in the first two S-band sections
in the ending C-band sections
C-band turned off and the gradients in the second S-section are reduced at
C-band turned on at

## Slide 39: SABINA Design and Simulations
The first problem for the SABINA undulator section is the lack of space due to the structural limitations of the room hosting the FEL. The constraint on the total length is . This in turn implies that the undulator has to be made up by a single module, or by more modules with reduced space between them
A single undulator module long is subjected to important mechanical stress and torque, so the best option is to choose an undulator consisting in three identical modules long spaced by of drift
There are two important disadvantages due to the lack of space:
Reduced space to install diagnostic devices or quadrupole doublets between the undulators
Limited length for the undulators requires a short gain length for the amplification process
Since we want to produce radiation with tunable polarization, we need to choose the undulator within the APPLE family. APPLE-X undulators have been chosen in order to have symmetric focalization on the low energy beam

## Slide 40: SABINA Design and Simulations
Preliminary considerations for the undulator design:
Total length (available space in SPARC_LAB)
Minimum Energy of to limit degradation by space charge effects
Short gain length: possible criticality at
Given a conventional operational for the undulator, it is possible to determine from:
The magnetic period should not be too long. Long periods for a fixed length reduce the number of periods and increase the gain length, reducing the performances of the FEL

## Slide 41: About the Undulator: the APPLE X Configuration
Requirement for tunable polarization undulator in the APPLE family
Symmetric focalizing properties are needed due to the absence of quadrupoles between the undulator modules: APPLE X is the best choice
Polarization and Energy can be tuned with longitudinal shifts of the magnetic array pairs. The intensity of along the undulator axis can be tuned by changing the gap

## Slide 42: FEL Output: GENESIS Simulation Results
-
-
Power Growth
Field Spectrum
Saturation condition for FEL dynamics:
Completely realized at ()
Partially realized at ()
Monochromatic pulses with the expected properties of:
High energy per pulse
Ps/sub-ps temporal duration

## Slide 43: FEL Output: GENESIS Simulation Results at 3 THz
Matching condition at the undulator relaxed
Beam constrained to match the Twiss parameter conditions at the undulator entrance
Beam dynamics simulated along the beamline up to the undulator entrance with different conditions:
Space charge on/off
Matching constraint at the undulator entrance
The results have been used as GENESIS input to verify the FEL performances Condition II. is crucial while space charge effects change slightly the output

## Slide 44: Endstation: User Facility
fs-LASER
EXP.
AREA
M5
THz Reflectance and Transmittance Setup for optical spectroscopy experiments
Femtosecond laser (pulses) synchronized with SABINA and coupled with:
Optical Parametric Amplificator (OPA) + Difference Frequecy Generator (DFG) to tune radiation in the range - by means of non-linear optical effects
High harmonic generation
Wide range pump probe setup
High magnetic field Optical Cryostat ( up to )

## Slide 45: Comparison between SABINA and other conventional sources
Femtosecond laser (pulses) with:
Optical Parametric Amplificator (OPA) + Difference Frequecy Generator (DFG) to tune radiation in the range - by means of non-linear optical effects
The laser power in the MIR spectral region is of the order of . Assuming a beam of and a RR of , the energy radiation per pulse is , which is one order of magnitude lower with respect to the SABINA radiation emitted in the same spectral range