## Slide 1
Ph.D. in Accelerator Physics – XXXVIII cycle
24 October 2024
Development of superconducting magnets for the future
Muon Collider
Daniel Novelli
Funded by the European Union (EU). Views and opinions expressed are however those of the author only and do not necessarily reflect those of the EU or European Research Executive Agency (REA). Neither the EU nor the REA can be held responsible for them.

## Slide 2: Why a Muon Collider?
The Muon Collider is a very promising post-LHC high physics facility:
  200 times heavier than electron ( m=105.7 MeV/c2 ,me=0.511 MeV/c2 ) → 109 times less radiation loss.
  elementary particle: all COM energy available for the collision, contrary to hadron machines.
BUT ecays in 2.2 in rest frame:
IMCC (Internation Muon Collider Collaboration) aims at studying the feasibility of a 10 km, 10 TeV center of mass energy Muon Collider, as indicated by the European Strategy for Particle Physics.
must be produced, accelerated and collided ASAP
decay products must be shielded to avoid damage to the machine or radiation
Notes: The energy at which the proton collider cross-section equals that of a muon collider. The dashed line assumes comparable Feynman amplitudes for the muon and the proton production processes. A factor of ten enhancement of the proton production amplitude squared, possibly due to QCD production, is considered in the continuous line

## Slide 3: Why a Muon Collider?
IMCC (Internation Muon Collider Collaboration) aims at studying the feasibility of a 10 km, 10 TeV center of mass energy Muon Collider, as indicated by the European Strategy for Particle Physics.
must be produced, accelerated and collided ASAP
decay products must be shielded to avoid damage to the machine or radiation
J.P. Delahaye et al., Muon colliders,
arXiv:1901.06150 [physics.acc-ph].
Physics?
Muon collisions in the range of 14 TeV
have comparable discovery potential to hadron (proton) collisions in the range of 100 TeV
The Muon Collider is a very promising post-LHC high physics facility:
  200 times heavier than electron ( m=105.7 MeV/c2 ,me=0.511 MeV/c2 ) → 109 times less radiation loss.
  elementary particle: all COM energy available for the collision, contrary to hadron machines.
BUT ecays in 2.2 in rest frame:
Comparable Feynman amplitudes for the muon and the proton production processes.
A factor of ten enhancement of the proton production amplitude squared,
possibly due to QCD production, is considered.

## Slide 4: Why a Muon Collider?
IMCC (Internation Muon Collider Collaboration) aims at studying the feasibility of a 10 km, 10 TeV center of mass energy Muon Collider, as indicated by the European Strategy for Particle Physics.
must be produced, accelerated and collided ASAP
decay products must be shielded to avoid damage to the machine or radiation
K. R. Long et al, Nature Physics, v.17, p.289, 2021.
Sustainability?
A 10 TeV muon collider
can provide the highest integrated luminosity
per unit of energy consumption.
The Muon Collider is a very promising post-LHC high physics facility:
  200 times heavier than electron ( m=105.7 MeV/c2 ,me=0.511 MeV/c2 ) → 109 times less radiation loss.
  elementary particle: all COM energy available for the collision, contrary to hadron machines.
BUT ecays in 2.2 in rest frame:
Collider size comparison
D. Schulte, The muon collider, IPAC2022, Bangkok, Thailand.

## Slide 5: Why a Muon Collider?
IMCC (Internation Muon Collider Collaboration) aims at studying the feasibility of a 10 km, 10 TeV center of mass energy Muon Collider, as indicated by the European Strategy for Particle Physics.
must be produced, accelerated and collided ASAP
decay products must be shielded to avoid damage to the machine or radiation
D. Neuffer and V. Shiltsev 2018 JINST 13 T10003
Affordability?
Its size is competitive because it is compact.
A 10 TeV muon collider making use of the LHC infrastructure could be the most cost-effective energy frontier collider
The Muon Collider is a very promising post-LHC high physics facility:
  200 times heavier than electron ( m=105.7 MeV/c2 ,me=0.511 MeV/c2 ) → 109 times less radiation loss.
  elementary particle: all COM energy available for the collision, contrary to hadron machines.
BUT ecays in 2.2 in rest frame:
Collider size comparison
D. Schulte, The muon collider, IPAC2022, Bangkok, Thailand.

## Slide 6: The Muon Collider Complex
Main stages of a muon collider complex
Purpose:
Evaluate realistic performance targets for the collider magnets, in close collaboration with studies of beam physics, cryogenics, and energy storage.
Produce a credible and affordable design study (contain costs, energy efficiency, sustainable operation).
Task 7.4
Magnets:
Dipoles
Quadrupoles
Sextupoles

## Slide 7: Collider Magnets Requirements
3 TeV collider (5 km ring):
Close to state of the art
11T/150mm (Nb3Sn)
600 magnets, 5 m length
Operating temperature: 4.5 K
10+ TeV collider (10 km ring):
HTS magnets, R&D is required
15T/150mm (ReBCO, hybrid)
1200 magnets, 5 m length
Operating temperature: 4.5…20 K
High field dipoles to minimize collider ring size and maximize luminosity.
Beam loss protection
High-energy electrons and positrons arising from muon decay and striking the collider ring magnets can cause radiation damage and unwanted heat load.
Courtesy of Patricia Borges de Sousa
https://indico.cern.ch/event/1250075/contributions/5357594/
Assuming 10 TeV machine and coil at 4.5 K
with HTS @20K the absorber can be thinner
Courtesy of A. Lechner
Shielding
Large aperture

## Slide 8: Collider Magnets Requirements
3 TeV collider (5 km ring):
Close to state of the art
11T/150mm (Nb3Sn)
600 magnets, 5 m length
Operating temperature: 4.5 K
10+ TeV collider (10 km ring):
HTS magnets, R&D is required
15T/150mm (ReBCO, hybrid)
1200 magnets, 5 m length
Operating temperature: 4.5…20 K
High field dipoles to minimize collider ring size and maximize luminosity.
Beam loss protection
High-energy electrons and positrons arising from muon decay and striking the collider ring magnets can cause radiation damage and unwanted heat load.
Courtesy of A. Lechner
Shielding
Large aperture
Difficult to define
a single magnet
specification
Arc:
Combined function magnets: B1, B1+B2 and B1+B3
B ≈ 8…16 T; G ≈ 320 T/m; G’ ≈ 7100 T/m2
Aperture ≈ 160 mm
Final focus:
Combined function magnets: B1, B2, B1+B2, B1+B3
B ≈ 4…16 T; G ≈ 100…300 T/m; G’ ≈ 12000 T/m2
Aperture ≈ 150…330 mm
V.V. Kashikhin et al.

## Slide 9: Introduction to A-B plots
Need for high fields in large apertures
We perform plots that can show the allowed area between aperture diameter (A) and bore field (B).
We consider Nb3Sn for the 3 TeV machine and HTS (ReBCO) for the 10 TeV collider.
Innovative approach, useful for interfacing the needs of beam dynamics with the technological limits (of today and the near future) related to superconducting magnets.
Immediate feedback capable of analyzing many possible configurations in a single plot

## Slide 10: Introduction to A-B plots
Need for high fields in large apertures
We perform plots that can show the allowed area between aperture diameter (A) and bore field (B).
We consider Nb3Sn for the 3 TeV machine and HTS (ReBCO) for the 10 TeV collider.
Limit curves are introduced by mechanical challenges (stress limit), critical current density (margin limit) and stored magnetic energy (quench protection), depending on the superconducting material.

## Slide 11: Method and Assumptions
A Python code is used to implement the analytic formulas for the cos-theta magnets in sector coil approximation.
Dipole
Quadrupole
(
( is 60° for the dipole and 30° for the quadrupole)

## Slide 12: Method and Assumptions
A Python code is used to implement the analytic formulas for the cos-theta magnets in sector coil approximation.
Cost model: by setting an upper limit to the cost of the magnet, the maximum coil width can be calculated for each aperture, taking into account the other components.
Total cost of the magnet = 400 kEUR/m (FCC-hh [ref])
Cost of the labour = 20 kEUR/m (LHC)
Aperture
150 mm
Bore
Coil
Structures
Iron
Example diagram with bore aperture set at 150 mm.
Aperture
150 mm
Aperture
150 mm
Coil width:
Structures:
SS cost: 10 EUR/kg (HL-LHC)
Iron yoke:
Fe cost: 8 EUR/kg (HL-LHC)
Materials | SC cost [EUR/kg] | Aspirational SC cost [EUR/kg]
Nb3Sn | 2000 | 700 (FCC target)*
ReBCO | 8000 | 2500 (realistic projection)**
The maximum total cost of the magnet is the same for both materials.
  ** 50 €/kAm: 1/3 of today prize (150€/kAm)
  Also based on projection of ref
  A. Molodyk and C. Larbalestier, Science, 2023
* 7€/kAm, FCC target 5€/kAm

## Slide 13: Method and Assumptions
A Python code is used to implement the analytic formulas for the cos-theta magnets in sector coil approximation.
Cost model: by setting an upper limit to the cost of the magnet, the maximum coil width can be calculated for each aperture, taking into account the other components.
The protection scheme consists in QH (or CLIQ) for classical insulated coils, limiting the hotspot temperature and the stored energy in the coils.
Materials | Hotspot T [K]
Nb3Sn | 350
ReBCO | 200
Courtesy of Tiina Salmi https://indico.cern.ch/event/1240045/
For the ReBCO, high cost requires small coil and very high current density  Protection will be a limiting factor
  Need to devise alternative protection schemes!
     Non-Insulated and Metal-Insulated coils
40 ms protection delay

## Slide 14: Method and Assumptions
A Python code is used to implement the analytic formulas for the cos-theta magnets in sector coil approximation.
Cost model: by setting an upper limit to the cost of the magnet, the maximum coil width can be calculated for each aperture, taking into account the other components.
The protection scheme consists in QH (or CLIQ) for classical insulated coils, limiting the hotspot temperature and the stored energy in the coils.
The margin limit is the limit due to the SC material itself, starting from the Bottura’s fit for the critical current density.
Materials | Operating T [K] | T margin [K]
Nb3Sn | 4.5 | 2.5 (HL-LHC)
ReBCO | 20 | 2.5
Jc refers to:
Nb3Sn: FCC cable target performance
ReBCO: Fujikura FESC-AP tape

## Slide 15: Method and Assumptions
A Python code is used to implement the analytic formulas for the cos-theta magnets in sector coil approximation.
Cost model: by setting an upper limit to the cost of the magnet, the maximum coil width can be calculated for each aperture, taking into account the other components.
The protection scheme consists in QH (or CLIQ) for classical insulated coils, limiting the hotspot temperature and the stored energy in the coils.
The margin limit is the limit due to the SC material itself, starting from the Bottura’s fit for the critical current density.
The stress limit considers the maximum mechanical stress we can have on the coils, starting from the analytical formula for the midplane pressure of cos-theta magnet in sector coil approx. (Reference: https://doi.org/10.15161/oar.it/143359 )
Materials | Peak Stress [MPa]
Nb3Sn | 150
ReBCO | 400
Currently, only stresses generated by Lorentz forces are considered.
LARP TQ
(P. Ferracin)
Tevatron dipole
(P. Ferracin)

## Slide 16: Dipole A-B Plots
HTS falls short of required performance with classical insulated coils. Assuming MI or NI magnets, the protection limit becomes comparable with the other limits.
Nb3Sn falls short of required performance because of operating margin and peak stress (at affordable cost !)
ARC [16T, 140 mm]
IR [10T, 300 mm]
ARC [16T, 140 mm]
IR [10T, 300 mm]

## Slide 17: HTS dipole A-B Plots
The curves shown in the plots are the limit curves,
i.e., for each aperture value the strictest limit is taken, excluding the limit for insulated magnets.
reduction
Cost
reduction
A reduction of HTS cost will result in wider design A-B range
A reduction of operating temperature will result in wider design A-B range
ARC [16T, 140 mm]
IR [10T, 300 mm]
ARC [16T, 140 mm]
IR [10T, 300 mm]

## Slide 18: Quadrupole A-B Plots
Nb3Sn is limited by peak stress and operating margin
HTS is mainly limited by cost production and protection. Working @20K the margin curve is also a limiting factor.
IR [115T/m, 290 mm]
ARC [240T/m, 170 mm]
ARC [330T/m, 130 mm]
IR [115T/m, 290 mm]
ARC [240T/m, 170 mm]
ARC [330T/m, 130 mm]

## Slide 19: HTS quadrupole A-B Plots
A reduction of HTS cost will result in wider design A-B range
A reduction of operating temperature will result in wider design A-B range
reduction
Cost
reduction
The curves shown in the plots are the limit curves,
i.e., for each aperture value the strictest limit is taken, excluding the limit for insulated magnets.
IR [115T/m, 290 mm]
ARC [240T/m, 170 mm]
ARC [330T/m, 130 mm]
IR [115T/m, 290 mm]
ARC [240T/m, 170 mm]
ARC [330T/m, 130 mm]

## Slide 20: FEM Crosscheck for Stress Curves
We implemented a FEM model for a sector dipole in ANSYS.
We implemented a Python code able to work with Ansys software
to run FEM simulations with the same inputs as the analytical study.
In the comparison, the FEM curves are always more restricting than the analytical ones
since they take the maximum pressure on the midplane instead of an average over the coil width.

## Slide 21: FEM Crosscheck for Stress Curves
We implemented a FEM model for a sector quadrupole in ANSYS.
We implemented a Python code able to work with Ansys software
to run FEM simulations with the same inputs as the analytical study.
In the comparison, the FEM curves are always more restricting than the analytical ones
since they take the maximum pressure on the midplane instead of an average over the coil width.

## Slide 22: Combined Function Magnet
Arc:
Combined function magnets: B1, B1+B2 and B1+B3
B ≈ 8…16 T; G ≈ 320 T/m; G’ ≈ 7100 T/m2
Aperture ≈ 160 mm
Final focus:
Combined function magnets: B1, B2, B1+B2 , B1+B3
B ≈ 4…16 T; G ≈ 100…300 T/m; G’ ≈ 12000 T/m2
Aperture ≈ 120…300 mm
Quad into dipole:
(ReBCO @20 K)
Dipole into quad:
(ReBCO @20 K)
Preliminary results obtained with ANSYS in a sector coil approximation
Quadrupole inside dipole is more efficient, in agreement with US-MAP [ref]

## Slide 23: Combined Function Magnet
Nested: Quad into dipole
2
Asymmetric Dipole
Asymmetric Quadrupole
B and G are not independent and the feasibility of windability still to be studied
Quadrupole inside dipole is the primary choice for the combined functions of the muon collider

## Slide 24: Combined Function Magnet
Python-Ansys Interface
a1_quad
w_quad
w_dip
30 mm
30 mm
Graphical representation
Scheme of the code
Data saving
Data study
What’s next? We would like to produce B-G plots in order to provide the allowed area for the combined function magnets

## Slide 25: Conclusions
The allowed magnet aperture (A) - magnetic field (B) phase spaces are provided and discussed, representing the starting point to define possible beam optics which are also acceptable from a technological point of view.
To address the issue of neutrino flux in the straight sections, combined function magnets must be used in the Muon Collider. In this regard, we are working to identify realistic target designs from a technological point of view.
Thanks to the A-B plots, we were able to identify a target design, allowing us to begin studying specific designs.
  In particular, we are exploring a cos-theta design and a block coil design.
Courtesy of F. Mariani
Courtesy of L. Alfonso

## Slide 26
Thank you
for your attention
Ph.D. in Accelerator Physics – XXXVIII cycle
24 October 2024
Daniel Novelli