## Slide 1: High throughput DAQ systems
Niko Neufeld, CERN/PH

## Slide 2: Outline
History & traditional DAQ
  Buses
  LEP / Tevatron
LHC DAQ
  Introduction
  Network based DAQ
  Ethernet
  Scaling Challenges
    Switches
    Nodes
    Challenges (buffer occupancy) Packet-sizes
    Push & Pull
  Real LHC DAQ architectures (bandwidth vs complexity)
  Eventfilterfarms
“Ultimate” DAQ
  Trigger-free / Sampling, ILC, Clic
  Almost there: CMB
  Longterm: LHC upgrade
  Ethernet (again)? / InfiniBand

## Slide 3: Disclaimer
I have been working in this field since 11 years and admit readily to a biased view
I have selected DAQ systems mostly to illustrate throughput / performance  not mentioned does not mean that it is not an interesting system
“High throughput” brings a focus on large experiments: the greatest heroism in DAQ is found in small experiments, where the DAQ is done by one or two people part-time and in test-beams. I pay my respects to them!

## Slide 4: Tycho Brahe and the Orbit of Mars
First measurement campaign
Systematic data acquisition
  Controlled conditions (same location, same day and month)
  Careful observation of boundary conditions (weather, light conditions etc…) - important for data quality / systematic uncertainties
I've studied all available charts of the planets and stars and none of them match the others. There are just as many measurements and methods as there are astronomers and all of them disagree. What's needed is a long term project with the aim of mapping the heavens conducted from a single location over a period of several years. Tycho Brahe, 1563 (age 17).

## Slide 5: The First Systematic Data Acquisition
Data acquired over 18 years, normally e every month
Each measurement lasted at least 1 hr with the naked eye
Red line (only in the animated version) shows comparison with modern theory

## Slide 6: Tycho’s DAQ in today’s Terminology
Trigger = in general something which tells you when is the “right” moment to take your data
  In Tycho’s case the position of the sun, respectively the moon was the trigger
  the trigger rate ~ 3.85 x 10-6 Hz (one measurement / month) compare with LHCb 1.0 x 106 Hz
Event-data (“event”) = the summary of all sensor data, which are recorded from an individual physical event
  In Tycho’s case the entry in his logbook (about 100 characters / entry)
  In a modern detector the time a particle passed through a specific piece of the detector and the signal (charge, light) it left there
Band-width (bw) (“throughput”) = Amount of data transferred / per unit of time
  “Transferred” = written to his logbook
  “unit of time” = duration of measurement
  bwTycho = ~ 100 Bytes / h = 0.0003 kB/s bwLHCb = 55.000 Bytes / us = 55000000 kB/s

## Slide 7: Lessons from Tycho
Tycho did not do the correct analysis (he believed that the earth was at the center of the solar system) of the Mars data. This was done by Johannes Kepler (1571-1630), eventually paving the way for Newton’s laws  good data will always be useful, even if you yourself don’t understand them!
The size & speed of a DAQ system are not correlated with the importance of the discovery!

## Slide 8: Physics, Detectors, Trigger & DAQ
rare, need many collisions
High rate collider
Fast electronics
Data acquisition
Trigger
decisions
Event Filter
Mass
Storage
data
decisions
data
signals

## Slide 9: Before the DAQ - a detector channel
Amplifier
Filter
Shaper
Range compression
clock (TTC)
Sampling
Digital filter
Zero suppression
Buffer
Format & Readout
Buffer
Feature extraction
Detector / Sensor
to Data Acquisition System

## Slide 10: Crate-based DAQ
Many detector channels are read-out on a dedicated PCB (“board”)
Many of these boards are put in a common chassis or crate
These boards need
  Mechanical support
  Power
  A standardized way to access their data (our measurement values)
All this (and more ) is provided by standards for (readout) electronics such as VME (IEEE 1014), Fastbus, Camac , ATCA, uTCA
Backplane Connectors
(for power and data)
VME Board
Plugs into Backplane
6/9U VME Crate
(a.k.a. “Subrack”)
19”
9U

## Slide 11: Example: VME
Readout boards in a VME-crate
  mechanical standard for
  electrical standard for power on the backplane
  signal and protocol standard for communication on a bus
Notes:     modules (6U x 200 mm, 9U x 400 mm)
    Crates 19’’ wide

## Slide 12: Communication in a Crate: Buses
A bus connects two or more devices and allows the to communicate
The bus is shared between all devices on the bus  arbitration is required
Devices can be masters or slaves and can be uniquely identified ("addressed") on the bus
Number of devices and physical bus-length is limited (scalability!)
  For synchronous high-speed buses, physical length is correlated with the number of devices (e.g. PCI)
  Typical buses have a lot of control, data and address lines
Buses are typically useful for systems << 1 GB/s
Device 1
Master
Data Lines
Slave
Select Line
Device 2
Device 4
Device 3
Device 2
Device 4
Master
Data Lines
Slave
Select Line
Device 1
Device 3
Notes: Address and data signals can be on separate electrical lines or share the same lines (multiplexed)

## Slide 13: Crate-based DAQ at LEP (DELPHI)
FE data
Full Event
200 Fastbus crates, 75 processors
total event-size ~ 100 kB
rate of accepted events O(10 Hz)
adapted from C. Gaspar (CERN)

## Slide 14: Combining crates and LANs: the D0 DAQ (L3)
ROC
ROC
ROC
ROC
ROC
Farm Node
Farm Node
Farm Node
Read Out Crates are VME crates that receive data from the detector. Event-size 300 kB, at ~ 1 kHz
Most data is digitized on the detector and sent to the Movable Counting House
  Detector specific cards in the ROC
DAQ HW reads out the cards and makes the data format uniform
Event is built in the Farm Node
  There is no dedicated event builder
Level 3 Trigger Decision is rendered in the node in software
Farm Nodes are located about 20 m away (electrically isolated)
Between the two is a very large CISCO switch… (2002)

## Slide 15: The DO DAQ in 2002 - 2011
ROC’s contain a Single Board Computer to control the readout.
  VMIC 7750’s, PIII, 933 MHz
  128 MB RAM
  VME via a PCI Universe II chip
  Dual 100 Mb ethernet
  4 have been upgraded to Gb ethernet due to increased data size
Farm Nodes: 288 total, 2 and 4 cores per pizza box
  AMD and Xeon’s of differing classes and speeds
  Single 100 Mb Ethernet
  Less than last CHEP!
CISCO 6590 switch
  16 Gb/s backplane
  9 module slots, all full
  8 port GB
  112 MB shared output buffer per 48 ports

## Slide 16: LHC DAQ
DAQ for multi-Gigabyte/s experiments

## Slide 17: Moving on to Bigger Things…
The CMS Detector

## Slide 18: Moving on to Bigger Things…
?
15 million detector channels
@ 40 MHz
= ~15 * 1,000,000 * 40 * 1,000,000 bytes
= ~ 600 TB/sec

## Slide 19: Know Your Enemy: pp Collisions at 14 TeV at 1034 cm-2s-1
(pp) = 70 mb --> >7 x 108 /s (!)
In ATLAS and CMS* 20 min bias events will overlap
HZZ
Z mm
H 4 muons:
the cleanest
(“golden”)
signature
And this
(not the H though…)
repeats every 25 ns…
*)LHCb @2x1033 cm-2-1 isn’t much nicer and in Alice (PbPb) it will be even worse

## Slide 20: LHC Trigger/DAQ parameters
# Level-0,1,2 Event Network Storage
Trigger Rate (Hz) Size (Byte) Bandw.(GB/s) MB/s (Event/s)
4 Pb-Pb 500 5x107 25 1250 (102)
p-p 103 2x106 200 (102)
3 LV-1 105 1.5x106 4.5 300 (2x102)
LV-2 3x103
2 LV-1 105 106 100 ~1000 (102)
2 LV-0 106 5.5x104 55 150 (2x103)
ALICE
ATLAS
CMS
LHCb
Notes: Trigger levels include HLT which is operating on entire events

## Slide 21: DAQ implemented on a LAN
Powerful Core routers
“Readout Units”
for protocol adaptation
Custom links from the
detector
Edge switches
Servers for event
filtering
Typical number of pieces
Detector
1
1000
100 to 1000
2 to 8
50 to 100
> 1000

## Slide 22: Event Building over a LAN
Data Acquisition
Switch
To Trigger
Algorithms
1
Event fragments are received from detector front-end
2
Event fragments are read out over a network to an event builder
3
Event builder assembles fragments into a complete event
4
Complete events are processed by trigger algorithms
Event Builder 3
Event Builder 2
Event Builder 1

## Slide 23: One network to rule the all
Ethernet, IEEE 802.3xx, has almost become synonymous with Local Area Networking
Ethernet has many nice features: cheap, simple, cheap, etc…
Ethernet does not:
  guarantee delivery of messages
  allow multiple network paths
  provide quality of service or bandwidth assignment (albeit to a varying degree this is provided by many switches)
Because of this raw Ethernet is rarely used, usually it serves as a transport medium for IP, UDP, TCP etc…
Ethernet
Flow-control in standard Ethernet is only defined between immediate neighbors
Sending station is free to throw away x-offed frames (and often does )
Xoff
data

## Slide 24: CMS Data Acquisition

## Slide 25: 2-Stage Event Builder
12.5 kHz
12.5 kHz
100 kHz
12.5 kHz
…
1st stage “FED-builder”
Assemble data from 8 front-ends into
one super-fragment at 100 kHz
8 independent “DAQ slices”
Assemble super-fragments into full events

## Slide 26: Super-Fragment Builder (1st stage)
based on Myrinet technology (NICs and wormhole routed crossbar switches)
NIC hosted by FRL module at sources
NIC hosted by PC (“RU”) at destination
~1500 Myrinet fibre pairs (2.5 Gbps signal rate) from underground to surface
Typically 64 times 8x8 EVB configuration
Packets routed through independent switches (conceptually 64)
Working point ~2 kB fragments at 100 kHz
Destination assignment: round-robin
loss-less and backpressure when congested

## Slide 27: Scaling in LAN based DAQ

## Slide 28: Congestion
2
"Bang" translates into random, uncontrolled packet-loss
In Ethernet this is perfectly valid behavior and implemented by many low-latency devices
Higher Level protocols are supposed to handle the packet loss due to lack of buffering
This problem comes from synchronized sources sending to the same destination at the same time
2
2
Bang

## Slide 29: Push-Based Event Building
Switch Buffer
Data Acquisition
Switch
1
Event Manager tells readout boards where events must be sent (round-robin)
2
Readout boards do not buffer, so switch must
3
No feedback from Event Builders to Readout system
“Send next event to EB1”
“Send next event to EB2”
Event Builder 2
Event Builder 1
Event
Manager

## Slide 30: Cut-through switching Head of Line Blocking
2
2
4
Packet to node 4 must wait
even though port to node 4 is free
The reason for this is the First in First Out (FIFO) structure of the input buffer
Queuing theory tells us* that for random traffic (and infinitely many switch ports) the throughput of the switch will go down to 58.6%  that means on 100 MBit/s network the nodes will "see" effectively only ~ 58 MBit/s
*) "Input Versus Output Queueing on a Space-Division Packet Switch"; Karol, M. et al. ; IEEE Trans. Comm., 35/12
4
2
1
3

## Slide 31: Using more of that bandwidth
Cut-through switching is excellent for low-latency (no buffering) and reduces cost (no buffer memories), but “wastes” bandwidth
  It’s like building more roads than required just so that everybody can go whenever they want immediately
For optimal usage of installed bandwidth there are in general two strategies:
  Use store-and-forward switching (next slide)
  Use traffic-shaping / traffic-control
    Different protocols (“pull-based event-building”), multi-level readout
    end-to-end flow control
    virtual circuits (with credit-scheme) (InfiniBand)
    Barrel-shifter

## Slide 32: Output Queuing
In practice virtual output queueing is used: at each input there is a queue  for n ports O(n2) queues must be managed
Assuming the buffers are large enough(!) such a switch will sustain random traffic at 100% nominal link load
2
2
Packet to node 2 waits at output to
port 2. Way to node 4 is free
2
1
3
4
4

## Slide 33: Store-and-Forward in the LHC DAQs
256 MB shared memory / 48 ports
Up to 1260 ports (1000 BaseT)
Price / port ~ 500 - 1000 USD
Used by all LHC experiments
6 kW power, 21 U high
Loads of features (most of them unused  in the experiments)

## Slide 34: Buffer Usage in F10 E1200i
Chart: Port (connected to edge-router)
 | 2298 | 2823.6 | 2557.6 | 2278 | 2986.8 | 1268.4 | 1805.6 | 1637.6 | 3394 | 2216.8 | 1476 | 1991.2 | 1303.6 | 1826.4 | 2718 | 2020.4 | 1754.8
Buffer usage in core-router with a test using 270 sources @ 350 kHz event-rate
256 MB shared between 48 ports
17 ports used as “output”
This measurement for small LHCb events (50 kB) at 1/3 of nominal capacity

## Slide 35: Push-Based Event Building with store& forward switching and load-balancing
Event Builder 1
Data Acquisition
Switch
1
Event Builders notify Event Manager available capacity
2
Event Manager
ensures that data are sent only to nodes with available capacity
3
Readout system relies on feedback from Event Builders
“Send next event to EB1”
“Send next event to EB2”
EB1:
EB2:
EB3:
0
0
0
“Send me
an event!”
“Send me
an event!”
1
1
1
“Send me
an event!”
“Send me
an event!”
0
1
1
0
0
1
“Send next event to EB3”
1
0
1
Event Builder 1
Event Builder 2
Event Builder 3
Event Manager

## Slide 36: DAQ networks beyond push and store & forward
Reducing network load
Pull-based event-building
Advanced flow-control

## Slide 37: Progressive refinement: ATLAS
3-level trigger
Partial read-out (possible because of the nature of ATLAS physics) at high rate
Full read-out at relatively low rate
 smaller network

## Slide 38: ATLAS DAQ (network view)
Farm interface processors
collect full data of accepted events from buffers and distribute them though backend core chassis to third level trigger processor farms
over a TCP routed network
Optional connection to use Level 2 farms for Level 3 use
2 * 1G trunks
Collect accepted events and transfer them over 10G fiber to storage and Grid

## Slide 39: Pull-Based Event Building
Event Builder 1
Data Acquisition
Switch
1
Event Builders notify Event Manager of available capacity
2
Event Manager elects event-builder node
3
Readout traffic is driven by Event Builders
“EB1, get next event”
“EB2, get next event”
EB1:
EB2:
EB3:
0
0
0
“Send me
an event!”
“Send me
an event!”
1
1
1
“Send me
an event!”
“Send me
an event!”
0
1
1
0
0
1
1
0
1
Event Builder 1
Event Builder 2
Event Builder 3
“Send event to EB 1!”
“Send event to EB 1!”
“Send event to EB 1!”
“Send event to EB 1!”

## Slide 40: Advanced Flow-control DCB, QCN

## Slide 41: Why is DCB interesting?
Data Center Bridging tries to brings together the advantages of Fibrechannel, Ethernet and InfiniBand on a single medium
It has been triggered by the storage community (the people selling Fibrechannel over Ethernet and iSCSI)
It achieves low latency and reliable transport at constant throughput through flow-control and buffering in the sources
802.1Qau, 802.1Qbb, 802.3bd could allow us to go away from store&forward in DAQ LANs ( extensive R&D required)

## Slide 42: Moving the data in and through a PC

## Slide 43: Sending and receiving data
Multiple network protocols result in multiple software layers
Data moving can be expensive
  Passing data through the layers sometimes cannot be done without copying
  Header information needs to be stripped off  splicing, alignment etc…
In Ethernet receiving is quite a bit more expensive than sending
Holy grail is zero-copy event-building (difficult with classical Ethernet, easier with InfiniBand)

## Slide 44: The cost of event-building in the server
Chart: Event-rate [Hz]
| 3000.0 | 2500.0 | 2000.0 | 1500.0 | 1000.0 | 500.0
CPU % | 56 | 48 | 38 | 26.8 | 18.5 | 9
MEM | 121 | 112 | 105 | 98 | 98 | 72
% CPU of one Intel 5420 core (a 4 core processor running at 2.5 GHz
MEM is resident memory (i.e. pages locked in RAM)
Precision of measurements is about 10% for CPU and 1% for RAM

## Slide 45: Frame-size / payload & frame-rate Or: why don’t they increase the MTU?
Chart: 
| 64.0 | 128.0 | 512.0 | 1500.0 | 4096.0 | 9000.0
frame-rate [kHz] | 1420.4 | 822.3 | 233.2 | 82 | 30.3 | 13.8
max payload [MB/s] | 67 | 89 | 110 | 116 | 118 | 118
1500 bytes leads to good link-usage
Network guys are happy
But frame-rate could still be lowered
Overheads calculated only for
Ethernet: 38 bytes / frame
IP adds another 20
TCP another 20(!)
Gigabit Ethernet = 109 bit/s

## Slide 46: Tuning for bursty traffic
In general provide for lots of buffers in the kernel, big socket buffers for the application and tune the IRQ moderation
Examples here are for Linux, 2.6.18 kernel, Intel 82554 NICs (typical tuning in the LHCb DAQ cluster)
/sbin/ethtool -G eth1 rx 1020 # set number of RX descriptors in NIC to max
# the following are set with sysctl -w
net.core.netdev_max_backlog = 4000
net.core.rmem_max = 67108864
# the application is tuned with setsockopt()

## Slide 47: Interrupt Moderation
Careful tuning necessary – multi-core machines can take more IRQs (but: spin-locking…)
Can afford to ignore at 1 Gbit/s but will need to come back to this for 10 Gbit/s and 40 Gbit/s

## Slide 48: High Level Trigger Farms
And that, in simple terms, is what we do in the High Level Trigger

## Slide 49: Event-filtering
Enormous amount of CPU power needed to filter events
  Alternative is not to filter and store everything (ALICE)
Operating System: Linux SLC5 32-bit and 64-bits: standard kernels, no (hard) real-time
Hardware:
  PC-server (Intel and AMD): rack-mount and blades
All CPU-power local: no grid, no clouds (yet?)

## Slide 50: Online Trigger Farms 2011
 | ALICE | ATLAS | CMS | LHCb
# cores | 2700 | 17000 | 10000 | 15500
total available power (kW) |  | ~ 2000(1) | ~ 1000 | 550
currently used power (kW) |  | ~ 250 | 450(2) | ~ 145
total available cooling power | ~ 500 | ~ 820 | 800 (currently) | 525
total available rack-space (Us) | ~ 2000 | 2400 | ~ 3600 | 2200
CPU type(s) | AMD Opteron, Intel 54xx, Intel 56xx | Intel 54xx, Intel 56xx | Intel 54xx, Intel 56xx | Intel 54xx, Intel 56xx
(1) Available from transformer (2) PSU rating

## Slide 51: Faster, Larger – the future A bit of marketing for upcomig DAQ systems

## Slide 52: SuperB DAQ
Collection in Readout-Crates
Ethernet read-out
60 Gbit/s
 if you look for a challenge in DAQ, you must join LHCb  - or work on the SLHC

## Slide 53: Compressed Baryonic Matter (CBM)
Heavy Ion experiment planned at future FAIR facility at GSI (Darmstadt)
Timescale: ~2014
Detector Elements
Si for Tracking
RICH and TRDs for Particle identification
RPCs for ToF measurement
ECal for Electromagnetic Calorimetry
AverageMultiplicities:
160 p
400 π-
400 π+
44 K+
13 K
800 g
1817 total at 10 MHz

## Slide 54: High Multiplicities
Quite Messy Events… (cf. Alice)
Hardware triggering problematic
  Complex Reconstruction
  ‘Continuous’ beam
Trigger-Free Readout
  ‘Continuous’ beam
  Self-Triggered channels with precise time-stamps
  Correlation and association later in CPU farm

## Slide 55: CBM DAQ Architecture

## Slide 56: CBM Characteristics/Challenges
Very much network based  5 different networks
  Very low-jitter (10 ps) timing distribution network
  Data collection network to link detector elements with front-end electronics (link speed O(GB/s))
  High-performance (~O(TB/s)) event building switching network connecting O(1000) Data Collectors to O(100) Subfarms
  Processing network within a subfarm interconnecting O(100) processing elements for triggering/data compression
  Output Network for collecting data ready for archiving after selection.

## Slide 57
LHCb DAQ Architecture from 2018
HLT
Readout
Supervisor
L0 Hardware
Trigger
Tell1
1 MHZ
1 Gb
Ethernet
Readout
Supervisor
Interaction
Trigger
Tell40
40 MHZ
1…40 MHZ
10 Gb
Ethernet
HLT++
Upgrade
Current
- All data will be readout @ collision rate 40 MHz by all frontend electronics (FEE)  a trigger-free read-out!
- Zero-suppression will be done in FEEs to reduce the number of the GigaBit Transceiver (GBT) links
GBT (4.8Gb/s)
data rate 3.2 Gb/s

## Slide 58: Requirements on LHCb DAQ Network
Design:
  100 kB@30 MHz (10 MHz out of 40 MHz are empty)  24 Tbit/s network required
  Keep average link-load at 80% of wire-speed
  ~5000 Servers needed to filter the data (depends on Moore’s Law)
We need:
  (input) Ports for Readout boards (ROB) from the detector: 3500x10 Gb/s
  (output) Ports for Event Filter Farm (EFF): 5000x10 Gb/s
  Bandwidth: 34 Tb/s (unidirectional, including load-factor)
Scaling: build several (8) sub-networks or slices. Each Readout Board is connect to each slice.

## Slide 59: Fat-Tree Topology for One Slice
48-port 10 GbE switches
Mix readout-boards (ROB) and filter-farm-servers in one switch
  15 x readout-boards
  18 x servers
  15 x uplinks
Non-block switching
use 65% of installed bandwidth
(classical DAQ only 50%)
Each slice accomodates
  690 x inputs (ROBS)
  828 x outputs servers
Ratio (server/ROB) is adjustable
Notes: Take advantage of unidirection

## Slide 60: InfiniBand
High bandwidth (32 Gbit/s, 56 Gbit/s …) – always a step ahead of Ethernet 
Low price / switch-port
Very low latency
 | SDR | DDR | QDR | FDR | EDR | HDR | NDR
1X | 2 Gbit/s | 4 Gbit/s | 8 Gbit/s | 14 Gbit/s | 25 Gbit/s | 125 Gbit/s | 750 Gbit/s
4X | 8 Gbit/s | 16 Gbit/s | 32 Gbit/s | 56 Gbit/s | 100 Gbit/s | 500 Gbit/s | 3000 Gbit/s
12X | 24 Gbit/s | 48 Gbit/s | 96 Gbit/s | 168 Gbit/s | 300 Gbit/s | 1500 Gbit/s | 9000 Gbit/s

## Slide 61: InfiniBand: the good, the bad and the ugly
Cheap, but higher-speed grades will require optics
Powerful flow-control / traffic management
Native support for RDMA (low CPU overhead)
Cabling made for clusters (short distances)
Very small vendor base
Complex software stack
Some of the advanced possibilities (RDMA, advanced flow-control) become available on “converged” NICs (e.g. Mellanox, Chelsio)

## Slide 62: Is the future of DAQ in the OFED?

## Slide 63: Future DAQ systems (choices)
Certainly LAN based
  InfiniBand deserves a serious evaluation for high-bandwidth (> 100 GB/s)
  In Ethernet if DCB works, might be able to build networks from smaller units, otherwise we will stay with large store&forward boxes
Trend to “trigger-free”  do everything in software  bigger DAQ will continue
  Physics data-handling in commodity CPUs
Will there be a place for multi-core / coprocessor cards (Intel MIC / CUDA)?
  IMHO this will depend on if we can establish a development framework which allows for longterm maintenance of the software by non-”geek” users, much more than on the actual technology

## Slide 64: Summary and Future
Large modern DAQ systems are based entirely on Ethernet and big PC-server farms
Bursty, uni-directional traffic is a challenge in the network and the receivers, and requires substantial buffering in the switches
The future:
  It seems that buffering in switches is being reduced (latency vs. buffering)
  Advanced flow-control is coming, but it will need to be tested if it is sufficient for DAQ
  Ethernet is still strongest, but InfiniBand looks like a very interesting alternative
  Integrated protocols (RDMA) can offload servers, but will be more complex

## Slide 65: Publicita / Publicité / Commercial

## Slide 67: Thanks
I acknowledge gratefully the help of many colleagues who provided both material and suggestions: Guoming Liu, Beat Jost, David Francis, Frans Meijers, Gordon Watts, Clara Gaspar

## Slide 68: Appendix

## Slide 69: Managing Online farms
How to manage the software: Quattor (CMS & LHCb) RPMs + scripts (ALICE & ATLAS)
We all *love* IPMI. In particular if it comes with console redirection!
How to monitor the fabric: Lemon, FMC/PVSS, Nagios, …
Run them disk-less (ATLAS, LHCb) or with local OS installation (ALICE, CMS)
How to use them during shutdowns: Online use only (ALICE, ATLAS, CMS), use as a “Tier2” (LHCb)

## Slide 70: LEP & LHC in Numbers

## Slide 71: Challenges for the L1 at LHC
N (channels) ~ O(107); ≈20 interactions every 25 ns
  need huge number of connections
Need to synchronize detector elements to (better than) 25 ns
In some cases: detector signal/time of flight > 25 ns
  integrate more than one bunch crossing's worth of information
  need to identify bunch crossing...
It's On-Line (cannot go back and recover events)
  need to monitor selection - need very good control over all conditions

## Slide 72: Constantly sampled
Needed for high rate experiments with signal pileup
Shapers and not switched integrators
Allows digital signal processing in its traditional form (constantly sampled data stream)
Output rate may be far to high for what following DAQ system can handle
With local zero-suppression this may be an option for future high rate experiments (SLHC, CLIC)
ADC
DAQ
Shaping
Sampling clock
DSP
(zero-sup.)

## Slide 73: Improving dead-time with buffers
ADC
Sensor
Delay
Proces-
sing
Discriminator
Trigger
Start
Buffers are introduced to de-randomize data,
to decouple the data production from the data
consumption. Better performance.
Busy Logic
FIFO
Full
DataReady
and
storage

## Slide 74: Trigger in 6 slides

## Slide 75: What is a trigger?
An open-source 3D rally game?
The most famous horse in movie history?
An important part of a Beretta

## Slide 76: What is a trigger?
Wikipedia: “A trigger is a system that uses simple criteria to rapidly decide which events in a particle detector to keep when only a small fraction of the total can be recorded. “
Simple
Rapid
Selective
When only a small fraction can be recorded

## Slide 77: Trivial DAQ
ADC Card
External View
sensor
sensor
CPU
disk
ADC
storage
Physical View
Logical View
Proces-
sing

## Slide 78: Trivial DAQ with a real trigger
ADC
Sensor
Delay
Proces-
sing
Interrupt
Discriminator
Trigger
Start
storage
What if a trigger is produced when the ADC or
processing is busy?

## Slide 79: Trivial DAQ with a real trigger 2
ADC
Sensor
Delay
Proces-
sing
Interrupt
Discriminator
Trigger
Start
Deadtime (%) is the ratio between the time the DAQ
is busy and the total time.
Set
Q
Clear
and
not
Busy Logic
Ready
storage

## Slide 80: Triggered read-out
Trigger processing requires some data transmission and processing time to make decision so front-ends must buffer data during this time. This is called the trigger latency
For constant high rate experiments a “pipeline” buffer is needed in all front-end detector channels: (analog or digital)
  Real clocked pipeline (high power, large area, bad for analog)
  Circular buffer
  Time tagged (zero suppressed latency buffer based on time information)
ADC
DAQ
Shaping
Channel mux.
Trigger
Constant writing