## Slide 1: Update from RIPTIDE lab
RIPTIDE meeting 11/09/2024
Claudia Pisanti UniBO & INFN BO
Alberto Mengarelli INFN BO

## Slide 2: Outline
Trigger for ASI camera
MCP status
Purchased material

## Slide 3: Trigger for the ASI Camera: Set-up
Black box
ASI 533 + optics
blue LED
Pulsed with ARDUINO
- 1 ms ON
- 5000 ms OFF
facing the LED
PMT
At 1200 Volt.
Oscilloscopio
Signal from the PMT
Discriminator
Dual Timer
To Arduino UNO
Analog PIN
Signal after reshaping
Output USB to the LAPTOP
Output USB to the LAPTOP
Threshold: 30 mV
Sig OUT : ~1.7 V
Sig IN : ~50 mV
Time width from ns to ms

## Slide 4: Trigger for the ASI Camera: Labview
In Labview pre-build libraries for ARDUINO and ASI-Camera
Start camera exposure
Wait for the PMT Trigger signal from ARDUINO
Stop camera exposure
Save DATA
LabView acquisition software

## Slide 5: Trigger for the ASI Camera: Output
Output on the camera

## Slide 6: MCP Status
MCP is in out lab!
need to make it work…

## Slide 7: Shopping June/July 2024
From Thorlabs:
Laser 405 nm, mounting rings and lenses, screw kit, cleaning set, mirror and holders ~ 1.5 keuro ✔
(M4 instead of M6)
From RS:
Banana-banana cables (10 red + 10 black), coaxial cable 50 m 75 Ω, connectors (micro bnc) ~ 300 euro ✔
(After 16 Oct.)