## Slide 1: MIZAR ASIC
A. Di Salvo, S. Garbolino, M. Mignone, S. Zugravel,
A. Rivetti, M. E. Bertaina, Antonio Palmieri
(INFN-TO, UNITO, POLITO)
November 11th 2023 34th JEM-EUSO Collaboration Meeting

## Slide 2: Take home message
MIZAR = Multi-channel Integrated Zone-sampling Analogue-memory based Readout
MIZAR ASIC in in the final design state
An order has been placed for production of 200 pieces (150 for PBR and 50 for Terzina) through CERN on 65 nm technology TSMC
Production run expected for February 2024
Delivery expected in 12 weeks (May 2024)
June and July 2024 devoted to chip characterization and verification of the requirements at INFN Torino, then distributed to the collaboration.
A second run will be precautionally booked for August 2024 in case of needed fine tuning.

## Slide 3: Design
● Detection of Extensive Air Showers.
● 64-channel ASIC implemented in a
commercial 65 nm CMOS technology.
● High level of configurability
● Segmentation:
- 32 cells (160 ns)
- 64 cells (320 ns)
- 256 cells (1.28 us)
● 400 MHz clock used at half rate for sampling and digitization (5 ns)
● Resolution:
8 - 12 bits
● Trigger:
- Internally generated
- Externally provided
● Mode:
- Imaging (hitmap)
Power target : <10 mW/ch

## Slide 4: Low and High thresholds available and generation of Hit Maps
Example of expected EAS (no bifocality)
Low threshold > 5 - 7 phe
High threshold > 10 – 15 phe
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 1 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Every 20 ns

## Slide 5: Hitmap Logic

## Slide 6: Hitmap Logic

## Slide 7: Trigger conditions for Terzina on FPGA (handled in ~150 ns)

## Slide 8: Serial Bus
The system works in Double Data Rate

## Slide 9: Camera and ASIC architecture
FPGA Plane
ASIC Plane
SiPM Plane

## Slide 10: THANK YOU