## Slide 1
1st Cost & Schedule Review Meeting A.Ghigo Frascati 11 Dicembre 2023
Andrea Ghigo on behalf of
EuPRAXIA@SPARC-LAB Collaboration
1st Cost & Schedule Review Meeting Frascati 11 Dicembre 2023
Status EuPRAXIA@Sparc_LAB Technical Design Report

## Slide 2
EuPRAXIA@SPARC-LAB: Machine and Building Layout
1st Cost & Schedule Review Meeting A.Ghigo Frascati 11 Dicembre 2023

## Slide 3
Laser & THz clean rooms
Particle experimental halls
Photon user experimental hall
Accelerator tunnel
Undulators tunnel
Klystron&modulators
Power supplies gallery
Plant gallery
Functional description of the areas
1st Cost & Schedule Review Meeting A.Ghigo Frascati 11 Dicembre 2023

## Slide 4
Courtesy of C.Vaccarezza
Starting from Beam Dynamics

## Slide 5
Linac, undulators and
user area layout
The components studied so far for the EuPRAXIA complex are:
the injector, the RF linac, the plasma acceleration module,
two undulator lines, two optical lines and two experimental stations
1st Cost & Schedule Review Meeting A.Ghigo Frascati 11 Dicembre 2023

## Slide 6
Injector 2D layout
Gun + 4 RF S-Band accelerating structure:
the first 3m long, the other 2m long
1st Cost & Schedule Review Meeting A.Ghigo Frascati 11 Dicembre 2023

## Slide 7
RF Photogun
E. Di Pasquale
Photogun SPARC type +
X band RF linearizer
1st Cost & Schedule Review Meeting A.Ghigo Frascati 11 Dicembre 2023

## Slide 8
Injector & RF distribution
S-Band Injector RF power distribution
1st Cost & Schedule Review Meeting A.Ghigo Frascati 11 Dicembre 2023

## Slide 9
X-Band Linac 2D layout
Low energy linac: 8 X-Band accelerating structures
Bunch compressor : magnetic chicane
High energy linac: 8 X-Band accelerating structures
Plasma acceleration module
1st Cost & Schedule Review Meeting A.Ghigo Frascati 11 Dicembre 2023

## Slide 10
X-Band RF module
CANON 25 MW Klystron
SCANDINOVA K300 Modulator
BOC Pulse Compressor +
2 x 90cm X-band Accelerating Sections
1st Cost & Schedule Review Meeting A.Ghigo Frascati 11 Dicembre 2023

## Slide 11
1st Cost & Schedule Review Meeting A.Ghigo Frascati 11 Dicembre 2023
Plasma section - Plasma sources for EuPRAXIA
HV generator
HV pulser
High current
HV pulser
High current
Delay generator
Voltage/current control
Discharge
trigger
control
HV generator
    Plasma sources larger than 40 cm (m-scale) with HV pulses less tahn 10 kV
    Longitudinal density modulation
    1.5 GV/m m-scale capillary - density 1016 cm-3
6 kV
6 kV
e

## Slide 12
ARIA: 5 undulator modules + dispersive section
AQUA and ARIA undulators lines
AQUA: 10 APPLE-X Undulator Modules 2m long
1st Cost & Schedule Review Meeting A.Ghigo Frascati 11 Dicembre 2023

## Slide 13
AQUA APPLE-X Undulators
Quadrupole-corrector magnet; Cavity Beam Position Monitor; view screen and pumping unit have been inserted between each module
1st Cost & Schedule Review Meeting A.Ghigo Frascati 11 Dicembre 2023

## Slide 14
ARIA Planar Undulator Module
with quads & diagnostics
1st Cost & Schedule Review Meeting A.Ghigo Frascati 11 Dicembre 2023

## Slide 15
FEL Users area
Diagnostic:
  Beam position monitors
  Intensity monitors
  Spectrometer
  Transverse dimension
  Longitudinal dimension & time arrival
  Wavefront measurement
  Polarization measurement
  Coherence measurement
Beam lines:
  Defining apertures
  Mirror and focusing
  Filter and attenuators
  Monochromator
  Split & delay
We have to select the beam line components
according to the needs of the user
1st Cost & Schedule Review Meeting A.Ghigo Frascati 11 Dicembre 2023

## Slide 16
1st Cost & Schedule Review Meeting A.Ghigo Frascati 11 Dicembre 2023
 | Chapter | Reference person/people
1 | executive summary | ferrario
2 | eupraxia in the european context | assmann/ferrario
3 | eupraxia@sparc_lab | ferrario/ghigo
4 | scientific case | stellato
5 | experience with the LNF test facilities | pompili/cardelli/biagioni
6 | beam physics | vaccarezza/giannessi
7 | machine layout | ghigo
8 | photoinjector | chiadroni
9 | X-band linac | alesini/gallo
10 | plasma accelerating module | pompili/biagioni
11 | Free Electron Laser | giannessi/petralia
12 | photon beam lines | villa
13 | experimental endstations | stellato/villa
14 | electron and photon diagnostics | cianchi/villa
15 | laser systems | anania
16 | timing and synchronisation | bellaveglia
17 | control system | pioli
18 | vacuum system | liedl
19 | magnets and power supply | sabbatini
20 | machine protection system | pioli
21 | civil infrastructures | rotundo
22 | radiation safety and beam dump | esposito
23 | integration, implementation and commissioning strategy | del franco
24 | system engeneering | cioeta
25 | project costs , timeline and management structure | falone
TDR Structure

## Slide 17
Building rendering
Courtesy MYTHOS cons., S.Incremona, U.Rotundo,
EuPRAXIA TDR Review Committee A.Ghigo Frascati 30/11-2/12 2022

## Slide 18
Final Draft has been validate
The «Conferenza dei Servizi» (Permitting authority committee) has given construction permission.
Mythos Consortium, the external designer, started the executive design, final step to start the tender for the construction
The bid for the executive project review from an external firm started
Cost updated has been presented at INFN management level (GE).
Progress in the design finalization and authorization process:
Courtesy S.Incremona, U.Rotundo
EuPRAXIA TDR Review Committee A.Ghigo Frascati 30/11-2/12 2022
    Infrastructure Status

## Slide 19
1st Cost & Schedule Review Meeting A.Ghigo Frascati 11 Dicembre 2023
    Equipments & Building CAD integration

## Slide 20
    Accelerator & lasers Area
1st Cost & Schedule Review Meeting A.Ghigo Frascati 11 Dicembre 2023

## Slide 21
    Undulators & users Area
1st Cost & Schedule Review Meeting A.Ghigo Frascati 11 Dicembre 2023

## Slide 22
Courtesy S.Incremona, U.Rotundo and MYTHOS company
The final version of the definitive project took place after several iterations with the consortium of designers and revisions by our technical division
Drawing of the linac tunnel section
1st Cost & Schedule Review Meeting A.Ghigo Frascati 11 Dicembre 2023

## Slide 23
The building: Linac & undulator
areas
Linac area
Undulator area
Building drawing of final draft
with air cooling distribution
S.Incremona, S.Cantarella
1st Cost & Schedule Review Meeting A.Ghigo Frascati 11 Dicembre 2023

## Slide 24
F.Cioeta
1st Cost & Schedule Review Meeting A.Ghigo Frascati 11 Dicembre 2023

## Slide 25: Thanks for the attention
1st Cost & Schedule Review Meeting A.Ghigo Frascati 11 Dicembre 2023