## Slide 1: School on Plasma Accelerators April 22–26th, 2024 Orto Botanico di Roma Introduction to linear accelerators (linacs)
Marco Bellaveglia
INFN-LNF, Frascati, Rome, Italy

## Slide 2: Lecture outline
Part 1: Basic concepts
Part 2: From DC to RF accelerators
Part 3: Longitudinal dynamics
Part 4: Linac technology

## Slide 3: Part 1 Basic concepts

## Slide 4: Linac main components and definitions
Particle source
Accelerated beam
Accelerating structures
Focusing elements
Transverse dynamics of accelerated particles
Longitudinal dynamics of accelerated particles
Thermionic effect
Photoelectric effect
Filed emission
Plasma sources
Radiation sources
Secondary emission
Accelerating and focusing fields

## Slide 5
Linac applications
Injectors for synchrotrons
Medical applications: radiotherapy
Industrial applications
Material treatment
Material/food sterilization
Free Electron Lasers
Spallation sources for neutron production
Material testing for fusion nuclear reactors
Nuclear waste treatment and controlled fission for energy production (ADS)
104 LINACs operating around the world
Ion implantation
National security

## Slide 6: Particle sources notes
Electrons sources:
  Thermionic effect (high temperature filaments)
  Photo-electric effect (photo-cathodes and RF guns)
  Filed effect (quantum tunneling, FEM, nanotubes)
  Secondary sources (targets of emissive material)
Proton and ions sources
  Plasma sources (thermal, electrical or electromagnetic heating)
  Secondary sources (targets of emissive material)
Anti-matter and other sources
  Secondary sources (targets of emissive material)
  Radiation sources (radioactive elements, cosmic radiation)

## Slide 7: Example: The SPARC_LAB RF gun
Photocathode system parameters
Max peak field on the cathode 120 MV/m
Repetition rate 10 Hz
Operating vacuum 10-9 Torr
Quantum efficiency max (typical) >5x10-6
Maximum gun solenoid field 0.3 T
Laser central wavelength 263 nm
RF frequency 2.856 GHz
RMS intrinsic emittance 0.7 mm mrad/mm
Beam charge 10-1000 pC
Number of cells 1.6

## Slide 8: Lorentz force: acceleration and focusing
ACCELERATION
BENDING AND FOCUSING
The basic equation that describes the acceleration/bending/focusing processes is the Lorentz Force.
Particles are accelerated through electric fields and are bended and focused through magnetic fields.
To accelerate, we need a force in the direction of motion
2nd term always perpendicular to motion => no energy gain

## Slide 9: Acceleration basics
109-1010V
100-200 V
105 V
The energy gained by the electrons travelling from the cathode to the anode is equal to their charge multiplied the DC voltage between the two electrodes.
Particle energies are typically expressed in electron-volt [eV], equal to the energy gained by 1 electron accelerated through an electrostatic potential of 1 volt.
The first historical linear particle accelerator was built by the Nobel prize Wilhelm Conrad Röntgen (1900). Electrons emitted by the heated cathode were accelerated while flowing to another electrode connected to the positive generator pole (anode). Collisions between the electron beam (originally called cathode ray) and the anode produced X-rays.
+
Electric field
Voltage V
Cathode
Anode
-
Another accelerator application is the cathode-ray-tube television (CRT TV)

## Slide 10: Single Particle Velocity VS Energy
Light particles (as electrons) are practically fully relativistic (1, >>1) at relatively low energy and reach a constant velocity (c). The acceleration process occurs at constant particle velocity
Heavy particles (protons and ions) are typically weakly relativistic and reach a constant velocity only at very high energy. The velocity changes a lot during the acceleration process.
This implies important differences in the technical characteristics of the accelerating structures. In particular, for protons and ions we need different types of accelerating structures, optimized for different velocities and/or the accelerating structure must vary its geometry to take into account the velocity variation.
rest mass m0
rest energy E0 (=m0c2)
total energy E
relativistic mass m
velocity v
momentum p (=mv)
Kinetic energy W=E-E0
Relativistic factor =v/c (<1)
Relativistic factor =E/E0 (1)
Heavy particles
Light particles
Kin. Energy [MeV]
e-
p+
e-
p+

## Slide 11: Part 2 From DC to RF accelerators

## Slide 12: Electrostatic accelerators
To increase the achievable maximum energy, Van de Graaff invented an electrostatic generator based on a dielectric belt transporting positive charges to an isolated electrode hosting an ion source. The positive ions generated in a large positive potential were accelerated toward ground by the static electric field.
LIMITS OF ELECTROSTATIC ACCELERATORS
DC voltage as large as 10 MV can be obtained (E10 MeV). The main limit in the achievable voltage is the breakdown due to insulation problems.
750 kV Cockcroft-Walton
Linac2 injector at CERN from 1978 to 1992
APPLICATIONS OF DC ACCELERATORS
DC particle accelerators are in operation worldwide, typically at V<15MV (Emax=15 MeV), I<100mA.
They are used for:
material analysis
X-ray production
ion implantation for semiconductors
first stage of acceleration (particle sources)

## Slide 13: RF accelerators: Wideroe «Drift Tube Linac»
The particles are accelerated by the electric field in the gap between electrodes connected alternatively to the poles of an AC generator. This original idea of Ising (1924) was implemented by Wideroe (1927) who applied a sine-wave voltage to a sequence of drift tubes. The particles do not experience any force while travelling inside the tubes (equipotential regions) and are accelerated across the gaps. This kind of structure is called Drift Tube Linac (DTL).
L1
Ln
If the length of the tubes (or, equivalently, the distances between the centers of the gaps) increases with the particle velocity during the acceleration such that the time of flight between gaps is kept constant and equal to half of the RF period, the particles are subject to a synchronous accelerating voltage and experience an energy gain of passing through each gap.
In principle a single RF generator can be used to indefinitely accelerate a beam, avoiding the breakdown limitation affecting the electrostatic accelerators.
The Wideroe LINAC is the first RF LINAC

## Slide 14: DC acceleration between two electrodes
Lorentz force
Energy-momentum relation
Ez
source
rate of energy gain per unit length
z (direction of acceleration)
energy gain per electrode pair
DV
+
-
z
Ez
gap
t
E

## Slide 15: RF acceleration Bunched beam
Ez
source
z
z
gap
tinj
E
Particles accelerated
Particles lost passing through the gap
t
charge
DC acceleration
t
charge
RF acceleration
Bunched beam (in order to be synchronous with the external AC field, particles must be gathered in non-uniform temporal structure)

## Slide 16: RF acceleration Transit time factor
Hyp. of symmetric accelerating field
Ez
source
z
z
gap
=
, with
-L/2
+L/2
Peak gap voltage
T<1
Transit time factor
Injection phase
Average accelerating field in the gap
Average accelerating field seen by the particle
t=z/v

## Slide 17: DTL synchronization Low energy particles
+
-
Ez
z
vn
Ln
Ln+1
Ln+2
+
-
Ez
z
Ln
Ln+1
Ln+2
vn+1
If now we consider a DTL structure, we have that at each gap the maximum energy gain is and the particle increase its velocity accordingly to the relativistic formulae. It is convenient to refer to the center of each gap as follows:
z
E
En
qVacc
z
v
vn
In order to maintain the particle synchronous with the accelerating field at the center of each gap, the distance between the centers of the gaps (Ln) must increase as:
The energy gain per unit length (i.e. the average accelerating gradient times q) is given by:
[eV/m]
En+1
vn+1
Gap n
Gap n+1
whereis the average particle velocity between the gap n and n+1

## Slide 18: Alvarez structures Proton and ions acceleration
Alvarez's structure can be described as a special DTL in which the electrodes are part of a resonant macrostructure.
The DTL operates in 0 mode for protons and ions in the range =0.05-0.5 (fRF=50-400 MHz, RF=6-0.7 m) 1-100 MeV;
In order to be synchronous with the accelerating field at each gap the length of the n-th drift tube Ln has to be:
The beam is inside the “drift tubes” when the electric field is decelerating. The electric field is concentrated between gaps;
The drift tubes are suspended by stems;
Quadrupoles (for transverse focusing) can fit inside the drift tubes.
Ez
z

## Slide 19: Alvarez structures Examples
CERN Linac2 (1978 - 2018):
200 MHz, 7 m x 3 tanks, 1 m diameter, final energy 50 MeV
CERN Linac4 (since 2013), in 2020 became the source of proton beams for the (LHC): 352 MHz frequency, Tank diameter 520 mm, 3 resonators (tanks), Length ~13 m Energy: 3 MeV to 40 MeV, =0.08 to 0.283  cell length from 68mm to 241mm. Final energy is 160 MeV, using accelerating structures of different types (Cell-Coupled DTL and Side Coupled Linac)

## Slide 20: High frequency accelerating fields
The condition Ln<<RF (necessary to model the tube as an equipotential region) requires <<1. Thus, the Wideröe technique can not be applied to relativistic particles.
Moreover, when particles get high velocities the drift spaces get longer and one loses efficiency. To obtain a larger average accelerating gradient (Eacc [V/m]), smaller RF (higher frequencies) must be considered.
High frequency and relative high-power sources became available after world war II pushed by military technology needs (such as radar). Moreover, the concept of equipotential DT can not be applied at small RF and the power lost by radiation is proportional to the RF frequency.
Consequently, we must consider accelerating structures different from drift tubes.
The solution consists of enclosing the system in a cavity, whose resonant frequency matches the RF generator frequency.
Each cavity can be independently powered from the RF generator
waveguide
Ez
Ez

## Slide 21: Accelerating structures: standing wave
High frequency RF accelerating fields are confined in cavities.
The cavities are metallic closed volumes were the e.m fields has a particular spatial configuration (resonant modes) whose components, including the accelerating field Ez, oscillate at some specific frequencies fRF (resonant frequency) characteristic of the mode.
The modes are excited by RF generators that are coupled to the cavities through waveguides, coaxial cables, etc…
The resonant modes are called Standing Wave (SW) modes (spatial fixed configuration, oscillating in time).
The spatial and temporal field profiles in a cavity must be computed (analytically or numerically) by solving the Maxwell equations with the proper boundary conditions.
B
E

## Slide 22: SW structures notes
Quality Factor
The shunt impedance is the parameter that qualifies the efficiency of an accelerating mode. The highest is its value, the larger is the obtainable accelerating voltage for a given power.
The quality factor Q is defined as the total energy stored in the cavity divided by the power dissipated on the walls
R over Q
The R/Q is a pure geometric qualification factor. It does not depend on the walls conductivity. R/Q of a single cell is of the order of 100.
Equivalent circuit
The reachable for a given power is proportional to but, on the other hand, the filling time is
Example:
  Q10000
fRF=1 GHz
F=3.1 s
Shunt Impedance
  NC cavity Q104
  SC cavity Q1010

## Slide 23: Accelerating structures: travelling wave
To accelerate charged particles, the electromagnetic field must have an electric field along the direction of propagation of the particle.
The field has to be synchronous with the particle velocity.
In the standing wave (SW) structures in which the field has basically a given profile and oscillate in time (as example in DTL or resonant cavities):
There is another possibility to accelerate particles: using a travelling wave (TW) structure in which the RF wave is co-propagating with the beam with a phase velocity equal to the beam velocity:
These structures can be view as iris-loaded waveguides. Due to the presence of the irises the phase velocity of the propagating wave (that for an empty waveguide is always greater than c) is kept slightly below the speed of light, allowing the synchronism with the particles that pass through the structure and experience an accelerating phase.
Typically, these structures are used for electrons because in this case the phase velocity can be constant all over the structure and equal to c. In fact, it is difficult to modulate the phase velocity itself very quickly for a low  particle that changes its velocity during acceleration.
Ez
z
Power flow
D

## Slide 24: TW structures notes
In a TW structure, the RF power enters into the cavity through an input coupler, flows (travels) through the cavity in the same direction as the beam and an output coupler at the end of the structure is connected to a matched power load.
If there is no beam, the input power, reduced by the cavity losses, goes to the power load where it is dissipated.
In the presence of a large beam current, however, a fraction of the TW power is transferred to the beam.
In a purely periodic structure, made by a sequence of identical cells (also called “constant impedance structure”),  does not depend on z and both the RF power flux and the intensity of the accelerating field decay exponentially along the structure:
The filling time is the time necessary to propagate the RF wave-front from the input to the end of the section of length L is:
L
Differently from SW cavities after one filling time the cavity is completely full of energy

## Slide 25: Part 3 Longitudinal Dynamics

## Slide 26: Synchronous particle
TRF
Vacc
t
s*
s
Vacc_s
Let us consider a SW linac structure made by accelerating gaps (like in DTL) or cavities.
In each gap we have an accelerating field oscillating in time and an integrated accelerating voltage (Vacc) still oscillating in time than can be expressed as:
Let’s assume that the “perfect” synchronism condition is fulfilled for a phase s (called synchronous phase). This means that a particle (called synchronous particle) entering in a gap with a phase s (s=RFts) with respect to the RF voltage receive an energy gain (and a consequent change in velocity) that allow entering in the subsequent gap with the same phase s and so on.
for this particle the energy gain in each gap is:
both s and s* are synchronous phases

## Slide 27: Phase Conventions
For circular accelerators, the origin of time is taken at the zero crossing of the RF voltage with positive slope
For linear accelerators, the origin of time is taken at the maximum of the positive crest of the RF voltage
t
s
t
s
circular accelerators
linear accelerators

## Slide 28: Principle of phase stability
Vacc
t
s*
s
Let us consider now the first synchronous phase s (on the positive slope of the RF voltage). If we consider another particle “near” to the synchronous one that arrives later in the gap (t1>ts, 1>s), it will see a higher voltage, it will gain a higher energy and a higher velocity with respect to the synchronous one. Therefore, its time of flight to next gap will be shorter, partially compensating its initial delay.
Similarly, if we consider another particle “near” to the synchronous one that arrives earlier in the gap (t1<ts, 1<s), it will see a smaller voltage, it will gain a smaller energy and a smaller velocity with respect to the synchronous one. Consequently, its time of flight to next gap will be longer, compensating the initial advantage.
On the contrary, if we consider now the synchronous particle at phase s* and another particle “near” to the synchronous one that arrives later or before in the gap, it will receive an energy gain that will increase further its distance from the synchronous one
The choice of the synchronous phase in the positive slope of the RF voltage provides longitudinal focusing of the beam: phase stability principle.
The synchronous phase on the negative slope of the RF voltage is, on the contrary, unstable
Relying on particle velocity variations, longitudinal focusing does not work for fully relativistic beams (electrons). In this case acceleration “on crest” is more convenient.
1
2

## Slide 29: Energy/phase equations (1/2)
In order to study the longitudinal dynamics in a LINAC, the following variables are used, which describe the generic particle phase (time of arrival) and energy with respect to the synchronous particle:
The energy gain per cell (one gap + tube in case of a DTL) of a synchronous and a generic particle are:
Subtracting the two equations, we obtain:
Dividing by the accelerating cell length L and assuming (average accelerating field):
Using the approximation :
Energy of the synchronous particle at a certain position along the linac
Energy of a generic particle at a certain position along the linac
Arrival time (phase) of the synchronous particle at a certain gap (or cavity)
Arrival time (phase) of a generic particle at a certain gap (or cavity)
z

## Slide 30: Energy/phase equations (2/2)
On the other hand, we have that the phase variation per cell of a generic particle and of a synchronous particle are: where symbols represent the time of flight between two accelerating cells
Subtracting the two equations, we obtain:
Then dividing by the cell length and using the approximation : where v, vs are the average particles velocities.
Eventually, we derived this system of coupled (non linear) differential equations describe the motion of a non synchronous particles in the longitudinal plane with respect to the synchronous one.
MAT:

## Slide 31: Small amplitude energy-phase oscillations Equation derivation
Deriving both terms of the second equation with respect to z:
And, substituing defined in the first equation: that is a general non linear differential equation that gives the phase evolution.
Assuming small oscillations around the synchronous particle , deriving both terms with respect to z and assuming an adiabatic acceleration <<1:

## Slide 32: Small amplitude energy-phase oscillations Longitudinal phase space
The condition to have stable longitudinal oscillations and acceleration at the same time is:
If we accelerate on the rising part of the positive RF wave, we have a longitudinal force keeping the beam bunched around the synchronous phase
The trajectory of a generic particle in the longitudinal phase space is an ellipse and the angular frequency is simply that scale with , thus, for ultra relativistic particles, shrinks to 0 (the beam is frozen)
the bunch occupies an area in the longitudinal phase space called longitudinal emittance and the projections of the bunch in the energy and phase planes give the energy spread and the bunch length.
t
s

More energy
Less energy
Arrive later
Arrive earlier
Synchronous particle
32
w

N. of particles
Bunch length
Energy spread
0
Longitudinal emittance is the phase space area including all the particles

w
N. of particles

## Slide 33: Real beam example SPARC_LAB beam ready for a SASE experiment
Beam parameters | 
Beam energy | 150 MeV
Relative energy spread (rms) | 9 x 10-4
Slice energy spread (rms) | 2 x 10-4
Bunch length (rms) | 2.6 ps
Electron charge | 400 pC
Beam current | 53 A
Repetition rate | 10 Hz
Vertical emittance | 2.9 mm mrad
Horizontal emittance | 2.5 mm mrad
(a) Phase space of the e-beam measured with time/energy dispersion induced by rf-deflector (in time) and a spectrometer dipole (in energy), (b) beam slice energy spread (A) and energy (B) and (c) beam current as a function of time along the bunch.

## Slide 34: Part 4 Linac technology

## Slide 35
Typical linac layout
The overall LINAC has to be designed to obtain the desired beam parameters in term of:
-output energy/energy spread
-beam current (charge)
-long. and transverse beam dimensions/divergence (emittance)
Having, in general, constraints in term of:
-space
-cost
-power consumption
-available power sources
…
Waveguide network

## Slide 36: Linac example SPARC_LAB photoinjector @LNF
In operation since 2006, originally as injector for FEL experient, it has undergone several upgrades
In its last configuration the photoinjector is made by:
  a 1.6 cell S- band RF gun used as 5.6 MeV electron source
  Two S-band TW structures at 2856 MHz used ass capturing section and booster
  C-band at 5712 MHz used as capturing section and energy booster
The R&D program has been carried out performing many experiments, such as: (i) conventional SASE and seeded FEL; (ii) Thomson back-scattering; (iii) THz generation; (iv) plasma beam focusing and acceleration (PWFA) with FEL generation; (v) laser interaction with matter.

## Slide 37: Thank you for your attention