## Slide 1
Angelo Biagioni
Technology of Plasma sources
On behalf of the Sparc_lab collaboration
National Institute for Nuclear Physics, Italy
EuPRAXIA_DN School on Plasma accelerators
Orto Botanico , Rome, Italiy | April 22 – 26, 2024

## Slide 2
Angelo.Biagioni@lnf.infn.it | EuPRAXIA_DN School on Plasma accelerators | Page 2/40
Plasma sources assume a large variety of shapes…
…Gas-filled capillary-discharge

## Slide 3
Angelo.Biagioni@lnf.infn.it | EuPRAXIA_DN School on Plasma accelerators | Page 3/40
Plasma sources assume a large variety of shapes…
…Gas cell
…Rubidium vapor oven
…Gas jet

## Slide 4
Technology of plasma sources
  Introduction and motivations
  Basic concepts
  Plasma source properties and implementation
    Gas cell
    Heat-pipe ovens
    Gas jet
    Gas-filled capillary-discharge
  Plasma diagnostics
    Spectroscopic techniques
    Interferometric tecniques
    Plasma temperature
  High repetition rate plasma sources for EuPRAXIA project
Angelo.Biagioni@lnf.infn.it | EuPRAXIA_DN School on Plasma accelerators | Page 4/40
Outline

## Slide 5
Angelo.Biagioni@lnf.infn.it | EuPRAXIA_DN School on Plasma accelerators | Page 5/40
n0 = 1016 cm-3 λp = 300 µm
Wave-breaking field
~ 10 GV/m
λp
Wakefield
Gas injection
Plasma source
Plasma formation process
RF structures 20-100 MV/m
Plasma structures 1-100 GV/m
LWFA Laser-driven wakefield acceleration
Drive beam is a laser pulse
PWFA Particle-driven wakefield acceleration
Drive beam is electron or proton beam
Plasma source design for:
Plasma formation process
Density profiles – lifetime – size – ramps – stability - RepRate
Acceleration – Focusing – deflection
Motivations

## Slide 6
Angelo.Biagioni@lnf.infn.it | EuPRAXIA_DN School on Plasma accelerators | Page 6/40
Basic concepts
Plasma generation mechanisms
Collisional ionization
  Electrical discharges
  Laser ionization
      Single-photon ionization
      Multi-photon ionization
      Tunneling ionization/field ionization (particle beams)
Laser beam
Laser beam
Particle beam
Plasma generation is fundamentally concerned with the ionization of a background medium, usually a gas, to produce electrons and ions in a controlled way
Electrical discharge

## Slide 7
Angelo.Biagioni@lnf.infn.it | EuPRAXIA_DN School on Plasma accelerators | Page 7/40
Basic concepts_ Electrical discharges
The most important collisional ionization mechanism is electron-impact ionization (Te/Tg)
  Dark discharge (Te>Tg)
    A-C region, background electrons (I ≈ 1 pA ÷ 1 nA)
    C-E region, the Townsend discharge (avalanche ionization)
  Glow discharge (Te>Tg)
    the current is still not dependent on the applied voltage
    It is determined by the secondary emission (γ) of electrons in the vicinity of the cathode (self-sustained discharge)
    the electron flux at the cathode is determined by the secondary emission, that is proportional to the ion flux present at the cathode
The first Townsend coefficient
α → , λe →
α→ Saha equaiton
p gas pressure
λe mean free path
E electric field
α
The second Townsend coefficient
Γe(0)
Xiao, Dengming, Gas Discharge and Gas Insulation (2016) Volume 6
Fundamental Theory of Townsend Discharge, pp. 47–88. doi:10.1007/978-3-662-48041-0_3

## Slide 8
Angelo.Biagioni@lnf.infn.it | EuPRAXIA_DN School on Plasma accelerators | Page 8/40
Basic concepts_ Electrical discharges
V
p pressure
d gas length
α
Paschen curve
During the dielectric breakdown, the electrons must be able to close the circuit Anode-Cathode, that is, they must reach the anode
Charge balance equation for both electrons and ions
There is still no a uniform plasma along the pipe

## Slide 9
Angelo.Biagioni@lnf.infn.it | EuPRAXIA_DN School on Plasma accelerators | Page 9/40
Basic concepts_Electrical discharges
  Arc discharge (Te>Tg – Te=Tg)
    triggered by the massive emission of electrons from the cathode due to intense heating of the cathode surface by the Joule effect obtained from the high current (thermoionic emission)
    H-J region, non-thermal regime Te>Tg, current 1-50 A
    J-K region, Te=Tg (LTE condition), currents can reach up to thousands Amps
H2
10 cm/1 mm
V = 10 kV
I = 500 A
p = 50 mbar
Gas-filled discharge capillary

## Slide 10
Angelo.Biagioni@lnf.infn.it | EuPRAXIA_DN School on Plasma accelerators | Page 10/40
Basic concepts_Laser ionization
P. Gibbon et Al, Short Pulse Laser Interactions with Matter: An Introduction, Imperial College Press, 2005
Single-photon ionization is possible when the photon energy is larger than the binding potential of the atom, hν > εion (800nm photons have hν = 1.55 eV)
Li | 5.39 eV
H | 13.59 eV
N | 14.53 eV
He | 24.59 eV
Multi-photon ionization, when the laser intensity is high enough then there can be a large enough number of photons in the atomic volume to give a high probability of multiple (N) photons simultaneously ionizing the atom, Nhν > εion
It is important to note that in multi-photon ionization, the energy of a single photon can amount to only a fraction of the minimum energy needed for removal of an electron
Photons

## Slide 11
Angelo.Biagioni@lnf.infn.it | EuPRAXIA_DN School on Plasma accelerators | Page 11/40
Basic concepts_Laser ionization
L. V. Keldysh, Ionization in the field of a strong electromagnetic wave, Sov. Phys. JETP 20, 1307–1314 (1965)
L. Gallmann et Al, Photoemission and photoionization time delays and rates, Structural Dynamics 4, 061502 (2017) https://doi.org/10.1063/1.4997175
Tunnel ionization, If we consider the intense laser light an electromagnetic wave rather than a stream of photons, one sees that in the dipole approximation, the electric field in a strong laser beam can bend the Coulomb potential such that an electron can tunnel through the created barrier out into the vacuum
IP
Potential energy
Radius
Columbian potential ~ 1/r
Bound electron state
Keldish parameter
Electromagnetic wave
ADK (Ammosov, Delone and Krainov) ionization rate
γ
MPI
Field ionization

## Slide 12
Angelo.Biagioni@lnf.infn.it | EuPRAXIA_DN School on Plasma accelerators | Page 12/40
Basic concepts_Laser ionization
Barrier suppression
ionization
External potential –eEr
Columbian potential ~ 1/r
V(r) - eEr
Atom | Ip (eV) | Ith (W/cm2)
H | 13.59 | 1.4x1014
He | 24.59 | 8.8x1015
Tunneling ionization
Threshold electric field, above which barrier suppression ionization occurs
*

## Slide 13
Angelo.Biagioni@lnf.infn.it | EuPRAXIA_DN School on Plasma accelerators | Page 13/40
Basic concepts_Field ionization by particle beams
Plasma production via field ionization occurs when an incoming particle beam is sufficiently dense that the electric field associated with the beam ionizes a neutral vapor or gas
Electron beams Coulomb fields can exceed the threshold electric field for barrier suppression ionization from the previous Eq* (ETh):
                Bunch length
                Charge
                Beam focusing (waist position )
nb
rb
Eth(H2) = 35 GV/m
Emax = 45 GV/m
nb = 1018 cm-3
rb = 5 um
, R=r/
M.V. Ammosov, N. B. Delone, and V. P. Krainov, Tunnel ionization of complex atoms and of atomic ions in an alternating electromagnetic field , Sov. Phys. JETP 64, 1191 (1986)
M. J. Hogan et Al, Multi-GeV Energy Gain in a Plasma-Wakefield Accelerator, (2005) PHYSICAL REVIEW LETTERS PRL 95, 054802DOI: 10.1103/PhysRevLett.95.054802
C. L. O’Connell et Al, Plasma production via field ionization, (2006) PHYSICAL REVIEW SPECIAL TOPICS - ACCELERATORS AND BEAMS 9, 101301 DOI: 10.1103/PhysRevSTAB.9.101301
nb
rb
Before
After

## Slide 14
Angelo.Biagioni@lnf.infn.it | EuPRAXIA_DN School on Plasma accelerators | Page 14/40
Plasma source properties and implementation
Gas jets
Heat-pipe ovens
Gas cells
Gas-filled discharge capillary

## Slide 15
Angelo.Biagioni@lnf.infn.it | EuPRAXIA_DN School on Plasma accelerators | Page 15/40
Plasma source properties and implementation_Gas jets
B. R. Lee et Al, Spatiotemporal characteristics of high-density gas jet and absolute determination of size and density of gas clusters. Sci Rep 10, 12973 (2020). https://doi.org/10.1038/s41598-020-69824-z
Ocean Zhou et Al, Effect of nozzle curvature on supersonic gas jets
used in laser–plasma acceleration, Phys. Plasmas 28, 093107 (2021); doi: 10.1063/5.0058963
The density ratio depends only on the Mach number and the adiabatic index of the target gas
At the nozzle exit, a lineout of the gas density will have a flattop profile with a diameter equal to the nozzle exit diameter and the peak density defined by first equation
Edges of the profile will gradually expand at an angle approximately equal to 1/M
+ 2
L
M = v/cs

## Slide 16
Angelo.Biagioni@lnf.infn.it | EuPRAXIA_DN School on Plasma accelerators | Page 16/40
Plasma source properties and implementation_Gas jets
M. Hansen et Al, Supersonic gas-jet characterization with interferometry and Thomson scattering on the OMEGA Laser Systema, Proceedings of the 22nd Topical Conference on High-Temperature Plasma Diagnostics (HTPD 2018) in San Diego, California, USA
B. R. Lee et Al, Spatiotemporal characteristics of high-density gas jet and absolute determination of size and density of gas clusters. Sci Rep 10, 12973 (2020). https://doi.org/10.1038/s41598-020-69824-z
Ocean Zhou et Al, Effect of nozzle curvature on supersonic gas jets
used in laser–plasma acceleration, Phys. Plasmas 28, 093107 (2021); doi: 10.1063/5.0058963
Argon
80 bar
Valve opening 70 ms
Gas jets properties
Supersonic nozzles provide a near-flat-top density profile for laser wakefield acceleration experiments
Plasma density can be controlled by means of backing pressure P depending on the nozzle geometry and desired density
      P in the range 10 - 100 bar
      ne typically in the range 1017 - 1020 cm-3
Length typically a few mm (nozzle arrays, but higher gas flow rates)
Larger nozzle diameters give lower densities for same P
High gas flow rates, operation necessarily in pulsed mode
No plasma confinement components are required, so there is no wear and tear of source parts due to high plasma temperatures
Nozzle geometry, Ar gas
Laser pulse
Laser pulse

## Slide 17
Kurz, T. et al. Nat Commun 12, 2895 (2021).
Couperus Cabada, J.P. et al. Phys. Rev. Research 3 L042005 (2021)
Plasma source properties and implementation_Gas jets
Staged LWFA-driven PWFA (LPWFA)
A density downramp injection (DDI) scheme induced by a hydrodynamic shock-front in a PWFA improve properties of the plasma source:
  Second shock front is the source of witness injection
  we achieve energy tuning capability by adjusting the position of injection and thus changing the effective acceleration length of the injected witness.
Angelo.Biagioni@lnf.infn.it | EuPRAXIA_DN School on Plasma accelerators | Page 17/40
A high-intensity laser pulse drives an LWFA in the first stage, generating a high peak-current (>10 kA) electron beam which propagates into the second stage, acting as the PWFA driver.
In the PWFA stage, a witness beam (yellow) is accelerated. the witness beam is mostly composed of trailing background electrons that went through the foil and get trapped in the beam-driven plasma wake, where they experience peak accelerating fields surpassing 100 GV m−1
After expansion in the intermediate vacuum, the drive beam is effectively recaptured as it enters the PWFA stage.

## Slide 18
Angelo.Biagioni@lnf.infn.it | EuPRAXIA_DN School on Plasma accelerators | Page 18/40
Muggli, P. et Al, Photo-Ionized Lithium Source for Plasma Accelerator Applications, IEEE Trans. Plasma Sci. 27 (1999).
Vafaei-Najafabadia, N. et Al, Meter Scale Plasma Source For Plasma Wakefield Experiments, AIP Conference Proceedings 1507, 650 (2012).
Plasma source properties and implementation_Heat-pipe ovens
Heat-pipe oven properties
Alkali metal (Li, Rb, Cs,…) heated to form vapor
The photo-ionized plasma is expected to have a very uniform transverse profile and a small longitudinal gradient (e.g. in AWAKE)
The maximum plasma density was 1014 - 1015 cm-3
Sharp boundaries and Plasma/Li density set by PHe
Li column length set by heating power (700-900°C) until the room temperature imposed by the jackets limits the length of this column
Long targets (m-scale)
Ionizable by drive beam or a laser pulse (low IP)
Beam-driven plasma accelerators

## Slide 19
Plasma source properties and implementation_Heat-pipe ovens
Adli, E. et Al, Acceleration of electrons in the plasma wakefield of a proton bunch, Nature 561, 363–367 (2018).
Gschwendtner, E. et Al, AWAKE, The Advanced Proton Driven Plasma Wakefield Acceleration Experiment at CERN. NIMA, 829 (2016).
Oz, E. et Al, AWAKE, An accurate Rb density measurement method for a plasma wakefield accelerator experiment using a novel Rb reservoir, arXiv:1511.08763 (2015).
Long, thin proton bunches (400GeV) undergo a process called self-modulation, a particle-plasma interaction that splits the bunch longitudinally into a series of high-density micro-bunches, which then act resonantly to create large wakefields.
Run2: 2021-2024 – two long plasma sections (electrical dscharge)
650pC
20MeV
< 1pC
2 GeV
Density gradient 2%
10 m long, 40 mm diameter oil-heated pipe
Plasma is laser ionized (low IP for Rb)
Alkali vapor expels buffer from heated region by collisions, steady-state when Palkali = Pbuff
Increasing heater power increases evaporation rate (but not Talkali) and so the Palkali
Pressure fixed by Pbuff, hence length of alkali column L can be varied by changing the heating power delivered to the oven
The density uniformity is achieved by imposing a uniform temperature (200 °C) (within 0.2 %) along the source. The oil temperature stabilized to ±0.05 °C. Appropriate density gradients increase the energy gain
A threshold ionization process for the first Rb electrons is used to turn the uniform neutral density into a uniform plasma density.
to ensure an efficient electron trapping one needs short density ramps (< 10 cm): a continuous flow system through orifices has been chosen to shorten the ramps. The Rb sources placed as close as possible to the orifices to minimize the density ramps
Laser ionization:
  Long focal length lens or “axicon” and large spot size
  Tunneling/BSI as threshold process yields flat-top profile
  - SPI/MPI scales with power of n-photons required and varies with laser intensity profile
10 m
Angelo.Biagioni@lnf.infn.it | EuPRAXIA_DN School on Plasma accelerators | Page 19/40

## Slide 20
Plasma source properties and implementation_Gas cells
Angelo.Biagioni@lnf.infn.it | EuPRAXIA_DN School on Plasma accelerators | Page 20/40
Laser pulse
Gas injection
Gas cell pressure P
Plasma/Gas ramps
Gas cells properties
Region of uniform neutral gas contained by differential pumping at two input/output extremities
If flow resistance of outlets larger than inlets, uniform density distribution in central volume
Gas flow small enough to operate in steady state regime with continuous flow (typically <1 bar)
Variable length gas cell designs by using mechanically moving parts
Plume of gas from front and back of cell, plasma ramps to be controlled
Density easily adjusted by controlling gas flow or geometry in the range: 1016 - 1019 cm-3
Erosion of inlet/outlet due to the high-power laser pulses
Small dimensions, 100-300 μm in diameter and few mm in length
Variable length gas cell
Very good behaviour to operate to high repetition rate (possible 1kHz)
HOFI plasma channels
Very small dimenisons

## Slide 21
Plasma source properties and implementation_Gas cells
Shalloo, R.J. et Al, Phys. Rev. Accel. Beams 22 (2019).
Alejo, A. et Al, Phys. Rev. Accel. Beams 25 (2022)
C.G. Durfee & H.M. Milchberg, Phys. Rev. Lett. 71, 2409 (1993)
The plasma channel is free-standing, no damages of the structure, so high repetition rate > 1kHz is possible
Latt ~ 1 m (axicon lenses)
since rapid collisional heating (depends on the gas density) requires high plasma densities, it has proved difficult to generate channels with low on-axis densities (ne > 1018 cm-3) and L > 1 cm
Ar/N2O
Hydrodynamic optical-field-ionized plasma channels (HOFI)
Angelo.Biagioni@lnf.infn.it | EuPRAXIA_DN School on Plasma accelerators | Page 21/40
The development of methods for guiding intense laser pulses through plasma is crucial for LWFA (hollow transverse profiles)
A column of plasma is generated by optical field ionization; this expands hydrodynamically into the surrounding gas, driving a radial shockwave and forming a plasma channel along the axis of the plasma column.
Conditioned Hydrodynamic optical-field-ionized plasma channels (CHOFI)
Depth of the channel increased by a factor of 10 to Δne = 1.3×1018 cm−3 (ne < 1017 cm-3) and Latt in the m-scale

## Slide 22
Plasma source properties and implementation_Gas-filled discharge capillaries
Gas injection
Plasma/Gas ramps
Plasma channel
HV
Electrodes
Discharge Plasma sources properties
Region of uniform neutral gas contained by differential pumping at two input/output extremities and realized by a thin capillary
Modulation of longitudinal gas distribution by special geometric shapes
Small gas flow to operate in steady state regime with continuous flow (P < 1 bar)
There is no movable parts
Small dimension of the HV source to produce plasma
Plume of gas from front and back of cell, plasma ramps to be controlled
Density easily adjusted by controlling gas flow, geometry or voltage in the range: 1015 - 1019 cm-3
Erosion of the plasma channel due to the electrical discharges to form plasma
Angelo.Biagioni@lnf.infn.it | EuPRAXIA_DN School on Plasma accelerators | Page 23/40
Gas inlets
Electrode
HV pulse
Plasma channel
Density profile
x1017
Time profile
Spatial profile
Acceleration

## Slide 23
Plasma source properties and implementation_Gas-filled discharge capillaries
Angelo.Biagioni@lnf.infn.it | EuPRAXIA_DN School on Plasma accelerators | Page 24/40
neutral gas distribution
0-5 ms
EuPRAXIA target
  40cm x 2mm
  1016 cm-3
  P = 20-30 mbar
  ~ 10 kV
Design of the gas-filled capillary-discharge
Geometry design
  Channel diameter to set plasma density
  Inlets for neutral gas distribution
  Materials (lifetime)
  HV-source design
    Voltage/current settings
    Gas injection
      Gas
      Continuous flow/pulsed flow system (Rep rate)
      Pressure
0 – 5 ms
4.5 ms
2.5E17
6E16
2E16
1 ms

## Slide 24
Plasma source properties and implementation_Gas-filled discharge capillaries
Active PlasmA alens (APL)
Angelo.Biagioni@lnf.infn.it | EuPRAXIA_DN School on Plasma accelerators | Page 25/40
Focusing
Time profile
J. van Tilborg et Al, Active Plasma Lensing for Relativistic Laser-Plasma-Accelerated Electron Beams, PRL 115, 184802 (2015)
R capillary radius
I0 peak current

## Slide 25
Plasma source properties and implementation_Gas-filled discharge capillaries
Angelo.Biagioni@lnf.infn.it | EuPRAXIA_DN School on Plasma accelerators | Page 26/40
Lens ON Acc ON Lens ON
3 us
Acc-200A
Lens-500A
Integrated capillary
Very long capillary
Curved capillary for APD
Design of m-scale capillaries for EuPRAXIA project by using segmented capillaries: design of HV-voltage circuits and discharge synchronization
Design of new geometries for curved channels: HV-circuits to allow high current pulses
Studies on cross-talk effects:
Design of electrodes and HV-circuits to reduce the interaction among discharges through plsam ramps
Segmented capillary
Pompili, Riccardo, et Al, Guiding of charged particle beams in curved capillary-discharge waveguides, AIP Advances 8.1 (2018)

## Slide 26
Angelo.Biagioni@lnf.infn.it | EuPRAXIA_DN School on Plasma accelerators | Page 27/40
Spectroscopic techniques
Plasma temperature
Interferometric tecniques
Plasma Diagnostics

## Slide 27
Angelo.Biagioni@lnf.infn.it | EuPRAXIA_DN School on Plasma accelerators | Page 28/40
Plasma diagnostics_Spectroscopy
HOW IS THE CAPILLARY CHARACTERIZED?DENING TECHNIQUE
The Stark effect is the shifting and splitting of spectral lines of atoms and molecules due to the presence of an external electric field, it is responsible for the pressure broadening (Stark broadening) of spectral lines by charged particles in plasmas
Hydrogen-like and helium-like lines are the most sensitive to Stark broadening
434nm
486nm
656nm
wavelength
Stark broadening effect
Δλ
Δλ
plasma light collection
Imaging of the plasma source
Ha
Hb

## Slide 28
Angelo.Biagioni@lnf.infn.it | EuPRAXIA_DN School on Plasma accelerators | Page 29/40
Plasma diagnostics_Spectroscopy
Position (mm)
λ (nm)
Electrode
shadow
Plasma
channel
Plasma plume
Δλ
Δ
Lorentzian fit
Lorentzian fit gives spectral line width Δλ (in Å in the formula)
  Doppler (Gaussian fit) → Temperature
  Pressure Broadening (Lorentzian fit) → Density
α value is a tabulated parameter
The spectrometer allows the balmer lines to be selected from the collected plasma light
Fast gate intensified CCD camera to acquire the plasma light
Vacuum
chamber
Electromechanical valve
Plasma light
Mechanical
regulator
H2 source
Spectrometer
Hβ
spectral line
ICCD camera
Capillary

## Slide 29
Angelo.Biagioni@lnf.infn.it | EuPRAXIA_DN School on Plasma accelerators | Page 30/40
Plasma diagnostics_Spectroscopy
Position (mm)
λ (nm)
Plasma properties characterization as a function of time and spatial coordinate
shortest gating time of the ICCD camera over which S/N is sufficient (few ns)
CCD camera resolution (10 – 30 μm)
Time

## Slide 30
Angelo.Biagioni@lnf.infn.it | EuPRAXIA_DN School on Plasma accelerators | Page 31/40
Plasma diagnostics_Temperature
486nm
I’
I
S. S. Harilal, Electron density and temperature measurements in a laser produced
carbon plasma (1997), J. Appl. Phys. 82 (5)
Hβ spectral line
The parameters f (oscillator strength), g (statistical weights), λ (wavelenght), a0 (Bohr radius), E (excitation energy of atom) EH (ionization energy of the Hydrogen atom ), E∞, ΔE∞ (correction to the ionization energy E∞ of the lower ionization stage due to plasma interactions) are all tabulated on the NIST database
Plasma light
Spectrometer
Capillary
spectral lines
ICCD camera

## Slide 31
Plasma diagnostics_Laser interferometry
The integrated path length or phase of a laser pulse traversing a plasma depends on the index of refraction of the plasma
In the Mach-Zehnder interferometer one laser arm has traversed a plasma and one has not
The interference created by combining two different laser arms
Δφ observed is a line-of-sight integral and therefore the geometry of the target can affect the measure (for cylindrical symmetry Abel inversion)
ω0 needs to see significant phase shift, not too far away from critical density or long plasma (i.e., critical 1018 cm-3 in transverse measure with 1 um lasers)
ω0 Laser frequency
ωp Plasma frequency
nc critical density
L length of plasma traversed
Δφ total integrated phase shift
Mach-Zehnder interferometer
Milan Kalal and Keith Nugent, Abel inversion using fast fourier transforms, Applied optics,
27(10):1956–1959, 1988.
Angelo.Biagioni@lnf.infn.it | EuPRAXIA_DN School on Plasma accelerators | Page 32/40

## Slide 32
Plasma diagnostics_Laser interferometry
400 nm pulses are intrinsically coupled and locked in timing, phase, pointing, and stability, since they experience the same optical path.
Single laser pulse frequency doubled → two co-propagating harmonics at 800 and 400 nm (red and blue)
Δφ (Δt) due to different group and phase velocities in plasma
On exiting the plasma, remaining 800 nm pulse is also doubled (all blue)
Spectral interference pattern reveals information about temporal delay, phase shift, and the plasma density
J. Van Tilborg et al, Optics Letters 43, 12 (2018)
Angelo.Biagioni@lnf.infn.it | EuPRAXIA_DN School on Plasma accelerators | Page 33/40
Two-color interferometer

## Slide 33
Angelo.Biagioni@lnf.infn.it | EuPRAXIA_DN School on Plasma accelerators | Page 34/40
High repetition rate plasma sources for EuPRAXIA project

## Slide 34
High repetition rate sources for EuPRAXIA project
Spectroscopic measure of the plasma temperature
EuPRAXIA accelerator will operate at 100 Hz in m-scale plasma sources
  Electrical discharge ionization process
    Solid-state high repetition-rate discharge system
    Strong materials capable of dissipating thermal energy
    Vacuum systems suitable for large quantity of gas in continuous flow regime (turbo and primary pumps cooling system)
    Electrical discharges in very log gas columns
      Laser ionization process
          High-power laser operating at high repetition rate (>100Hz)
          Vacuum systems suitable for large quantity of gas in continuous flow regime (turbo and primary pumps cooling systems)
          Laser guiding in long plasma sources
Gas injection
Plumes
Plasma channel
HV
Electrodes
Laser pulse
Gas injection
pressure P
Plumes
Angelo.Biagioni@lnf.infn.it | EuPRAXIA_DN School on Plasma accelerators | Page 35/40

## Slide 35
Mitigation of erosion of the capillary walls can be achieved by reducing the heat flux
Current pulse width and amplitude
Gas fill pressure
Capillary radius
PWFA (EuPRAXIA project)
5x1016cm-3 Pgas=20mbar
Ip=300A Rcap=2000um
Lcap=400mm Δt=600ns
T2=300K
r2 =5mm
T1,r1
Cooling system
300K
q
Conductive heat transfer law:
Cylinder geometry
Discharge
Heating
300A, 400Hz
Sapphire
2300K
k=40 [W/mK]
Diamond
3800K
k=1000
40W
P(W)
Plastic
400K
k=0.2
300A
100Hz
Glass
1700K
k=1-3
A. Gonsalves, et al, Demonstration of a high repetition rate capillary discharge waveguide, JAP, 119,10.1063/1.4940121
the energy deposited into the capillary per shot:
E = Rp Ip2 Δt = 100 mJ/shot
Angelo.Biagioni@lnf.infn.it | EuPRAXIA_DN School on Plasma accelerators | Page 36/40
Crucial role of the thermal conductivity
η
Rp = η Lcap/Scap
High repetition rate sources for EuPRAXIA project

## Slide 36
Angelo.Biagioni@lnf.infn.it | EuPRAXIA_DN School on Plasma accelerators | Page 36/40
To operate at high repetition rate with gas-filled capillary-discharge the key point is the thermal dissipation
  Solid-state high repetition-rate discharge system
  Strong materials capable of dissipating thermal energy
  Vacuum systems suitable for continuous flow gas injection (turbo and primary pumps cooling system)
Test of strong materials (sapphire and ceramics)
High repRATE can cause a rapid degradation of unsuitable soft materials
HV- generator
25 kV
20-200 mA
Current pulses from 100 to 2500 A at repetition rate from 1 to 400 Hz
Thermal dissipation of components is crucial
High voltage for plasma formation
High current output for high repRATE
HV-switch
Discharge capillary
2.2 kA
400 A
High repetition rate sources for EuPRAXIA project

## Slide 37
Angelo.Biagioni@lnf.infn.it | EuPRAXIA_DN School on Plasma accelerators | Page 37/40
Lifetime test of ceramic materials so far on 107 shots at 30-50 Hz repetition rate (7 days, 8h per day), thermal conductivity higher than sapphire (70-90 with respect to 40 W/mK)
Working conditions 100Hz – 30 days -24 h per day
So far no degradtion, but anyway slight modifications may be compensated by changing pressure and tension applied
Transverse profile after 107 shots
Transverse profile 0 shots
1.5x1017 cm-3
0.5x1017 cm-3
f=200 Hz
Pb=350 mbar
6.5 hours
a single
channel-forming
pulse (left)
(right) the second of a
pair of channel-forming
pulses separated by 1 ms (1kHz could be possible)
1 mJ
40 fs
5 mm
HOFI plasma channels
30 mm
Discharge capillary
A. Alejo,1, Demonstration of kilohertz operation of Hydrodynamic Optical-Field-Ionized Plasma Channels, Phys. Rev. Accel. Beams 25, 011301 (2022)
High repetition rate sources for EuPRAXIA project

## Slide 38
References
Xiao, Dengming, Gas Discharge and Gas Insulation (2016) Volume 6
Fundamental Theory of Townsend Discharge, pp. 47–88. doi:10.1007/978-3-662-48041-0_3
P. Gibbon et Al, Short Pulse Laser Interactions with Matter: An Introduction, Imperial College Press, 2005
L. Gallmann et Al, Photoemission and photoionization time delays and rates, Structural Dynamics 4, 061502 (2017) https://doi.org/10.1063/1.4997175
L. V. Keldysh, Ionization in the field of a strong electromagnetic wave, Sov. Phys. JETP 20, 1307–1314 (1965)
M.V. Ammosov, N. B. Delone, and V. P. Krainov, Tunnel ionization of complex atoms and of atomic ions in an alternating electromagnetic field , Sov. Phys. JETP 64, 1191 (1986)
M. J. Hogan et Al, Multi-GeV Energy Gain in a Plasma-Wakefield Accelerator, (2005) PHYSICAL REVIEW LETTERS PRL 95, 054802DOI: 10.1103/PhysRevLett.95.054802
C. L. O’Connell et Al, Plasma production via field ionization, (2006) PHYSICAL REVIEW SPECIAL TOPICS - ACCELERATORS AND BEAMS 9, 101301 DOI: 10.1103/PhysRevSTAB.9.101301
M. Hansen et Al, Supersonic gas-jet characterization with interferometry and Thomson scattering on the OMEGA Laser Systema, Proceedings of the 22nd Topical Conference on High-Temperature Plasma Diagnostics (HTPD 2018) in San Diego, California, USA
B. R. Lee et Al, Spatiotemporal characteristics of high-density gas jet and absolute determination of size and density of gas clusters. Sci Rep 10, 12973 (2020). https://doi.org/10.1038/s41598-020-69824-z
Ocean Zhou et Al, Effect of nozzle curvature on supersonic gas jets
used in laser–plasma acceleration, Phys. Plasmas 28, 093107 (2021); doi: 10.1063/5.0058963
Kurz, T. et al. Nat Commun 12, 2895 (2021).
Angelo.Biagioni@lnf.infn.it | EuPRAXIA_DN School on Plasma accelerators | Page 38/40

## Slide 39
References
Couperus Cabada, J.P. et al. Phys. Rev. Research 3 L042005 (2021)
Muggli, P. et Al, Photo-Ionized Lithium Source for Plasma Accelerator Applications, IEEE Trans. Plasma Sci. 27 (1999).
Vafaei-Najafabadia, N. et Al, Meter Scale Plasma Source For Plasma Wakefield Experiments, AIP Conference Proceedings 1507, 650 (2012)
Adli, E. et Al, Acceleration of electrons in the plasma wakefield of a proton bunch, Nature 561, 363–367 (2018).
Gschwendtner, E. et Al, AWAKE, The Advanced Proton Driven Plasma Wakefield Acceleration Experiment at CERN. NIMA, 829 (2016).
Oz, E. et Al, AWAKE, An accurate Rb density measurement method for a plasma wakefield accelerator experiment using a novel Rb reservoir, arXiv:1511.08763 (2015).
Shalloo, R.J. et Al, Phys. Rev. Accel. Beams 22 (2019).
Alejo, A. et Al, Phys. Rev. Accel. Beams 25 (2022)
C.G. Durfee & H.M. Milchberg, Phys. Rev. Lett. 71, 2409 (1993)
Pompili, Riccardo, et Al, Guiding of charged particle beams in curved capillary-discharge waveguides, AIP Advances 8.1 (2018)
J. van Tilborg et Al, Active Plasma Lensing for Relativistic Laser-Plasma-Accelerated Electron Beams, PRL 115, 184802 (2015)
S. S. Harilal, Electron density and temperature measurements in a laser produced
carbon plasma (1997), J. Appl. Phys. 82 (5)
Milan Kalal and Keith Nugent, Abel inversion using fast fourier transforms, Applied optics,
27(10):1956–1959, 1988.
J. Van Tilborg et al, Optics Letters 43, 12 (2018)
A. Gonsalves, et al, Demonstration of a high repetition rate capillary discharge waveguide, JAP, 119,10.1063/1.4940121
A. Alejo,1, Demonstration of kilohertz operation of Hydrodynamic Optical-Field-Ionized Plasma Channels, Phys. Rev. Accel. Beams 25, 011301 (2022)
Angelo.Biagioni@lnf.infn.it | EuPRAXIA_DN School on Plasma accelerators | Page 39/40

## Slide 40
Thank you for your attention