## Slide 1: Free Electron Lasers
An Introduction
Enrica Chiadroni (Sapienza Rome University and INFN-LNF)

## Slide 2: Outline
Motivation
FEL Physics
  Basic properties of the radiation from accelerated relativistic electron beams
  FEL collective instabilities and X-ray FELs
Properties of FEL Radiation
  SASE and Seeded schemes
High brightness beams for FELs

## Slide 3: Static Properties of Matter

## Slide 4: Static Properties of Matter
Required properties
Short wavelength (X-ray)
High energy per pulse
Ultra-short pulse (few femtoseconds)
Coherence
Static picture of a macro-molecule  Need light

## Slide 5: Dynamical Properties of Matter
https://www.youtube.com/watch?v=YTj4Hi1HdJQ

## Slide 6: Dynamical Properties of Matter
Required properties
Ultra-short pulses (few femtoseconds)
Monochromaticity
Defined polarization
Stability and reproducibility
Courtesy of C. Vozzi
Dynamics of a molecular, atomic or electronic process

## Slide 7: Requests for the Light Sources
Short-wavelength (X-rays)
High-energy
Ultra-short (few femtoseconds, or less)
Transverse and longitudinal coherence
Monochromaticity
Tunability in wavelength (10 to 0.1 nm)
Defined polarization
Stability and reproducibility

## Slide 8: Available Sources
In the IR/UV spectral region, the large majority of previously mentioned properties can be obtained by means of conventional table-top lasers
However, in the VUV/X-ray spectral domain only light sources based on “free” accelerated electrons are able to meet all the requirements
  free-electron lasers having laser-like properties in the VUV/X-ray spectral domain can reach a peak brilliance up to 9 orders of magnitude larger than the latest SR sources
9 orders of magnitude
Credits by J. Ulrich et al.,
Ann. Rev. Phys. Chem. 63, 635 (2012)

## Slide 9: Radiation from Free Accelerated Electrons
When does a free charged particle radiate?
  Radiation2D code by T. Shintake, New Real-Time Simulation Technique for Synchrotron and Undulator Radiations, Proc. of LINAC 2002, Korea
Accelerated electrons,
  synchrotron and undulator radiation
Constant velocity larger than c/n in a spatially homogeneous medium
  Cherenkov radiation
Stopping or starting charge
  Transition Radiation
Constant velocity for all times in a spatially non homogeneous periodic medium
  Smith-Purcell radiation
Radiation can be broadband or narrow band: All form of radiation are broadband except when a periodicity is imposed so that a narrow band is selected by interference

## Slide 10: Undulator Magnet
1951: H. Motz proposed the use of a long array of alternating magnetic fields, an undulator magnet, to generate narrow band radiation and have an extended radiation source
J. Appl. Phys. 22, 527–535 (1951)

## Slide 11: Undulator Radiation: Single Electron
is the undulator vector potential normalized to the electron rest energy
x
y
z
For a planar undulator, near the axis
Electron velocity
lu

## Slide 12: Undulator radiation: Resonance Condition
Interference effect
Observer
Using the expression for the velocity and assuming
Resonance condition
Radiation slips ahead by one wavelength per undulator period

## Slide 13: Undulator radiation: Bandwidth
Undulator with Nu periods
/
Each electron emits a wave train with Nu cycles
NUMERICAL EXAMPLE: LCLS case
- cm - => nm
3500 => 3x10-4 and mm (1 fs)

## Slide 14: Origin of FEL Tunability
The expression for the fundamental resonant wavelength on axis
shows that as the beam energy increases, the spontaneous emission moves to shorter wavelengths
NUMERICAL EXAMPLE
and cm:
Mildly relativistic beams: => mm => Microwaves
Relativistic beams: => mm => Infrared
Ultra-relativistic beams: => nm => X-rays
Further tunability is possible through and as

## Slide 15: Synchrotron Radiation Sources
1st generation => Parasitic facilities: bending magnets radiation
  SPEAR at SLAC
2nd generation => Dedicated ring for SR generation
  SRS at Daresbury, Photon Factory at KEK, …
3rd generation => Optimized for SR generation with insertion devices (e.g. undulators and/or wigglers)
  ESRF, APS, Spring-8, …
Needed brightness
for imaging experiments

## Slide 16: Ensemble of Particles
The frequency angular distribution for an ensemble of electrons is
Let us consider first the case when all the velocities are equal but there is a spread in the longitudinal position
The integral is the same for all electrons except for the phase factor

## Slide 17: Emission from Many Particles
Coherent emission
Incoherent emission
(Synchrotron radiation)

## Slide 18: Emission from Many Particles
Coherent emission
Radiated power
linear with electron current
Radiated power
quadratic with electron current
Incoherent emission
(Synchrotron radiation)

## Slide 19: Emission from Many Particles
Coherent emission
(FEL)
Radiated power
linear with electron current
Radiated power
quadratic with electron current
Incoherent emission
(Synchrotron radiation)
Order parameter:
Bunching factor

## Slide 20: Stimulated Undulator Radiation
Relativistic electron beam
Undulator

## Slide 21: Stimulated Undulator Radiation
Relativistic electron beam
Undulator
Electromagnetic field co-propagating with the electron beam and getting amplified
to the detriment of electrons’ kinetic energy

## Slide 22: Stimulated Undulator Radiation
Relativistic electron beam
Undulator
Electromagnetic field co-propagating with the electron beam and getting amplified
to the detriment of electrons’ kinetic energy

## Slide 23: Stimulated Undulator Radiation
Relativistic electron beam
Undulator
J. Madey, Stimulated emission of Bremsstrahlung in a periodic magnetic field, J. Appl. Phys. 42, p. 1906 (1971).
L. Elias, W. Fairbank, J. Madey, and T. Smith, Observation of stimulated emission of radiation by relativistic electrons in a spatially periodic transverse magnetic field, Phys. Rev. Lett. 36, no. 13, p. 717 (1976).
Electromagnetic field co-propagating with the electron beam and getting amplified
to the detriment of electrons’ kinetic energy

## Slide 24: FEL Collective Instability
l
Initial condition:
weak electromagnetic field
electrons randomly distributed in phase
bunching ≈ 0
bunching > 0
Electrons start bunching on a l scale
and the wave is amplified
electromagnetic field
electrons
Resonant interaction  Induced energy modulation  Density modulation  Coherent emission
R. Bonifacio, C. Pellegrini, L.M. Narducci Opt. Comm. 50-6, 373-378 (1984)

## Slide 25: Self-Consistent FEL System
Evolution of electron’s momentum and energy
Evolution of the co-propagating wave (1D): slow wave approximation
slowly varying function which satisfies , , thus Maxwell equations can be written for the slow term
electric and magnetic fields
of the co-propagating wave
vector potential
electrons’ transverse current

## Slide 26: FEL Equations: 1D Theory
Normalizing these equations
the FEL dynamics can be described in a «universal form», where only a single parameter r plays a role
yj phase of the j-th electron in the
combined “ponderomotive”
(radiation + undulator) field
hj energy deviation in units of the FEL parameter r
R. Bonifacio et al. Phys. Rev. Lett. 73, 70 (1994)
Phase
Energy
Field

## Slide 27: FEL r Parameter
All key characteristics of the system are given by universal FEL parameter
with the plasma frequency, thus r is
High density  higher gain!
Smaller growth rate at higher energies
Stronger magnetic field  higher gain
for X-ray…

## Slide 28: Self Amplified Spontaneous Emission (SASE)
P. Emma et al., “First lasing and operation of an ångström-wavelength free-electron laser,”
Nature Photon., vol. 4, pp. 641–647 (2010).
Exponential gain
Evolution of power and longitudinal beam density along the undulator from spontaneous radiation to FEL amplified radiation
Random
Well bunched

## Slide 29: Self Amplified Spontaneous Emission (SASE)
Evolution of average power and spectrum along the undulator from spontaneous radiation to FEL amplified radiation
X-ray emission
Output power: several of GW
Pulse duration: tens of fs
Spectral bandwidth: 10-3
High degree of transverse coherence
Limited longitudinal coherence
Strong shot-to-shot fluctuations
W. Decking et al. Nat. Photon. (2020)
XFEL,Hamburg (Germany)

## Slide 30: SASE Spectral and Temporal Performances
W. Ackermann et al., Nature, 2007
Temporal profile
Spectral profile

## Slide 31: High Brightness Electron Beams
 High brightness:

## Slide 32: Electron Beam Quality Conditions
The exponential growth occurs if
Cold electron beam
Electron-photon phase space matching
1 Diffraction losses from the beam less than the gain

## Slide 33: Effect of finite beam brightness on undulator radiation
Consider the resonance condition
The effect of energy, transverse angle-position spread, generates a spread in radiation wavelength.
The transverse position changes the values of K because the magnetic field increases when moving off the middle plane
/
Energy spread due to angle disribution
Energy spread due to transverse position

## Slide 34: Overcome SASE Limits
Use an external coherent seeding signal, instead of spontaneous emission, to generate electron bunching
   Seeded harmonic generation scheme
ls
ls/n
e- beam
Dispersive section
Radiator
Distance along the undulator
Power (W)
109
Courtesy of L. Giannessi/G. De Ninno

## Slide 35: Overcome SASE Limits
Use an external coherent seeding signal, instead of spontaneous emission, to generate electron bunching
   Seeded harmonic generation scheme
ls
ls/n
e- beam
Dispersive section
Radiator
Power (arb. units)
s t~ 50 fs
z (mm)
Spectrum profile
Pow. Spec. (arb. units)
Wavelength (nm)
Temporal profile
Courtesy of L. Giannessi/G. De Ninno

## Slide 36: Spectral Bandwidth
32.4 nm
Spectral peak jitter: < 1 part in 104
Spectral width: 0.1%
32.4 nm
FERMI FEL operated in SASE and HGHG mode
Courtesy of L. Giannessi/G. De Ninno

## Slide 37: First demonstration at SPARC_LAB

## Slide 38: Compact Short Wavelength FELs
4th generation  XFELs
5th generation light sources
Bridge gap between advanced accelerator concepts and FEL physics
  Plasma, Dielectric, IFEL, …
  High Brightness Beams required
   EuPRAXIA is a candidate!

## Slide 39: Conclusions
High brightness electron sources have played an enabling role in the development of X-ray FELs
Electron source development remains one of the major challenges for future FEL-based light sources
XFEL radiation represents the most powerful and multi-disciplinary modern probes for the study of the structure of matter in fields as diverse as physics, chemistry, biology, material science, earth sciences, environmental sciences, and cultural artifact restoration
X-rays have the uniquely useful properties that they are partially transparent to solid objects allowing that inner architecture to be investigated, while their wavelengths are comparable to typical interatomic distances and can, moreover, be tuned to be resonant with electron binding energies in atoms
Advanced accelerator concepts can enable compact XFELs moving towards more compact and sustainable user facilities

## Slide 40: References
G. De Ninno, Free-electron lasers: How do they work, Tutorial at IPAC2023
Z. Huang and K.J. Kim, USPAS course, FEL lecture notes, …
A. Marinelli and C. Pellegrini, Tutorial: Introduction to Free-Electron Laser Theory
G. Robb, Classical and Quantum Free Electron Laser, Talk
J. B. Murphy and C. Pellegrini, Introduction to the Physics of the Free Electron Laser, Laser Handbook, vol. 6 p. 9-69 (1990)

## Slide 41
Thank You all for the attention!