## Slide 2
Manuel Cargnelutti
Instrumentation Technologies, Slovenia
Introduction to Digital Low-Level RF Systems
Rome, April 26th, 2024
School on Plasma Accelerators

## Slide 3: Agenda
Instrumentation Technologies - company introduction
RF system and Digital Low-Level RF (LLRF)
Low-Level RF operation
Libera LLRF implementation
Towards a first commercial X-band LLRF

## Slide 4
Est. 1998
~50 employees
ISO 9001:2015 certified
Headquartered in Solkan, Slovenia
ISO

## Slide 5
Beam-diagnostics-and-control instrumentation
Company Business Units
Particle Accelerators
Nuclear Research Reactors
Nuclear Fusion
Custom data-acquisition products
Open-source general-purpose lab devices
Transportation Industry
Energy Industry
Test and Measurement
Universities
Research
Industry
SOLUTIONS
FOR INDUSTRIES

## Slide 6
LIBERA was the result of collaborations
Libera Electron
Back in 1998, all diagnostic systems were based on analog electronics, providing limited information about the beam.
Analog electronics were not stable against temperature and component aging.
Together with the synchrotrons in EU,
Instrumentation Technologies developed the
1st Libera instrument, consisting of an analog front end, fast A/D converters and a digital processor (FPGA).
The real-time processing power offered by the FPGAs, made fast communication between the instruments possible, enabling fast-feedback applications which are today a must in the new machines.

## Slide 7
7
…and was quickly adopted worldwide!
> 6,000 instruments sold
to > 80 laboratories worldwide

## Slide 8
8
And today addresses many applications and machines
Beam Diagnostics
Beam Position Monitoring
Beam Loss monitoring
Beam current / Beam phase
LLRF controls
LINACs
Proton synchrotrons
RF generation and transfer
Reference Master Oscillators
RF distribution systems
General Purpose
RF Digitizers
Current Meters

## Slide 9
9
Typical instrument architecture
Analog front-end and ADC
DAC and analog back-end
FPGA
Real-Time signal processing
CPU
Access to Signals and Parameters
Control System
Input
Signals
Actuators
LIBERA LLRF

## Slide 10: Agenda
Instrumentation Technologies - company introduction
RF system and Digital Low-Level RF (LLRF)
Low-Level RF operation
Libera LLRF implementation
Towards a first commercial X-band LLRF

## Slide 11: RF accelerators
  Principle: alternating the Electrical field across multiple plates along the particle accelerator.
  The RF field within the RF structures should be properly controlled in order to be in a certain phase relation with the accelerated particles.
Courtesy of Dr. G.Burt

## Slide 12: Digital LLRF purpose (I)
Master Oscillator signal
(Reference clock)
User Defined
Set-Point values
RF cavity
Beam
Waveguide (RF distribution)
Input Power
Coupler
Cavity Probe Signal
Drive signal
Power amplifier example
(Pulse modulator + Klystron)
LLRF system purpose:
Continuously measure RF cavity field amplitude and phase
Control high power RF to stabilize cavity amplitude and phase
LLRF system
Digital LLRF

## Slide 13: Digital LLRF purpose (II)
LLRF system purpose (continued):
Measure the cavity resonant frequency and control the cavity tuning
Trigger the machine protection system in case of unexpected signals in the cavity or in the RF distribution

## Slide 14: Cavity material and parameters
Normal conductive “warm” Copper cavities
Super conductive “cold”
Niobium cavities
Normal conductive cavities
Room temperature and water cooling
Easier to manufacture and operate
Pulsed beams
RF frequencies from few 100 MHz to X-band
Frequency tuning done with water temperature control and mechanical tuners

## Slide 15: Cavity material and parameters
Normal conductive “warm” Copper cavities
Super conductive “cold”
Niobium cavities
Normal conductive cavities
Room temperature and water cooling
Easier to manufacture and operate
Pulsed beams
RF frequencies from few 100 MHz to X-band
Frequency tuning done with water temperature control and mechanical tuners
Super conductive cavities
Cooling to 1.6K - 4.5K with liquid helium
Challenging to manufacture and operate ($$$)
Suitable for high duty cycle and CW operation
Much higher efficiency compared to copper
RF frequencies from few 100 MHz to few GHz
More complicated frequency tuning done with piezo tuners

## Slide 16: Example of normal conductive proton LINAC
To achieve the desired beam energies, several RF cavities are necessary. Depending on the particle beam, the cavity frequencies might change as well as the cavity type.
Every RF station including a power amplifier needs to be controlled and synchronized with each other -> each RF station needs a LLRF system.
In order to have a common clock distributed for all the LLRF stations, an RF distribution system is also required!
750MHz RFQ
1 RF station
S-Band (3GHz) SCDTL and CCL
12 RF stations

## Slide 17: Agenda
Instrumentation Technologies - company introduction
RF system and Digital Low-Level RF (LLRF)
Low-Level RF operation
Libera LLRF implementation
Towards a first commercial X-band LLRF

## Slide 18: Feed Forward operation (I)
In Feed-Forward operation, we use the LLRF to generate a drive signal (Forward drive) that produces in the cavity (Vcav) a voltage that is as close as possible to our desired voltage.
In this process, we should consider the following aspects:
The cavity has a filling time that depends on its quality factor. The same when the power goes off. It acts as a low-pass filter to the step response.
This implies that the beam should arrive after the RF pulse
Each cavity has a maximum voltage that can be filled in
Courtesy of J.Branlard (DESY)

## Slide 19: Feed Forward operation (II)
First step: defining the forward drive
amplitude to match the cavity amplitude
at the beginning of the beam time
Courtesy of J.Branlard (DESY)

## Slide 20: Feed Forward operation (III)
Second step: modulate the drive amplitude during
the beam time to maintain the desired gradient
Courtesy of J.Branlard (DESY)

## Slide 21: LLRF Feedback
No matter how precise we are setting the pulse shape, the system variations over time and temperature will require us to use a feedback loop to improve the regulation
Courtesy of J.Branlard (DESY)
We are very interested to maintain a certain amplitude and phase stability (RMS) within the pulse and from pulse to pulse. Both in short term (seconds) and on long-term (hours)

## Slide 22: Important LLRF specifications
Physical interfaces:
Number of RF inputs (8 or 16 or more) and expected signal levels
Number of RF outputs (1 or 2) and signal levels
Specific trigger signals (RF pulse, Beam pulse, Modulator signals)
Machine Protection System interfaces (Interlock)

## Slide 23: Important LLRF specifications
Physical interfaces:
Number of RF inputs (8 or 16 or more) and expected signal levels
Number of RF outputs (1 or 2) and signal levels
Specific trigger signals (RF pulse, Beam pulse, Modulator signals)
Machine Protection System interfaces (Interlock)
Machine specifications:
RF frequency
Type of cavity (NC, SC)
Pulsed (pulse duration, injection frequency) vs CW
Cavity tuning requirements
Control system interface
RF Frequency band | Frequency range
L-band | 1-2 GHz
S-band | 2-4 GHz
C-band | 4-8 GHz
X-band | 8-12 GHz
The higher the frequency, the smaller is the size of the RF components and RF structures -> more compact machines!

## Slide 24: Important LLRF specifications
Physical interfaces:
Number of RF inputs (8 or 16 or more) and expected signal levels
Number of RF outputs (1 or 2) and signal levels
Specific trigger signals (RF pulse, Beam pulse, Modulator signals)
Machine Protection System interfaces (Interlock)
Machine specifications:
RF frequency
Type of cavity (NC, SC)
Pulsed (pulse duration, injection frequency) vs CW
Cavity tuning requirements
Control system interface
Performance specifications:
Front-end and Back-end: Bandwidth, sampling rate, added noise
Short term amplitude and phase stability
Long term amplitude and phase stability

## Slide 25: Agenda
Instrumentation Technologies - company introduction
RF system and Digital Low-Level RF (LLRF)
Low-Level RF operation
Libera LLRF implementation
Towards a first commercial X-band LLRF

## Slide 26: Libera LLRF – overview and modules
Modular platform based on MTCA technology
Several modules are frequency dependent and require HW changes -> more customization flexibility
The number of input channels can be scaled with more RF input modules
Empty slots can be used for additional custom interfaces
The platform is also used for other company applications (e.g. BPM electronics)

## Slide 27: Libera LLRF – overview and modules
Inter Connection Computer module
RF input modules with RF front-end and ADCs
Timing and Clock management module
Vector modulator module with DACs and RF back end

## Slide 28: Libera LLRF with Temperature Stabilized Front End
For the machines with higher stability requirements (FELs for example), even the small environment conditions deviations (T, RH%) affect their performance.
For this case, a temperature-stabilized RF front-end was developed assuring internal temperature variations of < 0.01K

## Slide 29: Libera LLRF TSRF functionality

## Slide 30: Libera LLRF DSP block diagram

## Slide 31: Graphical User Interface (Expert GUI)

## Slide 32: Agenda
Instrumentation Technologies - company introduction
RF system and Digital Low-Level RF (LLRF)
Low-Level RF operation
Libera LLRF implementation
Towards a first commercial X-band LLRF

## Slide 33: The EuPRAXIA@SPARC_LAB project
The EuPRAXIA@SPARC_LAB electron LINAC will include
An S-band injector providing electrons at 150MeV
A series of X-band accelerating structures to boost the electron energy to 0.5-1GeV
A plasma accelerator (1m) to boost the electron energy to 5GeV
Source: CDR and website

## Slide 34: X-band Digital LLRF
A few challenges were identified when discussing the LLRF requirements with the RF group at INFN-LNF:
Controlling the RF pulse properties at 12GHz for very short pulses (100ns) is a challenge.
Temperature drifts influence the LLRF system stability even more at higher RF frequencies: need for temperature stabilized down-conversion implemented for X-band signals.
At the moment there is no commercial LLRF system working in X-band that meets the performance requirements of the EuPRAXIA@SPARC-LAB LINAC

## Slide 35: X-band Digital LLRF
A few challenges were identified when discussing the LLRF requirements with the RF group at INFN-LNF:
Controlling the RF pulse properties at 12GHz for very short pulses (100ns) is a challenge.
Temperature drifts influence the LLRF system stability even more at higher RF frequencies: need for temperature stabilized down-conversion implemented for X-band signals.
At the moment there is no commercial LLRF system working in X-band that meets the performance requirements of the EuPRAXIA@SPARC-LAB LINAC
A PhD project was proposed for the realization of a 2-channel LLRF prototype as part of the EuPRAXIA Doctoral Network
Phani Deep Meruga joined us in November 2023!

## Slide 36
manuel.cargnelutti@i-tech.si
Thanks for your attention!
www.i-tech.si

## Slide 37: DC accelerators
  In DC or electrostatic accelerators, the particles travel through a constant Electrostatic field.
  The energy they reach depends on the voltage gap between the two sides of the accelerator.
  As an example, the Cockroft-Walton that used a smart voltage multiplier in order to achieve few 10s of MV.
  The fundamental limitation is the voltage breakdown in the structures which limits the achievable voltage gradients to 3MV/m
Courtesy of Dr. G.Burt