## Slide 1
LOREM IPSUM DOLOR
SIT AMET
CNAO stato e prospettive
M. Pullia

## Slide 2: What is CNAO

## Slide 3: CNAO National Center for Oncological Hadrontherapy
Not-for-profit private foundation Created by the Italian Ministry of Health in 2001 “to build the National Center for Hadrontherapy designed by TERA Foundation”
The Board is formed by 14 Institutions:
5 hospitals
3 universities
2 research institutes
2 public entities (Ministry of Health and Town of Pavia)
2 bank foundations
Located in Pavia

## Slide 4
Risk and complexity in high-tech medical innovation
Medicine and Biology
Physics and Engineering
Management and Innovation
Clinical Activities
Post-graduate Education
Research
The Hadron Academy
(PhD Courses IUSS-CNAO)

## Slide 6: Origins - history
1990 – U. Amaldi and G. Tosi have the idea of promoting hadrontherapy in Italy
1991 – U. Amaldi and G. Tosi, “Per un centro di teleterapia con adroni”
1991 – ATER experiment at INFN
1992 – TERA Foundation is founded

## Slide 7: PIMMS (Proton Ion Medical Machine Study, 1996-1999)
Objective: define the optimal hadrontherapy centre without constraints
CERN-GSI-MedAUSTRON-Oncology2000-TERA
PL: P. Bryant (CERN+experts)
PAC: G. Brianti chairman
TERA: 25 manyrs
MedA.: 10 manyrs
O2000: 3 manyrs
GSI: experts advices

## Slide 8: Origins - history
1990 – U. Amaldi and G. Tosi have the idea of promoting hadrontherapy in Italy
1991 – U. Amaldi and G. Tosi, “Per un centro di teleterapia con adroni”
1991 – ATER experiment at INFN
1992 – TERA Foundation is founded
1996 – PIMMS starts (TERA+CERN+MedAustron+Onkologie2000+GSI)
2000 – 2001 the CNAO foundation is created within the Financial Law
2003 – CNAO gets the project and hires the design group

## Slide 9: The CNAO phases
Phase 1: construction
Years: 2005 - 2009
Phase 3: running
Years : 2014 …
Phase 2: experimentation
Years: 2010 - 2013
Phase 0: organisation
Years: 2002 - 2004
Hadrontherapy in LEA
Years : 2017 …
Phase 4: expansion
Years : 2019 …

## Slide 10: About 5000 patients treated
Increasing number of paediatric patients
(often with anaesthesia)
Longer time required
Chart: 
| 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023
 | 4 | 41 | 130 | 230 | 308 | 355 | 506 | 522 | 501 | 546 | 562 | 557 | 538

## Slide 11: What we do

## Slide 12: Comparison of the depth dose profiles
Protons/Carbon
Electrons
Photons
Tumour
Beam

## Slide 13: What we do at CNAO
The number of
particles varies
spot by spot
(courtesy of Siemens Medical)

## Slide 14: Microscopical advantage of C ions

## Slide 15: Microscopical advantage of C ions

## Slide 16: Microscopical advantage of C ions
1 10 100 LET
RBE
4
3
2
1
10 – 20 keV/mm = 100 – 200 MeV/cm =
20 – 40 eV/(2 nm)

## Slide 17: Carbon ions: high LET where needed
Low LET
High LET
Higher LET – Higher efficacy

## Slide 18: CNAO accelerator system
Accelerated ion p, C
Energy range (MeV/u) 60–227 (250) (p) (30-320mm)
115–400 (C) (30-270mm)

## Slide 19
2 Strip chambers (X and Y):
Beam position measure every 100 s, with 100 m of precision
1 Pixel chamber:
Beam position and dimension measure every 100 s/1 ms, with 200 m of precision
1 Integral chamber:
Beam Intensity measure every 1 s
1 Integral chamber:
Beam Intensity measure every 1 s
Integral 1
STRIP X
STRIP Y
Integral 2
PIXEL
Box 1
Box 2
Dose Delivery System: in house development
Dose driven
Real time measurement
Feedback on scanning magnets

## Slide 20: Patient positioning and position verification

## Slide 21: Need for access to suitable beamlines
At clinical facilities beam available during nights and weekends
Treatment rooms to be left when clinical activities start again (experiment to be removed)

## Slide 22
Experimental room
+1 Experimental Room
3 Treatment rooms
2 H
1 H+V

## Slide 23: Experimental Facility (XPR + Lab)
Multiple configuration
Accessible during treatment
Experiments can be installed
for many days
DDS customization possible
Biological laboratory with all the
necessary equipment to prepare
and process cell samples is
available on site.
Small animal irradiation is possible
taking advantage of the nearby
animal house facility of the
University of Pavia

## Slide 24: Experimental room open to external users
Monitoring system on rail
Modular line
Magnets on rail
Vacuum extension chamber

## Slide 25: Available beams
Protons
60-227 MeV
< 1010 p/spill
Carbon
115-400 MeV/u
< 4 x 108 C/spill
~2s
t
I
~1s
En.1
En.2
En.3
FWHM ~10 mm (particle and energy dependent)
Irradiation field
< 200 x 200 mm2 [iso4]
Max distance downstream target < 5.5 m
[iso1]
Low intensities (103 part/s) possible

## Slide 26: Research and development activities
Reasearch activities on technical, preclinical and translational subjects
Typical research subjects carried out at CNAO are aimed at improving treatment
  Improving the technical performance of the accelerator system
  Improving the technical performance of the dose delivery
  Improving the understanding of biological mechanisms
  Improving the knowledge of basic physical processes
  Providing new types of radiation (new weapons to the clinician)
Collaborations with many institutions

## Slide 27: Machine development

## Slide 28
Treatment execution
Sync
1 -3 s
Extracted beam
B ~ p~ E
acceleration
extraction
hysteresis ("washing ")

## Slide 29: Treatment execution with Multi Energy Extraction
Sync
1 s
Saved
time
Saved
time
(Courtesy K. Noda – CAS Medical)
Use remaining beam after slice completion

## Slide 30: Implementation of RFKO in addition to betatron
Dp/p
Amplitude
(b)
Amplitude-momentum
selection
X’
XES
Dp/p
Amplitude
(c)
RF-KO
X’
XES
Standard method
at CNAO
Being implemented
for multi energy
extraction studies

## Slide 31: RFKO
RFKO for protons under validation by medical physics crew
RFKO for carbon in final preparation phase by operation

## Slide 32: Electrostatic septum
Delivered to CNAO
Assembly and commissioning in progress
Tests of controls and motion ongoing

## Slide 33: Dose delivery development

## Slide 34: DDS developments
A new version has been developed in collaboration with GSI.
Multi-phase treatments can be delivered.
For moving organs multipe treatments are build to treat the target in different positions.
DDS switches between plan in real-time avoiding time waste as in gated modality.
Additional x and y tracking is implemented.
Energy layers scan kept (synchrotron).
Faster energy switch for multienergy extraction.
DDS 4.0
Single field
(interplay)
Multi-phase
4D delivery

## Slide 35: Motion-synchronized plan libraries
online plan changes, same mechanism as new spot
one IES, E=224.8 MeV/u
motion phase
motion phase without (remaining) beam spots: beam gate until next phase with spots
Courtesy of C. Graeff

## Slide 36: Upgrades and expansion

## Slide 37: New source
Aisha 1 in INFN LNS
Courtesy of L. Celona
Aisha 2 at CNAO – He, Li, O, Fe
Waiting for authorization

## Slide 38: New source

## Slide 39: CNAO Expansion phase 1 (ongoing)
Carbon gantry
New XPR
BNCT:
1 treatment room
1 experimental room
48 m
37 m
p gantry
BNCT

## Slide 40: Single room facility with gantry for protons
Synchrotron room
Treatment room
Contract signed with Hitachi: December 5th, 2019
360°isocentric gantry (Field size: 30x40 cm2)

## Slide 41: Accelerator based BNCT
Proton energy 2.5 MeV
Intensity 10-15 mA
p-Li reaction
Collaboration agreement signed September 2020
Notes: neutron yield at 10 mA
8.9 × 1012 [s-1]
Avg neutron energy 0.55 MeV at 0°
[/cell], [m-2] (30 minutes irradiation by flux [n/cm2/s ]):
(mostly fired)
(the half is not fired)
neutron yield at 10 mA
8.9 × 1012 [s-1]
Avg neutron energy 0.55 MeV at 0°
𝑁=〖10〗^9 [/cell], Φ=1.8×〖10〗^16 [m-2] (30 minutes irradiation by flux 〖10〗^9[n/cm2/s ]):
𝑃(0)=𝑒^(−6.84)=0.001 (mostly fired)
𝑃(0)=(⟨𝑛⟩^0 𝑒^(−⟨𝑛⟩ ))/0!=𝑒^(−⟨𝑛⟩ ) =" " 𝑒^(−𝑁𝜎Φ)
𝑁=〖10〗^9 "[/cell], " Φ=1.8×〖10〗^15 " [m−2] (30 minutes irradiation by flux " 〖10〗^8 "[n/cm2/s ]):"
𝑃(0)=𝑒^(−0.684)=0.505 (the half is not fired)

## Slide 42: BNCT
Boronated drug that selectively reaches the tumour cells and avoids the healthy tissues
Accelerator driven neutron production
First Approved BNCT Drug (in Japan), May 2020
Notes: STELLA PHARMA will launch
Steboronine®, the World's First BNCT Drug,
on May 20, 2020

## Slide 43
Building completed summer 2024
Hitachi installation starts spring 2024
TLS installation starts summer 2024
New technologies ready by middle 2025

## Slide 44: Leo Cancer Care chair + vertical CT
Gantry surrogate
To be installed in room #3

## Slide 45: CNAO Expansion phase 1-2
Carbon gantry
New XPR
BNCT:
1 treatment room
1 experimental room
48 m
37 m
p gantry
BNCT
Carbon gantry
New XPR

## Slide 46: SC Gantry
EuroSIG
CNAO-CERN-INFN-MedAustron collaboration
HITRI+ and IFAST

## Slide 48: Summarizing
CNAO treatments daily (5000 patients treated so far)
Research is a second pillar at CNAO
Education is the third pillar at CNAO. Doctoral school (with IUSS and UniCA)
A research facility is available at CNAO that can be used without interference with treatments
CNAO offers a large variety of beams and irradiation possibilities
He, Li, O and Fe will be added to the already available p and C
DDS customizations are possible
A BNCT room will soon be available

## Slide 49: Research is a must
Research and development is mandatory to keep a large investment up to date
Being able to make the system evolve requires knowing the system in its intimate details
Being able to make the system evolve requires being allowed to change it (CE label and equivalent certifications)
There are many research fields along the system: from the source to the dose delivery, where research, development and innovation can be beneficial
Notes:   I limited the talk to the description of the facility and I’ve neglected the research activities from the developments of the accelerator to the range verification,
  Dose/LET/Beam distribution optimization,
  Improved beam measurement for improved beam distribution,
  Basic physical data (e.g. foot)

## Slide 50
“If you think research is expensive, try disease!”
Mary Lasker