## Slide 1
Matteo Duranti
Istituto Nazionale Fisica Nucleare – Sez. di Perugia
Silicon in Space

## Slide 2: Silicon in Space
PhysRevLett.124.211102

## Slide 3: Silicon in Space
PhysRevLett.124.211102
Jokes apart:
- we use our detectors (mainly the Si trackers) to measure the Z of the CR particles
- input charge could be 62 or 82 (C and O), 142 (Si) or even 262 (Fe) or above, times a MIP…

## Slide 4
Matteo Duranti
Istituto Nazionale Fisica Nucleare – Sez. di Perugia
Silicon (μstrip) in Space
State of the art and perspectives for Si microstrip tracking systems in space

## Slide 5: Outline
Scientific case and state of the art
(far, intermediate and near) future
pros and cons of μstrips
LGADs?

## Slide 6: Cosmic Rays
Φ(E) ∝ E-γ
(γ ~ 2.7-3.1)
measuring in Space (or balloon) allows single particle measurements  precise composition and spectra measurement
BUT
cosmic ray spectra are tipically power laws:
1 order of magnitude in energy  2 orders of magnitude in flux (i.e. in statistics)

## Slide 7: The experimental challenge
No atmosphere:
  Stratospheric ballon
  Satellite / Space station
Limits on size / weight / time / power consumption
Detector design focused on specific measurements
Antimatter / Isotopes Magnetic spectrometers
Nuclei / e++e- / Gammas Calorimeters

## Slide 8: Astro-particle detectors – state of the art
accurate spatial resolution (<10 μm) Si-μstrip for Rigidity measurement up to TVs;
charge measurement capability (0.1 c.u.) for at least a couple of detectors (Tracker, Time of Flight);
Electromagnetic CALorimeter (17 X0) for e+, e-, γ Energy measurement;
Time of Flight (σt ~ 120 ps, σβ ~ %) for trigger, arrival direction (upward/downward) and isotopic composition (up to few GeV, then Ring Imaging Cherenkov, σβ ~ 0.1 %);
Transition Radiation Detector and ECAL to distinguish hadrons (90% of Cosmic Rays, CR, are protons, 10% He) from electromagnetic particles (e- are 1% of CR, e+ 0.1%), e/p identification;
~ 2 kW
AMS-02 (in orbit since 16/05/2011):
TRD
Tracker
ECAL
1
2
7-8
3-4
9
5-6
Time of Flight
Time of Flight
RICH

## Slide 9: Astro-particle detectors – state of the art
moderate spatial resolution (~60 μm) Si-μstrip for pair-production measurement;
electromagnetic calorimeter (10 X0) for e+, e-, γ Energy measurement;
plastic scintillator anticoincidence shield for charged CR veto;
electromagnetic calorimeter to perform e/p identification;
Tungsten plates in the tracker for photon conversion;
~ 1.5 kW
AMS-02 (in orbit since 16/05/2011):
TRD
Tracker
ECAL
1
2
7-8
3-4
9
5-6
Time of Flight
Time of Flight
RICH
Fermi-LAT (in orbit since 11/06/2008):

## Slide 10: Astro-particle detectors – state of the art
AMS-02 (in orbit since 16/05/2011):
TRD
Tracker
ECAL
1
2
7-8
3-4
9
5-6
Time of Flight
Time of Flight
RICH

CR
moderate spatial resolution (~40 μm) Si-μstrip for pair-production measurement;
charge measurement capability (0.1 c.u.) for at least a couple of detectors (Tracker, Plastic Scintillator Detector);
electromagnetic calorimeter (31 X0) for e+, e-, γ and hadron Energy measurement;
Plastic Scintillator Detector, PSD, for charged CR veto;
electromagnetic calorimeter to perform e/p identification;
Tungsten plates in the tracker for photon conversion;
~ 0.5 kW
DAMPE (in orbit since 17/12/2015):
Fermi-LAT (in orbit since 11/06/2008):

## Slide 11: Fight for your right (to have statistics)
flux
(given by Nature)
Energy bin
Exposure time
Acceptance
calorimeter (X0)
spectrometer (BL2)
surface AND solid angle

## Slide 12: HEP detectors in Space
Mechanical stress at launch:
Static acceleration
Random vibration
Sinusoidal vibration
Pyroshock
Life in space:
Thermal stresses due to Sun-light (seasonal / day-night effects)
Vacuum
Radiation
Careful Design, Model validation and Qualification are needed to ensure highest possible reliability

## Slide 13: Perugia / μstrip in Space
LIMADOU
AMS-02
DAMPE
future experiments
State of the art
strongly biased from/towards activities conducted in Perugia
focused on μstrip sensors. Why μstrip? Example AMS-02 tracker:
  ~6 m2
  total of 200k channels for ~ 200 watt
  100 μm pitch  10 μm (30 μm) spatial resolution in bending (non bending) plane
  Back of the Envelope:
  x-side =sqrt(6m2) ~ 2.5m2
  maximum length of ladders: l=0.5 m
  #ladders per y-side (or layers) = s/l
  pitch, p = 100 μm = 10-4 m
  #channelsstrip = (s/l) * s/p = 120k
   strip = 2*120k ~ 105
   pixel = 120k*120k ~ 1010

## Slide 14: AMS-02: Silicon "ladder"
192 flight units 5 – 15 wafers (28 – 60 cm) each  daisy chain (parallel!) of many wafers  impedance of the sensor of the order of 50-100 pF
1024 high dynamic range, AC coupled readout channels:
  640 on junction (S) side
  384 on ohmic (K) side
Implant/readout pitch (floating strips!):
  27.5/110 μm ("S"/junction/p-side/bending side)
  104/208 μm ("K"/ohmic/n-side/non-bending side)

## Slide 15: Wire bonding
Human hair
Merino wool
bonding wire: 25 μm
Merino wool: 20 μm
Human hair: 200 μm

## Slide 16: wire bonds vibration test

## Slide 17: Fermi-LAT (2008)
73 m2 surface
9216 sensors
2304 ladders
k channels
strip pitch 230 μm
readout pitch 230 μm

## Slide 18: AMS-02 Silicon Tracker (2011)
strip pitch 27.5 μm
readout pitch 110 μm
6.3 m2 surface
2264 sensors
192 ladders
197k channels
190 W

## Slide 19: The DAMPE Silicon TracKer (2015)
76 cm
strip pitch 120 μm
readout pitch 240 μm
6.9 m2 surface
768 sensors
192 ladders
74k channels
23 W

## Slide 20: the (far) future is in L2, a nice place in space

## Slide 21: ALADInO - Antimatter Large Acceptance Detector In Orbit
Diameter: 4.4 m
Length: 2.2 m
Acceptance: 3 m2sr
MDR > 20 TV
Silicon ladders: tracking
scintillators: ToF
CaloCube: energy
(INFN CSNV)
supercoducting coils: magnet
~100 m2 surface
O(5 μm) spatial resolution
2M channels 1 kW

## Slide 22: AMS-100
~200 m2 surface
O(5 μm) spatial resolution
10M channels 5 kW

## Slide 23: intermediate future: HERD
to be installed on board the Chinese Space Station (2027)

## Slide 24: HERD Silicon Charge Detector
2 m
2 m
1.2 m
~60 m2 surface, 8 layers 6144 SSD
768 ladders
80-100 cm long ladders

## Slide 25: The near future: AMS-02 L0 upgrade
AMS-02 Layer1
to be ready by early 2025
~ 8 m2 surface, 2 layers (45° stereo)
768 sensors
72 ladders
72k channels
~ 120 W

## Slide 26: The near future: AMS-02 L0 upgrade
the basic element of the detector
the detecting part: 8, 10 and 12 sensors
the readout
electronics
charge measurement:
high dynamic range FE
spatial resolution:
110 µm readout pitch
64-96 cm long ladders

## Slide 27: AMS-02 L0 upgrade
96 cm
101 cm
data/cmd
5 V

## Slide 28: Vibration test of a silicon detector

## Slide 29: Silicon Microstrip detectors in space
Most of space detectors for charged cosmic ray and γ-ray measurements require solid state tracking systems based on Si-μstrip sensors.
Si-μstrip detectors are the only solution to instrument large area detectors with larger number of electronics channels coping with the limitations on power consumption in space
[1] HERD Collaboration. HERD Proposal, 2018 https://indico.ihep.ac.cn/event/8164/material/1/0.pdf
[2] Battiston, R.; Bertucci, B.; et al. High precision particle astrophysics as a new window on the universe with an Antimatter Large Acceptance Detector In Orbit (ALADInO). Experimental Astronomy 2021. https://doi.org/10.1007/s10686-021-09708-w [3] Schael, S.; et al. AMS-100: The next generation magnetic spectrometer in space – An international science platform for physics and astrophysics at Lagrange point 2. NIM-A 2019, 944, 162561. https://doi.org/10.1016/j.nima.2019.162561
(see M. Duranti, V. Vagelli et al., Advantages and requirements in time resolving tracking for Astroparticle experiments in space, Instruments 2021, 5(2), 20; https://doi.org/10.3390/instruments5020020)

## Slide 30: AMS-02 (junction, "S", "p-side", "bending")
300 μm
14 μm
110 μm
27.5 μm
27.5 μm
27.5 μm
27.5 μm
spatial resolution:
- 10 μm @ Z=1
- 5-6 μm @ Z>1
to be compared with 27.5 μm /sqrt(12) ~ 8 μm
NOT
110 μm /sqrt(12) ~ 32 μm
read-out strip
floating strip
n-type
p-type
p-type

## Slide 31: AMS-02 (junction, "S", "p-side", "bending")
Ramo's theorem: only the closest strip (i.e. “digital")
 capacitive coupling permits to know the fired strip  27.5 μm /sqrt(12) ~ 8 μm
Thanks to charge sharing we can do even better than "digital"
75%
25%
300 μm
110 μm
27.5 μm
27.5 μm
27.5 μm
27.5 μm
n-type

## Slide 32: Sensor's scheme (junction)
backplane
capacitance
first-to-third strip
capacitance
interstrip
capacitance
Cb
Ci
Cii
Ci = interstrip capacitance ~ 1 pF/cm * l = 10 – 100 pF
Cd = decoupling capacitance ~ 1000 pF (DC sensors) or 120 pF/mm2 (AC sensors) > Ci Cb Cg Cii
Cb = backplane capacitance ~ 1 pF/cm * l * p/d = 0.5 – 2 * 10 – 100 pF
Cg = guardring capacitance << Ci
Cii = first-to-third strip capacitance << Ci
Cg
decoupling
capacitance
Cd
p = pitch
l = strip lenght
d = thickness

## Slide 33: AMS-02: Charge collection (few months of data)
After few months of data on space the galactic cosmic rays (GCR) nuclear abundances are easily observed with an unprecedented statistics
Entries
C
O
Si
Fe
Abundances not corrected for detector efficiencies
H and He prescaled

## Slide 34: AMS-02 (junction, "S", "p-side", "bending")
300 μm
75%
25%
25% x Ci/Cd
when the main two strips are saturated (at Front End level), the "overflow", towards other readout strips, allows to "recover" both the charge and the position

## Slide 35: Sensor's scheme (junction)
backplane
capacitance
first-to-third strip
capacitance
interstrip
capacitance
Cb
Ci
Cii
Ci = interstrip capacitance ~ 1 pF/cm * l = 10 – 100 pF
Cd = decoupling capacitance ~ 1000 pF (DC sensors) or 120 pF/mm2 (AC sensors) > Ci Cb Cg Cii
Cb = backplane capacitance ~ 1 pF/cm * l * p/d = 0.5 – 2 * 10 – 100 pF
Cg = guardring capacitance << Ci
Cii = first-to-third strip capacitance << Ci
Cg
decoupling
capacitance
Cd
p = pitch
l = strip lenght
d = thickness
What if we want a thin LGAD with a strip geometry?
Capacitance (Cb) become a big problem…

## Slide 36: Serial vs parallel
multi-SiPM readout:
b) typical "parallel" readout
✔︎ bias voltage independent of number of SiPMs
✘ total capacitance seen by readout FEE scales with the number of SiPMs
a) "serial" readout
✘ ︎ bias voltage scales with of number of SiPMs
✔ total capacitance seen by readout FEE scales down (!) with the number of SiPMs

## Slide 37: PRIN2022 - PTSD
INFN (PI M. Duranti) + ASI (Co-PI V. Vagelli)
~ 200 k€ received funds

## Slide 38: Ideas behind the project
combine a standard μstrip sensor (2D + Z) with an LGAD (2D + timing)
serial readout of the "stack" to reduce LGAD capacitance
use standard μtrip as "structural" material for a very thin LGAD layer

## Slide 39: Ideas behind the project
combine a standard μstrip sensor (2D + Z) with an LGAD (2D + timing)
serial readout of the "stack" to reduce LGAD capacitance
use standard μtrip as "structural" material for a very thin LGAD layer

## Slide 40: Ideas behind the project
combine a standard μstrip sensor (2D + Z) with an LGAD (2D + timing)
serial readout of the "stack" to reduce LGAD capacitance
use standard μtrip as "structural" material for a very thin LGAD layer
Is possible to "daisy chain" the sensors (LGAD but also standard μstrip) connecting them in series and not in parallel?
 capacitance would decrease as the length of the sensors increases!

## Slide 41: Si sensors

## Slide 42: Backup

## Slide 43: Preliminary work
Sensor (LGAD, standard)
decoupling C
bias resistor
backplane C
(50 pF LGAD, 10 pF standard)
leakage
diode

## Slide 44: Preliminary work
Sensor (LGAD, standard)
decoupling C
bias resistor
backplane C
(50 pF LGAD, 10 pF standard)
leakage
diode
CSA (values almost random…)

## Slide 45: Preliminary work
Sensor (LGAD, standard)
decoupling C
bias resistor
backplane C
(50 pF LGAD, 10 pF standard)
leakage
diode
CSA (values almost random…)
Simple serial conf, compared with other (reference) ones
Signal in sensor
Signal in sensor

## Slide 46: Preliminary work
1 LGAD + 5 standard
only LGAD
only (5) standard
only (1) standard
1 LGAD + 1 standard

## Slide 47: Preliminary work
✔︎ the LGAD signal is passing trough the standard sensor: seems working!
✔︎ the CSA should see only the standard sensor capacitance, being the lower
✘ the LGAD sees, as effective "decoupling capacitance", the standard sensor capacitance: the collected signal is depressed by the ratio of standard/LGAD capacitance (see violet and blue curves vs red one, and blue curve vs violet one)
✔︎ the standard sensor sees its whole decoupling capacitance, but also a "complex" (a network, including the LGAD) backplane capacitance: the signal is not severely but still depressed (blue curve vs green or orange). To be understood completely…
signal in LGAD signal in standard

## Slide 48: Cosmic Rays
if:
what we get is something like:
and this is what we use for the flux measurement
cosmic ray spectra are tipically power laws:
1 order of magnitude in energy  2 orders of magnitude in flux (i.e. in statistics)

## Slide 49: Spectrometer power consumption mitigation (AMS)
Placing the magnetic field in smart configurations (e.g. the Halbach array configuration in AMS) allows to have:
- bending direction
- non-bending (*) direction
* actually the particle is bent also in this direction. It's only true that its momentum in this direction is not modified…
This allow to push the spatial resolution (and so the power consumption) only in one direction.
For example in AMS, for He nuclei:
- bending direction, ~ 7μm;
- non-bending, , ~ 30μm;

## Slide 50: Astro-particle detectors – planned and dreamed
CR
CR
CR
CR
- exploit the CR "isotropy" to maximize the effective geometrical factor, by using all the surface of the detector (aiming to reach Ω = 4π)
- the calorimeter should be highly isotropic and homogeneous:
  the needed depth of the calorimeter must be guaranteed for all the sides (i.e. cube, sphere, …)
  the segmentation of the calorimeter should be isotropic
 this is in general doable just with an homogeneous calorimeter
 CaloCube
CALO
ToF
TRK
HERD on the CSS (2027):
AMS-100 (2050?):
ALADInO @L2 (2050?):

## Slide 51: AMS-02: Silicon Tracker
9 layers of double sided silicon detectors arranged in 192 ladders
~6 m2
total of 200k channels for ~ 200 watt
10 m (30 m) spatial resolution in bending (non bending) plane
momentum resolution ~10% @10 GeV
high dynamic range front end for charge measurement
wide temperature range (-20/+40 survival, -10/+30 oper.)
6 honeycomb carbon fiber plane
detector material ~ 0.04 X0

## Slide 52: AMS-02: Cooling with 2-phases CO2 pumped loop
Tracker Thermal Cooling System (TTCS)

## Slide 53: AMS-02: Silicon "ladder"
192 flight units 7 – 15 wafers (28 – 60 cm) each
Cb = 7pF
Cstrip = 1.2pF/cm
 Cb + Cstrip ~ Cstrip
Ccoupling = 700pF
 1/Cstrip + 1/Ccoupling ~ 1/Cstrip

## Slide 54: AMS-02: Silicon "ladder"
Y
Y
X
"multiplicity" (or "ambiguity"): the 1500-3000 K-side channels needed for each ladder are "merged" into 384.

## Slide 55: AMS-02 upgrade "L0"
Acceptance increased to 300% (10 years data becomes 30 years data)
y
z
x
New Silicon Tracker Plane
Existing Tracker L1
Front-end electronics
L0-Y
bending direction
7 micron
L0-U rotated 45o
10 micron bending
10 micron non-bending
ladders of
8 sensors
ladders of
10 sensors
ladders of
12 sensors
Si sensors
New Silicon Tracker Layer: one plane, two layers, each ~ 4m2
Notes: Acceptance increased by a factor 2.5-3, depending on the analysis and selections.

## Slide 56: MC simulation
MC Simulation:
based on Geant4 (via Generic Geant Simulation, GGS, Mori, N Nuc. Instr. Meth. Section A, Volume 1002, 21 Jun 2021)
simple geometry "a la DAMPE": only tracker + calorimeter
Informations saved:
energy lost and deposited
spatial coordinates
timing
…

## Slide 57: Back-scattering
tracker layers
particles produced from the interaction of the CR with the silicon detectors
1 TeV protons
Hits in the tracker (Edep >10 keV vs Δt between the ith hit and the 1st hit (i.e. the CR passing in the first layer of the tracker)
Hits from back-scattering
Δt=O(100ps)
Δt=O(10ns)
Δt=O(10μs)
Δt=5*65ps=5*c*2cm
back-scattering
measurements assuming 100 ps resolution
O(100ps) timing resolution enables to separate back-scattering from primary hits in the tracker  improved efficiency in track reconstruction

## Slide 58: Back-scattering
Simulating a timing resolution (gaussian with σ=100 ps)
Δt=65ps=c*2.2cm
A simple cut (e.g. 550 ps from the first), removes:
~ 40% of the hits
~ 90% of the back-scattering hits

## Slide 59: e/p identification
the electromagnetic shower is composed only by "ultra-relativistic" particles  the time arrival in the tracker is (at most):
~ 2d / c
the hadronic shower could be composed by "slow" particles  the time arrival in the tracker could be delayed
d

## Slide 60: e/p identification
only latest hit in tracker
all hits in tracker
looking at all the hits in tracker offers an "high statistic" tool to, for example, train a Multi-Variate algorithm
even the naive idea to look only at the "slower" hit in tracker shows two populations crearly distinct
5M primaries generated:
- 700 GeV electrons
- 1 TeV protons (depositing ~ 700 GeV in the ECAL)
the two populations (electrons and protons) are clearly distinct –> the e/p identification capability seems confirmed and seems also improving with energy

## Slide 61: Ideas behind the project
from: https://indico.cern.ch/event/1044975/contributions/4663642/attachments/2394145/4094091/VCI-AMS-100-TKirn.pdf

## Slide 62
ΔV = O(100V)
ΔV = O(100V)
LGAD-SiMS
SiMS
Front-End with timing
Front-End with CSA

## Slide 63
ΔV = O(200V)
LGAD-SiMS
Front-End with timing
LGAD-SiMS