## Slide 1: Irradiation facilities @ INFN
G. Cuttone
INFN-LNS
PIANOFORTE WP5 Infrastructures Workshop
Catania 29-30 Jan. 2024

## Slide 2: Irradiation facilities @ LNL

## Slide 3
INFN-LNL facilities for radiobiological studies:
Light ion broad beam irradiation facility at the 7MV Van de Graaff CN
electrostatic accelerator
(protons, deuterons, helium-3 and helium-4 ions; E: 0.8-12 MeV)
Light ion microbeam facility at the 7MV Van de Graaff CN
electrostatic accelerator for “single-ion single-cell” irradiation
(protons, deuterons, helium-3 and helium-4 ions; E: 0.8-12 MeV)
Heavy ion broad beam facility at the Tandem-ALPI accelerator complex (A>4; E: 5-26 MeV/amu)
Gamma beam Co-60
SPES Facility

## Slide 4
Ion Beam
glass
roundel
beam collimator
gold scatterer
vernier scale
CHAMBER #1
base plate
beam stopper
CHAMBER #2
top plate
on-line beam monitor
beam monitor assembly
beam collimator assembly
thin window supporting flange
Petridish holder
especially designed
Petridish
air inlet
aluminized mylar foil
turning beam
monitor table
beam
collimators
lemo connectors
lemo connectors
Flanged tube support
Teflon gasket
Thin mylar foil
Stainless steel coupling
cap
Teflon gasket
PETRIDISH
beam
INFN-LNL Broad-Beam Irradiation facility for Radiobiology Studies
Set up at the 7MV CN Van de Graff accelerator and at the Tandem-ALPI accelerator complex
Ref: Belli, Cherubini et al., NIM A256(1987)576-580
Equipment installed on the beamlines

## Slide 5
Dose rate 165 mGy/min @ 30 cm
Gamma Beam 60Co for irradiation with photons
Biological Dosimetry @LNL
Notes: Gamma Beam Co60 used for studies of biological dosimetry

## Slide 6
The SPES Project Cyclotron delivering a 40-70 MeV proton beam, up to 750 μA of current
Possibility of having a future beam-line at SPES
Dedicated bunker for nuclear cross section measurements (ca 100 nA)
Under commissioning

## Slide 7
Platform at 450 KV
Superconducting ECR Source SERSE
ECR Source Normal conducting CAESAR
Sputtering Sources
Accelerators at Laboratori Nazionali del Sud
Istituto Nazionale di Fisica Nucleare
LABORATORI NAZIONALI DEL SUD
LNS is recognized as ESA/ASi Irradiation Facility having:
- designed and implemented a system able to host the samples in front of the beam, by assuring both a very accurate positioning in front of the thinny beam and a very good beam diagnostic and particles counting;
- implemented a very rigorous QA/QC system, in order to guarantee an extremely high reproducibility of the testing parameters and reporting to the users.

## Slide 8
HVEC MP 15 MV Tandem in operation since 1984
In 2014-2015 a big upgrade done due to:
- infiltration of SF6 in tube 1
- obsoloscence of charging system (belt not available from HVEC)
Tandem
Substitution of tube 1 with a new one by Vivirad (France)
Belt replaced by Pelletron
Istituto Nazionale di Fisica Nucleare
LABORATORI NAZIONALI DEL SUD
1H, 2H
6Li, 7Li
9Be, 10Be
10B, 11B
12C, 13C
14N
16O, 17O, 18O
19F
23Na
24Mg, 25Mg
27Al
28Si, 29Si
32S, 34S
35Cl, 37Cl
40Ca
58Ni, 60Ni
63Cu, 65Cu
70Ge
79Br
93Nb
116Sn, 120Sn
127I
197Au

## Slide 9
Bending limit K=800
Focusing limit Kfoc=200
Pole radius 90 cm
Yoke outer radius 190.3 cm
Yoke full height 286 cm
Min-Max field 2.2-4.8 T
Sectors 3
RF range 15-48 MHz
(T/A)max = Kbending (Q/A)2 25 AMeV Au36+
(T/A)max = Kfocusing (Q/A) 100 AMeV fully stripped
AX E (AMeV)
H2+ 62,80
H3+ 30,35,45
2D+ 35,62,80
4He 25,62,80
He-H 10, 21
9Be 45
11B 55
12C 23,62,80
13C 45,55
14N 62,80
16O 21,25,55,62,80
18O 15,55
19F 35,40,50
20Ne 20,40,45,62
24Mg 50
27Al 40
36Ar 16,38
40Ar 15,20,40
40Ca 10,25,40,45
42,48Ca 10,45
58Ni 16,23,25,30,35,40,45
62,64Ni 25,35
68,70Zn 40
74Ge 40
78,86Kr 10
84Kr 10,15,20,25
93Nb 15,17,23,30,38
107Ag 40
112Sn 15.5,35,43.5
116Sn 23,30,38
124Sn 15,25,30,35
129Xe 20,21,23,35
197Au 10,15,20,21,23
208Pb 10
Superconducting Cyclotron
Istituto Nazionale di Fisica Nucleare
LABORATORI NAZIONALI DEL SUD
In operation from 1994 to 2020

## Slide 10
Setto: raffreddato direttamente
Nuovo materiale del setto: W vs. Ta
Spessore maggiore: 0.3 vs. 0.15 mm
Efficienza di estrazione 63% vs. 50%
13C4+ @ 45 AMeV Pextr = 150 watt
I=1020 enA= 1.5x1012 pps
Perdite schermo azoto
Scarsa tenuta tra camera di accelerazione e camera criostato per probabile fessurazione criostato in una delle n saldature
Motivation for upgrade: Beam intensity limitation and cryostat reliability
Istituto Nazionale di Fisica Nucleare
LABORATORI NAZIONALI DEL SUD
Electrostatic Deflextor
Cryostat

## Slide 11
2020
Ciclotrone Superconduttore
2023

## Slide 12
Extraction by stripping is based on the instantaneous change of the magnetic rigidity of the accelerated ion, when its charge state increases after crossing a thin stripper foil
For ions with A<40, and energies higher than 15 MeV/u, the abundance of q=Z exceeds 99%
Extraction by stripping: High efficency-> intensity gain of 100
Upgraded Superconducting Cyclotron
Ions Extracted by Stripping
Ions Extracted by Deflection

## Slide 13
Conditions for Tandem restart
- Completion on maintenance
- ordine NEC (may-june ‘24)
- air flow system summer ‘24
- smoke detector idem
- test w/o beam fall’24
- test with beam first semester ‘25
- Fire Safety system march’24-june’25
Beam to users september’25

## Slide 14
Conditions for Ciclotron restart
- completamento manutenzioni @LNS
-magnet&cryostat delivery december’24
- full set of magnetic measurements
- cyclotron fully assembled fall’25
- test w/o beam first quarter ‘26
- test with beam summer ‘26
- Fire safety system july’24-december’25
Beam to users last quarter ‘26

## Slide 15
RadioBiology Lab
Cyclotron
CATANA
Preclinical
THE UNIQUE NATIONAL NETWORK PROVIDING RESEARCH AND SERVICE ACTIVITY IN THE PRECLINICAL IMAGING, HADRONTHERAPY, FLASH AND ULTRA-FLASH THERAPY

## Slide 16
HUB Leader Mi-Bicocca
Spoke 4 (Leader UniCT)
Innovative radiotherapy techniques and imaging
(Flash therapy & BNCT)
INFN Units: CT, LNL, LNS, NA, PV, TO
Pilot 4.4: Preclinical Studies of Flash and Ultra-flash therapy at Catania.
INFN: LNS, Catania & Pavia Flash Therapy Study based on SIT Linac at Unict-Capir and Ultra Flash Therapy based on laser Plasma Acceleration at INFN-LNS

## Slide 17
Underground radiobiology
at LNGS laboratory
P. Morciano-Cosmic Silence Collaboration

## Slide 18: LNGS represents a unique opportunity for investigating the response of biological systems to below natural radiation background (extremely low radiation dose/dose rate)
All living organisms have to deal with the natural level of radioactivity on the Earth as well as with cosmic rays. Which is the role of natural variations of background radiation during the Life evolution? How does it contribute to the development of cellular defense mechanisms?
Relevant scenario for both basic and applied science
Opportunity to test the linear no-threshold (LNT) model currently used in radiation protection, for which stochastic risk is directly proportional to dose and no detriment is expected below the average natural environmental background
Study of fundamental mechanism(s) of action of low natural background radiation on living organisms and improvement of knowledge on adaptation and evolution
Opportunity for space research to untangle the contribution of the two stressors, microgravity and radiation.
Notes: Cosa rappresentano i LNGS in quanto laboratori sotterranei nella ricerca biologica

## Slide 19: Deep Underground Laboratories (DULs) allow to carry out studies at dose rates significantly lower than on the Earth’s surface Compared to that at the Earth’s surface, inside DULs, the dose/dose rate contribution due to photons and directly ionizing low-LET (mostly muons) cosmic rays can be considered negligible, being reduced by a factor between 104 and 107 depending upon shielding (muon rate ~ 1/m2h at LNGS). Radiation exposure due to neutrons is also extremely low, being reduced by a factor between 102 and 104 (103 at LNGS) One further contribution to the overall dose/dose rate can come from radon decay products, but it depends upon the radon concentration, which can be kept at the same levels of the reference radiation environment by a suitable ventilation system or it can be strongly reduced by radon abatement systems (Radon concentration is comparable between external and underground environment at LNGS). Terrestrial gamma rays represent the major contribution to the dose/dose rate inside the DULs and can be further reduced by shielding.
Notes: Quali sono le carattericìstiche salienti di un DULs con specifici riferimenti ai LNGS

## Slide 20
Map of the existing or planned worldwide DULs
green dots: the operating facilities
WIPP
Paarl
CJML
Modified from Adam et al. Paarl Africa Underground Laboratory_arXiv:2306.12083v1 [hep-ex] 21 Jun 2023
INFN-Laboratorio Nazionale del Gran Sasso (LNGS) is one of the largest in terms of size and infrastructure.
1400 m (3800 m.w.e. vertical depth)
Muon rate ~ 1/(m2 h)
Surface: 17800 m2
Volume: 180000 m3
Ventilation: 1vol/3hours
Three large experimental halls (~100x20x18 m3)
22 experiments currently running
Easy accessible via highway tunnel (no difference in atmospheric pressure with repect to the above ground facility)che
Notes: Una ventina di DULs nel mondo. LNGS è considerato uno dei più importanti in termini di complessità e dimensioni

## Slide 21
P. Morciano-Cosmic Silence Collaboration
Biology Labs
The LNGS Underground Laboratory and Biology Labs
Notes: Qualche immagine dei LNGS sotterranei e dove sono dislocati i lab di biologia

## Slide 22
LNGS BIOLOGY FACILITIES
CELL CULTURE
Pulex
Underground
Above ground
Cosmic Silence
SMALL ANIMALS
Low Radiation Environment, LRE
Reference Radiation Environment, RRE
Chemistry and Chemical Plant Service
SMALL ANIMALS
CELL CULTURE
Experimental approach: comparison between above ground and underground environments
Notes: Una slide per spiegare che ai LNGS ci sono tre lab di biologia. Uno all’esterno per esperimenti sia su cellule che su piccoli animali e due sotterranei (uno Pulex, dedicato agli esperimenti su cells e l’altro Cosmic Silence dedicato agli studi in vivo (piccoli animali)

## Slide 23
The design of an experiment is a delicate and challenging work
Among the most important ones:
Temperature and light (use of incubators or temperature/light control systems)
Pressure (monitoring)
Air quality (use of filters)
Radon (ventilation systems and monitoring)
Cell culture medium and reagents/food for organisms (purchase and use of the same products for the entire dutation of the experiment)
At doses comparable to the environmental background, there is little effect which can be masked by other health effects
All parameters (biological and physical) that can influence the response of a biological system must be taken into account and possible differences must be minimized in an attempt to make the radiation level the “only” difference between RRE and LRE
As for environmental radiation, dosimetric measurements of components of the radiation spectrum during the experiments are mandatory

## Slide 24
THE LNGS UNDERGROUND AND ABOVE GROUND
BIOLOGY LABORATORIES’ EQUIPMENT
SMALL ANIMAL (Drosophila) LAB:
2 identical refrigerated incubators
CO2 system to manipulate Drosophila
2 Stereo microscopes (one with camera)
Mice rack at LRE(not yet in use)
OTHER GENERAL EQUIPMENTS AND INSTRUMENTS
Refrigerator (4-6°C and -20°C)
Cryogenic storage dewars
Systems for gamma ray modulation: a 10 cm thick lead shield, an ancient iron shielding, Marinelli beakers filled with tuff, a natural gamma emitter
AlphaGUARD device measuring T°, relative humidity and radon concentration (for constant ambient monitoring)
CELL COLTURE LAB:
3 identical CO2 incubators
Biological hoods
2 Inverted microscopes
Optic microscope
Thermostatic water baths
mice rack
Support from LNGS Services: Chemistry & Chemical Plants, Special Techniques for detection of rare events, Computing and Network, Electronics, Accellerators, Mechanics, Industrial Design……
Refrigerated incubator
Biological hood
CO2 incubator
Ancient iron shielding
Gamma rays modulation systems
Notes: L’equipaggiamento e gli strumenti dei lab di biologia

## Slide 25
 | LNGS External (RRE) |  | LNGS Underground (LRE) | 
Photons and directly ionizing cosmic rays (low LET, mostly muons) (nSv/h) | 47a |  | negligible | 
Neutrons (high LET) (nSv/h) | 21b |  | negligible | 
Total -rays (terrestrial, low LET) (nSv/h) | 31a |  | 27a | 
Total low LET dose (nSv/h) | 78 |  | 27 | 
(a) measures with Reuter Stokes, Automess and TLD and evaluation, at the LNGS altitude, based on UNSCEAR 2008 (Vol I. Sources and Effects of Ionizing Radiation; (b) literature data
Dosimetric characterization of
above ground (RRE) and underground (LRE) environments
For further information see: Ampollini M et al. Front. Phys. 2023. doi: 10.3389/fphy.2023.1274110
Radon concentration kept at same level in the two environments (about 15-20 Bq/m3) thanks to an efficient air ventilation system in underground.
Reduction of total low LET dose of about 4 times in underground LRE with respect to the above ground RRE environment (that can be modified using shielding or exposure to natural emitting materials)
Radiation quality different in underground where cosmic ray and neutron contribution is almost negligible
Notes: Caratterizzazione ambientale con i contributi dei singoli componenti dello spettro di radiazione ambientale nei due ambienti esterno ed underground. Riferimento al lavoro che la descrive in dettaglio

## Slide 26
Saccharomyces cerevisiae cultured for 1 week (~120 generations) at LRE and RRE (University of Rome) | Mutation induction (hprt locus) | Satta et al., Mutat Res 1995
Long term experiments (months) |  | 
Chinese hamster V79 cells cultured for up to 9-10 months (>120 generations) at LRE and RRE (RRE: Istituto Superiore di Sanità, Rome; external LNGS laboratory) | Cell growth Antioxidant enzymes activity Apoptosis Mutation induction (hprt locus) | Satta et al., Radiat Environ Biophys 2002 Fratini et al., Radiat Environ Biophys 2015
TK6 human lymphoblasts cultured for up to 6 months at LRE and RRE (Istituto Superiore di Sanità Rome) | Cell growth Micronuclei induction Antioxidant enzymes activity | Carbone et al. Radiat Environ Biophys 2009
Short term experiments (weeks) | Long term experiments | 
A11 mouse hybridoma cells (short term experiments, few weeks) RRE (Istituto Superiore di Sanità Rome) | Cell proliferation caspase-3 activation PARP1 cleavage | Fischietti et al., Front Public Health 2021
Drosophila melanogaster (RRE: L’Aquila University) | Life span Ferility DNA repair (mutants) | Morciano et al., J. Cell Physiol. 2018 Morciano et al., Radiat. Res. 2018 Esposito et al., Front Public Health 2020
Drosophila melanogaster (RRE: external LNGS laboratory) | Chromosome breaks DNA repair (mutants) | Porrazzo et al., Int. J. Mol. Sci. 2022 Morciano et al., Frontiers in Physics 2023 Ampollini M. et al Frontiers in Physics 2023
LRE: Low Radiation Environment
RRE: Reference Radiation Environment
Fly
Summary of in vitro and in vivo experiments at LNGS
Cultured mammalian cells
Yeast
Notes: Una slide che mostra tutte le pubblicazione dell’attività di radiobiologia dal 1995 ad oggi

## Slide 27
The DISCOVER22 experiment
“DNA Damage and Immune System COoperation in
VEry low Radiation environment”
Interdisciplinary experiment divided in three work packages (WP)
WP1: Radioimmunobiology: in vitro studies (cells)
Task 1.1 - Immune system pathway activation
Task 1.2 - Modulation of immune system’s differentiation
WP2: Radioimmunobiology: in vivo studies
Task 2.1 – Analysis of the immune system genes in fruit fly, D. melanogaster
WP3: Physic studies
Task 3.1 - Microdosimetry
Task 3.2 - Biophysical modelling
INFN-CSN5 funded experiment (2023-2025)
For further information see: Morciano P, et al. Front. Phys 2023. doi: 10.3389/fphy.2023.1263338
Notes: L’attuale esperimento interdisciplinare di Commissione 5 in corso e le istituzioni coinvolte (Pubblicazione di riferimento)