## Slide 1: Radiation Field Simulation in GIF ++
Nicola Ferrara, INFN and Politecnico of Bari
Gabriella Pugliese INFN and Politecnico of Bari
Giuseppe Iaselli, INFN and Politecnico of Bari
Dayron Ramos, INFN and Polytecnic of Bari

## Slide 2: Geant4 GIF++ simulation code Source: Pfeiffer Dorothea Software developed in GEANT4-10.0 to simulate GIF++ radiation background [ref]
Software upgrade in the framework of the new DRD1 «collaboration».
Main steps:
Transition from GEANT4-10.0 to GEANT4-11.0
Description of the new bunker geometry
[ref] https://gif-irrad.web.cern.ch/documents/1-s2.0-S0168900217306113-main.pdf

## Slide 3: Transition from GEANT4-10.0 to GEANT4-10.7 (1)
New GEANT4 version: geant4-10-07-patch-03 [MT]
Change of one class in the GIF++ project ()
Issue: in class GIF++UserScoreWriter,
the typedef MeshScoreMap becomes defined in G4VScoringMesh
Solutions: Geant4 upgrades to G4VScoringMesh::MeshScoreMap

## Slide 4: Other Changes:
MeshScoreMap fSMap = fScoringMesh->GetScoreMap();
G4VScoringMesh::MeshScoreMap fSMap = fScoringMesh->GetScoreMap();
std::map<G4int, G4double*> * score = msMapItr->second->GetMap();
std::map<G4int, G4StatDouble *> &score = *(msMapItr->second->GetMap());
std::map<G4int, G4double*>::iterator value = score->find(idx);
std::map<G4int, G4StatDouble *>::iterator value = score.find(idx);
Transition from GEANT4-10.0 to GEANT4-10.7 (2)

## Slide 5: GIF++ geometry UPDATE
STEP file was opened with an open source FreeCAD to obtain the layout of the bunker
A new file GDML with FreeCAD was created and the geometry was described using a box model.
Note: The format of the GDML file is not compatible with the one used by GEANT https://gdml.web.cern.ch/GDML/
Some manipulation needed to solve the issue

## Slide 6: Upgrade geometry: layout
CAD Gif++ layout
GEANT gdml layout

## Slide 7: Preliminary Results
Simulated gamma: 2 106
Flux in the range 600-662 keV

## Slide 8: Dose calculation
Simulation with probe: 5*10-12 Gy
Simulation with SD in AIR : 2.73*10-24 Gy
Calculation of time:
2*106 gamma correspond to
Calculation of Rate Dose:
Rate Dose:
Cube of air of 10 cm

## Slide 9: Dose calculation
Cube of air of 10 cm
10-9

## Slide 10: Next steps
Start simulate filters
Simulation of different detectors installed inside the GIF
Validation of the simulation by comparing the estimated dose with some measurements done in several points inside the bunker

## Slide 11: Conclusion
A first simulation of the bunker succesfully done.
A simulation of gamma dose with sensitive volume.

## Slide 12: Backup

## Slide 13: Dose comparison
New Rate Dose with detector
Rate Dose Uc =