## Slide 1
Review of the Ignition campaign on the National Ignition facility
Sébastien Le Pape
hall laser LULI2000
enceinte d'expérience MILKA
compresseur APOLLON

## Slide 2
How to produce energy through fusion reaction

## Slide 3: On December 5, 2022, NIF exceeded the threshold* for ignition, with 3.15 MJ of fusion output for 2.05 MJ laser delivered
NIF shot N221204 achieved a target gain of 1.5 and a capsule gain of ~12
Preceding experiments quickly progressed from 100’s kJ – 1.35 MJ 1,2,3 and built understanding of ignition.
Achieving such yields required effort to improve:
  Target quality
  Laser accuracy and increased energy delivery
  Diagnostic capabilities
  Design
Improved understanding has led to design refinements enabling 5 shots that have exceed a MJ since Fall 2022
3
2.8
2.6
2.4
2.2
2.0
1.8
1.6
1.4
1.2
1.0
0.8
0.6
0.4
0.2
0
Fusion yield (MJ)
2011
2012
2013
2014
2015
2016
2017
2018
2019
2020
2021
2022
Year
Max laser energy available

## Slide 4: There are at least three ways to achieve nuclear fusion
Density
Temperature
Confinement time
104 x solid
1 keV
105 years
solid / 108
10 keV
seconds
103 x solid
10 keV
10’s ps
by Laser Implosion

## Slide 5: The idea of ICF is to compress fuel to thermonuclear conditions

## Slide 6
The capsule velocity follows a simple rocket model
Mass
Momentum
Energy
Starts with 3 conservation equations
This leads to the rocket equation
Where m0 is the initial mass and m
the initial minus the ablated mass
Vexp = expansion velocity of ablated material
This means the more you ablated the faster you go but hydro instabilities might kick in
You can also write

## Slide 7
Hydrodynamic instabilites : Rayliegh-Taylor
Dense matter pushes on light matter
g
The growth of the surface perturbation is exponential at a rate exp (
where = , g is gravity, is the spatial wave number and A the Atwood number =
So high R/

## Slide 8
Hydrodynamic instabilites : Rayliegh-Taylor
Why does it matter?
Alter the quality of the piston that compresses the fuel
Increase the losses due to radiation and thermal conductivity
Lead to loss of efficient heating by alpha particles
Caused by
- Defect of the target surface
- Defect in the irradiation homogeneity

## Slide 9
Ignition is about power balance in the hot spot
**H. Abu-Shawareb et al., Physical Review Letters 129, 075001 (2022).
Fusion energy > losses if Pressure (P) X confinement time (t) exceeds Lawson’s criterion
pdV provides heat until minimum volume, then becomes a loss

## Slide 10
DT ice
Ablator
(CH, HDC)
~20-30x convergence
~40 µm
~1 mm radius
>380 km/s
DT gas
mass of DT ~200 mg -> 67 MJ
peak velocity ~380 km/s
⇒ fuel kinetic energy ~14 kJ
energy needed to heat 200 µg to 5 keV = 116 kJ
but we only need to heat enough DT for rR~0.3 g/cm2
if rhs~100 g/cm3 ⇒ rhs~30 µm, and mhs~11 mg, so energy required in the hotspot ~6 kJ
(hence, the term central hotspot ignition)
Cold fuel
rR~1 g/cm2
100’s eV
Hotspot
T>5 keV
rR>0.3 g/cm2
Hot spot central ignition

## Slide 11: There are at least three ways to achieve nuclear fusion
Density
Temperature
Confinement time
104 x solid
1 keV
105 years
solid / 108
10 keV
seconds
103 x solid
10 keV
10’s ps
by Laser Implosion

## Slide 12
~600 MJ of electricity is used to generate 1.8MJ/480TW
192 Beams
Energy: 1.8 MJ
Power: 500 TW
(1000x the power in the US electrical grid)
Frequency Tripled Nd Glass
Wavelength: 351 nm
Pulselength: ~25 ns

## Slide 14: ~1.3MJ of X-rays is generated by the interaction of the laser with a high Z cavity
Laser pulse
Radiative temp
Major challenge: laser beam pointing and energy repartition in the hohlraum must be designed to symmetrically drive the capsule

## Slide 15: ~150 KJ of energy is absorbed by the 2 mm diameter low Z capsule
X-ray self-emission image from a DT implosion at peak compression
Diameter ≈ 50 μm
2 mm

## Slide 16
~20 KJ of kinetic energy is reached at peak velocity of the capsule
Major challenge: The capsule must be designed and driven to withstand hydro instabilities

## Slide 17
More than 800 experiments conducted over a decade enabled an increase in target gain of >1000X and fusion ignition
Increased energy coupling

## Slide 18: Dozens of diagnostics are applied to each experiment improving understanding
Shock Speeds, Timing
t
Liquid D2
Hot Spot Electron Temperature and Impurities
Yield / Fuel Uniformity
DT* Fuel Uniformity
Hot Spot and Fuel Shape
Burn Width, Bang Time
8.8
9.0
9.2
t (ns)
Ion Temperature,
Hot Spot Velocity, Fuel Areal Density, Yield
t (ns)
Spectrum
600
500
Hohlraum Radiation Flux
0
5
10
15
20
25
Time (ns)
0
50
100
150
200
250
300
Tr source (eV)

## Slide 19: A diagnostics suite to evaluate the degradation mechanisms
Hotspot Drift Velocity
(Vhs[km/s])
Hotspot bulk velocity from neutron Doppler Shift (NTOF) along 5 directions
Mix Mass
[ng]
Synthetic tomographic reconstruction and spectroscopy
Neutron
X-ray
Hotspot Symmetry
(P2[µm])
Neutron and X-ray imagers at peak emission
(Plot: J. Ralph)
(Plot: A. Pak)

## Slide 20
Is this scheme viable a route to clean energy?
1- Indirect drive is not energitically favorable
      1.9 MJ only 200 kJ absorbed by the capsule
2- target are very complex
3- highly non linear regime -> need of a more robust regime
350 km/s
230 km/s
1.35 MJ

## Slide 21
Alternate way: decouple compression from heating

## Slide 22
Fast ignition scheme leads to higher mass spot
Higher mass leads to higher yield
Hot spot: Isobaric spot from implosion
F.I.: Isochoric spot from fast electron heating

## Slide 23
Conclusion
Ignition has been achieved after 13 years of experiments on the NIF
Higher gain up to 10 MJ are envisioned in the near future
Europe has the expertise and is getting organized toward an IFE initiative (Hiper +)
Startups are emerging around the world