## Slide 1
Gabriele Cristoforetti
Intense laser irradiation Laboratory
Istituto Nazionale di Ottica
CNR – Pisa, Italy
gabriele.cristoforetti@cnr.it
www.ilil.ino.it
Novel “Octopus” diagnostics for the investigation of side stimulated Raman scattering at ICF laser intensities
ICFDT7 - 7th International Conference on Frontier in Diagnostic Technologies

## Slide 2
Relatore:
Evento:
Nome relatore
New laser sources and technology for ultraintense lasers
Laser-plasma acceleration
Flash radiotherapy research
Laser-plasma interaction for direct drive schemes of Inertial Confinement Fusion
PEOPLE
  Leonida A. GIZZI (head)
Gabriele CRISTOFORETTI
Luca LABATE
Fernando BRANDI
Petra KOESTER
Federica BAFFIGI
Lorenzo FULGENTINI
Daniele PALLA
Martina SALVADORI
TOPICS
http://ilil.ino.it
The Intense Laser Irradiation Lab
@ INO-CNR, Istituto Nazionale di Ottica, Pisa (Italy)
Sub-PW Experimental Laser Facility
Laser Front End
10 TW, 10 Hz
Power Amplifier
up to 250 TW
Radiobiology
Laser-Driven
Particles and Radiation
Shielded target Area for PW experiments
Room Control
Costanza PANAINO
Simona PICCININI
Emma HUME
Alessandro FREGOSI
Federico AVELLA
Davide GREGOCKI
Simon VLACHOS
Gianluca CELLAMARE
Paolo TOMASSINI

## Slide 3
Direct-Drive Inertial Confinement Fusion
Inertial Fusion Energy (IFE) schemes investigated in Europe are based on Direct-Drive approach
Coupling efficiency 4-5% Compared to Indirect-Drive (NIF) we can compress larger mass capsules and we need lower pressures to get ignition 140 Gbar vs. 350 Gbar
simpler targets, more compatible with high-repetition rate operation and requirements of fusion reactors.

## Slide 4
Laser Plasma Interaction
In ICF conditions, for > , several parametric instabilities (LPI) are driven in the plasma corona, producing:
the scattering of a significant percentage of laser energy (SRS, SBS)
the unbalance of multiple laser beams irradiation (CBET)
Small scale modulation of beam irradiation (filamentation)
Suprathermal (or hot) electrons, produced by damping of SRS and TPD plasma waves, prehating the fuel
Our
Job
Froula et al., Plasma Phys. Control. Fusion 54 (2012) 124016
Laser

## Slide 5
Side SRS: the most elusive LPI
The exit angle can be large and depends only on the density where SSRS is driven and on the density profile
SSRS grows more strongly along the spot in the S-direction and is preferentially scattered in the S plane
SSRS growth can be limited by the spot size or the density scalelength, depending on interaction conditions
Polarization
direction
P
SSRS growth
S
Laser spot
Back SRS
EPW
Side SRS
EPW
EMW0
EMW0
EMW1
EMW1
n1 n2 n3 n4
l1(n1)
l2(n2)
l3(n3)
l4(n4)
Laser

## Slide 6
Side SRS: experiments
Early studies in the 70s:
SSRS can have a dramatic
impact on ICF performance
Very few observations in the 80s
Drake, PRL 53, 1739, 1984; Phy. Fluids, 31, 3130, 1988; Phys. Fluids B 1, 1082, 1989
ESRSS ≈1/2 EBRS
I = 1014 – 2x1016 W/cm2 no RPP
No more
investigation
Recent experiments at Omega and NIF identify SSRS to be relevant and maybe dominant
Michel, Phys. Rev. E 99, 033203 (2019), Rosenberg, Phys. Plasmas 27, 042705 (2020), Hironaka, Phys.Plasmas 30, 022708 (2023)
TODAY
Our experiment at PALS in 2019
G. Cristoforetti et al., HPLSE, (2019), Vol. 7, e51
BSRS
SSRS
l0 = 351 nm L = Ly = 300 mm n = 0.08 nc
I > 5x1015 W/cm2
Why few observations ?
Observation limited by collisional absorption of scattered light
Limited by the beam size  high threshold
Intrinsic difficulty to measure and quantify light scattered in the whole solid angle

## Slide 7
The VULCAN experiment (2023)
K. Glize P.I.
LASER IRRADIATION DESIGN (PLANAR)
4 driver/heating beams (long beams)
E=250 J x 4, l=1053 nm, 3 ns
FWHM=800 mm, I ≈ 3x1013 W/cm2
interaction beam B8 bypassing compressor
E= 100 J, l=527 nm, 15 ps
FWHM ≈ 300 mm, I ≈ 6x1015 W/cm2 , f/# =3
A quarter of a sphere of radius 40 cm
Distribution of fibers in the solid angle
Angular resolved SSRS spectra
Conditions of large spots and large density wavelength (long plasmas)

## Slide 8
The PALS experiment (2023)
Aim : Investigate angular distribution of SSRS light and dependence on laser spot size/shape and density scalelength
G. Cristoforetti1, E. Hume1, S. Agarwal2,3, D. Batani4, D.E. Carleton2, M. Cervenak5, P. Devi2,3, R.Dudzak2,5, D. Ettel2, P. Gajdos5, K. Glize6, S. Jelinek2,3,5, L. Juha2, P. Koester1, M. Krupka2,5, M. Krus5, H.Larreur4,7, G. Malka4, D. Mancelli8,9, P.E. Masson-Laborde10, A. Morace2, J. Myatt11, Ph. Nicolai4, O. Renner2,5,12, D. Singapulli4, S. Singh2,5, M. Tatarakis8, Y. Wang13, N. Woolsey13, X. Zhao14, and L.A. Gizzi1
1 INO-CNR, Pisa, Italy
2 Institute of Physics of the CAS, Prague, Czech Republic
3 Faculty of Mathematics and Physics, Charles University, Prague, Czech Republic
4 Université de Bordeaux, CNRS, CEA, CELIA, Talence, 33405, France
5 Institute of Plasma Physics of the CAS, Prague, Czech Republic
6 Rutherford Appleton Lab, CLF, Didcot, UK
7 University of Salamanca, Salamanca, Spain
8 Institute of Plasma Physics and Lasers, Hellenic Mediterranean University, Rethymnon, Greece
9 Department of Electronic Engineering, Hellenic Mediterranean University, Chania, Greece
10 CEA, DAM, DIF, Arpajon, France
11 University of Alberta, Edmonton, Canada
12 The Extreme Light Infrastructure ERIC, Dolni Brezany, Czech Republic
13 York Plasma Institute, University of York, York, United Kingdom
14 Shanghai Jiao Tong University, Shanghai, China

## Slide 9
Experimental Setup: the «Octopus»
TCC
Arm «S»
Arm «P»
Fibers coupled
to Spectrometer
Laser Beam
Czerny Turner
spectrometer
CCD
slit
q
Polar
angle
f
Azimuthal
angle

## Slide 10
LASER

## Slide 11
Other diagnostics for characterizing laser-plasma interaction
l = 438 nm
Laser Energy : 100 – 230 J
Duration : 270 – 350 ps
Intensity : (0.5-1.5) x 1016 W/cm2
Shots @ 3w

## Slide 12
Cu
THICK (multilayer) TARGETs
Laser
CH - PyC
Al coating
circular
60 mm
100 mm
40 mm
P
small SSRS growth
large SSRS growth
P
P
medium SSRS growth
elliptical
elliptical
Interaction Conditions
Dependence on focal spot size and shape
Dependence on electron density scalelength
20, 60 or 100
5
mm
mm
THIN FOIL TARGETs
CH - PyN
Al coating
5
mm
CH - PyN
Al coating
3
mm
CH - PyN
Al coating
2
mm
(at 100 ps after the laser peak) | 63 | 76 | 86 | 115
 | 63 | 76 | 86 | 115
S
S
S
Focal spot shape is changed by laser phase manipulation
Density scalelength varies because of the different plasma hydrodynamics

## Slide 13
Side SRS spectra
(thick target)
S
SSRS spectrum is evident
There is a clear relation
l - q, i.e. n - q
The SSRS is much stronger
in S-plane vs. P-plane

## Slide 14
Side SRS spectra
(thick target)
S
w/2 (TPD) signal at
small angles as expected
Near Backward SRS
at small polar angles.
Similar in P and S planes
FABS spectrum
Backward SRS

## Slide 15
Dependence on spot size
SSRS intensity increases with the spot size D in the S direction
100
60
20
D (mm)
RPP2 S
RPP1
RPP2 P
From raytracing in 2D density maps we find SSRS resonance length
Lres ≈ 70 mm
RPP1, RPP2P
D < Lres
SSRS growth is limited by D
D = 100 mm
D = 60 mm
D = 40 mm

## Slide 16
Dependence on density scalelength L
(thick vs. thin targets)
Side SRS
Thick Target: Al flash + 60 mm CH + 7 mm Cu
Thin Target: Al flash + 2 mm CH
BSRS and Near-BSRS is strongly affected by density scalelength
L ≈ 60–80 mm
L ≈ 80–300 mm
RPP2 S & P
SSRS is not affected by density scalelength
BSRS - FABS calorimeter
RPP1
Near BSRS - Octopus
SSRS - Octopus
BSRS is limited by L
SSRS is limited by the spot size
L

## Slide 17
Octopus diagnostics can be easily used in laser-plasma experiments and allows angular-resolved spectroscopy of Side Stimulated Raman Scattering along polar angles in P and S planes
The combination of Octopus with focal spot manipulation by RPP technology allows the investigation of 3D angular emission and its dependence on laser spot geometry and laser polarization
In next step we aim at quantify SSRS efficiency, which implies an upgrade of Octopus diagnostics with more arms/fibers, as in the Vulcan experiment.
Conclusions

## Slide 18
References:
More info at www.ilil.ino.cnr.it
G. Cristoforetti et al., Euro Phys. Lett., 117, 35001, 2017
G. Cristoforetti et al., Phys. Plasmas 25, 012702, 2018
D. Batani et al., Nucl. Fusion, 59, 032012, 2019
G. Cristoforetti et al., HPLSE, (2019), Vol. 7, e51
S. Baton et al., High Energy Density Physics 36, 100796, 2020
P. Koester et al., Review of Scientific Instruments 92, 013501, 2021
G. Cristoforetti et al., HPLSE, (2021), Vol. 9, e60
This work has been carried out within the framework of the EUROfusion Consortium, funded by the European Union via the Euratom Research and Training Programme (Grant Agreement No 101052200 — EUROfusion). Views and opinions expressed are however those of the author(s) only and do not necessarily reflect those of the European Union or the European Commission. Neither the European Union nor the European Commission can be held responsible for them. The involved teams have operated within the framework of the Enabling Research Project: ENR-IFE.01.CEA “Advancing shock ignition for direct-drive inertial fusion"
THANK YOU FOR YOUR ATTENTION !
T. Tamagawa et al., Rev. Sci. Instrum., 93, 063505, 2022
G. Cristoforetti et al., HPLSE, Vol. 11, e24, 2023
K Kawasaki, Phys. Rev. Research 5, 033051, 2023
F. Wasser et al., Rev. Sci. Instrum. 94, 093503, 2023
G. Cristoforetti et al, Sci. Rep., 13, 20681, 2023
F. Wasser et al., Phys. Plasmas 31, 022107, 2024
*** papers on SSRS experiments in preparation ***

## Slide 19
Parametric instabilities
Parametric Instabilities are 3-waves coupling processes where the e.m. laser excites ion-acoustic or electron plasma waves
Thresholds are given by the damping of daughter waves
In inhomogeneous plasmas, the threshold of convective instabilities depends on the resonance region (v)
+
+
Stimulated Raman Scattering (SRS)
Stimulated Brillouin Scattering (SBS) &
Cross Beam Energy Transfer (CBET)
Two Plasmon Decay (TPD)
~1014 W/cm2
~1014 W/cm2
~1015 W/cm2
~1014 W/cm2
absolute
convective
CBET

## Slide 20
Side SRS spectra
(thick target)
Assuming 1D plasma
Why the angular distribution is different from the expected one ?
Plasma curvature affecting refraction?