## Slide 1
New diagnostic capabilities of DIII-D
DFSS
LLAMA
by​
Suk-Ho Hong​
General Atomics​
Many thanks to DIII-D team
​
​ ​
Presented at the ICFDT7 Conference
Oct 22, 2024
Te (eV)
2D DTS
ITER ECH Mark 3
ITER ECH
Mark 4

## Slide 2: Diagnostic development drives realization of fusion energy
The physics measurements are key to the success of the science program
DIII-D excels at developing innovative diagnostic sets for understanding physics and model validation for ITER and FPP
Multiple new diagnostic technologies to be developed in connection with public-private sectors.
New 2D Divertor TS
innovation
Strike point sweeping
Real-time 2D measurement

## Slide 3: Understanding physics and model validation for ITER/FPP are challenging in multiple ways
Multiple challenges arise
Many elements of solution trade-off against each other
Must explore in reactor relevant physics regimes
Stable core
Stability, stress heat loads
Transients
Disruptions ELMs, robust control
Exhaust handling Dissipative divertor
Wall Robust materials, PMI, mitigation
Core-Edge Integration
Interactions at high opacity, density & performance
High confinement
Compactness
Important to study these issues in an integrated & flexible device with innovative diagnostics, integrated and collaborative efforts
Also, vital to develop new diagnostic technologies for the reactor

## Slide 4: DIII-D has a Leading Diagnostic Set To Test Physics Models
Comprehensive diagnostics
  Profiles: current, rotation, Ti, Te, ne
  Magnetic sensor arrays
  Turbulence suite k=0.1-100cm–1
  Fast ion spectra & losses,
  Neutrons, g-ray imaging, SXR, ICE
  Bolometry, spectroscopy – UV, visible
  Infra red, Langmuir probes
Injectors and interactions:
  D2, Ar, Ne, Li/B granules, shattered
  Laser blow off system
  Material sample exposure facilities
2D Thomson scattering
g imaging
Turbulence Diagnostics
Remotely observe and measure multiple plasma physics phenomena

## Slide 5: DIII-D diagnostic set is the result of an integrated and collaborative effort
Over 130 participating institutions including universities, national laboratories, and industry, 17 institutions provide over 100 diagnostics
As of May, 2022

## Slide 6
Recent Diagnostic Innovation to Enable Research Goals
In DIII-D

## Slide 7: 2D real-time Divertor Thomson Scattering System
Gain the capability to investigate solutions from divertor detachment to core-edge integration in a wide range of parameters
Real-time 2D measurement of ne and Te at lower divertor down to <1eV
Flexible positioning of 82 measurement positions
More detailed infos in the invited talk of Fenton Glass
New 2D Divertor TS
In-vessel prism block
re-directs laser vertically
Ex-vessel fast steering mirror directs laser to prism block positions
Paul Schroeder et al. Rev Sci Instrum. 94 (2023) 23504

## Slide 8: Doppler-free saturation spectroscopy (DFSS)
DFSS is a laser-based technique used to measure spatial resolved, high-resolution spectral data to identify RF structure in SOL and its propagation
Requires two counter-propagating laser beams (pump/probe) that cross at a single point (i.e. the measurement point)
Helicon wave E-field vector and magnetic field vector will be measured
Under commissioning
DFSS Pump and Probe Laser Beams
David Su et al., IEEE Transactions on Plasma Science, doi: 10.1109/TPS.2024.3386594. k

## Slide 9: Hydrogenic Lyman alpha measurements to diagnose neutrals (LLAMA and ALPACA)
Investigate neutrals in upper and lower main chamber
Measure Lyman-α spectral line (λ=121 nm) and cut out extra bands
Study pedestal fueling in different divertor configurations
Explore high field/low field asymmetries
LLAMA is in routine operation
ALPACA in commissioning
A. Rosenthal, et al. Rev. Sci. Instr. (2021)
F.M. Laggner, et al. Rev. Sci. Instr. (2021)
SOLPS
LFS
HFS
LFS
HFS
LLAMA
ALPACA

## Slide 10: Other new diagnostics installed: ITER ECH detectors, TRIP, Textured tile version 2
Two additional ITER Electron Cyclotron Heating (ECH) detectors have been affixed to a lower port of the vessel.
The Radial Interferometer Polarimeter (RIP) has undergone a successful upgrade to have a toroidally displaced chord to measure high n numbers up to 50.
The textured Tile measures the campaign-integrated effect of the charge exchange neutral on the erosion/redeposition.
ITER ECH Mark 3
ITER ECH
Mark 4
TRIP
Original
RIP array
Textured tile
Version 2

## Slide 11
Developing New Reactor
Diagnostic Technology

## Slide 12: Developing new reactor diagnostic technology: FPP diagnostics will be very different from present-day and ITER
Diagnostics will be exposed to more harsh environments
  Neutron irradiation, higher heat and particle flux, thermomechanical stresses, relativistic effects
FPP will have a minimum set of diagnostics during the operation
  Very small and restricted spaces due to T breeding
  Miniaturization & modularization of essential diagnostics
Operating in the FPP reactor environment brings new challenges to the controls and diagnostics
J.-C. Jaboulay et al. / Fus Eng Des 124 (2017) 896–900

## Slide 13: DIII-D plays essential role in advancing Technology Readiness Levels (TRLs) of diagnostics for plasma controls of FPP
Decision to construct
Conceptual and preliminary
design review
Start of non-nuclear operation
Start of nuclear operation
NASEM report marge engineering design and construction in 5 years.
DIII-D 5-year plan FY24-FY29 (TRL~6)
Feasible plasma scenario, blanket concept, power conversion, fuel cycle, remote handling, safety analysis, machine protection, and diagnostic design must be finalized before the FPP engineering design phase (critical point).
Synthetic diagnostics combined with validated models predict plasma behavior for the plasma control and machine protection.
(TRL>6)
Critical point
NASEM report
(TRL>7)

## Slide 14: Diagnostic developments for the commercialization of fusion energy
DIII-D can advance TRLs only up to 6 (or early phase of 7)
  Advancing TRL 7 to 9 will be part of the FPP development and operation
  ITER could cover some of TRL 7
Miniaturization, modularization, and standardization of essential diagnostics are absolutely necessary.
As a new testbed, DIII-D will offer a flexible environment for the miniaturization, modularization, and standardization of essential diagnostics toward the commercialization of fusion energy

## Slide 15
TRL 3
TRL 4
TRL 5
TRL 6
TRL 2
Diagnostic solutions for plasma and burn control
Diagnostic solutions for Machine protection
Technology
Challenges
Hands-off and low-maintenance diagnostics
Identify the required maintenance schemes, control functions, and operation
[FY24]
[FY28]
Qualification test of plasma control, machine protection, and survivability of diagnostics
(TRL 6)
Remote handling /maintainability of diagnostics
(TRL 6)
[FY28]
Example of advancing TRL: Resolve diagnostic technology compatible with reactor constraints
[FY24-FY25]
Identify the required control functions and operational control solutions
[link to 3.1 Control functions required for fusion reactor]
goal/achievement
goal/achievement
goal/achievement
goal/achievement
goal/achievement
Conceptual design of a prototype remote/robotic hardware
[FY25]
[FY26]
Select candidate diagnostics and assessment of new approaches
[FY26]
Engineering design of a prototype remote/robotic hardware
Develop new diagnostic prototypes, e.g. fast wave interferometer and reflectometer
[FY27]
Develop new diagnostic prototypes, e.g. microwave thermal imaging
[FY27]
Demonstrate the remote maintainability of diagnostics at DIII-D
[FY27-FY28]

## Slide 16: EMI-free radiated power measurements by Fiber-Optic Bolometer (FOB) for FPP
Conventional bolometers suffer from temperature variation and electromagnetic interferences (EMI).
A Fabry-Perot interferometer to convert incident radiation into temperature variations.
Degradation of fibers by neutron irradiation can be calibrated (do not measure light intensity)
Images from Dr. Ming Han, May 2022

## Slide 17: Diag2Diag: Data-First Approach to Prediction of Fusion Dynamics and Reactor Scenario Design
Azarakhsh Jalalvand, SangKyeun Kim, Jaemin Seo, Qiming Hu, Max Curie, Peter Steiner, Andrew Oakleigh Nelson, Yong-Su Na, Egemen Kolemen, submitted to Nature

## Slide 18: Diag2Diag: Data-First Approach to Prediction of Fusion Dynamics and Reactor Scenario Design

## Slide 19: Diag2Diag: Data-First Approach to Prediction of Fusion Dynamics and Reactor Scenario Design
Comparison of the synthetic super resolution Thomson Scattering (SRTS) and the TS fired in “bunch mode” for measuring the electron density in DIII-D shot 153761 at the pedestal (Z=0.71m)
SRTS captures ELMs in comparison to the measured TS even in “bunch mode”.

## Slide 20: DIII-D Diagnostic Set is the Essential Key to the Realization of Fusion Energy
DIII-D provides a critical platform to develop vitally needed diagnostics for FPP
Maintaining top-quality diagnostics is important not only for accomplishing the DIII-D’s national mission but also for training the next generation of diagnosticians
Diagnostic innovation will provide critical insights in broader research program