## Slide 1
Tadas Pyragius, Graham Naylor
A new Near InfraRed Dispersion Interferometer for ST40 and future fusion reactors

## Slide 2
SMM
NIR
Refractive index
of plasma
(Near Infra-red laser interferometer)
(Sub milli-meter wave interferometer)
Effect of the plasma density on refractive index (speed of light)

## Slide 3
An interferometer can measure the plasma density by measuring
the change in path length of a light beam when propagating
through the plasma.
This is due to the change in refractive index with electron density
Approximation for frequencies
Well above the plasma frequency
Phase shift is smaller
for shorter wavelengths
Parasitic contribution to phase measurement
Bigger for smaller wavelengths
(Systematic error caused by thermal drifts and vibrations)
Interferometer measures plasma density

## Slide 4: Two wavelength (colour) interferometry
The systematic error caused by geometric path lengths can be compensated
by measuring at two wavelengths and using the wavelength dependence

## Slide 5
AOM
w+dw
=> Phase measurement at optical frequencies converted to a phase measurement at the IF (typically ~100MHz)
Measurement = Signal - Reference
Interference fringe= Scene Beam Reference Arm
Density phase shift = Beat Note phase - AOM drive phase
Window
AOM
l1,l2
w1,w2
(l1,l2)
+2pdd/l
(vibration)
Differential phase shift= Phase shift l1 - Phase shift l2
AOM=Acousto-Optic Modulator
How to measure phase change with an interferometer?

## Slide 6: Dispersion Interferometer benefits
Two wavelength interferometers are used to compensate for systematic errors, but normally require independent reference arms that also need to be kept very stable otherwise they will contribute geometric path length changes that are not compensated
A dispersion interferometer does not need a separate reference beam as it launches two wavelengths (the main laser beam and its second harmonic) that are in phase. The phase differential between these can be taken to measure the dispersion due to the plasma.

## Slide 7
https://en.wikipedia.org/wiki/Second-harmonic_generation
Two wavelengths in phase and co-linear
Second Harmonic generation

## Slide 8: Why go to shorter wavelength?
Advantages:
Sources and detectors commonly available
Frequency doubling much more efficient
Reduced chance of loss of signal and phase due to refraction of the beam away from the detector by the plasma (aka ‘fringe jump’)
Beams can go through small openings: propagate over long distances with small transverse dimensions
But note this is also a problem around 5mm!
Disadvantages:
Phase shift is smaller (Need to measure phase to high precision)
Subject to perturbation due to refraction in air
(Second source of systematic error)

## Slide 9: Effect of the refractive index (dispersion) of air
From:
A. Voronin & A. M. Zheltikov
” The generalized Sellmeier equation
for air” Nature Scientific reports DOI: 10.1038/srep46111

## Slide 10: A NIR Dispersion Interferometer (NIRDI) operating at 1.56mm
NIRDI beat signal

## Slide 11
Software Defined Radio on FPGA
- for phase measurement

## Slide 12: NIRDI Performance:
( 17m path in air )

## Slide 13: Systematic errors – ii) Air turbulence, beam stability
Optical table covers off (aggressive air conditioning
Optical Covers On no beam stabilisation
Optical table covers on, beam stabilisation on

## Slide 14
Summary and conclusions
The dispersion interferometer configuration cancels almost completely systematic errors due to mechanical motion of mirrors (eg vibrations)
A residual systematic error is still present due to atmospheric dispersion (this is tolerable for short path lengths such as ST40, but long paths will need to be carefully controlled using beam path tubes and perhaps windows/baffles to minimise air current across the laser beam path).
Operating a dispersion interferometer at a Near Infra-Red wavelength produces a robust and compact method for determining plasma density