## Slide 1
Diagnostics and control at FCC
Daniele Butti, CERN – Beam Instrumentation group
with many thanks to
B. Paroli, M. A. C. Potenza, M. Siano (Università degli Studi di Milano)
U. Iriso, A. A. Nosych, J. Nunez, E. Solano, L. Torino (ALBA-CELLS)
T. Lefevre, S. Mazzoni, A. Schlögelhofer, G. Trad (CERN)
7th International Conference on Frontier in Diagnostic Technologies
22nd October 2024

## Slide 2: Outline
Future Circular Collider
Diagnostics for FCCee
transverse diagnostics
synchrotron radiation diagnostics
X-ray Heterodyne Near Field Speckles
measurements at undulator beamline
future dipole beamline
development of optimized target materials
Conclusion

## Slide 3: Future Circular Collider
LHC
27 km
FCC
90 km
Proposal for CERN next-generation flagship collider after LHC era
Circular machine with four major experiments, commensurate to the size of the current CERN community
Multi-stage facility
FCCee a ~100 GeV electron-positron collider for ultra-precise measurements of Higgs and EW parameters
FCChh a ~100 TeV hadron collider for direct exploration of next energy frontier
end of Feasibility Study
FCCee construction
FCCee operation
FCChh
Project timeline
2025
~ 2030-2045
~ 2045-2060
> 2070
F. Gianotti
FCC week 2024
Geneva

## Slide 4: FCCee machine parameters
Parameter | Unit | Z | WW | HZ | ttbar
synchrotron radiation power | MW | 50 |  |  | 
beam energy | GeV | 45.6 | 80 | 120 | 182.5
beam current | mA | 1270 | 137 | 26.7 | 4.9
number bunches |  | 11200 | 1780 | 440 | 60
horizontal emittance | nm | 0.71 | 2.17 | 0.71 | 1.59
vertical emittance | pm | 1.9 | 2.2 | 1.4 | 1.6
bunch length with SR / BS | mm | 5.6 / 15.5 | 3.5 / 5.4 | 3.4 / 4.7 | 1.8 / 2.2
luminosity | 1034 cm-2s-1 | 140 | 20 | 5.0 | 1.25
integrated luminosity | ab-1/yr/IP | 17 | 2.4 | 0.6 | 0.15
Four operational modes to maximize physics output
→ changing energy (and current) at fixed SR power
4 years
5x1012 Z
LEP x105
2 years
>108 WW
LEP x104
3 years
2x106 H
5 years
2x106 tt pairs
M. Benedikt
FCC week 2024

## Slide 5: Diagnostics for FCCee
Inverse Compton Scattering for polarimetry and energy calibration
beam
laser
Compton photons
Compton electrons
Many challenges for diagnostics
scale → huge distributed systems
high radiation environment and power loads → critical rad-hardness and stability
high precision measurements → same or better demands than smaller facilities
high reliability → critical for smooth operation
cost and sustainability → little margin with such big machine
Conventional instrumentation employed but novel diagnostics necessary to achieve all requirements
Electro-Optical techniques for longitudinal diagnostics
bunch
laser pulse
EO crystal
cladding
core
Cherenkov radiation in fibres for losses diagnostics
lost electron
Cherenkov light

## Slide 6: Transverse diagnostics for FCCee
Beam 1
Beam 2
Interaction Point
SR extraction
FCCee is a high-energy circular accelerator
→ synchrotron radiation natural choice for diagnostics
Beam sizes in the order of (vertical)
→ X-ray diagnostics to maximize resolution
Smaller beam sizes and higher radiation levels in arcs
→ install diagnostics close to experimental regions
Conventional instrumentation (pinhole and screens) will be installed but more advanced diagnostics needed to meet accuracy requirements
Transverse beam size (emittance) affects collision rate (luminosity)
→ transverse diagnostics crucial for performance optimisation

## Slide 7: Synchrotron radiation techniques for transverse diagnostics
SR interferometry
interference target
monochromator
focusing optics
SR imaging
Imaging and interferometry often combined in synchrotron radiation diagnostics
imaging provides robust and precise relative measurements
interferometry used for accurate absolute measurements

## Slide 8: X-ray Heterodyne Near Field Speckles (HNFS)
monochromator
scatterers
single scatterer
many scatterers
power spectrum
Interference target is a dispersion of light-scattering nanospheres
Key features for implementation in FCCee
intrinsically two-dimensional measurement
compact, no need of long distances downstream of target
Silica spheres (500 nm)

## Slide 9: Beam size measurements with x-ray HNFS
Si(111) monochromator
nanospheres
undulator source
%
%
Credit: M. Siano
Measurements at ALBA synchrotron (Spain)
systematic validation at undulator beamline
measured beam size as small as

## Slide 10: Future tests with dipole source
Challenges to deploy technique at FCCee
high energy photons
broadband (dipole) SR source
new dipole line being equipped at ALBA for HNFS tests using dipole synchrotron radiation
In-vacuum multilayer monochromator
Layout of FE21 at ALBA, equipped for HNFS studies
Detector
Scatterers
Credit: U. Iriso

## Slide 11: Development of new target materials
Numerical simulations
(SRW, preliminary)
Credit: J. Nunez
Nanostructured gold target
Credit: S. Mazzoni
Silica nanospheres not usable in regular FCC operation
poor contrast of SiO2 with hard x-rays
stability issues such as sedimentation and aggregation of colloids
need to develop and study novel target materials
Ongoing R&D to design and manufacture gold-based scatterers, optimized for FCC applications, to be tested in new ALBA beamline

## Slide 12: Conclusion
FCC is a frontier machine that needs frontier diagnostics to maximize physics output
→ novel techniques under study in several diagnostic domains
Challenges to implement HNFS as operational diagnostics at FCCee
→ work in progress for test beamline at ALBA and R&D for optimized target materials
X-ray Heterodyne Near Field Speckles successfully tested at ALBA light source
→ promising option for accurate beam size measurement at FCCee

## Slide 13: Thank you for your attention!
13