## Slide 1: The EuPRAXIA project
F. Villa, INFN-LNF
On behalf of the EuPRAXIA@SPARC_LAB collaboration
ICFDT7

## Slide 2: Principle of plasma acceleration
Laser Wakefield Accelerator (LWFA):
Drive beam = laser beam
Plasma WakeField Accelerator (PWFA):
Drive beam = high energy electron or proton beam
Courtesy Sci. Am.

## Slide 3
Distributed Research Infrastructure
2
2
2
4
2
3
5
1
6
2
Beam-driven plasma user facility EuPRAXIA Headquarter
Laser-driven plasma user facility: candidates
Excellence Center
Horizon Europe
Second site will be decided in Preparatory Phase project.
Excellence centers (EC) perform technical developments, prototyping and component construction. Number of EC’s, locations, roles, responsibilities reviewed in Prep. Phase.
Beam-driven plasma user facility EuPRAXIA Headquarter
Technology Incubator (CZ - ELI)
User Data Center (H)
Theory & simulations (P)
Advanced Applications Beamlines (UK)
Laser-Plasma Acc. & 1 GeV FEL (F)
Plasma Acc. & High Rep. Rate Dev. (D)
2

## Slide 4
The EuPRAXIA Consortium today: 54 institutes from 18 countries plus CERN
Included in the ESFRI Road Map
Wide International Collaboration
Efficient fund raising:
  Preparatory Phase consortium (funding EU, UK, Switzerland, in-kind)
  Doctoral Network (funding EU, UK, in-kind)
  EuPRAXIA@SPARC_LAB (Italy, in-kind)
  EuAPS Project (Next Generation EU)
EuAPS project and diagnostics: see talk form F. Stocchi tomorrow

## Slide 5: EuPRAXIA@SPARC_LAB
159 m
45 m
Accelerator tunnel
Plasma
module
Undulator tunnel
AQUA beamline
Experimental hall
Lasers clean rooms
Laser and particle user rooms
Klystron & power supplies hall
Technical rooms
Preparations labs
ARIA beamline

## Slide 6: Expected electron parameters
Two different configurations:
  500 MeV beam from the X-band linac + 60 cm capillary PWFA acceleration up to 1.2 GeV
    Smaller accelerated charge
    Shorter pulses
    Final energy easily upgradable in future with similar building occupancy ()
  1 GeV beam from the X-band linac alone (with additional RF power)
    Larger charge per bunch
    Longer pulses
    At the upper limit of RF technology (not easily upgradable without extending the occupancy)
Parameter | Unit | PWFA | Full X-band
Electron Energy | GeV | 1-1.2 | 1
Bunch Charge | pC | 30-50 | 200-500
Peak Current | kA | 1-2 | 1-2
RMS Energy Spread | % | 0.1 | 0.1
RMS Bunch Length | 𝜇m | 6-3 | 24-20
RMS norm Emittance | 𝜇m | 1 | 1
Slice Energy Spread | % | ≤0.05 | ≤0.05
Slice norm Emittance | mm-mrad | 0.5 | 0.5
55 m

## Slide 7: Electron diagnostics in EuPRAXIA@SPARC_LAB
Cavity BPM
Electro-Optical Sampling
Transverse Deflecting Structure PolariX
YAG screen
Coherent Diffraction Radiation
Integrated
Current
Transformer
PolariX TDS
Dipole
Quadrupole Triplet
Screen
Emittance and LPS measurements
Plasma diagnostics: see talk form L. Crincoli tomorrow

## Slide 8: Radiation Generation: FEL
40 m

## Slide 9: Expected FEL radiation at undulators end
40 m
Parameter | Unit | AQUA PWFA | AQUA X-band | ARIA PWFA | ARIA X-band
Radiation Wavelength | nm eV | 3-10 415-120 | 4-10 310-120 | 50-150 25-8 | 50-150 25-8
Photons per Pulse |  | 0.25-1 | 0.25-1 | 10-60 | 12-150
Photon Bandwith | % | 0.3 | 0.3 | 0.05 | 3
Configuration |  | SASE | 30 | HGHG seeding | 30
Parameter | Unit | AQUA PWFA | AQUA X-band | ARIA PWFA | ARIA X-band
Radiation Wavelength | nm eV | 3-10 415-120 | 4-10 310-120 | 50-150 25-8 | 50-150 25-8
Photons per Pulse |  | 0.25-1 | 0.25-1 | 10-60 | 12-150
Photon Bandwith | % | 0.3 | 0.3 | 0.05 | 3
Configuration |  | SASE | 30 | HGHG seeding | 30
AQUA PWFA
linear
AQUA PWFA
circular
ARIA PWFA configuration

## Slide 10: FEL Beamlines
AQUA beamline
ARIA beamline
10m
20m
30m
12m
GDM
Mirror
Apertures
Spectrometer
Solid attenuators/filters
Polarization/time measure area
Monochromator area
Split & delay line area
Gas absorber
K-B mirrors
Exp. Chamber area
Valves
Screens
Laser hutch
50 m
BPM

## Slide 11: FEL Photon diagnostics
Gas Intensity Monitors and BPMs
Ionization streaking
Transient reflectivity
Wavefront sensors
Grating spectrometer
Bladed BPM
Longitudinal photon and virtual diagnostic workshops LNF, 6th-8th November 2024
https://agenda.infn.it/event/41662/overview
YAG screen
Coherence measurements (transverse and longitudinal)

## Slide 12: AQUA beamline scientific case
Coherent imaging
X-ray spectroscopy
Raman spectroscopy
Photo-fragmentation of molecules
(Large) Viruses
Organelles
Bacteria/Cells
Organic molecules
Metals
Semiconductors
Superconductors
Magnetic materials
Experimental techniques and typology of samples
50 m
3 nm 2 nm
4 nm

## Slide 13: ARIA beamline scientific case
Photoemission
Spectroscopy
Photoelectron Circular Dichroism
Raman spectroscopy
Photo-fragmentation of molecules
Time of Flight Spectroscopy
Gas phase & Atmosphere
(Earth & Planets)
Aerosols
(Pollution, nanoparticles)
Molecules & gases
(spectroscopies, time-of-flight)
Proteins
(spectroscopies)
Surfaces
(ablation & deposition)
Defining experimental techniques and typology of samples (and applications)
50 m
Fundamental research and applications with the EuPRAXIA facility at LNF LNF, 4th-6th December 2024
https://agenda.infn.it/event/42474/overview

## Slide 14: Timelines
Courtesy A. Falone

## Slide 15: Conclusions & Acknowledgements
Plasma accelerators have advanced considerably in beam quality, achieving FEL lasing.
EuPRAXIA is a design and an ESFRI project for a distributed European Research Infrastructure, building two plasma-driven FELs in Europe.
EuPRAXIA FEL site in Frascati LNF-INFN is sufficiently funded for first FEL user operation in 2029.
Aim at making EuPRAXIA an example of European innovation: new science to new applications and new areas in particle and photon physics
Greatly appreciate slides from and discussions with: A. Cianchi, F. Cioeta, M. Del Franco, E. Di Pasquale, A. Falone, A. Ghigo, L. Giannessi, M. Ferrario, S. Lauciani, R. Pompili, F. Stellato and THE ENTIRE EuPRAXIA@SPARC_LAB and EuAPS TEAMS

## Slide 16
Thank for your attention