## Slide 1: CMS RPC project overview from the present system to the upgrade
Dr. Pierluigi Paolucci
Istituto Nazionale di Fisica Nucleare &
CERN
CMS RPC Web page

## Slide 2: Outline
Muon system description
RPC collaboration
Brief history of the detector construction
Online tool and data analysis
Results 2010-2011 with collision data
2012-2013 Upgrade
Conclusions
Much more details in the CMS talks

## Slide 3: Muon system overview
ENDCAP (0.9 < || < 2.4):
540 - Cathode Strip Chamber
432 - Resistive Plate Chamber
BARREL (0 < || < 1.2):
250 - Drift Tube
480 - Resistive Plate Chamber
About 3.000 m2 of RPC detectors

## Slide 4: RPC collaboration
Belgium
CERN
Bulgaria
CHINA | 2
KOREA | 16
INDIA | 4
BELGIUM | 10
COLOMBIA | 2
PAKISTAN | 6
EGYPT | 3
CERN | 4
ITALY | 28
BULGARIA | 12
TOTAL | 84
Barrel | Italy | Bulgaria | China | Colombia | 
Endcap | Korea | Pakistan | China | Belgium | CERN
Upgrade | Italy | Pakistan | India | Colombia | CERN
 | Korea | China | Belgium | Finland | Egypt

## Slide 5: RPC system: few numbers
RPC info | 
Bakelite thickness | 2 mm
Bulk resistivity | 1-2 1010 W cm
Gas mixtures | 96.2%C2H2F4 + 3.5%C4H10 + 0.3%SF6
Operating HV | 9.4 – 9.8 kV

## Slide 6: Past Construction lines (2004-2007)
Two parallel lines have been developed to build gaps:
  Barrel gaps in Italy for 480 chambers
  Endcap gaps in Korea for 432 chambers
Chamber assembly:
  Barrel chamber - Italy
  Endcap chamber – China, Pakistan and CERN
Front-end electronics – Italy
Off-chamber electronics – Warsaw, Finland

## Slide 7: from construction to commissioning
7
ISR
DT-RPC coupling
DT-RPC test at ISR
DT-RPC envelope
DT-RPC at SX5
DT-RPC installed
DT-RPC commissioning
2004-2008

## Slide 8: RPC chambers installation

## Slide 9: Endcap disk ready to work

## Slide 10: A photogenic and powerful “detector”

## Slide 11: How judge the RPC muon system ?
Detection efficiency and stability
  Plateau curves
  Overall efficiency
Background:
  Noise rate & Dark current
Trigger rate & efficiency stability
Aging effect:
  Dark current & noise rate
  Plateau position (HV at 50% eff)
  Muon Radiographies
high Luminosity 1033
millions of muons
many runs (time)
high beam intensity
time
sophisticated analysis

## Slide 12: RPC online Monitoring tools
Detector
PVSS
OMDS
ORCOFF
POPCON
DATA
Online
DQM
Noise
scalers
WBM
Trigger
Link sys
Plot and results
ONLINE
OFFLINE

## Slide 13: Hardware Status
Masked channels
dead channels
Inactive channels: ~1.6%
(~0.9% masked, ~0.7% dead)
Averge noise
Rate 0.1 Hz/cm2
Averge noise
Rate 0.1 Hz/cm2
Intrinsic electronic noise is indeed
subtracted in the background studies

## Slide 14: efficiency: 2172 plateau
99% of the 2172 rolls (half-chamber) have a perfect plateau
After about 5-7 years from the gap construction and 3 years of data taking
TO BE DONE EVERY beginning of the YEAR
barrel
barrel
barrel
endcap
endcap
endcap

## Slide 15: Efficiency: more results
ENDCAP
BARREL
Barrel
RMS 64 Volts
Endcap
RMS 84 Volts
All barrel plateau

## Slide 16: Stability: cluster size .vs. pressure
2010 (pressure dependence)
2011 (HV normalized to P)
Cluster size .vs. HV
Cluster size
distribution
Cluster size .vs. Pressure
After having studied the performance
of the system we decided to remove one of the last source of instability (3-5%):
HV working point is now corrected with the atmospheric pressure

## Slide 17: Stability in time
Without Pressure correction
With Pressure correction
October 2011
April 2011
CMS Preliminary 2011

## Slide 18: Background studies
CMS Preliminary 2011
Outermost station
Innermost station
Bottom sectors are less affected by neutron background due to the shielding
of the cavern floor
External chambers have rate greater than internal chambers (closer to the beam)
CMS Preliminary 2011
Outermost station

## Slide 19: Dark Current .vs. luminosity
Beam Intensity in a single fill
No beam
beam
Current is correlated to the beam intensity
Current without beam is stable in time
Max Current < 5-6 mA (few cases)
Average Current trend .vs. time
No beam
beam

## Slide 20: Current .vs. luminosity
CMS Preliminary
CMS Preliminary
Linear correlation between
current and luminosity
from 1.8 mA to 6.0 mA
when L increase 8-times
Current distribution shift
Versus luminosity

## Slide 21: Summary performance table
 | Single gap | Dead chamber
Barrel | 7 | 5
Endcap | 24 | 3
Data Loss for RPC 19 pb‐1 – 0.37%
Overall Operating Channels 98.4%
Average Efficiency 95%
Average Cluster Size < 2
Average Noise rate (3 ·1033 cm-2 s-1) 1.3 Hz/cm2
Max Noise rate (3 ·1033 cm-2 s-1) RE-2/2/C < 7 Hz/cm2
Average intrinsic noise (no-beam) ~ 0.1 Hz/cm2
Average current (no-beam) ~ 1 mA
Average current (with beam) ~ 1.5 mA
Temperature < 21.5 oC

## Slide 22: Do we believe to the statistic ? 
I showed you how well the RPC system is working showing many results and plots
BUT
We can also have a different and more statistic-independent approach (visual approach) and ASK for events and visual inspections
AND HERE THEY ARE

## Slide 23: Visual inspection of the chambers
Even with the visual inspection it is clear we are running very well our system and no aging effect are visible until now

## Slide 24: Visual inspection of the chambers
Here you see the spacers and the corner 

## Slide 25: RPC trigger results
RPC Trigger rate is much more stable after pressure correction of the WP

## Slide 26: RPC Upgrade: station 4 + Ring 1
Upgrade
2013-2014
Upgrade
2017-2018

## Slide 27: Upgrade Trigger improvements

## Slide 28: Conclusions
RPC system construction was an incredible adventure done by only 9 institutions.
We are now 15 institutions (90 FTE)
All the chambers are working very well
Very few leaky chamber but still running
2011 has been an important year; thanks to the millions of muon, we were able to study in details our system and learn a lot about it.
Let me thanks Pino Iaselli for leading in the best way this project, from the first nanosecond to the 2010

## Slide 29: Conclusions
I would like to remember and thanks Beppe Belli (Pavia University) not only for the great job done in the RPC project since the production of the first Bakelite sheet but especially for his outstanding
Humanity, Willingness and Honesty
Thanks Beppe