## Slide 1
BULLKID Readout Electronics
T. Muscheid, R. Gartmann, O. Sander, L. Ardila-Perez, F. Simon

## Slide 2: Research background: ECHo experiment
Ho163 decay rate: 10 Bq per MMC pixel
400 channels with resonances between 4 – 8 GHz
Resonator bandwidth:
1.6 MHz
15 MUX needed for 12.000 sensors!
Ho163 spectrum:
ECHo detector + μMUX:
Upper limit of electron neutrino mass
Electron capture using magnetic microcalorimeters

## Slide 3: ECHo readout concept & system design
Software-defined radio (SDR) system:

## Slide 4: ECHo firmware
Channelization stage
Fluxramp Demodulation
Event Detection
Tone separation into TDM-Scheme
Recovery of raw sensor signal

## Slide 5: BULLKID readout requirements
Resonator spectrum:
Preliminary characteristics
Frequency range: 700 – 950 MHz
~ 150 channels per MUX
Channel bandwidth up to 100 kHz
10 – 15 wafers

## Slide 6: BULLKID readout electronics proposal
Built around AMD RFSoC (Radio Frequency System on Chip)
Source: AMD

## Slide 7: Hardware
Custom Frontend Board:
BalUn + Lowpass + Equalizer
ZCU216 Evaluation Board:
16x 14-bit, 9.85 GSPS DAC
16x 14-bit 2.5 GSPS ADC
Plenty of PL resources
CLK104 clock board
Low jitter PLL (LMX2594)

## Slide 8: Custom frontend
Prototype board with 4 channels
Evaluation of various combinations of BalUn transformer and lowpass
DAC channel characterization:

## Slide 9: Firmware overview
Resource utilization for 4 chains (16 chains):
BRAM: 40% (180%*)
DSP: 20% (77%)
LUT: 26% (74%)
26 W dissipation
* Additional URAM resources available

## Slide 10: Converter configuration

## Slide 11: Converter characterization

## Slide 12: Frequency comb generation
250 MHz usable bandwidth
SNR > 70 dBm
Arbitrary number of tones
Configurable frequency, amplitude and phase

## Slide 13: Channelization concept

## Slide 14: Channelization concept (2)

## Slide 15: Output of channelization stage

## Slide 16: ADC noise measurement
Calculation of PSD with Welch‘s method
Noise increases with increasing number of tones
Strategy for improvement:
  Increase power of readout tones
  Optimization of DAC and ADC

## Slide 17: Software stack
Custom C++ server daemon for communication with the platform
Configuration and read-back of PL modules during runtime
Commands are sent via gRPC to the user

## Slide 18: How to use it?
Custom python user interface
gRPC wrapper, no processing
Currently preparing extensive documentation
Package will be published soon as open source on PyPI
CIRQUE: Communication Interface to Readout electronics for QUantum Experiments

## Slide 19: Step 1: Connect to platform
from cirque import servicehubutils
from cirque import pimc platform_ip = "192.168.1.105"
con = servicehubutils.FPGAConnection(ip=platform_ip,port=50058)
# Connect to the PIMC (platform information and management core)
pimc = pimc.PIMC(con)
# Check if SDR is ready (Converters and Clocks configured)
print(f"Platform ready: {pimc.get_platform_ready()}")

## Slide 20: Step 2: Instantiate available modules
from sdr_utils import platform
platform.print_endpoints(con)
from cirque import stimulation
from cirque import multichannelddc
from cirque import dmacontroller
stim_0 = stimulation.Stimulation(con, "stimulation_0")
ddc_0 = multichannelddc.MultiChannelDDC(con, "ddc_0")
ddc_1 = multichannelddc.MultiChannelDDC(con, "ddc_1")
dma = dmacontroller.DMAController(con)

## Slide 21: Step 3: Generate readout tones
from sdr_utils import tone_generation frequencies = tone_generation.set_tone(stim_0, 720e6, 0.2, 0)
Option B: Generate tones from file
Option A: Manually generate tones
from sdr_utils import tone_generation tones = tone_generation.import_tones_from_file("tones.csv")
frequencies = tone_generation.set_tones(stim_0, tones)

## Slide 22: Step 4: Configure channelization
from sdr_utils import channel_configuration
chain_0 = channel_configuration.Subchain(ppc_0, ddc_0)
chain_1 = channel_configuration.Subchain(ppc_1, ddc_1)
ddc_chain = channel_configuration.DownConversion()
ddc_chain.add_chain(chain_0)
ddc_chain.add_chain(chain_1)
channel_configuration.initialize_ddc(ddc_chain, frequencies)

## Slide 23: Step 5: Data acquisition
from cirque import dmacontroller dma = dmacontroller.DMAController(con)
data, loss = dma.snapshot(samples=1000, dtype=numpy.int16(),
subchains=[0,1], channels=[5,9,18],
package_mode=False)
Data is returned as numpy array
Parallel raw data stream from two processing chains possible
Event-based readout takes data from all chains
Acquisition modes: Snapshot, FileSnapshot, FileStream

## Slide 24: Open issues
Tone power needs to be increased!
  Fully utilize DAC power
  Use external amplifiers
Optimization of filter values
  Compromize between attenuation and ressource consumption
  Depends on other parts of readout chain
Modify and extend event detection module
  Switch between amplitude and phase signal
  Implementation of additional trigger logic to acquire neighboring channels

## Slide 25: Outlook
Measurements at INFN Rome this week
Scale up firmware and hardware to 16 channels
Implement new features such as automatic peak finder via integrated VNA
Optimization of channelization and system configuration according to application-specific requirements

## Slide 26: Conclusion
Coarse processing chain successfully implemented
  Signal generation
  Channelization, down-conversion and data decimation
  Event detection
  Data acquisition and storage
Custom frontend for transceiver evaluation and optimization assembled
Firmware to be optimized iteratively with sample measurements