## Slide 1
Beta decay and neutrino mass: KATRIN and beyond
Magnus Schlösser Karlsruhe Institute of Techology Institute for Astroparticle Physics Tritium Laboratory Karlsruhe
Neutrino Oscillation Workshop NOW 2024, Otranto, Italia
© C. Grupe, KIT (2024)

## Slide 2: The role of massive neutrinos and motivations to measure it
Model for mass generation needs:
mixing matrix AND mass scale
Neutrino masses bring in a fundamental energy scale (besides Higgs scale)
Cosmology and the role of neutrinos therein may be more complex (what is DE, …?)
Signal is „in reach“: Minimal mass scales exist!
“m(νe)“ > 10 meV (normal mass ordering)
“m(νe)“ > 50 meV (inverted mass ordering)
0vββ observation not necessarily points to an neutrino mass

## Slide 3: Ways to access the neutrino mass
 | Cosmology | Search for 0νββ | β-decay & electron capture
Observable |  |  | 
Present upper limit | 0.12 eV (0.072 eV) | 0.156 eV | 0.8 eV
Model dependence | Multi-parameter cosmological model | Majorana ν contributions other than m(ν)? nuclear matrix elements, gA | Direct, only kinematics; no cancellations in incoherent sum
This talk

## Slide 4: Complementarity and need for direct mass measurements
KATRIN(2022)
Lightest neutrino mass (eV)
Lightest neutrino mass (eV)
Lightest neutrino mass (eV)
(eV)
(eV)
(eV)
NuFit, J. High Energ. Phys. 2020, 178 (2020).
Planck, Astron. Astrophys. 641 (2020) A6 DESI, 2406.14554
KamLAND-Zen, PRL 130, 051801 (2023)
KATRIN, Nat. Phys. 18 (2022) 160
Standard neutrino picture: observations have to be found in colored regions
Inspired by IUPAP neutrino panel white paper, www.iupapneutrinopanel.org
KamLAND-Zen (2023)
Planck (2020)
Tie-breaker needed to exclude exotic models in neutrino nature or cosmology
Planck (2020)
Planck (2020)
Planck (2020)
DESI (2024)

## Slide 5: Direct mass experiments
Direct, model-independent access to neutrino mass
(Anti-) neutrino mass determined from shape distortion near kinematic endpoint
decay
Electron capture
Measurement of kinetic energy of electron
Measurement of internal excitation of daughter atom
Tiny fraction

## Slide 6: Challenges for achieving mass low sensitivity
High signal ( statistics)
Low background ( statistics)
High energy resolution ( sensitivity)
Low and quantified systematic effects
 | -decay | Electron capture
Chosen isotope | 3H = T | 163Ho
Endpoint | 18.6 keV | 2.8 keV
Half life | 12.3 years | 4570 years
Typ. production | n-capture in D2O | n-irradiation of 162Er
 |  | Electron capture
Chosen isotope | 3H = T | 163Ho
Endpoint | 18.6 keV | 2.8 keV
Half life | 12.3 years | 4570 years
Typ. production | n-capture in D2O | n-irradiation of 162Er
Tiny fraction
  Low kinematic endpoint, high decay rate
This talk
See Talk
06 Sep, 17:50
Elena Ferri

## Slide 7: Tritium beta decay experiments
Direct, model-independent access to neutrino mass
E0 = 18.6 keV
T1/2 = 12.3 y
KATRIN’s aim: Measurement of mν with a sensitivity of 0.2 eV/c²

## Slide 8: Molecular decay
Atomic decay
Final-state distribution
Decay from a molecule
+ further inner excitations (rotation / vibration)
Molecular effects need to be taken into account in neutrino mass analysis
„model-dependence“

## Slide 9: Established measurement principles
MAC-E filter
CRES
Magnetic Adiabatic Collimation with an Electrostatic Filter
Measuring energy by applying a high-pass filter
Cyclotron Radiation Emission Spectroscopy
Measuring energy via frequency
Calorimeters
Low-temperature micro calorimeters
Measuring energy by temperature change
See Talk
06 Sep, 17:50
Elena Ferri

## Slide 10: Basic principle of KATRIN-like experiment
Calibration
Tritium source
Electron Filter
Electron detector
Tritium reduction
T2 in
T2 out
Electron transmission if above filter potential
Electron transport along B-field lines

## Slide 11: Karlsruhe Tritium Neutrino Experiment (KATRIN)
ultra-stable high-luminosity windowless gaseous tritium source (1011 Bq)
high-resolution MAC-E filter with < 1 eV energy resolution
KATRIN’s aim: Direct measurement of mν with a sensitivity of 0.2 eV/c²
70 m long setup at KIT campus north
JINST 16 T08015 (2021)

## Slide 12: Tritium Laboratory Karlsruhe (TLK) A facility for high activity tritium experiments
We are able to setup and operate a large variety of experiments with tritium
We develop safe tritium technology and versatile tritium analytics since 1993
Licensed for 40 g Tritium
Closed tritium cycle for recycling and purifying tritium in gram amounts
> 50 experience scientists, engineers and technicians
Two missions:
  Fuel cycle for fusion reactors
  KATRIN Experiment

## Slide 13: KATRIN timeline
Phase 2 (Differential) keV sterile
Phase 1 (Integral) Neutrino mass
Neutrino mass
R&D Phase for KATRIN++
Differential detection demonstrators
Atomic Tritium Demonstrator
2019-2025
2026-2027
2028-2034
Scientific goal
This talk
See Talk
04 Sep, 18:50
Andrea Nava
KATRIN: keV sterile neutrino search
See Talk
06 Sep, 18:10
Richard Salomon
Details of the latest KATRIN data analysis
This talk
TRISTAN detector

## Slide 14: KATRIN data releases and neutrino mass results
2019: m𝛎 < 1.1 eV (90% CL)
2022: m𝛎 < 0.8 eV (90% CL)
~6 Mio counts
Current data set
259 measurement days
1757 𝛽-scans
~36 Mio counts
PRL 123 (2019) 221802
PRD 104 (2021) 012005
Nature Phys. 18 (2022) 160
Expected sensitivity < 0.5 eV
First 5 campaigns: taking data while finding optimal operation conditions

## Slide 15: Data combination challenges
59 stacked spectra with
+ 28 + 14 x 28 + 28 + 14 x 28 + 14 x 25 + 14 x 28 =
1609 data points
Retarding energy (eV)
Rate per pixel (cps)
Measurement time
See Talk
06 Sep, 18:10
Richard Salomon
Details of the latest KATRIN data analysis
Challenges arisen from KATRIN‘s learning curve
Combination of 7 sub-data sets with different settings
Source temperature
Tritium column density
Measurement time distribution
MAC-filter configuration
Operation modes

## Slide 16: Systematic uncertainties
Statistical uncertainties dominate
Significant reduction of the background-related systematics
Better control over source scattering
Increased conservative uncertainties in this release
  Reduced uncertainties in current data
  Reduction of the molecular final-states uncertainties
Forecast: individual systematics in final KATRIN analysis (post 2025) expected to be > 0.01 eV² range

## Slide 17: New best fit and upper limit
New KATRIN release improves direct neutrino-mass bound by a factor of 2
This release
This release
New best fit compatible with vanishing neutrino mass
Resulting in an new upper limit
https://arxiv.org/abs/2406.13516

## Slide 18: KATRIN data taking continues
14 measurement campaigns completed in the next week.
> 175 Mio counts recorded – x4 of this release!
More data to come in 2024-2025 + calibration/systematics improvements
Cumulative counts
in 40 eV range
Ongoing data taking through 2025 → 𝚺 1000 days
 target sensitivity below 0.3 eV

## Slide 19: Established measurement principles
MAC-E filter
CRES
Magnetic Adiabatic Collimation with an Electrostatic Filter
Measuring energy by applying a high-pass filter
Cyclotron Radiation Emission Spectroscopy
Measuring energy via frequency
Calorimeters
Low-temperature micro calorimeters
Measuring energy by temperature change
See Elena Ferri

## Slide 20: Cyclotron Radiation Emission Spectroscopy
~fW
Differential measurement with antenna arrays around a (atomic) tritium source
 Frequency measurement

## Slide 21: Project 8 – Results
Phase I: First use of CRES for electron spectroscopy (83mKr)
Phase II: First use of CRES for tritium beta decay electron spectroscopy  Neutrino mass limit (V)
D. M. Asner, et al., Phys. Rev. Lett. 114, 162501 (2015)
A. Ashtari Esfahani et al.Phys. Rev. Lett. 131, 102502 (2023)
Copied from presentation by N. S. Oblath TAUP 2023

## Slide 22: Outline
KATRIN on way to achieve 1000 d measurement time (final sensitivity < 0.3 eV). Next result : ~ 0.5 eV sensitivity
We will be ready for TRISTAN-Operation at the end of 2025 (Search for keV sterile neutrinos)
Phase 2 (Differential) keV sterile
Phase 1 (Integral) Neutrino mass
Neutrino mass
R&D Phase for KATRIN ++
Differential detection demonstrators
Atomic Tritium Demonstrator
2019-2025
2026-2027
2028-2034
Scientific goal

## Slide 23: Going beyond KATRIN
KATRIN final: < 0.3 eV (90% CL) Distinguish between degenerate and hierarchical scenario
New technologies: < 0.05 eV Cover inverted ordering
KATRIN
New
technologies
n3
n1
n2
n1
n2
n3
IO
NO
KATRIN++ mission
Next generation experiment
Identify and develop scalable technology
Use KATRIN/TLK infrastructure for R&D phase (~ 7 years)

## Slide 24: Going beyond KATRIN
Differential measurement (FWHM < 1 eV)
  Better use of statistics
  Lower background
Atomic tritium
  Avoid broadening (~ 1 eV)
  Avoid limiting systematics of T2
T2, integral (DE = 1 eV, bg = 0.01 cps)
T2, differential (FWHM = 0.2 eV, bg = 10-5 cps/eV)
T-atom, differential (FWHM = 0.2 eV, bg = 10-5 cps/eV)
IO
NO
KATRIN source
Stat only
10 eV region
1000 days
Preliminary
S. Mertens
Current KATRIN performance (integral, DE = 2.7 eV, bg = 0.1 cps)
S. Heyns
Notes: So what does it take to really go beyond KATRIN?
If we would continue with a KATRIN-like integral measurement mode, we would need much more tritium
The first key to boost the sensitivity is…
The second key to boost the sensitivity is…

## Slide 25: KATRIN and TLK as ideal R&D facilities
Differential detector technology
Atomic source technology
Notes: Grüner Kasten weg  andere Frage
Ggf. 20 + 21 kombinieren

## Slide 26: KATRIN and TLK as ideal R&D facilities
eV resolution for differential detection
immune to Rydberg-like backgrounds
Option 1 Micro-calorimeters / Quantum sensor
Option 2 Time-of-flight via electron tagging
Further options?
Technologies by community?
Differential detector technology
Notes: Grüner Kasten weg  andere Frage
Ggf. 20 + 21 kombinieren

## Slide 27: Quantum sensors as high resolution differential detectors
Thermometer
Absorber
  e.g. Metallic Magnetic Calorimeters (MMC)
  Temperature-dependence in sensor magnetization
  Read-out by SQUID
  Energy resolution: - Current: - Midterm: - Future:
Electron
Weak thermal link
Thermal bath
Time
Temperature
Advantages
Energy resolution O(eV) compared to conventional detectors O(100 eV)
Nearly 100% quantum efficiency
Broad spectrum of possible applications
absorber
sensor
SQUID
Not yet tested with external electrons
incoming particle
27.02.2024

## Slide 28: Next R&D goal: Demonstrate KATRIN with a quantum sensor array
Challenges of coupling quantum sensor detector array to KATRIN infrastructure
  Type of quantum sensor
  Operation in magnetic field (~10 mT)
  Coupling of mK cryo-platform with RT spectrometer
  Large area detector and multiplexing of ~1e6 channels
  Limits to energy resolution
+
T2, integral
T2, differential
IO
NO
KATRIN source
Stat only
10 eV region
1000 days
Preliminary
106 x
Use existing / well-characterised beamline
with Milano‘s cryo expertise

## Slide 29: ELECTRON: e- spectroscopy with quantum sensors
8 channel detector chips & front-end SQUID chips
170 µm
KIT-IMS (Kempf group)
Energy / keV
FWHM ~ 25 eV
Calorim. Kr-83m spectrum @ highest resolution
Next: tritium spectroscopy
Metallic Magnetic Calorimeters (MMC)
Kr-83m
x-ray and electron lines

## Slide 30: Next R&D goal: Demonstrate single electron tagging for ToF
Tagger: start (~1000 Hz)
Fast detector: stop
Pre-spectrometer: limit rate < 1 khz
Main spectrometer: delay line due to retardation pot.
R&D ongoing at U North Carolina
Coreless cryogenic current comparator
Single electron tagging is challenging
Cyclotron radiation emission detection (CRES)
Tiny signals vs. minimal noise floor
KATRIN Source: 1011 Bq
Strategy
„Single channel“ detector  less complex than quantum sensor array (QSA)
Differential measurement with ToF before QSA ready
Work on techniques to improve ToF resolution (U Münster)

## Slide 31: KATRIN and TLK as ideal R&D facilities
Atomic source technology
Differential detector technology
Notes: Grüner Kasten weg  andere Frage
Ggf. 20 + 21 kombinieren

## Slide 32: KATRIN and TLK as ideal R&D facilities
Atomic source technology
Molecular effects  spectral broadening
Intrinsic broadening to about 1 eV FWHM
Atomic source cannot be adapted to existing KATRIN beamline
Notes: Grüner Kasten weg  andere Frage
Ggf. 20 + 21 kombinieren

## Slide 33: Atomic Tritium Demonstrator at TLK
Essential for next generation neutrino mass experiment (e.g. KATRIN++) : Demonstrate the large scale generation and cooling (~10 mK) of atomic tritium
Molecular
tritium
Atomic
tritium
(hot, 2500 K)
Atomic
tritium
(cold)
Atomic
tritium
(trapped, injected)
Loss
Inline
reprocessing
Impurity
processing
return T2 + impurities
2022-2025
TLK
2025-2028
TLK+Mainz
2028…
TLK+P8?/…
Aim for investigation
  Develop atom cooling mechanism
  Trapping times / max. densities
  Interplay of beta-driven plasma (meVeV) and ultra-cold trapped atoms (neV)
Tritium atom throughput on the order of 10 g/day (c.f. KATRIN: 40 g/day)

## Slide 34: Atomic source R&D progress
Installation of first ever atomic tritium source at TLK ongoing
First results expected in 2024
Mass spectrometer
Source
Non-tritium hydrogen cracker being operated
Characterization measurements for tritium beamline ongoing
Decontaminated glove box

## Slide 35: Atomic Tritium Demonstrator at TLK
TLK is offering room and infrastructure for extended atomic tritium experiments
Molecular
tritium
Atomic
tritium
(hot, 2500 K)
Atomic
tritium
(cold)
Atomic
tritium
(trapped, injected)
Loss
Inline
reprocessing
Impurity
processing
return T2 + impurities
2022-2025
TLK
2025-2028
TLK+Mainz
2028…
TLK+?/…
~20 m

## Slide 36: CRES plans aiming at 40-50 meV sensitivity
https://www.project8.org/
https://www.hep.ucl.ac.uk/qtnm/
Concept: CRES readout in magneto-gravitational trap for atomic tritium
Concept: CRES readout in race-track for atomic tritium
Staged approach: - Proof-of-principle
- Demonstrators
- Final experiments in 2030s

## Slide 37: Future of direct neutrino mass detection
Aim: direct detection of big-bang neutrinos; determination of neutrino mass is „by-product“
M.G. Betti et al JCAP07(2019)047
Combine technologies (TES, CRES, novel drift filter) with large scale O(100g) tritiated graphene target
Start of technology demonstrator @LNGS soon
Content from „Nicola Rossi, EPS-HEP July 2023 Hamburg“
https://ptolemy.lngs.infn.it/

## Slide 38: KATRIN++ and other next generation projects
Currently, no technology proven to reach ultimate sensitivity
Neutrino mass detection must be confirmed by independent technologies
Atomic tritium trap is key independently of detection techniques
CRES, bolometer and ToF complementary
CRES antenna
Bolometer array
Bolometer array
CRES
B-field
Acceptance wrt B-field
Tagger
and ToF
measurement

## Slide 39: Atomic source research
Mission: Realize (global) Atomic Tritium Demonstrator (at TLK)
ATD** consortium
KATRIN++
Atom / molecular physics, .. communities
Possible partners:
Ubachs (VU Amsterdam), T2, DT, HT
Schiller (U Düsseldorf) HT+
Pohl (U Mainz) T
….
KAMATE
**placeholder name
* CRES-based
Form joint working group (kick-off meeting in September)
Atomic tritium trap is key independently of detection techniques

## Slide 40: Final R&D goal Atomic tritium with Quantum sensor array
Conceptual idea
Atomic T flow in
Flow out
Atomic T trap
Electron filtering
Warm/cold
interfacing
Sensor array
Work started
- concept
- sensitivities
- R&D

## Slide 41: Beta decay and neutrino mass: KATRIN and beyond
Phase 2 (differential) keV-sterile
Neutrino mass
Differential detection demonstrators
Atomic tritium demonstrator
Differential detection R&D
Atomic tritium R&D
Phase 1 (integral) neutrino mass
R&D phase for KATRIN++
2019-2025
2026-2027
2028-2034
Scientific goal
KATRIN on way to achieve 1000 d measurement time (final sensitivity < 0.3 eV). Next result : ~ 0.5 eV sensitivity
We will be ready for TRISTAN-Operation at the end of 2025 (Search for keV sterile neutrinos)
Ultimate neutrino mass experiment (Normal Ordering; sensitivity on < 40 meV) requires differential detector principle und an atomic tritium source  R&D Plan for PoF-V
KATRIN++ invites research groups for tackling challenges together

## Slide 42: KATRIN collaboration
Collaboration meeting, March 2024, TUM
Czech Republic:
https://www.linkedin.com/company/tritiumlab/

## Slide 44: Atomic vs molecular tritium
~70% of decays to electronic GS
Atomic FSD
~57% of decays to electronic GS
Molecular FSD
~ 8 eV shift of endpoint
Intrinsic broadening to about 1 eV FWHM

## Slide 45: Going beyond KATRIN
Differential measurement (FWHM < 1 eV)
  Better use of statistics
  Lower background
Atomic tritium
  Avoid broadening (~ 1 eV)
  Avoid limiting systematics of T2
T2, integral (DE = 1 eV, bg = 0.01 cps)
T2, differential (FWHM = 0.2 eV, bg = 10-5 cps/eV)
T-atom, differential (FWHM = 0.2 eV, bg = 10-5 cps/eV)
IO
NO
KATRIN source
Stat only
10 eV region
1000 days
Preliminary
S. Mertens
S. Heyns
Current KATRIN performance (integral, DE = 2.7 eV, bg = 0.1 cps)
Notes: So what does it take to really go beyond KATRIN?
If we would continue with a KATRIN-like integral measurement mode, we would need much more tritium
The first key to boost the sensitivity is…
The second key to boost the sensitivity is…

## Slide 46: Improved measurement principle
Retarding voltage (scanned!)
Integral measurement (high pass filter)
Energy resolution determined by filter
Detector „only“ counts
Reduced statistics
Differential measurement
Energy resolution determined by
A) detector or
B) time of flight
threshold
All energies at onces
arXiv:1806.00369v2
More signal
Less background
27.02.2024
Notes: Integral spectrum
TRITIUM2019 Proceedings
Differential spectrum
arXiv:1806.00369v2 [physics.data-an] 28 Jun 2018

## Slide 47: Next R&D goal: Demonstrate single electron tagging for ToF
Tagger: start (~1000 Hz)
Fast detector: stop
Pre-spectrometer: limit rate < 1 khz
Main spectrometer: delay line due to retardation pot.
R&D ongoing at U North Carolina
T. Tanabe et al., Nucl. Instr. Meth. A 427 (1999) 455
Coreless cryogenic current comparator
Single electron tagging is challenging
Cyclotron radiation emission detection (CRES)
Tiny signals vs minimal noise floor
KATRIN Source: 1011 Bq
See Project 8
Strategy
„Single channel“ detector  less complex than quantum sensor array (QSA)
Differential measurement with ToF before QSA is ready
Work on techniques to improve ToF resolution (U Münster)

## Slide 48: KAMATE – Karlsruhe Mainz Atomic Tritium experiment
Scientific / technical goals
Atomic beam characterization
  Atomic fraction
  Maximal flow rates / pressure limits
  Isotopic effects
  Angular dispersion
  Time-of-flight (upgrade)
  Wire-detector
Cooling / accommodation (upgrade)
  Velocity measurement
  Recombination
Sophisticated setup based on Mainz setup
Multi chamber / collimation design, tilting mechanism, beam control, source parameter control, beam analytics
A. Lindman
Karlsruhe
Mainz

## Slide 49: KAMATE – Karlsruhe Mainz Atomic Tritium experiment
KAMATE 0.5 (at Mainz)
Identify best source at MATS with H/D
KAMATE 1.0 (at TLK)
Operate KAMATE 0.5 setup with T.
T(Beam) ~ 2500 K
KAMATE 2.0 (at TLK)
Add accommodator as first stage cooling. T(Beam) ~ 150 K
KAMATE 3.0 (at TLK)
Add nozzle for second stage cooling and beam temperature measurement setup (time of flight).
T(Beam) ~ 4 K
A. Lindman
Karlsruhe
Mainz
KAMATE stages
2024
2028

## Slide 50: Preparing TLK for Atomic Tritium Demonstrator (ATD)
Decontamination completed
Installation ongoing
ALTEX Box
In process of disposal/repurposing of former experiment
Next step: decontamination
PETRA box
e.g. former tritium retention system, gas bottles, control cabinets, …
 Relocation in progress
Other systems
e.g. large tritium retention system (~500k€), tritium supplies, …
 Acquisition on-going
ATD Glove box infrastructure

## Slide 51: Working principle of KATRIN
Artwork L. Köllenberger