## Slide 1
First studies of crystal collimation for the FCC-ee
G. Broggi1,2,3, A. Abramov2, M. Boscolo3, R. Bruce2, D. Mirarchi2, S. Redaelli2
2 CERN, Meyrin, Switzerland
1 Sapienza University of Rome, Italy
3 INFN-LNF, Frascati, Italy
Channeling 2024 – Riccione, Italy, 09/09/2024
Many thanks to:
L. Bandiera, B. Lindstrom, L. Nevay, F. Zimmermann

## Slide 2
Collimation for the FCC-ee
FCC-ee is the FCC first stage e+e- collider
  90.7 km circumference, tunnel compatible with FCC-hh
  4 beam operation modes, optimized for production of different particles:
  Z (45.6 GeV), W (80 GeV), H (120 GeV), ttbar (182.5 GeV)
FCC-ee presents unique challenges
  Unprecedented stored beam energy for a lepton collider: up to 17.5 MJ in the Z operation mode (45.6 GeV)
  Highly destructive beams: collimation system indispensable
  The main roles of the collimation system are:
    Reduce background in the experiments
    Protect the machine from unavoidable losses
  Two types of collimation currently foreseen for the FCC-ee:
    Beam halo (global) collimation
    Synchrotron Radiation (SR) collimation – around the IPs
    Tertiary collimators for local protection and particle shower absorbers under study
Comparison of lepton colliders
Damage to coated collimator jaw due to accidental beam loss in the SuperKEKB – T. Ishibashi (talk)
G. Broggi | First studies of crystal collimation for the FCC-ee
09/09/2024

## Slide 3
FCC-ee halo collimation system
Dedicated halo collimation system in PF
  Dedicated collimation optics (M. Hofer)
  Two-stage betatron and off-momentum collimation system in one insertion
  Ensure protection of the aperture bottlenecks in different conditions
    Aperture bottleneck at Z: 14.6σ (H plane), 84.2σ (V plane)
  First collimator design for cleaning performance – relies on amorphous collimators
    Ongoing studies for optimizing the collimator design (G. Broggi – IPAC’24 paper)
Name | Plane | Material | Length [cm] | Gap [σ] | Gap [mm] | δcut [%]
TCP.H.B1 | H | MoGr | 25 | 11 | 6.7 | 8.9
TCP.V.B1 | V | MoGr | 25 | 65 | 2.4 | -
TCS.H1.B1 | H | Mo | 30 | 13 | 3.8 | 6.7
TCS.V1.B1 | V | Mo | 30 | 75 | 2.5 | -
TCS.H2.B1 | H | Mo | 30 | 13 | 5.1 | 90.6
TCS.V2.B1 | V | Mo | 30 | 75 | 3.0 | -
TCP.HP.B1 | H | MoGr | 25 | 18.5 | 4.2 | 1.3
TCS.HP1.B1 | H | Mo | 30 | 21.5 | 4.6 | 2.1
TCS.HP2.B1 | H | Mo | 30 | 21.5 | 16.8 | 1.6
FCC-ee beam halo collimator parameters and settings (Z mode)
FCC-ee Z V23, tridodo_572 collimation optics
betatron
off-momentum
Further materials will be studied in the future
M. Hofer
G. Broggi | First studies of crystal collimation for the FCC-ee
09/09/2024

## Slide 4
Crystal collimation for the FCC-ee: motivation
As an alternative to the baseline design relying on amorphous collimators, crystal collimation is also being explored:
Cleaning efficiency
Angular deflection by bent crystals increases the impact parameter of beam halo particles on the absorbers (secondary collimators)
Impedance
Short (sub-mm) bent crystals in place of tens of cm long amorphous primary collimators
Potentially larger absorber (secondary collimator) mechanical gaps
Power deposition on collimators
Short (sub-mm) bent crystals in place of tens of cm long amorphous primary collimators
Potentially increase beam halo spot size at the absorbers employing bent crystals
Power deposition on absorber could still be challenging
Working principle of a crystal collimation system
D. Mirarchi, PhD thesis
G. Broggi | First studies of crystal collimation for the FCC-ee
09/09/2024

## Slide 5
Crystal collimation for the FCC-ee: first considerations
Particle steering exploiting channeling in bent crystals more challenging for q<0
  First focus on e- crystal collimation exploiting planar channeling in Si (111) plane
  Studies extended to e+ crystal collimation
First checks to identify possible show-stoppers
  Beam divergence at crystal candidate location in the FCC-ee vs. critical angle
  Crystal bending angle needed to deeply impact an absorber downstream
  Crystal bending radius vs. critical bending radius
First bent crystal parameters based on optimization of channeling efficiency through channeling simulations:
  Geant4 (10.4.03) crystal channeling routine through the BDSIM simulation toolkit
  Crystal data from E. Bagli, G4_MC_CHANNELING Git repository
  Good agreement with exp. results – efficiencies agreement within few % (e.g., U. Wienands et al., Observation of Deflection of a Beam of Multi-GeV Electrons by a Thin Crystal)
First collimation tracking simulations with selected bent crystal parameters
experiment
simulation (BDSIM)
G. Broggi | First studies of crystal collimation for the FCC-ee
09/09/2024

## Slide 6
Crystal candidate location: FCC-ee Z mode
Current locations of FCC-ee primary betatron collimators (TCPs) chosen as crystal candidate locations
At such locations:
TCP.H.B1 and TCP.V.B1 might be replaced by bent crystals
Absorber candidate locations are the same as secondary collimators (TCSs): phase advance is optimal
FCC-ee Z V23, tridodo_572 collimation optics
betatron
off-momentum
Name | Plane | Material | Length [cm] | Gap [σ] | Gap [mm] | δcut [%]
TCP.H.B1 | H | MoGr | 25 | 11 | 6.7 | 8.9
TCP.V.B1 | V | MoGr | 25 | 65 | 2.4 | -
TCS.H1.B1 | H | Mo | 30 | 13 | 3.8 | 6.7
TCS.V1.B1 | V | Mo | 30 | 75 | 2.5 | -
TCS.H2.B1 | H | Mo | 30 | 13 | 5.1 | 90.6
TCS.V2.B1 | V | Mo | 30 | 75 | 3.0 | -
TCP.HP.B1 | H | MoGr | 25 | 18.5 | 4.2 | 1.3
TCS.HP1.B1 | H | Mo | 30 | 21.5 | 4.6 | 2.1
TCS.HP2.B1 | H | Mo | 30 | 21.5 | 16.8 | 1.6
FCC-ee beam halo collimator parameters and settings
relatively high β-functions ↔ large beam sizes ↔ large collimator half-gaps
small Twiss α-functions ↔ small beam divergence
G. Broggi | First studies of crystal collimation for the FCC-ee
09/09/2024

## Slide 7
Divergence at crystal location and critical angle
Angular spread of a beam halo distributions with impact parameter b=10 μm at crystal candidate locations:
Si planar channel | U0 [eV] | [μrad]
(111) | 25.6 | 33.5
(110) | 22.8 | 31.6
(100) | 12.9 | 23.8
Si planar channel | U0 [eV] | 
(111) | 25.6 | 33.5
(110) | 22.8 | 31.6
(100) | 12.9 | 23.8
FCC-ee Z mode (E = 45.6 GeV)
U0: potential well depth of the planar/axial channel [eV]
E: particle energy [eV]
NOTE: At the highest FCC-ee beam energy of 182.5 GeV (ttbar mode) the critical angles reduce by about a factor 2 w.r.t FCC-ee Z beam energy
14.4 ± 0.7 μrad
H plane
b
V plane
3.6 ± 0.3 μrad
b
NO show stoppers identified
G. Broggi | First studies of crystal collimation for the FCC-ee
09/09/2024

## Slide 8
First focus on H plane – the study will then be extended to the V plane
Different bending angles scanned (50 μrad, 100 μrad, 150 μrad)
Bending radius R: to ensure smooth particle steering and enhance channeling efficiency
Crystal bending angle, bending radius and length
maximize impact parameter on absorber
safety margin w.r.t mechanical aperture (30 mm)
Critical bending radius (Si, E = 45.6 GeV)
U’(xmax): maximum potential gradient [eV/cm]
G. Broggi | First studies of crystal collimation for the FCC-ee
09/09/2024

## Slide 9
Channeling efficiency
Particles are considered channeled if:
: bending angle
: critical angle
Deflection of 100 μrad of 45.6 GeV e- using the Si (111) planar potential of a 100 μm long Si crystal.
Deflection of 100 μrad of 45.6 GeV e+ using the Si (111) planar potential of a 200 μm long Si crystal.
NOTE: safety margin w.r.t mechanical aperture for 150 urad angular kick is tight.
G. Broggi | First studies of crystal collimation for the FCC-ee
09/09/2024

## Slide 10
Collimation tracking simulations
beam halo
beam pipe aperture
bent crystals
BDSIM geometry
Simulation workflow:
  Stand-alone BDSIM simulation for FCC-ee (Z) beam halo interacting with bent crystal
  Channelled halo distributions used as input for Xsuite-BDSIM
  5x106 macroparticles (45.6 GeV) tracked through the FCC-ee lattice - including:
    Nonlinearities
    Synchrotron Radiation (mean model)
    RF cavities
    magnet tapering
    detailed aperture model
    halo and SR collimators
    For 1 machine turn.
Results compared with standard (amorphous) collimation system one-turn cleaning
G. Broggi | First studies of crystal collimation for the FCC-ee
09/09/2024

## Slide 11
One-turn cleaning of the e- beam
One-turn cleaning is comparable
In the crystal collimation case:
Replacement of primary collimators with 100 μm bent Si crystals (100 μrad bending angle)
  Most beam halo losses end up on the absorbers – as expected
  Significant reduction (up to a factor >100) of local losses in PF
  Increase of losses on a vertical SR collimator upstream IPD – to be investigated
G. Broggi | First studies of crystal collimation for the FCC-ee
09/09/2024
Standard collimation
Crystal collimation

## Slide 12
  Most beam halo losses end up on the absorbers – as expected
  Significant reduction (up to a factor >100) of local losses in PF
  Increase of losses on a vertical SR collimator upstream IPD – to be investigated
One-turn cleaning of the e+ beam
Replacement of primary collimators with 200 μm bent Si crystals (100 μrad bending angle)
G. Broggi | First studies of crystal collimation for the FCC-ee
09/09/2024
One-turn cleaning is comparable – compare again the performance considering smaller impact parameters b
In the crystal collimation case:
Standard collimation
Crystal collimation

## Slide 13
Summary
Crystal collimation might be an interesting solution for FCC-ee collimation
  Feasibility studies have started: no show-stoppers identified
  First crystal parameter optimization studies performed
    Planar channeling of e- and e+ in Si (111)
    100/200 μm Si crystals with 100 μrad bending angle
First collimation tracking simulations with crystals performed: performance gain over standard collimation cannot be demonstrated yet – further studies are needed (e.g., considering smaller impact parameters)
Next steps
Extend the analysis using more complete channeling routines including
Extend the analysis for studying crystal collimation in the V plane
Possibly extend the current analysis to:
  Axial channeling – potentially more promising for the e- beam
  (Multiple) volume reflection
Optimize absorber parameters (materials, length, retraction, etc.)
Extend the capabilities of the Xsuite-BDSIM simulation tool to allow for multi-turn collimation tracking with crystals
G. Broggi | First studies of crystal collimation for the FCC-ee
09/09/2024
radiation emission
strong field effects

## Slide 14
Thank you!
G. Broggi | First studies of crystal collimation for the FCC-ee
09/09/2024

## Slide 15
Oscillation period
Si crystal
dp: interplanar distance [Ang]
Umax: maximum potential well depth [eV]
E: particle energy [eV]
Planar channel | dp [A] | Umax [eV] | [um]
(111) | 2.35 (0.78) | 25.6 | 22.0
(110) | 1.92 | 22.8 | 19.1
(100) | 1.36 | 12.9 | 18.0
Planar channel | dp [A] | Umax [eV] | 
(111) | 2.35 (0.78) | 25.6 | 22.0
(110) | 1.92 | 22.8 | 19.1
(100) | 1.36 | 12.9 | 18.0
Z mode (E=45.6 GeV)
Planar channel | dp [A] | Umax [eV] | [um]
(111) | 2.35 (0.78) | 25.6 | 44.1
(110) | 1.92 | 22.8 | 38.2
(100) | 1.36 | 12.9 | 36.0
Planar channel | dp [A] | Umax [eV] | 
(111) | 2.35 (0.78) | 25.6 | 44.1
(110) | 1.92 | 22.8 | 38.2
(100) | 1.36 | 12.9 | 36.0
ttbar mode (E=182.5 GeV)

## Slide 16
Electron beam distribution impacting absorbers