## Slide 1
ESRF-EBS: a low emittance lattice
for high brilliance X-ray production

## Slide 2: outline
Synchrotron light sources:
beam emittance and brilliance
a brief history
lattice evolution
The ESRF EBS
design
commissioning
operation
Applications

## Slide 3: History of synchrotron radiation
X-rays were discovered in the late XIX century.
X-ray tubes are still used a lot, but they produce low brilliance beam.
The first synchrotron radiation (SR) was observed in 1947.
We talk about 4 generations of synchrotron light sources: from 1961 to 2020.
1024
1023
1022
1021
1020
1019
1018
1017
1016
1015
1014
1013
1012
1011
1010
109
108
107
106
1900 1920 1940 1960 1980 2000 2020
Brilliance (photons/s/mm2/mrad2/0.1%BW)
X-ray tubes
First generation
Second generation
Synchrotron Radiation
Third
generation
ESRF (2014)
ESRF (1994)
ESRF-EBS (2020)

## Slide 4: Beam emittance and Brilliance of synchrotron radiation
The brilliance is the main figure of merit for a synchrotron light source.
The brilliance is the number of photons in a small bandwidth per unit of time, area and solid angle. [#photons / (mm2 mrad2 0.1% bandwidth)]
Photon emittance from a single electron depends on the photon wavelength
1 nm rad for 100 eV
100 pm rad for 1 keV
10 pm rad for 10 keV
The reduction of the electron beam emittance is a way to increase the X-ray brilliance until we reach the diffraction limit.
The emittance is the area in the phase space of the electron or the photon beam. [pm rad] or [nm rad]
The emittance of the photon beam is the convolution of the emittance of the electron beam and the photon emittance from a single electron.

## Slide 5: First generation synchrotron light sources (1960-1970)
The first synchrotron light source is considered to be the 180 MeV synchrotron of the US national institute of standards and technology, where in 1961 a tangent section was added to extract the SR.
SR has been used in parasitic mode in many particle physics accelerators for decades.
First synchrotron radiation (SR) seen in 1947 from a 70 MeV synchrotron in the General Electric Laboratories

## Slide 6: Second generation light sources (1980)
Second generation light sources were dedicated to Synchrotron Radiation. Mostly based on Chaseman-Green Double Bend Achromat (DBA) lattice cells.
1981: University of Wisconsin Synchrotron Radiation Center 1 GeV storage Ring
1982: National Synchrotron Light Source (NSLS at Brookhaven National Laboratory) 700 MeV and 2.5 GeV storage rings
1982 – Tsukuba KEK Laboratory 2.5 GeV storage Ring – Photon Factory
1982 – Berlin 0.8 GeV storage Ring – Bessy I
France: 1987 – Orsay – Lure Laboratory 0.8 GeV storage Ring – Super-ACO
Then SSRL in Stanford, HasyLab at Dasy, SRS at Daresbury.

## Slide 7: 3rd generation from the (1990-2000-2010)
A few high energy machines:
1994: ESRF in Grenoble (France) 6 GeV, 844 m
1995: APS in Argonne (USA) 7 GeV, 1100 m
1997: Spring8 in Japan 8 GeV, 1500 m
2009: Petra III in Hamburg (Germany) 6 GeV, 2300 m
And a lot of 1.5 to 3.5 GeV small machines
Elettra (1993), ALS (1993), Bessy2 (1998), Anka (2000), Diamond (2001), Soleil (2006), Alba (2012), NSLSII (2015), Solaris (2016), …
From third generation, the SR is regularly produced by undulator magnets.
Spring8

## Slide 8: Fourth generation (2015-2020)
Fourth generation synchrotron light sources are based on Multi-Bend achromat lattices, with more than 1 order of magnitude emittance reduction.
Max-IV (3 GeV) and ESRF-Extremely brilliant source (EBS) (6 GeV) are the first two of them.
ESRF-EBS
Max-IV

## Slide 9: Sources of radiation
There are two possible sources of radiation in synchrotron light sources: the bending magnets and the undulators.
Bending magnet
Undulator

## Slide 10: Bending magnets radiation
Spectrum from a 0.679 T bending magnet with a 8 GeV beam (Spring8).
Critical energy 28.9 keV.
First and second generation synchrotron light sources were taking the radiation from the bending magnets.
Electrons
Photons
Critical photon energy: half of the power is radiated at larger energy and half at lower
Power emitted by an ultra-relativistic
particle in a bending magnet
r is the radius of curvature
Bending magnet

## Slide 11: Undulator radiation
Fundamental undulator wavelength l1
The undulator parameter K<1 can be changed by varying the magnetic gap.
Undulators and wigglers magnets were first proposed in the ‘40s, then the first undulator was installed in a Linac at Stanford in 1953.
Third and fourth generation synchrotron light sources produce the radiation mostly from undulators.

## Slide 12: How emittance is generated: damping + diffusion
High energy particles emit more SR than low energy ones. RF cavities give back the same amount of energy to all the electrons. The energy oscillates and damps to the nominal value. This would send the energy spread to zero.
In the old ESRF:
τs = 3.5 ms, fs = 2.1 kHz
In the EBS:
τs = 9.1 ms, fs = 1.3 kHz
The graininess of the photon emission cause a fluctuation of the residual electron energy.
Many weak dipoles would reduce the average energy of the radiated photons and decrease the quantum fluctuation.

## Slide 13: Distribution of the stored electrons
Only radiation damping
Radiation damping and quantum diffusion
Dipoles bend more the low energy electrons: energy spread becomes horizontal position spread.
The emittance is the equilibrium between radiation damping and quantum diffusion.

## Slide 14: Lattice evolution: FODO
QF
QD
Bending magnets
Most of the colliders have long arcs with periodic FODO lattices:
QF - dipole - QD - dipole
FODO lattices are not designed for low emittance.
b functions (envelope of transverse oscillations) are oscillating

## Slide 15: Lattice evolution: Double bend achromat
Most of 2nd and 3rd generation synchrotron light sources use the Chaseman-Green Double Bend Achromat (DBA) lattice cells proposed in the ‘70s and used for about 40 years.
An achromat is a lattice that starts and ends with zero dispersion.

## Slide 16: First proposal of Multi-Bend Achromat lattice
1995: D. Einfeld and J. Schaper propose the Multi Bend Achromat low-emittance lattice.
Many weak dipoles in each cell, to reduce the energy of the emitted photons.
DIFL, proposed in 1995:
7 bend achromat, 3 GeV, 500 pm
Max IV, built in 2016:
7 bend achromat, 3 GeV, 350 pm

## Slide 17: challenges of Multi-bend achromats
Many weak dipoles and small beta-functions => strong quadrupoles and large chromaticities
Many weak dipoles => small energy dispersion => strong sextupoles => bad nonlinear dynamics
Still the Max IV ring works, but a new design has been proposed in 2012 by Pantaleo Raimondi.
Hybrid Multi-Bend Achromat lattice (ESRF-EBS)
Multi-Bend Achromat cell (Max-IV)
The Hybrid Multi Bend Achromat:
two dispersion bumps at –I phase advance, inspired by the Super-B factory lattice.
Nonlinear resonances are canceled thanks to the –I phase advance between the sextupoles.
Less and weaker sextupoles than standard MBA.

## Slide 18: outline
Synchrotron light sources:
beam emittance and brilliance
a brief history
lattice evolution
The ESRF EBS
design
commissioning
operation
Applications

## Slide 19: Nonlinear dynamics: Dynamic aperture
The dynamic aperture is the area of the stable region in the 6D phase space coordinates.
In a linear machine it would be infinite. Sextupoles are needed for chromaticity correction, but they create chaotic motion at large amplitudes.

## Slide 20: Nonlinear dynamics: Dynamic aperture
Injection is performed off-axis. So the dynamic aperture has to be large enough to accommodate the injected beam and the thickness of the septum blade.

## Slide 21: Nonlinear dynamics: Touschek lifetime
Touschek effect is a large angle electron electron scattering inside a bunch.
It has been first observed at AdA.
Horizontal momentum is transferred to longitudinal, exceeding the momentum acceptance.
The 2 electrons are lost!
x
z
The Touschek effect is the main lifetime limitation in the electron storage rings.

## Slide 22: Nonlinear dynamics Optimizations
Nonlinear dynamics optimizations are strongly based on multi-objective evolutionary algorithms (NSGA2, MOPSO, …) or parameter scans.
Big computer cluster are needed to design new storage rings.
The Touschek lifetime simulations require to find the momentum acceptance by particle tracking

## Slide 23: error studies
Source of errors:
Alignment x,y,z
Tilts
Power supplies
Multipole components
Each error source has been studied to find the tolerable value, giving a small reduction of dynamic aperture and Touschek lifetime.

## Slide 24: the ebs upgrade at esrf
Dipole
Dipole
Dipole
Dipole
Dipole
Dipole
Dipole-quadrupoles
Sextupoles
Sextupoles
Sextupoles
Quadrupoles
Quadrupoles
Quadrupoles
Quadrupoles
Quadrupoles
Octupole
Octupole
Magnet type | ESRF | ESRF EBS
Dipoles | 64 | 128
Dipole-Quadrupoles | 0 | 96
Quadrupoles | 256 | 512
Sextupoles | 224 | 192
Octupoles | 0 | 64
Correctors | 0 | 96
The ESRF Extremely Brilliant Source (EBS) has 31 magnets per cell instead of 17 of the old machine.
Free space between magnets (for one cell): 3.4 m instead of 8 m.
Dipoles cover 38% of the total length instead of 18%.

## Slide 25: EBS components: magnets
128 [132] Permanent Magnet Dipoles
96 [100] Dipole-quadrupoles
512 Quadrupoles
(128 [132] HG, 384 [392] MG)
192 [196] Sextupoles
96 [98] Correctors
64 [66] Octupoles
More than 1000 Magnets
Assembled in house
TESLA
TESLA (MG)
DANFYSIK
DANFYSIK (HG)
BINP
SEF

## Slide 26: Preparation of the tunnel
The EBS has been installed in the tunnel of the old machine.
Storage ring tunnel during the 2019 shutdown.

## Slide 27: Preparation of the tunnel

## Slide 28: Installation of the EBS
Preassembled girders lifted from the roof.

## Slide 29: Installation of the EBS
The girders have been driven to their location in the tunnel with a special vehicle.

## Slide 30: DQ2 installation
DQ2 magnets in between two girders installed from the roof.

## Slide 31: ESRF Booster adaptations
Linac
Gun
KI
SI
TL1
KE
SE1
B3
B2
B1
TL2
RF
CTRM
The ESRF booster has a FODO lattice with three arcs and three straight sections: injection, extraction, RF.
Only two quadrupole families and two sextupole families.
Off-energy operation:
ex = 120 nm => 85 nm.

## Slide 32: Hardware modifications: Booster CIRCUMFERENCE reduction
Length of old ESRF: 844.391 m (fRF = 352.1997 MHz)
Length of EBS: 843.977 m (fRF = 352.3722 MHz)
RF frequency of EBS is 172 kHz higher than for ESRF.
The booster had to share the same RF source, so it had to be realigned to reduce its circumference, but it runs off-energy with 40 kHz mismatch.
Length of the booster with EBS: = 299.51 m, instead of 299.62 m
All the girders have to be moved by 17.5 mm, perpendicularly to the beam trajectory.
Off-energy operation: electrons are bent by dipoles and quadrupoles
=> more damping, smaller emittance: 120 nm => 85 nm.

## Slide 33: Booster realignment
The 17.5 mm displacement of the main girders of the arcs is within the range of adjustment capability.
Distance between two dipoles is reduced by 1.5 mm and bellows can handle the reduction.

## Slide 34: Booster emittance exchange
With emittance exchange in the booster, the injection efficiency improved by 5-10%
Vertical tune
Time from injection (ms)
The vertical tune is changed by 0.1 at extraction time
Emittance exchange in the booster done by crossing the tunes changing the vertical quickly

## Slide 35: ESRF-EBS: beam Commissioning
December 15th
Accumulation
December 6th
Beam stored
November 28th
First turns
January 30th
First Beam on 26 Beamlines
February 28th
200 mA achieved
3 physical obstacles on the beam path and poor vacuum in a few ID NEG coated chambers slowed down the overall commissioning.

## Slide 36: ESRF-EBS: beam Commissioning – physical obstacles found
3 physical obstacles on the beam path found during commissioning.
Detected, get around, resolved by:
Very useful beam loss and turn by turn BPM diagnostics
Bumps, non-closed injection bump, off-energy operation, distorted close orbit,,…
Intervention to remove the obstacles one by one
Largely beneficial to injection efficiency, lifetime, optics tuning
Piece of wire accidently into SS-23 ID chamber
Installation mistake Cell8-Bellow 9-11
Obstacle in Cell-5 Ch7
AL piece fall during installation of DQ2
Nominal position
Installation error in cell8

## Slide 37: ESRF-EBS: beam Commissioning – cross talk between magnets
Magnetic simulations show a cross-talk effect among neighboring magnets.
G.Le Bec, J.Chavanne
-0.8%*QD2A
+1.3% *QF4B
model tunes: 76.2100 27.3400
+ Cross Talks: 76.6973 26.0038
-1.3 Qy
Thin lens fix field multipole
Gradient recomputed + calibration scaling

## Slide 38: Da studies: dA vs orbit correctioN
Better orbit correction gives a smaller beta-beating and larger dynamic aperture
 Smaller closed orbit residual 
 Smaller closed orbit residual 
Decided from these simulations to go to 162
Orbit correction is performed with an SVD pseudo-inversion of the orbit response matrix (ORM).
ORM has 288 lines and 320 columns. During the design phase we were using only 64 eigenvectors to limit the correctors strengths.
64 eigenvectors

## Slide 39: ESRF-EBS: Commissioning from 28/11 to 01/04
SR current ramping
Injection efficiency
30%
0.1%
20%
55%
5%
90 %
200 mA
Beamline commissioning
Winter shutdown
75%
28/11/2019
01/04/2020

## Slide 40: Reliability of EBS very high
User mode of EBS started in mid 2020.
Statistics of beam availability are improving and are now at the level of the old machine.
 | 2017 | 2018 | 2020 | 2021 | 2022 | 2023(07)
 |  |  | EBS | EBS | EBS | EBS
Availability (%) | 98.3 | 98.5 | 96.1 | 96.4 | 99.1 | 99.3
Mean time between failures (h) | 64.3 | 104.3 | 46.0 | 66.4 | 88.5 | 121.7
Mean duration of a failure (h) | 1.11 | 1.60 | 1.80 | 2.42 | 0.83 | 0.8

## Slide 41: Further improvements of the EBS: vertical halo reduction
The EBS is operated with low vertical emittance: ey=10 pm
sy about 10 mm,
but a small fraction at hundreds of sigmas: the beam halo
Beam halo does not allow to close more the undulator gaps
Brilliance of an invacuum undulator
From simulation, we see that off-energy particles can cross a resonance and start to have large vertical oscillations.
Different low halo optics have been tested and will allow low-gap operations. Results will be published soon.

## Slide 42: Further improvements of the EBS: off-energy operation
Operating the EBS with a 1% lower energy (RF frequency 300 Hz higher) the horizontal emittance is 20 % smaller.
Electrons pass off-axis in the quadrupoles and emit some more radiation, reducing the equilibrium emittance.
For some undulators harmonics, the gain in brilliance by operating off-energy can be about 10 %.
The off-energy operation mode is under study. Results will be published soon.

## Slide 43: Further improvements of the EBS: harmonic cavity
A fourth harmonic RF cavity at the correct amplitude and phase => bunch length increase by a factor 3 to 5.
Touschek lifetime is increased by the same factor.
The beam is more stable and less affected by collective effects.
A design of an active copper cavity has been done and a prototype should be produced.

## Slide 44: outline
Synchrotron light sources:
beam emittance and brilliance
a brief history
lattice evolution
The ESRF EBS
design
commissioning
operation and future improvements
Applications

## Slide 45: BM 18, a new beamline designed for the EBS
BM 18 is a very long new beamline taking the light from a 1.56 T 3 poles wiggler.
Lung of a covid patient
Specialized in high resolution imaging of large samples
Hominid skull
fossil of arthropod in an amber block
High value objects

## Slide 46: 9 ERC grant currently at the ESRF
The ESRF EBS has 40 beamlines with very wide research topics.
Currently, there are 9 European Research Council grants on different topics and in different beamlines.

## Slide 47: Many thanks for you attention