## Slide 1
Plasma sources design for plasma-based accelerators
Angelo Biagioni
Lucio Crincoli
Angelo.Biagioni@lnf.infn.it
Laboratori Nazionali di Frascati INFN, 6 Aprile 2024

## Slide 2
What is a plasma?
Principles of accelerator physics
Plasma-based particle acceleration
SPARC_LAB test facility
  Gas-filled capillary plasma source
Plasma module to confine and characterize plasmas
How is the capillary characterized?
  Stark broadening technique
  Outside the capillary
Contents

## Slide 3
Cold or non-thermal plasma is less well ionized:
although the electrons are high temperature, the positive ions and neutral particles are at a lower temperature. When a fluorescent lighting tube is switched on, cold plasma (at room temperature) is set up within the tube.
The plasma approximation: Charged particles must be close enough together that each particle influences many nearby charged interacting with the closest particle (these collective effects are a distinguishing feature of a plasma). The plasma approximation is valid when the number of electrons within the sphere of influence (called the Debye sphere whose radius is the Debye (screening) length) of a particular particle is large.
Examples of plasma:
Aurora
Sun
What is a plasma?

## Slide 4
Bulk interactions: The Debye length is much smaller than the physical size of the plasma. This criterion means that interactions in the bulk of the plasma are more important than those at its edges, where boundary effects may take place. When this criterion is satisfied, the plasma is quasineutral.
Collisionessless: The electron plasma frequency (measuring plasma oscillations of the electrons) is much larger than the electron–neutral collision frequency. When this condition is valid, electrostatic interactions dominate over the processes of ordinary gas kinetics. Such plasmas are called collisionless.
Artificial plasmas:
Ip = 0.3 – 1 kA
Tp ~ 2-10 eV
Vp = 5-20 kV
Natural plasmas
Artificial plasmas
Natural plasma:
Ip = 10-200 kA
Tp ~ 4-5 eV
Vp =106 kV
What is a plasma?

## Slide 5
Main components of an accelerator:
Particle source
  Thermoionic gun
  Photocatode
Accelerating RF structure
Magnets for beam guiding
Vacuum system
Particle source
N
N
S
S
Magnet
RF structures
Principles of accelerator physics

## Slide 6
Dipole
Quadrupole
A particle accelerator is a device that uses electromagnetic fields to propel charged particles to high speeds and to contain them in well-defined beams.
ELECTRIC FORCE:
Used to accelerate the particles
MAGNETIC FORCE:
Used to bend and focus the beam
-
Principles of accelerator physics

## Slide 7
Speed of light (c)
Velocity
Energy
Energy gain:
One electron is accelerated with 1V gain an energy of 1eV
Accelerating a particle does NOT necessarily signify increasing the velocity. What increases is p=mv
One electron becomes relativistic (velocity close to c) when his energy E>5MeV
One proton needs an energy 1000 more than an electron to become relativistic.
Light particles
Heavy particles
Principles of accelerator physics

## Slide 8
Main limitations
Circular accelerators:
  Heavy particles , strong magnetic fields are required
  Light particles -> Synchrotron radiation
Linear accelerators:
  Limited gradient to avoid discharges
Principles of accelerator physics

## Slide 9
Plasma Wakefield acceleration
Plasma density measurement represents a crucial point to implement plasma-based devices.

## Slide 10
An intense laser beam is used to drive a relativistic plasma wave, within which are formed strong longitudinal electric fields able to accelerate beams of charged particles.
A driver bunch of ultra-relativistic electrons or protons are sent through a stationary plasma
Plasma
e-
DRIVER
Plasma Wakefield acceleration

## Slide 11
1
2
4
Linear regime
Quasi-Linear regime
Non-Linear regime
Linear regime (α < 1)
Weakly NL regime (α = 1)
Non-linear regime (α > 1)
Plasma Wakefield acceleration

## Slide 12
Active Plasma Lenses
90 μm
25 μm
Focusing (Compactness)
Bφ > 500 T/m
Plasma-based focusing

## Slide 13
Advantages of plasma accelerators:
Compactness
Accelerating gradient
S-band accelerating structures(2): 20 MV/m
C-band accelerating structures(3): 35 MV/m
Up to 10-100 GV/m for Plasma-based
accelerating structures
Sparc_lab test facility
SPARC_LAB test facility

## Slide 14
e-beams have to be produced and prepared for plasma modules (hundreds of MV/m)
RF-Gun
RF-band
Plasma module
FEL
Users
Energy increasing up to several GV/m:
PWFA
LWFA
At EuPRAXIA@SPARC_LAB user facility
SPARC_LAB test facility

## Slide 15
COMB Chamber
SPARC_LAB test facility

## Slide 16
Integrated capillary for stage focusing and acceleration
Plasma capillary
Plasma capillary
Focusing
lens
Acelerating
section
Extraction
lens
Integrated plasma module
Alinegment issues
Compactness (20 cm)
No motors to move PMQs
Strong current-modulated magnetic field (1 kT/m)
Lens ON Acc ON Lens ON
3 us
Acc-200A
Lens-500A
Current pulses
Plasma formation
Quadrupoles are essential
to achieve plasma acceleration
Active plasma
lens

## Slide 17
Integrated capillary for stage focusing and acceleration
Driver
Witness
5 MeV/3cm acceleration in 19 cm long integrated plasma module with 200 pC driver/50 pC witness
  3 cm long accelerator with 200 A ionization current
  3 cm long plasma lenses with 500 A ionization current
  Plasma density inside the accelerator set to 2x1015 cm-3
  ~150 MV/m accelerating gradient
  Stability of the accelerated beam

## Slide 18
3cmx1mm
two inlets
10cmx1mm
single inlet
Gas-filled capillary plasma source

## Slide 19
Plasma module to confine and characterize plasmas
Capillary shapes:
Length (Energy)
Radius (Density)
Spectrometer:
Grating
Optical alignment
Camera timing:
Delay time
Gate time
Timing:
Valve opening time
Voltage delay time
Trigger of ICCD camera

## Slide 20
ICCD
camera
Spectrometer
Vacuum
10-7 mbar
Plasma Diagnostic
Discharge circuit – 550 A
Capillary
Gas injection system – 3 ms
Current pulse
Our chamber is an experimental chamber that is a little bit different from the real COMB chamber used on the accelerator machine
Gas injection
Capillary shape | 3 cm 1mm | 10 cm 1mm | 40 cm 1mm
Opening time | 5 ms | 14 ms | 48 ms
Voltage | 6 kV | 11 kV | 60 kV
Parameters: 10 Hz/3 ms | 
Duration | Vacuum (mbar)
Starting values | 1.3x10-9
t0 | 4.3x10-8
60 min | 6.4x10-8
Vacuum
Plasma module to confine and characterize plasmas

## Slide 21
Using Paschen curves it is possible to determine the minimum HV to apply for producing plasma
First step: producing the plasma
10 cm - 1 mm
3 cm - 1 mm
3 cm - 1 mm
3 cm - 2 mm
1 cm - 1 mm
2 cm - 1 mm
Vb (V)
PRESSURE LENGTH | 600mbar | 800mbar | 1000mbar
1cm | 600 | 800 | 1000
3cm | 1800 | 2400 | 3000
10cm | 6000 | 8000 | 10 000
Plasma module to confine and characterize plasmas

## Slide 22
Mirror 1
Mirror 2
Mirror 3
Lens 1
Lens 2
p
q
f
In case of two lenses, there will be p1 and p2, q1 and q2, f1 and f2
MAGNIFICATION FACTOR:
LENSMAKER’S EQUATION:
Plasma discharge capillary characterization

## Slide 23
434nm
488nm
656nm
Lyman Series:
91-121 nm -> UV region
Balmer Series:
364.6- 656 nm -> visible region
Paschen Series:
1458-4051 nm -> IR region
Hydrogen Balmer series spectral lines of emission
Stark broadening technique

## Slide 24
434nm
488nm
656nm
wavelength
Stark broadening effect
Stark broadening technique

## Slide 25
By using the Stark broadening method to measure the plasma density, we obtain the following results:
the larger is the Balmer line (Δλ), the higher is the electron density of plasma
Tabulated α values
Broadening of
the spectral line
Stark broadening technique

## Slide 26
Position (mm)
λ (nm)
Electrode
shadow
Plasma
channel
Plasma plume
Δλ
Balmer β line
Capillary
Images acquired by using an ICCD camera:
Gate: 100 ns
Delay: 500-2500 ns
Area: 1024 x 255 pixel
Stark broadening technique

## Slide 27
Longitudinal characterization
Temporal characterization
Stark broadening technique

## Slide 28
In order to understand what happens to the electron beam outside of the capillary we have studied the plasma parameters in such areas:
Plasma density
Velocity of plasma
Dielectric capillary
Plasma discharge
Electrode shadows
+V
-V
L = 30 mm
Electrode
H2 inlets
Ø = 1 mm
e-
Outside capillary:
Plasma plumes
Outside the capillary

## Slide 29
L = 30 mm
Electrode
H2 inlets
Ø = 1 mm
e-
Plasma plumes depend on different conditions of pressure, temperature and density between inside and outside (vacuum) of the capillary
The expansion velocity and so the plume lengths depends on several terms as the dicharge voltage and the geometric properties of the capillary
Plasma
discharge
Plasma
plume
Outside the capillary

## Slide 30
Photocathode side: POSITIVE
Undulator side: NEGATIVE
Delay: 20 images separated by 100 ns = 2 µs
Gate: 10 ns
Area: 1000 x 500 pixel
Outside the capillary

## Slide 31
Discharge voltage 18 kV
Capillary
Electrode
Plasma channel
20 mm/2 μs
Vacuum
Plasma density ramps at the ends of the capillary can reach a total expansion length around 40 mm (20 mm each one) that is comparable with the channel length of 30 mm, so they can strongly affect the beam properties that passes through the capillary
Biagioni et al. (2019), DOI: 10.1088/1748-0221/14/03/C03002
Outside the capillary

## Slide 32
Thank for your attention