## Slide 1: (n,cp) measurements at n_TOF for tritium breeding in nuclear fusion reactors
Giulio Perfetto, Uniba and INFN sezione di Bari
2025 September 28th - October 5th, Monopoli (Bari) - Italy

## Slide 2: Outline
Nuclear fusion and tritium breeding
The SINBA detector at n_TOF
Results of GEANT4 simulations

## Slide 3: The Tritium cycle in fusion reactors
Lithium (breeder) and Beryllium (neutron multiplier)
in the breeding blanket
Tritium is radioactive and rare
Objective:
Tritium Breeding Ratio >1
(14.2 MeV)

## Slide 4: New measurements are essential to model the TBR accurately
Neutron Energy
We have submitted a proposal to the INTC:
https://cds.cern.ch/record/2929615/files/INTC-P-739.pdf?version=1
n +  α + t
  Very high cross section at low neutron energies
  Burns neutrons
  Well known and modelled
n +  α + t + n’
  Cross section peaks around 6 MeV
  Does not burn neutrons
  Missing data and discrepancies.
Li produces Tritium through (n,cp) reactions: a nucleus capture a neutron and emits a light charged particle.

## Slide 5: The n_TOF facility @CERN
Neutron beam, produced by spallation of protons.
Measurement of neutron-induced reactions cross sections.
Unique features: high intensity and neutron energy range from thermal to GeV  Suitable for new (n,cp) measurements
EAR2
EAR1

## Slide 6: The SiNBa detector
The SIlicon Ntd Barrell detector: two double sided annular detectors and four squares, arranged in a cylindrical geometry.
Expected efficiency ≈ 35/40 %
Highly segmented:
Angular acceptance:
  20° - 35° forward
  130°-150° backward
  37°-78° square

## Slide 7: Innovative features of this measurement
An example of different Pulse shapes and identification matrices. From Assié, M. et al, “Characterization of light particles (Z ≤ 2) discrimination performances by pulse shape analysis techniques with high-granularity silicon detector.”
Pulse Shape Discrimination + Digital Pulse Shape analysis
This combination allows for the measurement of interactions across a wider neutron energy range compared with traditional techniques.

## Slide 8
Preliminary Experimental test
Noise ≈ 50 keV
Background ≈ 250 keV
Empty
LiF
Preamplifier signals

## Slide 9: GEANT4 Simulation Results
Neutron
4 cm
4.5 cm
Neutrons
5 cm
7 cm
Annular
Square Sample

## Slide 10: Alpha particles are more sensitive to identification threshold in
2 MeV
2 MeV
Efficiency corrections needed

## Slide 11: Background and coincidences in sample
Alpha and Triton Coincidences > 1 MeV
BA
FA
S
1H/2H are expected to be negligible < 14 MeV
BA
FA
S

## Slide 12: Conclusions
First experimental test planned for end of 2025
Tritium breeding is essential for fusion, but key experimental data are missing.
We developed the SiNBA detector and MC simulations confirm its suitability for (n,cp) measurements.
A Proposal to the INTC was approved for Lithium, and an addendum for Beryllium was submitted.

## Slide 13
THANKS !
Giulio Perfetto PhD Student, University of Bari & INFN Sezione di Bari g.perfetto1@phd.uniba.it
Supervisor: Nicola Colonna INFN Sezione di Bari & n_TOF Collaboration nicola.colonna@ba.infn.it

## Slide 16: The ML algorithm
From G. Vecchio et al 2022 JINST 17 P09040, “Pulse identification and shape analysis by derivative-based peak detection using a Convolutional Neural Network”
Traditional threshold-based techniques
Pulse discrimination with CNN and adaptive threshold
CNN

## Slide 17: Neutron damage
(n,cp) reactions: a nucleus capture a neutron and emits a light charged particle.
Very troublesome. They cause formation of bubbles in material that severely alter the thermomechanical properties.
TEM image of He bubbles in various metals. From Li,S. et al “Radiation-Induced Helium Bubbles in Metals”
We are working on a proposal for the INTC related to this issue

## Slide 18: Identification and background for sample
PID threshold is not an issue
1H/2H are expected to be negligible < 14 MeV

## Slide 19: Detector Efficiency with Alpha Particles
Alpha Point-Like isotropic source 5 MeV energy
Total ε = 36.8 ± 0.2 %
Annular
Square
backward
forward