## Slide 1: IDEA VERTEX DETECTOR INTEGRATION
Filippo Bosi1
G. Baldinelli2, M. Boscolo3, F. Fransesini 3, S. Lauciani 3, F. Palla1, C. Turrioni2
1INFN Sezione di Pisa, Italy
2INFN Sezione di Perugia, Italy
3INFN Laboratori Nazionali di Frascati (RM), Italy
RD _FCC WP- SILICON MINI-WORKSHOP
TORINO
April 22-23, 2024

## Slide 2: Requirements
Interaction region detectors must be integrated with the beam pipe
  The vertex detector innermost radius should profit of the reduced beam pipe diameter (2 cm) and should cover
  Must not interefere with the Luminosity Calorimeter (clearance of ~120 mrad)
  The mounting of the vertex tracker must be done inside the support tube
  Minimize the radiation lengths
RD _FCC WP- SILICON MINI-WORKSHOP

## Slide 3
Inner Vertex detector:
Modules of pixel size
3 barrel layers at
13.7, 22.7 and 34.8 mm radius
Outer vertex tracker:
Modules of pixel size
Intermediate barrel at 13 cm radius (improved reconstruction for)
Outer barrel at 31.5 cm radius
3 disks per side
DRIFT CHAMBER
EXSTERNAL CILINDER
OUTER TRACKER
MEDIUM TRACKER
INNER TRACKER
DISK 3
DISK 3
DISK 1
DISK 1
DISK 2
DISK 2
RD _FCC WP- SILICON MINI-WORKSHOP

## Slide 4: Sensors technology and dimensions
Depleted Monolithic Active Pixel Detectors
  Inner Vertex (inspired to ARCADIA):
    Lfoundry 110 nm process
    50 µm thick, 25 µm x 25 µm
    Module dimensions:
    Power density (core )
    Current at 100 MHz/cm2
  Outer Vertex and disks (inspired to ATLASPIX3)
    TSI 180 nm process
    50 µm thick (50 µm x 150 µm)
    Module dimensions:
    Power density: assume
    Up to 1.28 Gb/s downlink
RD _FCC WP- SILICON MINI-WORKSHOP

## Slide 5
Layer 1
15 overlapping staves of 6 modules each
Overlap to allow alignment ~500 µm
Pinwheel geometry: all modules at the same (smallest) radius
Power budget ~12 W
Total weight ~22 grams
Total thickness 0.25% X0
Silicon: 0.053% X0
Power and readout bus: 0.056% X0
RD _FCC WP- SILICON MINI-WORKSHOP

## Slide 6: Layer 1 stave detail
Reticular lightweight support to provide stiffness
Thin carbon fiber walls interleaved with Rohacell
2 buses (data and power) 1.8 mm wide and 250 µm thick (50 µm Al, 200 µm kapton) per side
  Inspired to low mass hybrid R&D
Sensors facing interaction point w/o any other material in front
Readout chips either sides
Air cooled

## Slide 7
Layer 2
24 overlapping staves of 10 modules each
Pinwheel geometry
Counter-rotated wrt layer 1 to mitigate charge-asymmetry effects in track reconstruction
Power budget
~32 W
Total weight ~63 grams
Total thickness 0.25% X0
RD _FCC WP- SILICON MINI-WORKSHOP

## Slide 8
Layer 3
36 staves of 16 modules each
Lampshade geometry.
Charge symmetric track reconstruction
Total weight ~150 grams
Total thickness 0.25% X0
Power budget
~77 W
RD _FCC WP- SILICON MINI-WORKSHOP

## Slide 9
Cooling Third layer
Cooling Second Layer
Cooling First Layer
Cooling Pipe
Inner vertex detector is supported by a conical structures in carbon fiber on elliptical chamber
~450 grams
The support is engineered for air ducts and thermal isolation from the beam pipe during bakeout
RD _FCC WP- SILICON MINI-WORKSHOP

## Slide 10: Inner Vertex support
Anchored to the conical chamber
Air cooled
Thermally isolated from the beam pipe during bakeout, by peek supports
Cooling Third layer
Cooling Second Layer
Cooling First Layer
Cooling Pipe
Air Cooling
Cables
Paraffine for pipe cooling
RD _FCC WP- SILICON MINI-WORKSHOP

## Slide 11: AIR COOLING DUCTS AND AND BELLOWS
RD _FCC WP- SILICON MINI-WORKSHOP
Contact with the beam pipe

## Slide 12
Elastic connection
Inner Tracker
Service cones for cooling and cables
Cone exit cable layer3-Cooling in layer3
Cone exit cable layer2-1-Cooling in layer 2-1
RD _FCC WP- SILICON MINI-WORKSHOP

## Slide 13
AIR COOLING CONE LAYER 1-2
RD _FCC WP- SILICON MINI-WORKSHOP
Attack of the air cone to the support carbon fiber
Bellows

## Slide 14: AIR COOLING LAYER 3
RD _FCC WP- SILICON MINI-WORKSHOP
Attack of the air cone to the support carbon fiber
Bellows

## Slide 15
Air cooling (simulations)
Cooling with air/He flow along the detector.
  Air temperature: Tair = 15°C
  Max sensor temp on layer 3 (hottest one) ~25/30 ºC with He/Air.
  Vibrations studies ongoing
Air inlets
Air outlets
Air flow
Inner Tracker
Disk 3
Disk 2
Disk 1
RD _FCC WP- SILICON MINI-WORKSHOP

## Slide 16
Middle Barrel
At 13 cm radius
22 staves of 8 modules each.
Lightweight reticular support structure (ALICE/Belle-II like)
Readout chips either side
Power budget
~342 W
Total weight ~1 kg
Water cooled (2 pipes of 2 mm diameter)
Similar prototype
built @ Pisa
Outer barrel is similar but longer (see backup)
RD _FCC WP- SILICON MINI-WORKSHOP

## Slide 17
Outer Vertex Tracker Barrel
At 31.5 cm radius
51 staves of 16 modules each
Lightweight reticular support structure (ALICE/Belle-II like)
Total weight ~3.7 kg
Readout chips either side
Power budget
~1400 W
Water cooled (2 pipes of 2 mm diameter)
RD _FCC WP- SILICON MINI-WORKSHOP
Notes: NB. Qui la struttura reticolare deve stare giù perché sennò non si riesce ad ottenere il raggio esterno più grande e vicino alla DCH.

## Slide 18
Outer Vertex Tracker Disk 1
2 sides (front and back) each with 4 petals.
One petal is made of different staves of overlapping modules
Total modules per disk: 196
Total weight ~850 grams
Power budget ~ 336 W
Cooling using 1 water pipe (2 mm diameter)
Similar geometry for the other two disks
RD _FCC WP- SILICON MINI-WORKSHOP

## Slide 19: Overall layout and dimensions
RD _FCC WP- SILICON MINI-WORKSHOP

## Slide 20: Simulated material budget
In agreement with CAD estimates
Smaller X/X0 wrt IDEA CDR estimates even including power and readout cables in the sensitive region
Silicon only ~15% of the total
Inner Vertex only
Beam pipe
RD _FCC WP- SILICON MINI-WORKSHOP

## Slide 21: Support cylinder
All elements in the interaction region (Vertex and LumiCal) are mounted rigidly on a support cylinder that guarantees mechanical stability and alignment
  Once the structure is assembled it is slided inside the rest of the detector
Aluminium ribs
Aluminium endcaps
1mm CF + 4mm HC + 1mm CF
    M. Boscolo, F. Palla, F. Fransesini, F. Bosi and S. Lauciani, Mechanical model for the FCC-ee MDI, EPJ Techn Instrum 10, 16 (2023). https://doi.org/10.1140/epjti/s40485-023-00103-7

## Slide 22: Conclusions
A Vertex Detector layout for IDEA detector concept has been engineered
  Uses low power, thin (50 µm) DMAPS technology
  Integration with the machine detector elements developed
  Services integration and cooling being finalised
  Material budget kept at the level of per layer
  Documented in
    M. Boscolo, F. Palla, F. Fransesini, F. Bosi and S. Lauciani, Mechanical model for the FCC-ee MDI, EPJ Techn Instrum 10, 16 (2023). https://doi.org/10.1140/epjti/s40485-023-00103-7
RD _FCC WP- SILICON MINI-WORKSHOP

## Slide 23: Thank you for your attention.
23

## Slide 24: Backup

## Slide 25: Outer Tracker and Disks
RD _FCC WP- SILICON MINI-WORKSHOP

## Slide 26: MIDDLE TRACKER
RD _FCC WP- SILICON MINI-WORKSHOP

## Slide 27: OUTER TRACKER
RD _FCC WP- SILICON MINI-WORKSHOP

## Slide 28: DISK 2
RD _FCC WP- SILICON MINI-WORKSHOP

## Slide 29: DISK 3
RD _FCC WP- SILICON MINI-WORKSHOP