## Slide 1: Update on the activities in Milano
M. Citterio and N. Neri
on behalf of INFN and University of Milan
SuperB Meeting: SVT Parallel Session

## Slide 2: Bus status (1 of 2)
  Production of BUS is finally starting
    The layout is final and «single» layers are at the beginning of the production
      Opening on the ground/power planes have been agreed upon
      Production will take approximately 5 weeks
    Bonding Scheme (Bus to Sensor and FE chip) .... We really hope is it acceptable to Pisa  see next slide

## Slide 3: Bus bonding Scheme (2 of 2
It could be feasible at least for the prototype phase

## Slide 4: Fan-out layer 0
  First exercise made using CERN information
    Two layer of Kapton + Aluminum
      Kapton thickness ~ 20 um
      Aluminum thickness ~ 10 um
      Glue ~ 10 um
      Pitch ~ 70 um
        It could maybe be reduced if the results on prototypes are encouraging. Real limit could be 60 um

## Slide 5
Striplets L0 detector and fan-out: case study
W=12.9 mm
L=97.0 mm
…
…
…
…
595 full length strips
173 shorter strips
900 um
shortest strip
TOP-view
BACKWARD
side
FORWARD
side
Dead-A
0.2 mm2
50 um pitch
ACTIVE
AREA
From F.B.design:
L=104.0mm-W=12.9mm
R=15.0mm
Z

## Slide 6
Detector not yet optimized
Reasonable for this exercise
W=12.9 mm of active area
~ 173 shorter strips
…
…
…
…
From F.B.design:
L=104.0mm-W=12.9mm
R=15.0mm
~ 595 full length strips
Goal: fan-out widtht ~ 31 mm

## Slide 7
Fan out made of two layers: case study
…
…
…
…
173 shorter strips
Drawing not to scale !!!!
Staggering to compensate pitch towards ICs
Staggering to compensate different pitch in bonding

## Slide 8: Outermost layer
~ drives half of the strips
~ 30.1 mm

## Slide 9: Innermost Layer
~ drives half of the strips
~ 31.9 mm

## Slide 10
Material | X0(cm) | Thickness (μm) | X0(%)
Glue | 28 | 40x2=80 | 0.0286
Kapton | 28.6 | 20x2=40 | 0.0140
Al | 8.897 | 10x1=20 | 0.0112
Total |  |  | 0.0538
Amount of material for Layer side
Al
Kapton
Glue
Al
Kapton
Glue
Sensor
Cross section

## Slide 11
Fanout | X0(%)
side (x 2.0) | 0.1076
Total amount of Fanout material for Layer0
Material | X0(%)
overlap (x 2.0 ) | 0.1076
Overlap material is at larger radius wrt L0 sensor

## Slide 12
SuperB HDI
Some Open Issues | 
No systematic impedance control | Limited possibility to change the dielectric layer thickness with the standard process. By print screening company prefers a standard “3 pass” procedure  dielectric thickness ~ 50 um. Some avenue to be pursued: evaluate the usage of dielectric in tape (predefined thickness)  limited choices of thick film materials compatible with AlN Mix AlN and Al2O3 materials. Possible after the first power/ground layer.
Clock lines were “qualified” by try and test in Babar | Difficult prediction of Z  dielectric constant usually not well specified by material manufacturer (ex. in next slide)
Some prototypes were produced to master the technology | Same approach to be pursued. Of particular interest is the implementation of differential lines (digital signal ~ 150-250 MHz) Prototype: small substrate (length counts), two layer (plane and one signal), array of lines of minimum size (number to be defined)
AUREL INTEREST
Update

## Slide 13
  AUREL is ready to produce 20 test structure on standard alumina and on AlNi to measure characteristics of various transmission lines
    Layout is simple, parallel lines with lenght similar to HDI lenght
    Signal integrity tests will be performed both at AUREL production site (Modigliana) and in Milan
    Alumina structrure will be used as reference
SuperB HDI Impedance Test Structures

## Slide 14: Read-out chain
No real activities on going on the transition card and power distribution card
Some measurements on the copper tails  on-going
Power lines gauges and drops will be revisited a soon as we have a nominal power consumption for the FE and HDIs  next two months

## Slide 15: Data/Clock and Control Cables
Signal: 39 AWG, Bifilar magnet wires (Cu)
Differential Impedance: to be measured
Capacitance: 75 pF/m
Propagation Delay: to be measured
Dielectric costant: 2.1
Twisting is not needed for such a small wire
It can not be purchased in tape
- grouping of individual wires could introduce signal degradation
 NSQP project at CERN
Electrical test on individual pair is starting
- on individual wires
- on few (up to 10 couples) wires with or without a braid around the bundle