## Slide 1
DCH FEE
LNF GM December 2011

## Slide 2: Outline
Design goals
Readout: Charge Measurement Option
  Requirements
  System block diagram
  On-Detector electronics
    Preamplifier simulation and preamplifier boards
    Signal cabling
    HV distribution
  Off-Detector electronics
Readout: Cluster Counting Option
  Requirements
  System block diagram
  On-Detector electronics
    Preamplifiers and cabling
    HV distribution
  Off-Detector electronics
TDR Outline
Conclusions

## Slide 3
Design goals

## Slide 4: Design goals
SuperB Drift Chamber (DCH) front-end electronics is designed to extract and process the 8056 (to be finalized) sense wire signals to:
measure the electron drift times to the sense wires for tracking purpose (momentum of charged particles)
Measure the energy loss of particles per unit length, dE/dx (particle identification)
provide hits information to the trigger system (trigger primitives)
Measurement of the energy loss of particles per unit length, dE/dx (particle identification) can be implemented by
Charge Measurement Option: measuring the charge collected on the sense wire (discarding high values to remove Landau fluctuations)
Cluster Counting Option: Counting the number of cluster generated by the particle crossing the cell

## Slide 5
Charge Measurement Option
Requirements & Block Diagram

## Slide 6: Charge Measurement Option: Specifications for charge measurements
Overall expected single cell σE ≈ 30 % (dominated by chamber contribution)
  Electronic contribution must be enough low to make it negligible; e.g.: σEL= 15% of σE corresponds to σEL= 4.5%  sqrt(σE2 + σEL2 ) ≈ σE
Assuming ≈ 50 fC the charge released from a mip (gas gain=105) , σEL ≈ 5%
single channel ENC ≈ 50 fC * 0.05 ≈ 2.5 fC
σE dominated by gas amplification effects:
  Lower range: σEL (2.5 fC ) (could be 3σEL)
  Higher range: ≈ 500 fC (BaBar experience)
Dynamic range
dE/dx Goal: measure particle energy loss with precision of the order of 7.5% (BABAR) despite large fluctuations involved in single measurement (“truncated mean” method)
Resolution
Linearity of the order of 2% matches system requirements
Linearity

## Slide 7: Charge Measurement Option: Specifications for time measurements
Overall expected σS ≈ 130μm  dominated by chamber contribution
  σS limits:
    Chamber: statistics of primary ionization, electrons diffusion
    Electronic: time measurement uncertainty
  Chamber contribution (σSC ) raw estimation ≈ 440/sqrt(NP) ≈ 110 μm for a 90/10 He/Iso gas mixture
  σEL ≈ sqrt(σS2 - σSC2 ) ≈ 70 μm  σt ≤ 1.5 ns ( 3 * 16 μm/ns drift velocity close to the wire)
    Main error sources are jitter (time walk + noise) and TDC (digitizing noise)
    Jitter
    Noise contribution: Δt = σN/ (dV/dt) ≈ σN* τ/Vmax (τ = peaking time)
      Assuming σN = 4 mV rms, Vmax = 30 mV, τ = 4 ns  σEL NOISE ≈ 0.5 ns
    Time walk contribution: assuming τ = 4 ns a time walk of the order of 1.5 ns with 20 dB input signal dynamic is obtained  quite high  possible (partial) compensation using FADC sampled values
        Digitizing noise ≈ Δ/sqrt(12) with Δ ≈ 1 ns  ≈ 0.3 ns
Time resolution (≈ 1.5 ns) is dominated by signal time walk
TDC range depends on gas mixture drift velocity and cell size  SuperB DCH max drift time ≈ 600 ns
TDC range ≈ 1us
Dynamic range
Particle tracks reconstruction based on (ionized) electrons drift time toward the sense wire
Resolution
A linearity of ≈ 1% fulfill measurement requirements
Linearity

## Slide 8: Charge Measurement Option: Block diagram
< 10 m
cables
#173 (48 chs)
121
DAQ
173 OL
16 (12 cores) OL
#16
DAQ
16 OL @ 2Gbits/sec
ECS
16 OL/Copper links
DATA-ECS
CONCENTRATORS
Pre-HV boards
121
TRIGGER
TRIGGER
Superlayers (10) Track Finder
OL to Track Finder
#10 ?!
ON-DETECTOR ELECTRONICS
DCH BACKWARD END-PLATE
8056 chs
121
ECS
12 cores Fiber Optical Cable patch-panel
18 (12 cores) OL
or Copper Links
OFF-DETECTOR ELECTRONICS
Data Conversion
Trigger Primitive Generation
Boards
173 OL
SLayer | chs | Boards | Links
1 | 1504 | 32 | 3
2 | 472 | 10 | 1
3 | 536 | 12 | 1
4 | 600 | 13 | 2
5 | 664 | 14 | 2
6 | 728 | 16 | 1
7 | 792 | 17 | 2
8 | 856 | 18 | 2
9 | 920 | 20 | 2
10 | 984 | 21 | 2
Super-layers structure is preserved in Data Conversion Boards (Trigger requirement)

## Slide 9: Charge Measurement Option: ON DETECTOR electronics (Preamplifiers & HV distribution)
Charge Measurement
ON DETECTOR electronics

## Slide 10: Charge Measurement Option: On Detector Electronics - Preamplifiers
Front End Boards contain HV blocking capacitors, protection networks, preamplifiers and (eventually) shapers.
Boards are located on the backward end-plate to maximize S/N ratio and are connected to the Data Conversion Boards (located on external crates) through coaxial or shielded twisted pairs cables
Connection up to 10 mt length can be achieved providing good shielded cables
The end-plate will be divided in (sub)sectors  more cells will be grouped in a single multi-channel preamplifier-shaper board (sub-division will be finalized as soon as DCH final design parameters will be available)
Preamplifier
Wire signal is used both for charge and time measurement
   preamplifier should not worsening too much signal time information (rise time).
Because the gas mixture slow drift velocity and the moderate detector parasitic capacitance a transimpedance configuration with a dominant pole around 25-35 MHz should match the measurement requirements providing that the second pole is enough far to ensure a good phase margin.
Channel density is not so high and circuit design not so complex
   approach based on SMT technology possible
   We can profit of high bandwidth, low noise SiGe devices developed for mobile-phone applications
Charge measurement caveats
BONUS: SiGe HBT transistors technology is inherently radiation hard
Radiation Environment

## Slide 11: Charge Measurement Option: On Detector Electronics - Preamplifier Simulation
400 mV
-400 mV
8 ns
6 ns
10 ns
12 ns
14 ns
16 ns
0 mV
0 ns
CD=0pF
4 ns
2 ns
300 mV
200 mV
100 mV
-100 mV
-200 mV
-300 mV
Preamplifier main features (Pspice Simulator) | 
Linearity (-2 fC ÷ -200 fC) | ≈ 1%
Output signal balance | ≈ 1%
ZIN | 100 ohm
Gain ( CD = 0 pF) | ≈ 6.8 mV/fC (Differential)
Gain (CD = 24 pF) | ≈ 4 mV/fC (Differential)
tr – tf (Cd = 0 pF) | 2 ns – 7 ns
tr – tf (Cd = 24 pF) | 3 ns – 10 ns
erms (Cd= 0pF) | 1100 erms
erms (Cd= 24pF) | 1900 erms
PSRR | ≈ 20 dB
Vdd | 4V
Pd | 32 mW
10fC
100fC
Preamplifier topology allows to implement shaping on input signal
Head transistor current must be optimized vs CD and shaping time
Output (driver) stage can be differential or single-ended

## Slide 12: Charge Measurement Option: On Detector Electronics – Preamplifier Boards
Preamplifier boards modularity should match trigger super-layer structure
  i.e. assuming a 48 chs off-detector boards preamplifier (and HV distribution) cards should fit off-detector boards modularity in such a way we can send signal belonging to a single super-layer to track finder trigger boards
Signal output cables can be differential (shielded twisted pairs) or single ended (coaxial)
Cable length can reach up to 10 mt providing good shielding and fully differential receiving stage on off-detector boards (to minimize loop area).
  Twisted pairs cables: shield must be connected only on one side to avoid current flow through the shield (in case of differences in ground potential between the two ends of the circuit).
  Coaxial cables: “The best way to protect against magnetic fields at the receptor is to decrease the area of the receptor loop” (H.W. Ott - Noise reduction techniques in electronic systems)
Field wires grounding board
Signal decoupling & protection network
Pre
Shaper
Driver
On Detector electronics possible setup
Driver
Detector ground
Driver
Detector ground

## Slide 13: Charge Measurement Option: On Detector Electronics – Cabling
ON DETECTOR electronics will provide good amplification, but signal levels are still quite low.
Micro-coaxial cables or shielded twisted cables must be used to minimize noise environmental pickup
  Problem can arise due to the cable jacket. Many halogen free cable are quite rigid (large bending radius)
Braid shield twisted pairs offer a good compromise between cost, noise environmental shielding and bandwidth. Nevertheless shielded connectors could be a problem in the on-detector side (because the size)
Both micro-coaxial and braid shielded twisted pairs are available in round and flat assembling. Flat assembling is (generally) better for on-detector front end boards connection, while round cables are better for routing and Digitizing Boards connections.
dE/dx based on charge measurement
Micro-coax: 50 Ω
0.83 – 1.3 mm diameter
Micro Coax Cable quotation requirement
A feasibility study (production/cost) for a custom micro-coax cable has been required to a company
Cable main specs:
  Impedance: 50 (±2) Ω
  Shield: copper braid
  Attenuation (dB/100m) : ≈ 36 dB/100 m
  External diameter : < 2 mm
  Halogen free (still maintaining good flexibility)
  Assembling: flat mixed (7 signal cables + 2 LVPS cables + 7 signal cables + 2 LVPS cables)

## Slide 14: Charge Measurement Option: On Detector Electronics – HV distribution boards
Enough modularity to avoid too many dead channels in case of single chamber channel failure
Modularity is function of the distance from inner layer (example: 2 boards in inner layer – 5 boards in outer layer)
Good feedback of the current dragged by the inner layers (≈ 1 nA) and by the outer layers (≈ 100 nA)
General considerations
1MΩ
2.2 nF
1MΩ
500 pF
10MΩ
10MΩ
Ch 1
Ch 8
Filter Box
[Outside Detector]
Distribution Board
[number of boards is a function of chamber layer]
Main Power Supply
BOARD #1
BOARD #N
1MΩ
500 pF
10MΩ
10MΩ
Ch 1
Ch 8
HV Distribution – dE/dx by means of charge measurement
NB: HV distribution boards located on forward end-plate

## Slide 15: Charge Measurement Option: Off Detector Electronics
Only rad-tol FPGA (Actel ProAsic equivalent devices) will be used for Off-Detector electronics
Locating Off-Detector electronics on the top of experiment could be useful for setup and maintenance (cable length ?)
Off-Detector Feature Extraction can be simply implemented if minimum trigger spacing is ≈ 70 – 100 ns. FEX could be (anyway) implemented by using an intermediate buffer (see CC option).
Feature EXtraction
FEX on Off-Detector Electronics
All events have a fixed structure and a fixed length
Digitizer Module Address (2 Bytes)
Flag (1 Byte)
Trigger Tag (1 Byte) – 5 bits in BaBar
Counter (1 Byte)
Charge (2 Bytes)
Time (2 Bytes)
1st ADC sample for time walk correction (1 byte)
Data Stream Example (10 bytes)
NO FEX on Off Detector electronics
Minimum trigger spacing ≈ 50 ns ( ≈ 0.8 mm @ 16 μm/ns drift velocity)
Raw data (minimum amount) - 32 bytes ADC + over-threshold discriminated signals (TDC)
Data stream do not have fixed length (consecutive events properly tagged can be contained in the same data stream)

## Slide 16
Cluster Counting Option
Requirements & Block Diagram

## Slide 17: Cluster Counting option
Pros
  Particle identification improvement
  Dedicated time measurement not required
  Possible improvement in spatial resolution
Cons
  High sampling frequency digitizers
  Fast processing
  Wide bandwidth and high power requirement for front-end (environment noise sensitivity increases)
  High Bandwidth-Low losses cables for on-detector  off-detector connection required
  Termination resistor required (system noise baseline) with dedicated PCB
FADC resolution is a function of the lowest sampled signal and system noise
  6 fC wire signal (gas gain 3x105), 10 mV/fC shaper-amplifier, safety factor = 2  30 mV signal
  If we consider only the noise contribution of termination resistor (bottom limit: peaking time = 3 ns - gain = 10 mV/fC ) we get about 2 mV rms
Resolution
Pros & Cons
Total ionization in 1.2 cm high cell (average) ≈ 30e (90/10 – He/Iso)
Each electron correspond to a different level in output voltage  3 bits/electron  8 bits FADC
Linearity ≈ 2%
Dynamic range and linearity

## Slide 18: Cluster Counting Option: Block diagram
< 5 m
cables
#1152 (8 chs) boards
121
DAQ
# 1152 OL
96 (12 cores) OL
#32
DAQ
32(?) OL @ 2Gbits/sec
ECS
32 OL / Copper Link
DATA-ECS
CONCENTRATORS
Pre-HV boards
Concentrator
+
121
TRIGGER
TRIGGER
Superlayers (10) Track Finder
OL to Track Finder
#10 ?!
ON-DETECTOR ELECTRONICS
DCH BACKWARD END-PLATE
8056 chs
121
ECS
12 cores Fiber Optical Cable patch-panel
18 (12 cores) OL
or Copper Links
OFF-DETECTOR ELECTRONICS
Data Conversion
Trigger Primitive Generation
Boards
1152 OL
Increase of trigger latency ?

## Slide 19: Charge Measurement Option: ON DETECTOR electronics (Preamplifiers & HV distribution)
Cluster Counting
ON DETECTOR electronics

## Slide 20: Cluster Counting Option: Preamplifiers and Cabling
Cables for Cluster Counting must features high bandwidth, low losses and controlled impedance (Shielded Controlled Impedance cables)
There are several assemblies available. Cost is a function of modularity, type of connector and type of cable, but is generally higher than the solution for charge measurement because the BW requirement.
  Decision on type of cable will depend on the technique adopted for dE/dx measurement
dE/dx based on Cluster Counting
Our Price: $1.38
Mated height: 1.4 mm (55.12 mil)
Cable diameter: 0.7 mm (27.6 mil)
Length: 5.9" (150 mm)
Connectors: Super micro plug
Frequency: DC-7GHz
VSWR: 1.4:1 max
Standard lead time: 4 weeks ARO
1.88 mm diameter
A wide bandwidth preamplifier has been designed and has been tested on a Drift Chamber. Results will be shown asap.
Preamplifiers

## Slide 21: Cluster Counting Option: Off Detector Electronics
Only high performances FPGA can be used for Off-Detector electronics. Unfortunately they are prone to SEU
  use neutron shielding (pure polyethylene ..) ???!!!
As already said locating Off-Detector electronics on the top of experiment could be useful for setup and maintenance but long cables could be a problem because SNR reduction and cost.
If Off-Detector Feature Extraction is not used complete event data (≈ 1kB) must be moved to DAQ !!!
  8000 (bits) x 8056 (chs) x 10% (occupancy) x 150 kHz (Average Trigger rate) ≈ 967 Gbits/sec
Feature Extraction implications
< 1 μs
FADC
8 bits
dE/dE by means of Cluster Counting – Latency, FEX, Readout Buffer
Latency Dual Port
SRAM
FEX Dual Port
SRAM
Readout
Dual Port SRAM
16 bits data bus
64 bits data bus
64 bits data bus
1000 samples (8 bits) @ 1 GHz
L1
DCH trigger is based on super-layers track finder. Because the Off-Detector boards low modularity we should use concentrators  increase of latency ?
Trigger implications
State Machine
≈ 4 μs for FEX

## Slide 22: Cluster Counting Option: On Detector Electronics – HV distribution boards
1MΩ
2.2 nF
Filter Box
[Outside Detector]
Distribution Board
[number of boards is a function of chamber layer]
BOARD #1
BOARD #N
HV Distribution – dE/dx by means of Cluster Counting
1MΩ
500 pF
10MΩ
Ch 1
RT
10MΩ
Ch 8
RT
1MΩ
500 pF
10MΩ
Ch 1
RT
10MΩ
Ch 8
RT
500 pF
500 pF
500 pF
500 pF
Assuming the same general considerations of Charge Measurement Option
NB: HV distribution boards should be located on forward end plate and require high frequency ground connection because the termination resistors
Main Power Supply

## Slide 23: TDR outline
1 Electronics – (Felici, Martin) 14 pages
  Design Goals
  Truncated mean method
    Specification for charge measurements
      Resolution
      Dynamic range
      Linearity
    Specifications for time measurements
      Resolution
      Range
      Linearity
    System block diagram
    On-Detector Electronics
    Off-Detector Electronics
    HV Distribution
  Cluster Counting method
  Specification for clusters and time measurement
      Resolution
      Dynamic range
      Linearity
    System block diagram
    On-Detector Electronics
    Cabling
    Off-Detector Electronics
  Cabling
Optical links
Patch Panels
Slow control system
Low Voltages Power Supply
Grounding policy
Radiation environment policy

## Slide 24: Conclusions
Design goals have been defined
Two different implementation of dE/dx measurements have been evaluated and will be reported in TDR.
The technique used for dE/dx measurement has a NOT minor impact on number of boards, power requirement, interconnections cables, HV distribution boards and grounding (shielding).
HV distribution modularity should follow the chamber layer (less cells for the internal layers, more cells for the external ones)
Only Rad Tol components will be used in front-end boards (charge measurement option). If selected components has no qualification they will be qualified.
Grounding/shielding policy has not been defined yet
    Board design will start after the decision on what technique will be used for
    dE/dx measurement

## Slide 25
Front-end and Counting Algorithms on Cluster Counting
LNF GM December 2011

## Slide 26: Outline
Preamplifier Impulse response estimation
Garfield simulation
Convolution effects on the generated signal
Counting algorithms
Gaussian noise effects on counting algorithm
Conclusions

## Slide 27: Preamplifier Features
Preamplifier Board
Transimpedence preamplifier
Differential amplifier/shaper output
Unipolar amplifier/shaper output
Preamplifier main features
Number of channels : 7
Zin ≈ 60 Ω
Gain ≈ 8.8 mV/fC
Noise ≈ 2500 erms @ 250 MHz BW
Rise time ≈ 2.4 ns
Unipolar & Differential outputs (50 Ω – 110 Ω)
Test input
Supply Voltage : + 7V (310 mA) - 7V (190 mA)
Power Dissipation : 490 mW/ch
5 mV/div
50 mV/div
5 ns/div
average
1.8 pF injecting capacitance

## Slide 28: Preamplifier Impulse Response Fitting
Fitting function:
Preamplifier board has been connected to the chamber and pulsed through a 1.8 pF internal capacitor.
Output pulse has been fitted to find out the preamplifier impulse response.
Shape=a1*exp(-((t-b1)./c1).^2)+
a2*exp(-((t-b2)./c2).^2)
Where:
A1= 0.479
B1= 24.367
C1= 1.797
A2= 0.691
B2= 25.983
C2= 2.305

## Slide 29: Preamplifier response convolution example #1
Convolution output
Garfield output (Gas gain 3x10^5 – preamp gain 4mV/fC)

## Slide 30: Preamplifier response convolution example #2
Garfield output (Gas gain 3x10^5 – preamp gain 4mV/fC)
Convolution output

## Slide 31: Preamplifier response convolution example #3
Convolution output
Garfield output (Gas gain 3x10^5 – preamp gain 4mV/fC)

## Slide 32: Cluster counting algorithm
Peak Found Condition
Proposed by Luigi Cappelli
on behalf of CLUTIM Group
V
Algorithm applied to a garfield data set

## Slide 33: Counting Algorithm applied to example #1
Convolution output
Garfield output (Gas gain 3x10^5 – preamp gain 4mV/fC)
N. Cluster = 31
N. Cluster = 24

## Slide 34: Garfield waveform samples
Garfield output (Gas gain 3x10^5 – preamp gain 4mV/fC)
Impact parameter = 0 mm
Impact parameter = 2.5 mm
Impact parameter = 5.0 mm
Impact parameter = 7.5 mm

## Slide 35: Counting Algorithm @ different impact parameters
Mean = 0.72
Std = 0.16
Impact parameter = 0 mm
Garfield avg. clusters = 29.89
Convolved avg. clusters = 21.5
Mean = 0.73
Std = 0.16
Mean = 0.71
Std = 0.17
Mean = 0.72
Std = 0.19
Impact parameter = 2.5 mm
Garfield avg. clusters = 30.28
Convolved avg. clusters = 21.38
Impact parameter = 5 mm
Garfield avg. clusters = 31.28
Convolved avg. clusters = 21.92
Impact parameter = 7.5 mm
Garfield avg. clusters = 27.77
Convolved avg. clusters = 19.68
Efficiency= Mnc/Rnc
Rnc = Real Number of Clusters
Mnc = Measured Number of Cluster after convolution and noise addition
Analysis performed on 1000 data sets

## Slide 36: Counting Algorithm @ different impact parameters
Mean = 27.42%
Std = 16.22
Impact parameter = 0 mm
Garfield avg. clusters = 29.89
Convolved avg. clusters = 21.5
Mean = 27.27%
Std = 16.13
Mean = 28.07%
Std = 16.61
Mean = 28.07%
Std = 16.61
Impact parameter = 2.5 mm
Garfield avg. clusters = 30.28
Convolved avg. clusters = 21.38
Impact parameter = 5 mm
Garfield avg. clusters = 31.28
Convolved avg. clusters = 21.92
Impact parameter = 7.5 mm
Garfield avg. clusters = 27.77
Convolved avg. clusters = 19.68
% of Detected Cluster= (Rnc-Mnc)/Rnc *100
Rnc = Real Number of Clusters
Mnc = Measured Number of Cluster after convolution and noise addition
Analysis performed on 1000 data sets

## Slide 37: Noise Effect on Convolved Signal
SNR evaluated considering single electron cluster average amplitude (~10mV)
SNR=10
SNR=6
SNR=2
SNR=Signal Amplitude/Noise RMS

## Slide 38: Threshold effect on cluster counting at constant SNR
The RMS of the noise is evaluated on the last 300 samples
Thr=0.8*RMSNoise
N. clusters = 23
Thr=1.0*RMSNoise
N. clusters = 20
Thr=1.5*RMSNoise
N. clusters = 18

## Slide 39: Detected Clusters vs SNR at 1.5* sigma threshold
Efficiency = Mnc/Rnc
Rnc = Real Number of Clusters
Mnc = Measured Number of Cluster after convolution and noise addition
Impact parameter = 0 mm
Impact parameter = 2.5 mm
Impact parameter = 5 mm
Impact parameter = 7.5 mm

## Slide 40: Detected Clusters vs SNR at 1.5* sigma threshold
% of Detected Cluster= (Rnc-Mnc)/Rnc *100
Rnc = Real Number of Clusters
Mnc = Measured Number of Cluster after convolution and noise addition
Impact parameter = 0 mm
Impact parameter = 2.5 mm
Impact parameter = 5 mm
Impact parameter = 7.5 mm

## Slide 41: Conclusions
Garfield output has not been tuned to real signals in particular concerning gas amplification fluctuation.
We have carried out a cluster counting feasibility study using an algorithm that can be easily implemented on an FPGA.
The analysis have been performed using data set based on garfield simulations at different impact parameters.
Results show that after garfiled data convolution with preamplifier response there is a loss of about 28% in detected clusters for different impact parameters.
The addition of Gaussian noise with different SRN increase the counting inefficiency from 40% (SNR=10) to about 70% (SNR=2). In any case results show huge fluctuations in the counted clusters due to the noise contribution.

## Slide 42: DCH - 1 page x Dominique
Design goals have been defined
Two different implementation of dE/dx measurements have been evaluated and will be reported in TDR.
  Truncated mean method has already been used by other experiments and, according to BaBar experience, should provide a σE around 7-8 %
  Cluster Counting is under study and measurements both at LNF and TRIUMF are going on. Simulations using GARFIELD data have been carried out as well by using real preamplifier response convolution and different SNR.
Impact parameter = 0 mm
% of Detected Cluster= (Rnc-Mnc)/Rnc *100
Rnc = Real Number of Clusters
Mnc = Measured Number of Cluster after convolution and noise addition
Threshold = 1.5*σ
HV distribution system has been defined and modularity will be finalized as soon as chamber final design will be available. HV distribution boards should be located on FORWARD end-plat.
On-Detector electronics (preamplifier boards) will be located on BACKWARD end-plate. We are investigating the possibility of exiting the cables from the outer layer of the chamber
We are also investigating the possibility of using the top of the detector to locate off-detector electronics then simplifying setup and maintenance of the system