## Slide 1: Updates on the R&D for the SVT Front End Readout chips
F. Giorgi – INFN Bologna

## Slide 2: Summary
Strip readout architecture
  Investigated architecture
  Preliminary simulations
3D pixel submissions
  Apsel_VI
  SuperPix1

## Slide 3: Strip Readout Architecture
Updates on Job Status

## Slide 4: Strip readout architecture under development
BUF #1
Sparsifiers
FE
Ctrl
logic
Buf
#k
...
Buf
#1
ADC
Or ToT
readout/slow control
strip #127
strip #0
FE
Ctrl
logic
Buf
#k
...
Buf
#1
ADC
Or ToT
~hit_rate * trig_latency
How many buffers?
How many barrels?
Triggered hits only
Asynchronous logic assumed:
Triggered event size not known a-priori
(thus readout time as well)
Pre-trigger buffer array
PISA
BOLOGNA pixel-like hit extraction architecture

## Slide 5: Development Status
All elements have been modeled on both sides
  VHDL for hit extraction system and slow control
  SystemVerilog for the strip FE logic and buffers (see R. Beccherle presentation)
CERN SVN repository created and proficiently in use
  svn.cern.ch/reps/vipix/StripChip/
Test Benches under development:
  Shared Elements:
    Monte Carlo hit generator
    I2C interaction routines (simulation utility package)
  Independent and parallel test benches:
    separated test vectors and procedures  enhanced code coverage.
  Simulation Tool: ModelSim SE (allows mixed code simulations)
So Far:
  Interface defined  must be verified
  Separate tests on our own blocks for functional debug
Next to come: full chip simulations and digital efficiency study.

## Slide 6: Test Bench Scheme
MC generator
Reduced and rivisited version of the one used for pixels
128 Strip channels
FE logic and trigger buffer
Readout equivalent to:
4 sub-matrices
256 rows
1 column
(with minor revisions)
FE logic
Trigger buffers, TS tag/request handling ecc.
Trigger handling
Hit encoding
Hit de-queue

## Slide 7: MC gen self test
MCgen
CMP
Busy
loopback
hit generated with a ToT = 14
another hit generated @ 19775 ns
CMP not re-triggered  total CMP length is 140 ns = prev. ToT (14) *10 ns ToT resolution
busy_hit_count incremented by 1
rough inefficiency estimate due to occupancy by busy_hit_count/hit_count.

## Slide 8: Trial analog efficiency study
Hit Rate (MHz) | ToT freq. MHz | Min (ns) | Max (ns) | Effi
30 | 100 | 10 | 150 | 98.3%
20 | 100 | 10 | 150 | 98.9%
10 | 100 | 10 | 150 | 99.3%
30 | 200 | 5 | 75 | 99.1%
20 | 200 | 5 | 75 | 99.5%
10 | 200 | 5 | 75 | 99.8%
ToT range (4 bit TOT used)
busy_hit_count
hit_count
1 -
No physical information included
Pulse widths uniformly distributed over ToT range

## Slide 9: 3D-IC submissions
Deadline: March 26th 2012

## Slide 10: The projects
Apsel-VI
  MATRIX 96x128(2 sub-m. 48 x128)
  Rows divided in:
    4 sparsifiers
    32 rows for each sparsifier
    8 zones for each sparsifier (Wzone= 4 pixels)
SuperPix1
  MATRIX 32x128 (2 sub-m. 16x128)
  Rows divided in:
    4 sparsifiers
    32 rows for each sparsifier
    8 zones for each sparsifier (Wzone= 4 pixels)

## Slide 11: Readout architecture
Few revisions w.r.t. INMAPS architecture.
  In-pixel threshold adjust DAC  serial vs I2C loading? I2C very time-expensive for protocol overhead, till now used to program the peripheral registers and to mask the few defective pixels here and there. Meant for the slow control of several chip with 2 shared serial lines, not to transfer large amount of data (~ 250k bit for the big chip).
New component proposed by PV/BG:
  Internal pulser for Gain scans
    No external pulser needed, digitally controlled.
    Peripheral DAC to trimmer the pulses
      An additional mixed signal component in the floorplan  needs Physical synthesis of std. cells and interconnection to peripheral RO.
    Injection mask loading? (see above)
  Possible in principle. I need to investigate HOW.

## Slide 12: Conclusion
Strip
Strip FE architecture defined and modeled, ready to be tested.
Digital readout efficiency goal value: 100%, to be verified.
3D Pixels:
Architectures ALMOST defined and modeled. Specifications must be closed a.s.a.p. to proceed.
Internal deadline: end of Feb. 2012 (Fortunately it’s a leap year!), ~3 weeks before actual submission to CMP.

## Slide 13: Back-Up

## Slide 14: Strip Rates
Strip rates as given by Riccardo C. (5/13/11):
new values old values
    L0: 2060 kHz/strip ~ =
    L1: 687 kHz/strip (268 kHz/strip)
    L2: 422 kHz/strip (179 kHz/strip)
    L3: 325 kHz/strip (52.5 kHz/strip)
    L4: 47 kHz/strip (21.9 kHz/strip)
    L5: 28 kHz/strip (18.7 kHz/strip)

## Slide 15: Max peaking times (ns) at fixed strip efficiency
Target strip efficiency |  | 97.6% |  | 95% |  | 91%
 | SF=5 | SF=1 | SF=5 | SF=1 | SF=5 | SF=1
L0 | 5 | 25 | 10 | 52 | 19 | 95
L1 | 15 | 74 | 31 | 156 | 57 | 286
L2 | 24 | 120 | 51 | 253 | 93 | 466
L3 | 31 | 156 | 66 | 329 | 121 | 605
L4 | 215 | 1077 | 455 | Max | 836 | Max
L5 | 361 | 1807 | 763 | Max | 1403 | Max
M. Villa