## Slide 1
FLASH – Trento Activity
Research Objectives
1) Explore the possibility of using a Microstrip SQUID Amplifier (MSA) in a 300 mK small-size refrigerator inserted in the FLASH cryostat
MSA noise vs T measurements down to 20mK
2) Explore the possibility of simultaneous measurement of multiple cavity modes
Tests at 4.2K of 2-3 MSA and “TBD devices” coupled to a single antenna
Microstrip SQUID Amplifier (MSA)

## Slide 2
Purchases
MSAs (4 k€ each)
Low noise cryogenic and room temperature RF amplifiers
Microwave-cryo-spares (filters, power splitters, cables, connectors...)
Liquid helium
Helium liquifiers with gas recovery system
Dilution Refrigerator
Equipment available
Dilution refrigerator -> MSA tests down to Tbase = 20 mK
Liquid helium transport and lab dewars -> MSAs-antenna tests at 1-4.2K
Helium liquefier with gas recovery system -> liquid helium at affordable prices
Electronics (Signal generators, VNA, oscilloscope/spectrum analyzer 500 MHz)
FTE: Paolo Falferi 30%, Andrea Vinante 30%
FLASH – Trento Activity

## Slide 3
Input coil and SQUID washer form a capacitor in parallel to the input coil inductance -> Resonant circuit (typically ν0 ≈ 40 MHz)
The effect of the parasitic capacitance between input coil and SQUID washer can be exploited to operate the input coil as a transmission line resonator
Microstrip SQUID Amplifier
«Standard» Square Washer SQUID
Main differences between dc SQUID and MSA
Mück and McDermott, Supercond. Sci. Technol. 23 093001 (2010)
Amplifiers based on this principle have shown gains of 20 dB at frequencies below 1 GHz and up to 10 dB at 5 GHz

## Slide 4
It is possible to tune the resonant frequency of the MSA by terminating the microstrip resonator with a varactor diode.
The varactor doesn’t change the noise temperature of the MSA (here 0.9K @ 200 MHz, 4.2K)
A broad bandwidth can be obtained with a second MSA as a postamplifier. Here the resonance frequencies of the first and second amplifiers were about 280 and 400 MHz, respectively.
Mück et al. Appl. Phys. Lett., 75, 3545,1999
Matching the Flash cavity bandwidth (117–206 and 206-360 MHz)
Tuning the microstrip resonator with a varactor diode
Two cascaded MSA tuned to different resonant frequencies
Lower MSA resonator Q -> wider bandwidth (but lower gain)
A broad bandwidth can be obtained with a lower quality factor of the resonator but at the expense of a lower gain

## Slide 5
END

## Slide 6
Mück et al., Appl. Phys. Lett. 78, 967 (2001)

## Slide 7
Cryogenic Services Facility with equipment for helium gas recovery: two helium liquefiers (total capacity 12 l/h), storage dewar 500 l, gas storage capacity 250 m
ν0 = 117–360 MHz Er=1-> λ = 2.56-0.83m
3ν0 = 351–1080 MHz Er=1-> λ = 0.85-0.28m
Microstrip on Si h=0,65mm, er=11.7, line l=0.5mm h=35um
Z=50 Ohm, Eeff=7.675
ν0 = 117 MHz Eeff=7.675 -> λ = 924mm
3ν0 = 1080 MHz Eeff=7.675 -> λ = 100mm