## Slide 1
Leszek Ropelewski, CERN, Switzerland
on behalf of the RD51 Collaboration
12th Pisa Meeting on Advanced Detectors, Isola d’Elba, 20-26 May 2012
OUTLINE:
RD51 Motivation and Main Objectives
RD51 Collaboration Activities and Results
Large area detectors
Electronics
Software tools
MPGD workshop upgrade & industrialization
Technology Transfer
RD51 test beam facility
Training
Summary and Outlook
The RD51 Collaboration,
Micro-Pattern Gas Detector Technologies and Applications

## Slide 2
Current Trends in Micro-Pattern Gas Detectors (Technologies)
Electrons
Ions
60 %
40 %
Micromegas
GEM
THGEM
MHSP
Ingrid
2
Semiconductor Industry technology:
Photolithography
Etching
Coating
Doping
Wafer postprocessing

## Slide 3
2x106 p/mm2
Micro-Pattern Gas Detectors Performance Summary
Rate Capability
High Gain
Space Resolution
Time Resolution
Energy Resolution
Ageing Properties
Ion Backflow Reduction
Photon Feedback Reduction
Spatial
resolution
s ~ 12 mm
Ar/CO2/CF4
(45/15/40)
rms = 4.5ns
GEM
THGEM
Micromegas
GEM
Micromegas
Micromegas
MHSP

## Slide 4
MPGD are mostly used/proposed for high-rate tracking and photodetectors
COMPASS Upgrade:
Micromegas and GEM detectors for high-rate tracking
Photon Detectors Using THGEM technology for RICH 1
KLOE2 Upgrade:
Large-area cylindrical GEMs for Inner Tracker
RHIC Upgrades:
GEM Tracking for STAR Experiment
GEM Tracking for PHENIX Experiment(+ drift micro-TPC);
development of Ring Imaging version of HBD for particle ID
Future JLAB Projects:
Thin-Curved Micromegas for JLAB/CLAS12
GEM Tracker for JLAB/Hall A High Luminosity (SBS) experiments
Future FAIR Facility:
GEM Tracker and GEM TPC for the PANDA Experiment
GEM/Micromegas tracking in CBM Muon Chamber (MUCH)
Future Electron - Ion Collider Facility:
Tracking and particle ID detectors based on MPGD-technology
Demand for the Micro-Pattern Gas Detectors

## Slide 5
5
~ 80 institutes
~ 450 people involved
Representation (Europe, North America, Asia, South America, Africa)
RD51 Collaboration
“RD51 aims at facilitating the development of advanced gas-avalanche detector technologies and associated electronic-readout systems, for applications in basic and applied research”
Freiburg , Germany, May 2010
The main objective of the R&D programme is to advance technological development of Micropattern Gas Detectors
RD51 contributes to the LHC upgrades, BUT, the most important is:
RD51 serves as an access point to
MPGD “know-how” for the world-wide community
Kobe, Japan, September 2011

## Slide 6
“Transverse organization” of MPGD activities in 7 Working Groups
6
RD51 Collaboration – Working Groups

## Slide 7
WG1: large area Micromegas, GEM; THGEM R&D; MM resistive anode readout (discharge protection); design and detector assembly optimization; large area readout electrodes and electronics interface
WG2: double phase operation, radiation tolerance, discharge protection, rate effects, single-electron response, avalanche fluctuations, photo detection with THGEM and GridPix
WG3: applications beyond HEP, industrial applications (X-ray diffraction, homeland security)
WG4: development of the software tools; microtracking; neBEM field solver, electroluminescence simulation tool, Penning transfers, GEM charging up; MM transparency and signal development, MM discharges
WG5: scalable readout system; Timepix multi-chip MPGD readout
WG6: CERN MPGD Production Facility; industrialisation; TT Network
WG7: RD51 test beam facility
7
Consolidation around common projects: large area MPGD R&D, CERN/MPGD
production facility, common electronics developments, software tools, beam tests
RD51 Collaboration Organization
RD51 Collaboration Organization

## Slide 8
8
Second Polyimide etching
Chemical Polyimide etching
Copper electro etching
Stripping
Result
WG1: Large area detectors
Single mask GEM technology
Large area GEM detectors for KLOE2 tracker
Frascati
D. Domenici

## Slide 9
9
Large Prototype: GE1/1
Beam Test @ RD51 setup
Requirements:
Rate capability : 104/mm2
Space/Time resolution: ~ 100 m / ~ 4-5 ns
Efficiency > 98% ; Excellent Long Term Operation
Large areas ~ 1m x 2m with industrial processes
S. Colafranceschi
CMS High Eta MPGD Project (GE1/1 1.6>h>2.1)
GEM for CMS Collaboration
Goals:
Development and evaluation of large size GEM detectors for tracking and triggering.
Assembly optimization for cost reduction
Production transfer to industry

## Slide 10
10
  Time resolution for different
  gas mixtures and gap configurations:
  Ar(45):CO2 (15):CF4 (40)
  [gaps 3/1/2/1]
  Ar(70):CO2(30)
  [gaps 3/2/2/2]
CMS High Eta MPGD Project
S. Colafranceschi
Self-stretching technique:
Assembly time reduction: 3 days  2 hours

## Slide 11
Goals and Requirements:
Space-charge effects at 50 kHz Pb-Pb continuous readout too high with wires
  Limit GEM ion back-flow to 0.25% at gain 1500 –R&D required
Maintain excellent dE/dx resolution for particle Id uniformity and time stability
Total area: 32.5 m2
Chamber size 46x50 cm2 and 88x112 cm2 -> Use single mask GEM technology
ALICE endplates TPC upgrade with GEMs
V. Manzari

## Slide 12
PCB
lamination
Mesh deposit
lamination
development
WG1: Large area detectors
Bulk MicroMegas technology
12
Fine segmentation 1cm², thickness 8mm for ILC Hadronic calorimetry
Tested in the RD51 1 kHz beam
Bulk Micromegas ILC DHCAL first m2
LAPP Annecy

## Slide 13: MicroMegas detectors for the upgrade of the ATLAS muon system
Goals:
Development of large-area (≈2 x 1 m2) bulk-MicroMegas chambers for high-rate applications that combine precision measurement and trigger functionality
Spark neutralization and/or suppression
Resistive coating on readout strips
Multi-stage amplification schemes
Transfer of know-how to competent industry
Large-scale production in industry
1.2 x 0.6 m2 prototype chamber with 2048 readout strips (0.5 mm strip pitch) during construction in CERN/TE-MPE workshop
March 2011
M. Byszewski
Requirements and Performance:
Spatial resolution ~30μm (Ar:CO2 93:7)
Single plane efficiency 98%
Gains above 104
Clean signals up to >1 MHz/cm2, with some loss of gain
Stable response over duration of neutron irradiation equivalent to 20 years LHC (5x1034 cm-2s-1)

## Slide 14
M. Byszewski

## Slide 15
MM Resistive strip protection
Gain ≈ 5000
M. Byszewski

## Slide 16
ThickGEM photon detector for COMPASS RICH-1
Requirements:
Reduced photon and Ion BackFlow (IBF)
Reduced aging
High stable gain - high photoelectron detection efficiency
Large area
Short integration time
High rate environments
In collaboration
with industrial PCB company
ELTOS S.p.A. Arezzo Italy
F. Tessarotto

## Slide 17
Ion backflow reduction with “Flower THGEMs”
“Flower THGEM” configuration:
THGEM 1 has holes of 0.6 mm diameter, 1.2 mm pitch
THGEM 2 has holes of 0.3 mm diameter, 0.6 mm pitch,
with 1/3 of the holes missing: the ones below the THGEM 1 holes
This configuration
provides charge
splitting and allows
for ion backflow
minimization
current flow for the standard triple THGEM configuration:
current on TOP of THGEM 1 in %
for the “FLOWER” configuration:
F. Tessarotto

## Slide 18
FEC cards
Virtex-5 FPGA, Gb-Ethernet, DDR buffer, NIM and LVDS pulse I/O
High speed Interface connectors to frontend adapter cards
ADC frontend adapter
for APV and Beetle chips
ADC plugs into FEC to make a 6U readout
unit for up to 2048 channels
Frontend hybrids so far all based on APV25 chip
VFAT and Beetle being designed
18
More than 10 full systems delivered
SRS Production 2012 (commercial): PRISMA, Alexandoupulis Gr, sales via CERN store, CERN contract KTT
 Scalable Readout System
Scalability from small to large system
Common interface for replacing the chip
frontend
Integration of proven and commercial
solutions for a minimum of development
Default availability of a very robust and
supported DAQ software package.
H. Muller
Electronics for MPGD

## Slide 19
CERN experiments
ATLAS CSC upgrade MMegas ( 8kch APV-SRS systems, 1st SRS testbeams, MMDAQ developer )
ATLAS CSC upgrade MMegas, (VMM1 readout chip developer, SRS Adapter by Arizona Univ, MMDAQ )
ALICE EMCaL + FOCAL, SRU-based backend ( 50 kHz upgrade via SRS, DATE, new: Focal readout via SRS-Beetle ?)
ALICE TPC upgrade, SRS readout electronics with DATE backend ?
NA62 ref. tracker with Micro-Megas (1kCH-SRS Minicrate, MMDAQ )
CMS high Eta GEM collaboration ( VFAT hybrid and VFAT SRS adapter, in prep. )
Totem upgrade R&D , SRS VFAT readout, DATE ?
Applications with Cosmic Tomography
FIT Florida, Muon Tompography for homeland security, GEMs ( 1st 16K SRS application, DATE )
Geoscienes CRNS- Waterquality in Rocks, MMegas ( 5kCh SRS Crate , DATE , Labview)
R&D with MPGD’s ( small systems )
Bonn/Mainz Univ, Timepix readout ( SRS- Timepix adapter card )
Helsinki HIP, GEM-MMega ( SRS evaluation, Trigger pickup box via CSP )
MEXICO UNAM, THGEM 2x ( SRS Minicrate, DATE )
C.E. Saclay, Micromegas ( 2k Ch SRS Minicrate , MMDAQ)
WIS Israel, THGEM 3x ( Minicrate, Beetle hybrid, SRS- Labview Beta tester
INFN Naples (Minicrate, Labview for SRS developer, CTF card , Zero-supression code
HEP experiments
NEXT Coll., dual Beta decay, SiPM, PM ( Collaboration on SRS HW & FW, FEC cards, DATE )
BNL GEM detector readout ( 2kCH. APV Minicrate, PHENIX SRDAQ porting to SRS )
Jeff. Lab Virginia Univ. GEM prototyping, ( Minicrate , Offline Data evaluation via AMORE + DATE)
* in red: SRS developers in green: to be confirmed in blue: USER
Teams waiting for commercial SRS delivery (orders via CERN store )
RD51 lab, Radcore, WIS, USTC, SAHA, INFN Bari, INFN Napoles, Stony Brook, Freiburg Univ
Yale Univ, J-Parc-RIKEN, East Carol. Univ., Jeff-Lab, Tsinghua Univ, Univ Texas,
SRS crate 16k ch.
SRS Minicrate up 4k ch.
RD51 SRS User Status
H. Muller

## Slide 20
C++ version of Garfield:
C++ class that has the functionality of the Garfield Fortran for gas has been developed. Lots of effort went into benchmarking and validating the new C++ code.
Gas properties (i.e. Magboltz) and primary ionization (i.e. Heed) have been implemented.
Drift path integration algorithms and analytic field calculations had already been translated, and it opens the path to TPC-like calculations.
Microscopic, MC and Runge-Kutta charge transport techniques are in place.
Progress is being made in a second generation and final interface to Geant4 from Garfield C++.
Maintenance:
Ionization processes – Heed and MIP (cluster size distribution, electron range and Fano limit)
Field calculations – BEM method validated for MPGD
Gas properties – Magboltz tables extended and updated (Ar, Xe, He, Ne; GeH4,SiH4, C2H2F4 )
(Import ant in view of the next generation electroluminescent detectors for dark matter and double beta decays searches)
Generic studies:
Penning transfers
Avalanche statistics and gain fluctuations
Neutron detection in gases
Photon feedback
Modeling:
MicroMegas transfer properties
GEM charging up
IBF for TPC application
20
WG4: MPGD Simulation Tools
Focus on providing techniques for calculating electron transport in small-scale detectors.
The main difference with traditional gas-based detectors is that the electrode scale is comparable to
the collision mean free path.
R. Veenhof

## Slide 21
WG4: MPGD Simulation Tools
21
R. Veenhof
S. Didlick
H. Schindler

## Slide 22
Detector Technology | Currently produced | Future Requirements
 | cm * cm | cm * cm
GEM | 40 * 40 | 50 * 50
GEM, single mask | 70 * 40 | 200 * 50
THGEM | 70 * 50 | 200 * 100
RTHGEM, serial graphics | 20 * 10 | 100 * 50
RTHGEM, Kapton | 50 * 50 | 200 * 100
Micromegas, bulk | 150 * 50 | 200 * 100
Micromegas, microbulk | 10 * 10 | 30 * 30
1) Current: CERN-MPGD workshop is the UNIQUE MPGD production facility
(generic R&D, detector components production, quality control)
RD51
Collaboration
Survey:
2) Future MPGD R&D: Reinforcement of CERN-MPGD workshop infrastructure to produce 2x1m
Bulk Micromegas and 2x0.5 m GEMs has been approved by CERN Management (Nov. 2009)
Participation the AIDA proposal
3) Technology Industrialization  transfer “know-how” from
CERN workshop to industrial partners for MASS PRODUCTION
22
RD51– MPGD Production
R. De Oliveira

## Slide 23: New TE/MPE/EM Workshop Building 107
New location
Water treatment plant
Present location
R. De Oliveira
Start of the construction : beginning 2012
Completion: October 2013

## Slide 24
GEM Technology
New Flex (Korea, Seoul)
Tech-ETCH (USA, Boston)
Scienergy (Japan, Tokyo)
Keerthi Industries (India)
MicroMETAL GmbH (Germany, Muellheim)
Micromegas Technology
ELTOS S.p.A. (Italy)
TRIANGLE LABS (USA, Nevada)
SOMACIS (Italy, Castelfidarco)
CIREA (France, CHOLET)
THGEM Technology – ELTOS S.p.A. (Italy)
24
Technology Industrialization
Potential partners
Industrial test runs for each technology foreseen in 2012 after selection of the best candidates
New Flex Facilities and the first evaluation GEM foils produced there

## Slide 25
25
Example
Θ
Θ
~ 1.5 cm
Cargo container
hidden &
shielded
high-Z
nuclear
material
MPGD Tracking Detector (GEMs)
Gas
Electron
Multiplier
Detector
M. Hohlmann,
WG6: Technology Transfer and Spinoff
Homeland Security
Cosmic Muon Tomography
Spherical GEM
For X-Ray Diffraction
Scalable Readout System

## Slide 26
GOSSIP/GridPix
THGEM for HCAL
THGEM for RICH
WG7: Test Beam Facility at H4 SPS
26
2012 RD51 beam allocation
4 – 18 June
9 – 23 July
2 – 15 November
Y. Tsipolitis
2 beam telescopes; services; DAQ, FEE

## Slide 27
GEM for CMS High-Eta upgrade
GEM for TOTEM T1 upgrade
Micromegas TPC for ILC (Saclay)
DHCAL Micromegas for CALICE
DHCAL Micromegas
CMS High-Eta & TOTEM T1 upgrades
WG7: Test Beam Facility at H4 SPS
27
THGEM for RICH (upgrade for COMPASS)
GOSSIP/GridPix (NIKHEF) ATLAS inner tracker upgrade
THGEM for HCALs (Aveiro/Coimbra/UTA/Weizmann)
Resistive MicroMegas for JLAB and COMPASS (Saclay)
MicroMegas TPC for nuclear physics (Demokritos Athens)
Y. Tsipolitis

## Slide 28
RD51 Simulation School (19-21 January 2011)
Contents:
Introduction to Geant4
Introduction to FEM, COMSOL
Field calculations
Transport of electrons in small-scale devices
Calculation of signals and their processing
25 participants; enthusiastic feedback
RD51 Simulation School
28

## Slide 29
29
“GEM Detectors”
The principles of GEM-based detectors and their applications will be explained. GEM detectors will be
assembled, and afterwards tested in X-ray stands. Concepts such as detection of X-rays will be explained and
pulse height gain, and counting rate measurements will be carried out.
Professors of excellence and Tutors: L.Ropelewski, G.Bencivenni
“GridPix and Micromegas”
The set-up consists of two tests stations:
A complete GridPix/Gossip detector(s): PolaPix, Dice, Gossip including gas system, new miniHV supplies and
readout systems. Students will operate the set-up and take data with various sources and cosmic rays, followed
by data analysis: track fitting, dE/dX, interaction of ionization radiation with gas.
The second set-up consists of a 10x10 cm2 bulk Micromegas read out by a charge preamp, amplifier- shaper and
a Multi-Channel analyzer, and a 1726-channel TPC in a gasbox, read out by T2K electronics. Fundamental
concepts such as X-ray conversion, diffusion, electron collection and gas amplification will be understood via
measurements with a full DAQ and analysis chain.
Professors of excellence and Tutors: H.van der Graaf, P.Colas
Excellence in Detectors and Instrumentation Technologies CERN, Geneva, Switzerland - 31 January - 10 February 2011

## Slide 30
consolidation of the Collaboration and MPGD community integration
considerable progress in MPGD technologies in particular large area GEM, THGEM, Micromegas; some picked up by experiments (including sLHC upgrades) for feasibility studies and prototyping
secured future of the MPGD technologies development through the TE MPE workshop upgrade and FP7 AIDA contribution (upgrade in progress)
improved MPGD simulation software framework allows for first applications
infrastructure for common RD51 test beam facility (~20 user groups)
development of common, scalable electronics (~20development and user groups)
contacts with industry for large volume production, first runs
30
Summary and Outlook