## Slide 1: EuPRXIA@SPARC_LAB energy boosting to 5 GeV by LWFA and external injection
Andrea R. Rossi

## Slide 2: From EuPRAXIA CDR

## Slide 3: Boundary conditions
Wall
Injector
Plasma
But also an operating user facility!

## Slide 4: The interaction chamber, transfer line and diagnostic dipole
INTERACTION CHAMBER:
Contains plasma target and optics for matching and capture of the electron bunch(es)
TRANSFER LINE:
A chicane for separating driver(s) from witness.
Quadrupoles for transport and matching to the dipole.
Diagnostics.
DIPOLE:
A bending magnet that opens dispersion and allows energy measurement.
We assume 22 deg bending angle.
DUMP:
Only a placeholder!

## Slide 5: The spectrometer dipole @ 5 GeV
https://www.sesame.org.jo/accelerators/technology/magnets-and-ids
SESAME bending dipole @ 2.5 GeV
EuPRAXIA@SPARC_LAB bending dipole @ 5.0 GeV
Assuming a bending angle as the 1 GeV spectrometers (same resolution)
SC option?
Possible, but expensive.

## Slide 6: Transfer line
Driver - Witness separation chicane:
most probably not needed.
Transfer - matching line (3125 mm).
Very rough approximation:
Again, SC magnets could be a viable but expensive alternative.

## Slide 7: The PWFA option: high transformer ratio
…
…
Train of 4 bunches (3D+1W) with tuned, increasing charge and tailored current profile

## Slide 8: Plasma chamber: the PWFA option
1 GeV plasma target: , int chamber (contains PMQs)
ASSUME:
5 GeV plasma target: , int chamber (?)
The only way to reduce size is improving WP average field.

## Slide 9: LWFA: external injection
I assume discharge capillaries. The high power laser pulse needs to be guided for the whole capillary length.
I am NOT considering the laser transport system!

## Slide 10: Plasma chamber: the LWFA option
ASSUME:
5 GeV plasma target: , int chamber

## Slide 11: Straight PWFA
5 m
10 m
4 m
The most trivial solution is “invasive”!
It’s implementation prevents facility operation for a long time and requires significant intervention and careful planning

## Slide 12: Dogleg PWFA
5 m
10 m
4 m
PROS:
Compatible with facility current layout
All PWFA
CONS:
Large bending angle (22 deg)
Highly risky: dogleg + COMB structure

## Slide 13: Dogleg PWFA: building constraints

## Slide 14: Dogleg LWFA: injection @ 500 - 600 MeV
3 m
10 m
4 m
PROS:
Compatible with facility current layout
Dogleg with smaller angle (10 deg)
Works with 12J laser on target
Undulator room downstream
CONS:
No PWFA at all
Risky: long laser guiding
Low rep rate
Laser should be removed

## Slide 15: Dogleg LWFA @ 500 MeV: building constraints
3 m
10 m
4 m

## Slide 16: Dogleg LWFA: injection @ 100 MeV
3 m
10 m
4 m
PROS:
Compatible with facility current layout
Dogleg with smaller angle (10 deg)
Lot of space downstream
CONS:
No PWFA at all
Lower injection energy, requires 1 PW laser
Risky: long laser guiding
Low rep rate

## Slide 17: Dogleg LWFA @ 100 MeV: building constraints

## Slide 18: Hybrid PWFA + dogleg LWFA, option 1
3 m
10 m
4 m
PROS:
Compatible with facility current layout
PWFA + LWFA!
CONS:
Large angle dogleg
Risky: long laser guiding
Staging
From PWFA:
Eout = 1.0 - 1.7 GeV
LWFA:
Eout = 5.0 GeV
Ein = 1.0 - 1.7 GeV

## Slide 19: Hybrid PWFA + LWFA 1: building constraints

## Slide 20: Hybrid PWFA + dogleg LWFA, option 2
PROS:
Compatible with facility current layout
Small dogleg angle (10 deg)
Only 1D + 1W in dogleg
PWFA + LWFA!
CONS:
Comb structure in dogleg
Risky: long laser guiding
Staging
3 m
10 m
4 m
2m
2m
Ein = 500 MeV
Eout = 1.0 GeV
PWFA:
Ein = 1.0 GeV
Eout = 5.0 GeV
LWFA:

## Slide 21: Hybrid PWFA + LWFA 2: building constraints
3 m
10 m
4 m
2m
2m

## Slide 22: Risk mitigation
Hose instability/dispersion related problems: Dumper bunch, arXiv:2409.12041v1
Long guiding channel: filament, HOFI
Laser removal: plasma mirror

## Slide 23: Thanks for your attention

## Slide 24: Backup slides

## Slide 25: Dogleg LWFA: injection @ 500 - 600 MeV
Laser parameters:
σtr = 40 μm
El = 12 J
στ = 30 fs
Bunch parameters:
q = 30 pC
Ein = 500 MeV
στ = 13 fs
n0 =