## Slide 1: Virtual Diagnostics ?!
Dr. Jan Grünert
X-ray Photon Diagnostics Group
Frascati, Italy 08 November 2024
Enlightening Science

## Slide 2: Photon Beamlines (photon tunnels)
** very real, not so virtual **

## Slide 3
EuXFEL photon beam diagnostics hardware (real, physical)
Beam parameters of interest:
  pulse energy
  beam position / shape
  wavelength / spectrum
  polarization
  arrival time
  pulse duration
  wavefront
Filter Ch. & IMGTR
Pop-in Monitor
SR-imager
MCP-detector
K-mono
HIREX
single shot spectrometer
PES
X-ray Gas Monitor (XGM)
  ~ 50 distinct diagnostic hardware installations in 3 undulator beamlines
  ~ 15 to 20 of these are continuous online diagnostics
Overview Reference : J.Grünert et al., J. Synchrotron Rad. 26 (5), 1422–1431 (2019)
** very real, not so virtual **

## Slide 4: What‘s virtual beam diagnostics?
  In a strict sense: a software-based beam-diagnostic monitor without physical hardware embodiment
  In a wider sense, it could also be: data mining that creates additional information about the properties of the beam
  Or maybe: access to beam property B via a monitor originally deployed for property A
  And also: new insights about the beam by combinations of monitors

## Slide 5: What‘s NOT virtual beam diagnostics?
  Lengthly offline post-processing of (e.g.) user experiment data
  Software monitors that don’t increase the knowledge about photon beam properties

## Slide 6: What can we gain by introducing virtual diagnostics?
  Improve the measurement resolution for a specific beam property the measurement accuracy, fidelity
  Simplify the measurements (decrease the need for human experts) the calibrations and the data analysis
  Become non-invasive online monitoring of beam properties which previously were only accessible invasively  increase information availability
  ....

## Slide 7: What are practical foundations to obtain these benefits?
  Existance of online diagnostics hardware - implemented and well characterized - must exist in the locations of interest
  Availability of online diagnostics - in operation - tuned to actual current beam conditions - must produce reliable data
  Automation of online diagnostics
  The virtual diagnostics software itself

## Slide 8: How can we create virtual diagnostics?
  Aggregate data from several existing (hardware) monitors e.g. beam pointing from several transmissive imagers
  Find deterministic correlations between data of several monitors
  Beyond deterministic, use machine learning to create maps between several monitors which then allow to stop one of them (because it‘s invasive, costly, difficult, ...)

## Slide 9: Let’s go virtual !
Tunnel flight April 2016
XPD group