## Slide 1: Linacs for FLASH radiotherapy
Young@INFN seminar
Lucia Giuliano, PhD
Sapienza University of Rome
SBAI Department

## Slide 2
OUTLINE
FLASH radiotherapy
ElectronFLASH@Institut Curie
Safest for deep tumors
FlashLab@Sapienza

## Slide 3
FLASH THERAPY is a new way to deliver the dose:
ms pulses of radiation,
beam-on time < 100-200ms
high dose per pulse (>1 Gy)
high mean dose rate (>40-100Gy/s)
FLASH effect in Radiotherapy
Fig. Courtesy of Vincent Favaudon - Curie Institute
Dose rate =0,1 Gy/s
Dose rate =125 Gy/s
Example n=100Hz
Healthy Fibrosis Healthy
Control 17 Gy CONV 17 Gy FLASH
 | Conventional | FLASH
Facility | Cs | e- LINAC
Nominal energy (MeV) | 0,66 | 4,5
Pulse vs continuous | Continuous | Pulsed
Pulse repetition frequency (Hz) | - | 150 Hz
Dose (Gy) | 17 | 17
Mean Dose rate (Gy/s) | 0,03 | 60
Temporal width of pulse | few ms | 1 ms
 | Conventional | FLASH
Facility |  | e- LINAC
Nominal energy (MeV) | 0,66 | 4,5
Pulse vs continuous | Continuous | Pulsed
Pulse repetition frequency (Hz) | - | 150 Hz
Dose (Gy) | 17 | 17
Mean Dose rate (Gy/s) | 0,03 | 60
Temporal width of pulse | few ms | 1 ms
Favaudon et al., Science Translational Medicine 6, 2014
FLASH irradiation protects healthy tissues from damage and remains as efficient as CONV irradiation in the repression of tumor growth

## Slide 4
FLASH THERAPY is a new way to deliver the dose:
ms pulses of radiation,
beam-on time < 100-200ms
high dose per pulse (>1 Gy)
high mean dose rate (>40-100Gy/s)
FLASH effect in Radiotherapy
Fig. Courtesy of Vincent Favaudon - Curie Institute
Dose rate =0,1 Gy/s
Dose rate =125 Gy/s
Example n=100Hz
Healthy Fibrosis Healthy
Control 17 Gy CONV 17 Gy FLASH
 | Conventional | FLASH
Facility | Cs | e- LINAC
Nominal energy (MeV) | 0,66 | 4,5
Pulse vs continuous | Continuous | Pulsed
Pulse repetition frequency (Hz) | - | 150 Hz
Dose (Gy) | 17 | 17
Mean Dose rate (Gy/s) | 0,03 | 60
Temporal width of pulse | few ms | 1 ms
 | Conventional | FLASH
Facility |  | e- LINAC
Nominal energy (MeV) | 0,66 | 4,5
Pulse vs continuous | Continuous | Pulsed
Pulse repetition frequency (Hz) | - | 150 Hz
Dose (Gy) | 17 | 17
Mean Dose rate (Gy/s) | 0,03 | 60
Temporal width of pulse | few ms | 1 ms
Favaudon et al., Science Translational Medicine 6, 2014
FLASH irradiation protects lungs from radiation-induced fibrosis and is as efficient as CONV irradiation in the repression of tumor growth

## Slide 5: Accelerator to investigate the FLASH effect
Understanding the FLASH RT limits (min/max dose/time)
Clarify the bio mechanisms underlying FLASH effect
Defining conditions for clinical practice
Institut Curie commisioned a new Linac dedicated for Flash therapy and radiobiology experiments.
We have developed the RF and beam dynamics design of the accelerator built by the company S.I.T. Sordina IORT Technologies S.p.A.

## Slide 6: Realization of ElectronFLASH
Linac installed at Institut Curie (5 - 7 MeV)
Medical Linac for preclinical FLASH studies
Low energy electrons (max 9 MeV)
High peak current to deliver high dose

## Slide 7
The resonant modes have a fixed spatial configuration
They oscillate in time
The electromagnetic energy is reflected back and forth at both ends of the cavity
S-band linac (f=2,998 GHz)
Bi-periodic geometry
Standing wave structure (SW)
p/2 mode: Coupling cells are empty (no field inside)
Magnetic coupling with hole off axis
Input power
Cathode
Linac @Instut Curie: electromagnetic design
E field

## Slide 8: In vivo and vitro experimental set-up
In vitro
In vivo

## Slide 9: Dosimetry Issues in FLASH-RT
The films must be verified by a second dosimeter
Analysis require long time (24h to scanner film and several time to analyzed them)
Current precision on dose with film dosimetry > 5%
Pic. Courtesy of S. Heinrich
Accurate dosimetry of these ultra-high dose rates is a major challenge and crucial for the safe transition of FLASH radiotherapy into clinical practice.
  Ionization chambers and classical dosimeters need to be adapted to operate under high dose rate conditions: they read dose > 40 Gy in less than 100 ms

## Slide 10: Irradiations at Institut Curie
IRRADIATED SAMPLE
RADIOCROMIC FILM

## Slide 11
FLASH effect was identified with low energy electron-beam not appropriate to treat deep tumors:
SAFEST
SApienza Flash Electron Source for radio-Therapy

## Slide 12
SAFEST PROJECT general layout
Frequency | 5.712 GHz
Beam Energy | 65 - 100 MeV
RF Repetition rate | 100 Hz
C-band average accelerating gradient | 45 MV/m
RF pulse duration | 1.2 – 2.5 ms
In pulse dose rate | > 10^6 Gy/s
Average dose rate | > 100 Gy/s
Dose per pulse | >> 1 Gy
C-band combines a high shunt impedance with a high transmission efficiency:
high peak current for FLASH regime.
Hybrid configuration with SW Injector and TW accelerating structures with one klystron
An asymmetric power splitter allows avoiding the circulator for the SW

## Slide 13
SAFEST PROJECT general layout
Frequency | 5.712 GHz
Beam Energy | 65 - 100 MeV
RF Repetition rate | 100 Hz
C-band average accelerating gradient | 45 MV/m
RF pulse duration | 1.2 – 2.5 ms
In pulse dose rate | > 10^6 Gy/s
Average dose rate | > 100 Gy/s
Dose per pulse | >> 1 Gy
Standing wave Injector

## Slide 14
Electron source: pulsed DC thermionic gun at 15 kV.
Electrons source and SW injector
Other contribution L. Faillace and D. Francescone
DC gun
Standing wave, bi-periodic geometry with on-axis coupling cells
p/2 mode
Nose - cone geometry: produces very high electric field in the middle of the accelerating cells
Bunching section for low-energy beam capture (> 45%)
Beam energy up to ≈ 10 MeV and 100 mA beam peak current
Power in
Bunching section
Freq | Rshunt | Q
5.712 GHz | 116 MW/m | 11260
Single cell parameters [mm]
D | g | L | Rb | Ro | a
38.25 | 15.6 | 24.4 | 3 | 6 | 30°

## Slide 15
Accelerating Field measurement
RF power
Power In
Beam axis
C-Band (f=5.712 GHz) prototype comprises five identical accelerating cells, representing the linac’s speed-of-light section
The bead-pull measurements showed an almost equal flatness of the electric field in the five accelerating cells.
The electric field measurements confirmed the presence of the π/2 mode with a high electric field in the accelerating cells and no field in the coupling cells.

## Slide 16
Traveling wave structure
Frequency | 5.712 GHz
Beam Energy | 65 - 100 MeV
RF Repetition rate | 100 Hz
C-band average accelerating gradient | 45 MV/m
RF pulse duration | 1.2 – 2.5 ms
In pulse dose rate | > 10^6 Gy/s
Average dose rate | > 100 Gy/s
Dose per pulse | >> 1 Gy
SAFEST PROJECT general layout

## Slide 17
TW prototype RF design
Power in
Power out
Dual-feed different input and output RF power couplers
Electric field polar plot with cell-to-cell phase advance
Single Cell design
a | b | d | R0 | t | r1/r2
5 | 21.03 | 17.5 | 6 | 3 | 1.25
cell-to-cell phase advance @5.712 GHz
TW Constant Impedance ( a = 5 mm )
  Decrease the filling time, which will be shorter than the RF pulse.
  Reduce the losses of particles on the walls, thus reducing issues related to radiation protection.
  The shunt impedance remains at an acceptable compromise value: 95 MW/m for t = 3 mm and r1/r2 = 1.25
HG structure with average gradient for equal to = 45 MV/m (unloaded), with an RF input power of Prf = 30 MW for a structure length = 1.0 m
Asymmetric cell to facilitate mechanical processing.
3D Electric field on beam axis
a.u.

## Slide 18
Prototyping phase
Brazing alloy
Pre-prototypes on 5-cells without couplers to test the brazing procedure, vacuum sealing and the in-house mechanical design.
Prototype of 12 cells with couplers has been brazed @INFN LNF –FRASCATI oven to perform low-power RF tests.
Main contributors: D. Alesini, R. Di Raddo, L. Faillace, L. Giuliano, M. Magi, M. Migliorati
In house building of the accelerating cavities
Screws
Screws: prevent external clamping and ensure alignment and easier assembly

## Slide 19
BeadPull measurements after tuning
The structure after mechanical processing is untuned: tuning by deformation
Others contribution: F. Cardelli, D. Alesini,L.Faillace, L.Ficcadenti A. Mostacci
Input coupler
Output coupler
tuners
Electric field after tuning
120 degree the phase shift of the electric field in the adjacent cell

## Slide 20
Asymmetric power splitter
Phase shifter
Attenuator
SW Injector
TW Structure
30 MV/m
5 MW 4 ms
Pulse compressor 20 MW, 1 ms
First step@Sapienza
Machine for pre-clinical studies of FLASH was funded with budget of 1.6 ME
30 MeV
1 mt

## Slide 21
M. Magi, M. Migliorati, A. Mostacci, L. Palumbo (Sapienza University of Rome)
L. Ficcadenti, (INFN-ROMA, Rome)
D. Alesini, R. Di Raddo, L.Faillace, B. Spataro (LNF-INFN, Frascati)
SiT Sordina IORT technology spa Company
Thanks to…
..and to you for your attention!!
Young@INFN

## Slide 22: FlashLAB@SBAI