## Slide 1: ASTERIX (Accelerating STructures made of multiplE sectoRs In X-Band) 3 anni (2025-2027) Units: LNF, LNS, Roma1 Research line: Accelerators and related technologies
L. Faillace (Resp. Naz.) - LNF
July 09, 2024
Nuova Proposta di Esperimento in CSN5 (INFN)
Support from INFN-LNF Laboratory
External Collaborators: V. Dolgashev (SLAC), Tetsuo Abe (KEK)
PhD student from the University of Science and Technology of China (USTC)
Esperimenti in CSN5 correlati:
MICRON (2022-2024)
ARYA (2020-2023)
DEMETRA (LNF/LNS)

## Slide 2: ASTERIX team
LNF
Roma1
LNS
LNF | FTE | LNS | FTE | Roma1 | FTE
L. Faillace (Resp. Naz.) | 0.4 | G. Torrisi (RL) | 0.1 | L. Ficcadenti (RL) | 0.3
D. Alesini | 0.2 | D. Mascali | 0.05 | M. Petrarca | 0.2
M. Bellaveglia | 0.05 | G. Mauro | 0.1 | M. Migliorati | 0.2
S. Bini | 0.2 | G. Sorbello | 0.2 | G. Silvi | 0.2
F. Cardelli | 0.3 | T. Isernia | 0.3 | L. Palumbo | 0.4
M. Carillo | 0.2 | R. Palmeri | 0.3 |  | 
E. Chiadroni | 0.2 | A. Locatelli | 0.1 |  | 
A. Falone | 0.2 | C. De Angelis | 0.1 |  | 
A. Gallo | 0.15 | L. Vincetti | 0.1 |  | 
A. Giribono | 0.2 |  |  |  | 
A. Liedl | 0.1 |  |  |  | 
L. Piersanti | 0.1 |  |  |  | 
S. Pioli | 0.2 |  |  |  | 
B. Spataro | 0 |  |  |  | 
C. Vaccarezza | 0.2 |  |  |  | 
Tot./Unit | 2.7 |  | 1.35 |  | 1.3
Total FTE
5.35
L. Faillace CdL (Preventivi) INFN-LNF, 09-07-2024

## Slide 3: Motivation
The Accelerating gradient is the key parameter
for the design, construction and cost of future linear accelerators
Linacs must be reliable and cost-effective
World-wide intense and systematic research (SLAC/INFN/KEK/CERN/Tsinghua Uni) on high-gradient accelerating RF structures started with the investment for the construction of normal-conducting linear colliders, new generation X-FELs, etc.
In order to be feasible the design of linear colliders posed a minimum value on the accelerating gradient  100 MV/m.
L. Faillace CdL (Preventivi) INFN-LNF, 09-07-2024

## Slide 4: Research Context
Framework of a continuous more-than-two-decade-long collaboration on the study of RF structures with increasing accelerating gradients and the RF breakdown physics: SLAC (USA), INFN-LNF and KEK (Japan)
Study of various geometries, materials, surface processing techniques and technological developments of advanced accelerating structures working in X-band (11 – 12 GHz):
  This research is strongly required by a demand for ever more advanced accelerating structures, with accelerating gradients well-above 100 MV/m, since higher efficiency and robust manufacturing play a major role for the next generation of linear particle accelerators for research;
  These structures are made of hard copper and hard copper alloys  better high-gradient performance;
  Different geometries, e.g. “open-type” structures (two halves, four quadrants, etc.)
  Alternative “braze-free” joining techniques, e.g. EBW and TIG welding.
Applications: future linear colliders; existing and new-generation X-FELs, such as EuPRAXIA@SPARC_LAB; industrial, and medical applications.
L. Faillace CdL (Preventivi) INFN-LNF, 09-07-2024

## Slide 5: State-of-the-art
“Single-cell” cavities (open and closed; disk-type and multi-sector)
TW multi-cell structures (open and closed; disk-type and multi-sector)
Open-type multi-sector cavities, typically of small lengths (20- 25 cm).
Dolgashev VA, Faillace L, Spataro B, Tantawi S, Bonifazi R. High-gradient rf tests of welded X-band accelerating cavities. Physical Review Accelerators and Beams. 2021 Aug 10;24(8):081002.
CLIC-G-OPEN
30 cm
KEK (Tetsuo Abe) 2023
X-band
4 quadrants
EBW welding
To be High-power tested.
TIG
EBW
open
T. Abe, et al., High-gradient test results on a quadrant-type X-Band single-cell structure.
30 cm
22 cm
CERN 2007
X-band
4 quadrants
Clamped, high T-treated
High-power Tested:
 Gradient: 80 MV/m with 40 ns pulse length.
SLAC/CERN 2018
X-band
2 halves, open structure
Brazed
High-power tested:
 Gradient: 100 MV/m with 200 ns pulse length.
L. Faillace CdL (Preventivi) INFN-LNF, 09-07-2024
One quadrant
62.448 mm

## Slide 6: Goal
First-time demonstration of practical, meter-long, X-band RF accelerating structure for real linear accelerators:
high accelerating gradients (>100 MV/m);
composed of four-quadrants (“open-type”);
made out hard copper;
joined and vacuum sealed by using TIG welding (“braze-free” technique).
Requirement to be competitive among the world-wide collaboration
cost-effective and robust manufacturing.
ASTERIX stands apart from state-of-the-art
cancellation of the dipole and quadrupole EM field components, detrimental for the beam dynamics
improved pumping speed and easy insertion of HOM absorbers (in case of multi-bunch operation)
Superior high-gradient performance, compared with soft copper
L. Faillace CdL (Preventivi) INFN-LNF, 09-07-2024

## Slide 7: Full TW multi-cell X-band structure
90 cm
Fabrication out of hard copper
Increase in vacuum pumping speed
Overall reduction of the fabrication costs
Easy insertion of HOM absorbing materials
TIG-welded
4-quadrants
«open-type»
27 cm
TIG welding joints
Integrated
mode-launcher
Cooling channels
tuners
L. Faillace CdL (Preventivi) INFN-LNF, 09-07-2024

## Slide 8: Full TW multi-cell X-band structure
Single quadrant
Alignment pins
TIG welding joints
Secondary vacuum chamber (extra pumping, easy insertion of HOMs absorbers in multi-bunch operation,…)
L. Faillace CdL (Preventivi) INFN-LNF, 09-07-2024

## Slide 9: Objectives
MULTI-BUNCH GEOMETRY
SINGLE-BUNCH GEOMETRY
DESIGN
FABRI-
CATION
LOW RF POWER TEST
HIGH RF POWER TEST
RF and thermo-
mechanical analysis
Wakes/HOMs mitigation
Multipacting analysis
Tolerance and misalignment analysis.
Low-precision full model for mechanical tests (quadrant straightness and alignment, TIG welding process, vacuum tightness)  1° year
Prototyping activity, nominal precisions (small-scale structure, 30 cm and 20 cells)  2° year
Full-scale structure with four-port RF mode-launchers  3° year
DESIGN
Asterix& Obelix
HIGH RF POWER TEST
Validate the structure's fabrication within required tolerances for tuning:
measure key RF parameters (resonant frequency, quality factor, and coupling coefficient  scattering parameters.
Bead-pull for on-axis electric field amplitude and phase.
High-gradient performance (compressed pulse up to 200 MW from VKX8311A 50 MW X-band klystron by CPI and BOC-type compressor):
Accelerating gradient
RF breakdown probability
Dark current (surface field emitted electrons)
Limited time, budget
Future experiments
Version 2.0
Asterix &Obelix
World-wide collaboration
&
EuPRAXIA@SPARC_LAB scenario
Reasonable scope, time and budget
Cell with HOM WGs
LATINO Laboratory
INFN-LNF
TEX facility INFN-LNF
L. Faillace CdL (Preventivi) INFN-LNF, 09-07-2024
Cell without HOM WGs
tuners
Secondary vacuum chamber

## Slide 10
L. Faillace CdL (Preventivi) INFN-LNF, 09-07-2024

## Slide 11
RF and Wakefields/HOMs Optimization
Low-precision Full-scale fabrication/mechanical characterization
Report 1
Report 2
Fabrication of small-scale
prototypes/mechanical Validation
Low and High RF power testing of small-scale protoypes
Fabrication of final
Full-scale structure and Mechanical Validation
Low and High-power Testing of Final full-scale structure
Report 6
Report 3
Report 4
Report 5
7 Milestones
6 Deliverables
End
2025
End
2026
Start
2025
End
2027
Report of the Feasibility Study (RF and Wakefields/HOMs);
Report of the Mechanical Engineering of the low-precision prototype with standard RF couplers for Mechanical, TIG welding and vacuum testing;
Report of the Mechanical Engineering of the small-scale structures with ad-hoc integrated RF Mode Launcher couplers;
Report of the low/high RF power testing of the small-scale structures;
Report of the Mechanical Engineering of the Full Structure with with ad-hoc integrated RF Mode Launcher couplers;
Final Report of low and High RF power testing of final full-scale structure.
Prototyping Activity
Final full-structure Tests
Feasibility Study
30 cm
4-port Mode-launchers
30 cm
Standard couplers
90 cm
4-port Mode-launchers
90 cm
quadrant straightness and alignment
TIG welding process
vacuum tightness

## Slide 12: Budget
YEAR |  | Cost | Quantity | INFN Units | 
1 | Software License – CST Microwave Studio | € 31,000.00 | 2.00 | LNF/LNS | Ask for advance
 | Inventariabile (Workstation) | € 6,000.00 |  | LNF | Ask for advance
 | Consumabili | € 35,000.00 |  |  | 
 | Missions | € 4,500.00 |  | LNF/LNS/Roma1 | 
 | TOT. 1st year | € 76,500.00 |  |  | 
2 | Consumabili | € 70,000.00 |  | LNF | Prototyping (max 30 cm)
 | Cavi+WG adapters, 2xRF power loads | € 56,500.00 |  | LNF | Activity: Cavity+MLs
 | 2xFCs | € 4,800.00 |  | LNF | 
 | Turbopump and Scroll | € 8,000.00 |  | LNF | 
 | Missions | € 12,000.00 |  | LNF/LNS/Roma1 | 
 | TOT. 2nd year | € 151,300.00 |  |  | 
3 | Consumabili | € 130,000.00 |  | LNF | Full structure (90 cm)
 | Missions | € 12,000.00 |  | LNF/LNS/Roma1 | 
 | TOT. 3rd year | € 142,000.00 |  |  | 
TOT |  | € 369,800.00 |  |  | 
L. Faillace CdL (Preventivi) INFN-LNF, 09-07-2024

## Slide 13: Thanks for your attention!
L. Faillace CdL (Preventivi) INFN-LNF, 09-07-2024