## Slide 1: Cryopumps
Vapor pressure
Evaporation and condensation
Thermal desorption and sojourn time
Sticking probability
Adsorption isotherms
Basic structure of a cryopump
Equilibrium pressure of «trapped» gases
GM refrigerator: no LHe needed
Main commercial cryopump parmeters
Cryopump operation
Cryopump regeneration

## Slide 2
Pressure vs. Time
Fm Vacuum Techonolgy II P.D. Rack

## Slide 3: Equilibrium condition
Q
J. P. Langeron,
IUVSTA 1996

## Slide 4: Evaporation and equilibrium vapor pressure
Saturated
Not saturated
Equilibrium vapor pressure: is the pressure exerted by a vapor in thermodynamic equilibrium with its condensed phase in a close system at a certain temperature.
It corresponds to the equilibrium between the number of evaporated and condensed molecules.

## Slide 5: Latent heat of evaporation

## Slide 6: Vapor pressure
p in Torr (!)

## Slide 7: Vapour pressure vs. temperature

## Slide 8: Evaporation: vapor pressure of elements
RCA Charts
See for instance:
https://old.mcallister.com/vacuum.html

## Slide 9: Evaporation: vapor pressure of elements
T in °C

## Slide 10: Evaporation: vapor pressure of elements
T in K

## Slide 11: Evaporation: vapor pressure of elements
T in °C
T in K

## Slide 12: Phase diagram for water
H2O
20 mbar

## Slide 13: Cryopumps
Notes: 13

## Slide 14: History of cryopumping
Cryopumping goes parallel to cryogenics
Gas liquefaction:
  Liquid nitrogen, 77.3 K, Dewar, 1874
  Liquid hydrogen 20.4 K, Dewar, 1898
  Liquid helium, 4.2 K, Kammerlingh Onnes, 1908
Successful use of liquid-nitrogen-cooled traps to prevent oil backstreaming from diffusion pumps was reported in the 1910s by Gaede and Langmuir.
First large-scale applications of cryopumping were triggered by the first space projects in the 1950s. They often included operation with liquid hydrogen. Space simulation chambers.
In the second half of the last century, liquid helium bath-cooled cryopumps: high pumping speed, oil free UHV
1960: cryogen free regenerative refrigerator as Gifford – McMahon cyogenerators.

## Slide 15: Basic concept
Absolute temperature
Vapor pressure, saturated vapor pressure
Desorption
Sojourn time
Adsorption and desorption, adsorption isotherms

## Slide 16: The absolute temperature
A
B
°C
K
100
0 °C
273.15 K
0 K
-273.15 °C
100
Ice melting
Boiling water
Notes: 16

## Slide 17: Saturated vapor pressure
The saturated vapor pressure: pressure to which a balance between the number of molecules condensed and those evaporated is formed
If you are in thermal equilibrium, the net flow is equal to zero.
.
H2O
Saturated
Not saturated
Notes: 17

## Slide 18
Thermal desorption: first order
Fm Vacuum Techonolgy II P.D. Rack
The rate of desorption is proportional to the initial concentration and time dependent as
exp(-t/tR) with tR that goes as exp(-1/T)
The rate of desorption decreases with time, as the surface becomes less and less populated. The variation of rate vs. time is given by
The cryopumping is the inverse mechanism w.r.t desorption: the adsorbing surface is cooled, and the equilibrium goes in the direction of the adsorption, and gases and vapor are trapped / pumped and removed from the chamber for a “certain” time

## Slide 19
Thermal desorption: FIRST ORDER DES.
tR Values (average residence time)
system | Desorption energy | Residence time (s) |  | 
 | Mj/(kg-mole) | @77 K | @22 °C | @450 °C
H2O/H2O | 40.6 | 1015 | 10-5 | 10-9
H2O/metal | 96 | - | 105 | 10-5
H2/Mo | 160 | - | 1017 | 1
For LARGE Ed and low T, Long average Residence Time, i.e. «pumped»
s
Ed = Binding Energy
k = 86.17 10-6 eV/K)

## Slide 20: Sojourn time at cryogenic temperature
V. Baglin, CAS 2017
E(eV) | 1.9 K | 4.2 K | 50 K | 70 K
0.01 | 1 106 years | 0.1 s | 1 ps | 0.5 ps
0.02 | ∞ | 3 103 years | 10 ps | 2 ps
0.15 | ∞ | ∞ | 130 s | 6 ms
0.21 | ∞ | ∞ | 5 years | 130 s
0.3 | ∞ | ∞ | 1 104 years | 12 years
Cryosorption occurs till ~ 100 k

## Slide 21: Capture factor Cf
The “capture factor” takes into account the geometry of the system. In practice evaluate the conductance of the aperture of the cryopump for the different gases.
As the cryopump baffle.
Capture factor vary with baffle conductance
Baffle in a cryopump

## Slide 22: Sticking Coefficients 
Function of gas, surface, surface coverage, temperature of gas and surface temperature

## Slide 23: Cryopumping regimes
Physisorption
Sub-monolayer coverage : attractive force (van der Waals) between a gas molecules and a material
Binding energy for physical adsorption
H2 from 20 to 85 meV for smooth and porous materials resp.
1 h sojourn time at 5.2 K and 26 K for smooth and porous materials resp.
Condensation
For thick gas coverage, only forces between gas molecules
Energy of vaporisation 9 to 175 meV for H2 and CO2 resp.
1 h sojourn time at 2.8 K and 53.4 K for H2 and CO2 resp.
 sub-monolayers quantities of gas can be physisorbed at their boiling temperature
(ex : H2 boils at 20.3 K and a bake-out above 100 ºC removes water)
Cryotrapping
Use of a easily condensable carrier (e.g. Ar) to trap molecules with
a high vapor pressure gas (e.g. He, H2)
V. Baglin, CAS 2017

## Slide 24: Adsorption Isotherms
Singolo monostrato
Langmuir
Catalogazione BDDT: Brunauer, Lola S. Deming, W. Edwards Deming e Edward Teller
J. P. Langeron,
IUVSTA 1996
Lineare: piccola copertura
<< 1 monostrato
Langmuir: 1 monostrato
BET:
Brunauer Emmett Teller
Più strati, con comportamento diverso tra primo monostrato e i successivi

## Slide 25: Adsorption Isotherms

## Slide 26: How do we get the gas out of the space?
Cryo-pump design and performance
Cool
(H2O only)
Safety Relief
Inlet
Cold
Refrigerant
Cold Charcoal
Water
Nitrogen and Oxygen
Helium
Hydrogen, Ne
1st stage: 80 K
Baffle: 80 K
2nd stage:
14 K
Notes: A cryogenic pump operates by condensing and trapping the molecules on cold (or really cold) surfaces.
The water is condensed at the top on cool surfaces so that it doesn’t clog-up the rest of the pump. The nitrogen, oxygen, argon and process gases are adsorbed (caught) on the lower surfaces which are kept at about 50 Kelvin (-220˚C). For gasses that don’t condense (helium and hydrogen) there is an activated charcoal region under a cold cap. It’s hidden so that it doesn’t fill up with other gasses..
There are not moving parts in the vacuum, but a compressor is located remotely to the pump head.
If there is a problem and the pump warms up the gas that’s been trapped is released. This can cause the pressure to go up to unsafe levels. A relief valve is intended to vent the system in such emergency situations.
When the pump reaches its capacity (usually by filling with water at the top or helium on the charcoal) it must be regenerated. This is done by pumping the system with a rough pump while allowing the cryo to slowly warm to room temperature.
Pump speed is between hundreds and thousands of liters/second for water and air. Much less for hydrogen and helium.
Ultimate pressures can be 10-10Torr.

## Slide 27: Basic structure of a cryopump
2nd stage:
14 K
1st stage: 80 K
Baffle: 80 K
Coconut
charcoal
Notes: 27

## Slide 28: Cryopumping regimes
Physisorption
Sub-monolayer coverage : attractive force (van der Waals) between a gas molecules and a material
Binding energy for physical adsorption
H2 from 20 to 85 meV for smooth and porous materials resp.
1 h sojourn time at 5.2 K and 26 K for smooth and porous materials resp.
Condensation
For thick gas coverage, only forces between gas molecules
Energy of vaporisation 9 to 175 meV for H2 and CO2 resp.
1 h sojourn time at 2.8 K and 53.4 K for H2 and CO2 resp.
 sub-monolayers quantities of gas can be physisorbed at their boiling temperature
(ex : H2 boils at 20.3 K and a bake-out above 100 ºC removes water)
Cryotrapping
Use of a easily condensable carrier (e.g. Ar) to trap molecules with
a high vapor pressure gas (e.g. He, H2)
V. Baglin, CAS 2017

## Slide 29: Equilibrium pressure for condensation
It depends on:
The condenser properties (specific surface, etc)
The gas nature (vapor pressure)
The condenser temperature
The amount of condensed material.
Notes: 29

## Slide 30: Saturation vapour pressure of various gases
CONDENSED!
Notes: 30

## Slide 31: Saturated vapor pressure curves

## Slide 32: Saturation vapour pressure of various gases
He, H2 and Ne
cannot be
pumped by cryo-condensation
cryo-sorption at charcoal
on cryo-panel
is applied
Minimum closed cycle cryopump temperature
Notes: 32

## Slide 33: Equilibrium pressure for condensation and adsorption of H2 on charcoal
Usually glued with Stycast
Notes: 33

## Slide 34: Cryosorbing materials
Large SURFACE AREA
Large temperature working range (up to ~ 30 K)
 Large capacity
 Large pumping speed
e.g. Activated Charcoal used for closed cycle cryopumps 20 K cryopanels
Density: 0.2 g/cm3
Specific Surface area: 500 to 2000 m2/g
  !one football pitch is 100 x 70 m2, 7000 m2, eq. 8 g, 40 cm3 CHARCOAL
  Capacity ~ 1022 H2/g i.e. 1021 monolayers (P. Redhead, Physical basis of UHV,1968)
  Sticking coefficient ~ 30 % at 30 K (T. Satake, Fus. Tech. Vol 6., Sept. 1984)

## Slide 35
Refrigerator (GMM) cryopump
Notes: 35

## Slide 36: Cryopumps
High vacuum flange
Radiation shield
Baffle
Pump housing
Safety valve
Helium low pressure
connection(green)
Helium high pressure
connection(red)
Cold head motor connection
COOLVAC PM Pump Module
TTR 90 Vacuum gauge
(wired)
V2 Forevacuum valve
(controlled by SC)
Cold head motor
Notes: 36

## Slide 37: Vacuum schematics for cryopump operation
Component of
the cryo-pump
Backing pump
V1 High-vacuum gate valve
V2 Forevacuum valve pump
V3 Forevacuum valve
vacuum vessel
V5 Venting valve
V8 Safety valve, pump vacuum
TM1 Vacuum gauge head
TM2 Forevacuum gauge
PM High-vacuum gauge
Scarico
Notes: 37

## Slide 38: Operating principle of a GM refrigerator
Motor
Control Valve
Weld-on Pipe
Displacer 1st Stage
Expansion volume 1st Stage
Copper flange 1st Stage
Displacer 2nd Stage
Expansion volume 2nd Stage
Copper flange 2nd Stage
Pump out connection
for insulation vacuum
He Outlet (Low pressure)
Overpressure relief valve
He Inlet (High Pressure)
Control disk
Second stage temperature: about 14 K
Notes: 38

## Slide 39
Criopompe a refrigeratore
Notes: 39

## Slide 40: Bilancio energetico di una criopompa
Refrig.
Structural support
Thermal Insulation
Heat Load
Tlow
Thigh
Conduzione parte meccanica
Conduzione gas
Radiazione termica
Variazione entalpia raffreddamento gas
Variazione entalpia passaggio fase gas
Bilanciameno potenza dovuto a

## Slide 41: Il ciclo frigorifero GM
f: numero di cicli al secondo
Valori tipici temperatura e potenza:
Primo stadio, 30 K, 20 – 120 W
Secondo stadio: 10 K, 2 – 20 W
Due stadi in serie: il gas freddo del primo stadio va al secondo per una successva espansione.
Notes: 41

## Slide 42: Cryopump application
Semiconductor production: coating, sputtering
  Advantages: pumping faster, excellent ultimate pressure, high flow rate for Ar, clean vacuum
Industrial processes:
  Advantages: pumping faster, clean vacuum
Applications: EB welding (Ti, Nb), implanters, Large Area Coating
Furnaces for brazing in vacuum:
  High flow, low pressure, fast cycles with automatic regeneration
Particle accelerators:
  HV and UHV lines of beams and rooms with targets in clean vacuum
Space simulation chambers:
  Pumping of large chamber at pressures less than 1x10-6 mbar, with large load of water vapor and few load of process gas
Produzione semiconduttori: coating, sputtering
  Vantaggi: pompaggi più veloci, ottima pressione finale,alta portata per Ar, vuoto pulito
Processi industriali:
  Vantaggi: pompaggi più veloci, vuoto pulito
  Applicazioni: EB welding (Ti, Nb), impiantatori, Large Area Coating
Fornaci per brasatura in vuoto:
  Alta portata, bassa pressione, cicli veloci con rigenerazione automatica
Acceleratori di particelle:
  Linee di fasci HV e UHV e camere con bersagli in vuoto pulito
Camere a simulazione spaziale:
  Pompaggio di grandi camere a pressioni minori di 1* E –06 mbar, con grosso carico di vapor d‘acqua e pochi gas di processo
Notes: 42

## Slide 43
Velocità di pompaggio (l/s)
Portata massima (mbar*l/s)
Pressione di avviamento (mbar)
Crossover value (mbar*l)
Crossover pressure
Capacità (barl) per ciascun gas
Intervallo di rigenerazione
Parametri importanti di una criopompa
Notes: 43

## Slide 44
Caratteristiche di una criopompa (f 160 mm)
Notes: 44

## Slide 45
Caratteristiche di una criopompa „grande“: 60000 l/s
60000 l/s cryopump, f 1300 mm
Parameter Value
Pumping speed (l/s) water 180000
Nitrogen 57000
Hydrogen 60000
Argon 47000
Helium 15000
Maximum throughput (mbar l /s) Argon 25
Hydrogen 12
Pumping capacity (bar l) Argon 9000
Hydrogen 150
Cool-down time (h) 5 – 6 h
Crossover (mbar l) 1000
Weight (kg) 450
Notes: 45

## Slide 46
Velocità di pompaggio S (l/s)
Parametri importanti di una criopompa
Di solito riferita a 273 K.
Dipende principalmente dalle dimensioni e dalla geometria della struttura della pompa, a patto che queste siano a temperature sufficientemente basse.
Qualche volta è indicata anche la velocità di pompaggio specifica (l/s cm2) di apertura
La trappola che pompa il vapor d’acqua limita in parte la conduttanza (trasparenza) per gli altri gas, ma garantisce altissimo valore della velocità di pompaggio per acqua (x 4 o più), dipende dal design della baffle
Notes: 46

## Slide 47: Cryopanel efficiency

## Slide 48
Pressione di avviamento (mbar) e crossover (p×V)
Parametri importanti di una criopompa
La massima pressione di avviamento è la massima pressione alla quale la pompa può essere raffreddata senza problemi. Tipicamente il valore è inferiore a 10-2 mbar.
Il valore di crossover rappresenta il massimo valore impulsivo di portata (mbarl). In pratica il prodotto tra il VOLUME della camera e la PRESSIONE che la pompa vedrà al momento dell’apertura della sua valvola, a pompa fredda a t < 20 K.
Valori tipici per una pompa 3000 l/s: 500 mbar l (500 l a 1 mbar)!
Se non sarà presente una valvola, con grossi volumi, la pompa crio farà fatica a raggiungere le temperature operative. Il limite di crossover con camere grandi e flusso continuo può essere di due / tre ordini di grandezza inferiore.
Notes: 48

## Slide 49
Portata massima (mbar*l/s)
Parametri importanti di una criopompa
Rappresenta la massima portata massiva che la pompa è in grado di sopportare mantenendo il secondo stadio a una temperatura < 20 K.
In alcune pompe specifiche per l’industria dei semiconduttori questa grandezza è massimizzata, e può raggiungere anche qualche decina di scc/s di argon.
La pompa da 60000 litri è in grado di funzionare con un flusso continuo di 25 mbar l/s (25 cc/s!)
Notes: 49

## Slide 50
Capacità (bar*l) per ciascun gas
Parametri importanti di una criopompa /2
Rappresenta la quantità di gas che la pompa è in grado di assorbire, con una riduzione limitata della velocità di pompaggio.
Tipicamente si considera la pompa satura quando la velocità di pompaggio si è ridotta alla metà di quella nominale.
La quantità di gas pompabile è molto grande per i gas condensabili (CO2, Ar, N2,O2), anche dell’ordine del migliaio di litri.
La pompa da 60000 l/s è satura dopo aver pompato 9000 litri di N2 a pressione atmosferica (9 kg)!
Per quanto riguarda l’idrogeno che viene crioassorbito può essere dell’ordine di qualche decina di normal litri. (la 60000 satura a 1500 st. L)
Quando la pompa sarà satura dovrà essere rigenerata.
Notes: 50

## Slide 51: Vacuum schematics for cryopump operation
Component of
the cryo-pump
Backing pump
V1 High-vacuum gate valve
V2 Forevacuum valve pump
V3 Forevacuum valve
vacuum vessel
V5 Venting valve
V8 Safety valve, pump vacuum
TM1 Vacuum gauge head
TM2 Forevacuum gauge
PM High-vacuum gauge
Scarico
Notes: 51

## Slide 52
La rigenerazione di una criopompa
TRE modalità:
Riscaldamento naturale in vuoto
Riscaldamento elettrico con possibilità di rigenerazione parziale
Riscaldamento con gas caldo
Notes: 52

## Slide 53
La rigenerazione parziale/2

## Slide 54
Rigenerazione parziale vs. rigenerazione totale
Durata rigenerazione totale: 2.5 ore
! Formazione di acqua liquida da EVITARE!

## Slide 55
Rigenerazione parziale vs. rigenerazione totale
Durata rigenerazione fast: 40 minuti
! Formazione di acqua liquida da EVITARE!

## Slide 56
Compressore elio per criopompa

## Slide 57
Compressore elio per criopompa
Notes: 57

## Slide 58: Cryopumps: summary charactersistics
High cost
Mechanics uncritical
No risk for venting, only DELAYS
It operates in any position
Rotary pump only required at the start and during regeneration
SHe low
Finite capacity: required regeneration
Between two service life> 10 000 hours
Really large and huge pumps av. (>> 30000 l/s)
Cooling water: almost always necessary
Hydrocarbon contamination: no, FREE
Final pressure limit: 10-10 mbar
Has vibration (1 - 2 Hz)
Notes: 58