## Slide 1
ISOLPHARM_Admiral:
ISOL beams for medical applications
Meeting WP2- WP4 : 20/06/2024
Alberto Andrighetto (INFN) – Project Leader

## Slide 2: The ISOLPHARM Project – 4 pillars
Also…Scientific and training hub
2. Innovative Method
Innovative production @SPES of several (medical)
Carrier Free + High Purity
radionuclides
(111Ag,89Sr,136Cs..)
3. Facility at SPES
An irradiation station,
using the SPES
Low Energy Beams, is
planned in the SPES building
.
4. Activities, INFN Experiments
Financed by CSN5 (physics application): ISOLPHARM_Ag +
ISOLPHARM_EIRA + ADMIRAL
1. National Collaboration
Broad, focused on radio-
pharmaceutical development:
synthesis,characterization
and preclinical tests (vitro/vivo)

## Slide 3
The ISOLPHARM collaboration
Development of a β-imaging
system based on solid-state detector
Development of a γ-imaging scintigraphic system
Radiobiological characterization
Radiopharmaceutical
production

## Slide 4: ISOLPHARM: Innovative Method
The ISOLPHARM method is capable of selecting and isolating a
SINGLE RADIO-ISOTOPE
+ high specific activity
+ radionuclide purity
The ISOLPHARM Method is an INFN Patent

## Slide 5
The ISOLPHARM beamline
Detection and quality control station station
SPES low energy experimental area

## Slide 6
The ISOLPHARM beamline (June 2024)
Isolpharm Beam Line

## Slide 7
→ 111Ag has dosimetric behavior equal to 186Re, which was recently studied in Phase I / II trials
→ 111Ag exhibits possible ‘theranostic’ properties
similar to 177Lu which was recently approved by FDA.
111Ag properties
β- emitter (average energy 360 keV)
Good half-life (7.45 days)
Average tissue penetration (1.8 mm)
Medium energy γ rays -> SPECT candidate
111 Isobaric chain | Half-Life T½ | Decay | Target Yield
Cadmium-111 | Stable |  | Low yield production
Silver-111 | 7.45 days | β─ | Good yield production
Palladium-111 | 23.4 min | β─ | Bad release, short T1/2
Rhodium-111 | 11 sec. | β─ | No release, very short T1/2
→ No Isobaric 111 contamination in the secondary target (also with LASER off)!
→ Silver-111 can be produced @ SPES with high purity & with high production rate
→ No radiopharmaceuticals radiolabeled with 111Silver in the market.
Radiopharmaceutical radiolabeled with 111Ag

## Slide 8: ISOLPHARM: a 10 years adventure
Simulations and feasibility evaluation
of Ag as radiopharmaceutical precursor
First production of 111Ag in reactor and beginning of in-vitro and in-vivo testing
Providing new tools for preclinical trials on 3D scaffolds
2018 - 2019
2020 - 2022
2023 - 2025
2014 - 2017
Interdisciplinary Study Group on production of medical radioisotopes at SPES
2024 - 2025
Follows the technological aspect for the radionuclide production
INFN experiments
PRIN

## Slide 9
ISOLPHARM-ADMIRAL strategy
WP2 :
β-imaging
WP3 :
γ-imaging
WP4:
Targeted Radiobiology
Mechanics & electronics design
Monte Carlo simulations for mechanics and detector design
Detector characterization and tests with fluorescence
INSTRUMENTATION
PHARMACOLOGY
RADIOBIOLOGY
Production of Ag-111 at the LENA facilities, purification and quality control
Radiochemistry of Ag-111
Pharmacology
Bioengineering of 3D scaffolds
Monte Carlo simulations for detector design
Planar imaging detector construction for Ag-111 γ detection
Characterization and test of the planar system
Cell survival tests in 2D flasks
Cell survival tests in 3D scaffolds
Dose computation in cell cultures
PHYSICS
CHEMISTRY

## Slide 10
WP1: 111Ag production & separation

## Slide 11
WP1 – experiments with 111Ag
MS1.1 – Routine production of Ag-111 at the LENA facilities, purification and quality control
In March, 2024, Ag-111 was produced and used for 3 experimental applications, conducted simultaneously:
In vivo test @ Capir (WP1)
Beta detector resolution test @ L.E.N.A. (WP2)
In vitro test @ UniPv (WP4)
The same activities will be performed again in July, 2024
and October, 2024.
50 MBq
3 MBq
20 MBq

## Slide 12
2 mm
3 mm
5 mm
Can Ag-111 be imaged?
Bruker In-Vivo Xtreme can perform pre-clinical imaging via 111Ag radiopharmaceuticals:
  Used the Direct Radioisotopic Imaging (DRI)
  PMMA Phantoms filled with 111Ag solution
Xtreme will be used to evaluate the targeting efficiency-> Only planar distribution
DRI
WP1: Test with 111Ag in phantoms (2023)
Nicola Zancopè, M.Sc. thesis - Uni. Padova, 2022

## Slide 13
13
WP1: Imaging with free 111Ag (March 2024)
150 mg of 110Pd
irradiated in the LENA
central thimble
Obtained 88 MBq of 111Ag
111Ag
biodistribution
in vivo imaging
5 days after injection

## Slide 14
WP3 – Detector construction
MS3.2 Planar imaging detector construction for Ag-111 γ detection
Device used to image γ radiation emitting radioisotopes;
Selected elements:
Electronics
CAEN FERS DT5202
Optical photon detectors (SiPM)
Hamamatsu S14161 8x8 ch 3x3 mm²
Collimator (tungsten)
2 mm holes, 1 mm septa, 30 mm length
Scintillating crystal (GAGG)
1x1x26 mm3 matrix
System built up to now:

## Slide 15
MS3.3 Characterization and test of the planar system
Experiments were conducted at Bologna (S. Spadano E. Borciani);
Simulations can give a reference.
The signal from 25 channels is integrated
First tests with Ag-111 are planned by the end of the year.
WP3 – System characterization

## Slide 16
Laser flat field correction
64 channels

## Slide 17
Main goals for 2024
111Ag production & separation
@ LENA
111Ag compound into a scaffold (WP1)
111Ag compound in front a β detector (WP2)
111Ag compound in front a γ camera (WP3)
111Ag compound into a cell cultures (WP4)
111Ag compound into a mice -> 3 run

## Slide 18
ISOLPHARM budget for 2025

## Slide 19
The ISOLPHARM Team
Thank you for your kind attention!
Visit our webpage: https://isolpharm.pd.infn.it/web/
Post-graduate students:
Alberto Arzenton, Daiyuan Chen, Jessica Delgado, Giorgio Grosso, Omorjit Singh Khwairakpam, Aurora Leso, Davide Serafini, Nicola Zancopè