## Slide 1: Beam-based Stability Evaluation in the LINAC of European XFEL.
Feedback & Monitoring Systems.
Marie Kristin Czwalinna, Björn Lautenschlager, Holger Schlarb
On behalf of :
group for accelerator beam controls (DESY, MSK)

## Slide 2: Agenda
Introduction
Typical Stability
Enhanced Stability
Beam-based Monitoring & Failure Detection
Summary & Outlook
3.5km long X-Ray FEL Facility

## Slide 3: Introduction

## Slide 4: European XFEL
  10Hz burst mode,
  4.5MHz bunch rep. rate,
  User bunch selection at final beam energy
100ms (10Hz bursts)
SASE 2
SASE 3
SASE 1
dump
≤600 µs
Beam Region 1
Beam Region 2
Flat-top
kicker
Tph(FWHM) = σe(rms)
<te>  <tph>
FEL pulse width at saturation:
Timing Relation Bunch to FEL
Relative fluctuations in arrival time of the center of mass
Arrival times
Longitudinal
Bunch Properties
Beam Energy
FEL pulse energy  center wavelength
Bandwidth of the spectrum
Peak current, Bunch Current profile
Intensity of FEL pulses
Number of modes / FEL pulse width
…
Operated in burst-mode, 10Hz, 600us.
3.5km

## Slide 5: Sections with Longitudinal Dispersion
 Beam Monitoring & Evaluation of RF Stability.
Q(s)
Δt, ΔE
C,
current profiles
s
s
s
s
s
s
longitudinal phase space
δE/E(s)
Magnetic Bunch Compressor Chicane, R56>0
Off-crest acceleration
bunch compression
bunch arrival-time

## Slide 6: Burst-Mode Operation with 600us RF Pulses
LLRF Vectorsum Regulation & Multi-Cavity Controller.
LLRF: Control  Amplitude A and Phase φ
Calculates drive signal for high power provided by the klystron
Three different parts
  Filling
  Flat-tops, bunches are accelerated
  Decay
Complex System: Different controller types combined : MIMO, PI, or learning feedforward
In-loop signal are shown here

## Slide 7: Typical Performance Energy  Arrival-time Stability

## Slide 8
tarrival  Alaser
Typical resolution 3 fs (100…250pc)
Electro-optical Bunch-Arrival-time Monitors
Measures Deviation from Expected Arrival-Time with Femtoseconds Resolution.
In-loop FB monitors
Out-of-loop monitors
BC2
BC1
BC0
40GHz
Arrival-time Deviation
 Measure for Energy Deviations
ΔT ~ ΔE/E

## Slide 9: Requirements on RF Stability
Arrival-time Jitter?  Ultimately Limits Performance in Timing-Sensitive User Experiments.
Arrival time jitter (fs rms) over 10 sec.
Bunch numbers 1 to 550 per train
Inj. : 55 fs
BC0 : 45 fs
BC1 : 2 8fs
BC2 : 20 fs
BAM 0
BAM 1
BAM 2.1 and 2.2
BAM 3, 4.1 and 4.2
BC2
BC1
BC0
Inj.
BAM
BAM
BAM
BAM
BAM
BAM
BAM
BAM
BAM
BAM
Derived from a linear compression, the timing jitter after BC dependents on
Initial jitter
RF phase jitter
Relative amplitude noise
Typically <0.01% rel.Amp. & <0.01deg Phase
Goal = 10 fs rms

## Slide 10: Enhanced Stability  Using Beam-based Feedbacks

## Slide 11: Beam-based Feedback Loop as Integral Part of the LLRF Controller
Intra-burst Stabilization & Removal of Repetitive Errors.
  Slope removal, adaptive feedforward
  Jitter reduction, feedback within bunch-train
Burst-to-burst jitter
Non-uniformity
But repetitive
Bunches
Arrival time
Target
LLRF
Controller
BC
Accelerator
Module
BAM
Arrival time,
per bunch data
A, φ
Basic feedback loop:
Error signal combination in the LLRF controller.
Field
detection
Drive signal

## Slide 12: Intra-Train Stabilization
Suppression of RF field fluctuations within 25kHz BW.
Energy corrections ~ 10-6 (e.g. ±5MeV @2.4GeV),
Adaptation time ~ 10-15 µs,
Operation stable over days,
Limited regulation range  offset correction by slow feedbacks.
Mean = 5.5 fs
Mean = 24 fs
In-loop arrival time jitter of 600 bunch-trains
L-IBFB Off
L-IBFB On
BAM resolution
3 – 4.5fs
L-IBFB Off
L-IBFB On
BAM noise floor
~ 25kHz BW
Facility | Best | Daily
EuXFEL | 3.3 fs | ~ 4…5 fs
FLASH | 4.7 fs | ~ 6 fs

## Slide 13: Beam-based Monitoring & Failure Detection

## Slide 14: Example 1, Dynamic Cavity Tuning
Automation with Piezo Actuators (DC + AC Voltage)
Dynamic cavity tuning (piezos)
  detuning of individual RF cavities
  Compensates microphonics
  high degree of automation
 Essential component in multi-cavity control
when absent,
  increased energy, thus timing jitter
  deterioration of field stability within the burst
Arrival time jitter [fs] ,100 shots
~15fs, piezo automation ON
30-45fs, piezo automation OFF
Bunch No.

## Slide 15: Example 2, Observe Unusual Behavior of Beam
High complexity of HPRF + LLRF controllers
Lack of out-of-loop monitoring in RF controls
 valuable information from beam
continuous monitoring
Uses single-shot beam monitors (timing, energy, compression, …)
Implemented as middle-layer server
  Online statistics (mean, std, slopes,…)
  When thresholds exceeded  alarm
Beam-based Monitors as Possibility for Detecting LLRF Control Errors
timing jitter [fs] over 100 shots
BR1
BR2
transition
L-IBFB active on BR2
time-series plot,
1st bunch of each BR
Inj.  GUN + Inj. Laser,
BC0 additive jitter in booster (A1/AH1)
BC1
BC2
BC1
BC0
BC2
Inj.

## Slide 16: Example 2, Observe Unusual Behavior
Requires expert knowledge to investigate  Capability to add Data-driven Fault Diagnosis
Identified Cause: Oscillation in detuning automation
Solved: reduction of gain in regulation loop (piezo AC voltage)
L-IBFB active on BR2
Injector  sees GUN + Inj. Laser,
BC0  sees Booster (A1/AH1)
BC1
BC2

## Slide 17: Example 3, Short-circuited Cavity Probe
Disturbance introduced on beam  Thorough Investigation to Find a Solution
Identified Cause:
Cavity with faulty probe connector but still requires to be included in vector sum regulation
Large effect on beam ~ 300fs unwanted arrival-time slope (over 600us)
… Details see Poster today,
Possible way for mitigation.

## Slide 18: Summary & Outlook

## Slide 19: Conclusion & Outlook
Achieved :
Beam-based Information for Fault Detection & Fault Diagnosis of LLRF Systems
Requires sufficiently precise beam monitoring
  Resolve energy deviation ~ 1E-6
  Resolve phase deviation ~ 10mdeg
RF Field Stability  ΔE/E
Active beam stabilization [10Hz…100Hz]
~ 10-6
< 5 fs
Importance of Monitoring Systems.

## Slide 20
Czwalinna, Marie Kristin
marie.kristin.czwalinna@desy.de
+49 (0)40 8998 9 2912
Thank you .