## Slide 1: High-precision clocks and triggers for longitudinal beam measurements in high energy synchrotrons
G. Papotti,
H. Damerau, G. Hagmann, T. Levens, A. Spierer
CERN, Geneva, Switzerland
LLRF Topical Workshop on Timing, Synchronization, Measurements and Calibrations
Frascati, 29 October 2024

## Slide 2: outline
introduction on SPS, SPS RF
SPS longitudinal beam observation systems
  in particular Mountain Range and Beam Quality Monitor
standard triggering scheme
  including limitations, especially for ion operation
triggering scheme with WR2RF

## Slide 3: introduction: the SPS
Super Proton Synchrotron (SPS): second largest CERN accelerator
  LHC injector, fixed target program in North Area, AWAKE, HiRadMat
  different “users” served in the same minute
SPS status display (Page 1)

## Slide 4: introduction: SPS RF
6x 200 MHz Travelling Wave structures
  designed for 10 - 450 GeV/c protons
  bandwidth: 199.5 - 200.4 MHz
  for p+, fRF = h frev, with h = 4620
    Df = 0.06-0.2%
  note: operation for heavy ions is more complex
p [GeV/c] | frev [kHz] | fRF [MHz] | bucket [ns]
10 | 43.186 | 199.5185 | 5.012
14 | 43.279 | 199.9468 | 5.001
26 | 43.347 | 200.2645 | 4.993
450 | 43.375 | 200.3944 | 4.990

## Slide 5: SPS longitudinal beam observation systems
several different systems
  remotely controlled programmable attenuators
  ~100 m on cable or fibre to ADC
  ADC on the surface
  (triggering scheme on next slide)
two main systems used in operation
  “Mountain Range” for visual checks
    beam structure, injection phase, …
    older pickup, transmission on cable
  “Beam Quality Monitor” for automated evaluation of longitudinal beam quality and pattern
    inhibits injection into the LHC if parameters out of spec
    newer pickup, transmission on optical fibre for improved profile quality
beam
attn
cable / fibre
(~100m)
ADC
wall current monitor
pickup
shielding
accelerator
tunnel
surface building
(Faraday Cage)
(~15m)
MR
BQM

## Slide 6: longitudinal observation triggering scheme
General Machine Timing
  telegram broadcast on cable to synchronize equipment to events like injection, start of ramp, start of flat top, start of fast or slow extraction…
Local Timing receiver
  outputs pulse triggered by timing event, with option of additional delay (generally ms precision)
VME Trigger Unit
  RF-synchronous counter, thanks to frev and fRF inputs (despite the changing frequencies)
  precise to the bucket + fine alignment down to 20 ps precision
  started by local timing pulse and frev
    alternatively to local timing, could also be started by e.g. injection or extraction pulse, for turn accuracy
  can do single pulse, or pulse burst at chosen spacing
VME Trigger Unit finally triggers the ADC
  for desired user/cycle, at desired time in the cycle, at desired bucket, with fine alignment
i.e. beam synchronous triggers at any azimuth with resolution of 20 ps
  example: for standard MR, acquire bucket 1 for 42 consecutive turns (i.e. 1 ms) at every injection
General Machine Timing
Local Timing
receiver
ADC
VME
Trigger Unit
frev
fRF

## Slide 7: examples of acquisitions with protons
1 ms (42 turns)
MR at injection
10 s
MR along the cycle

## Slide 8: observation jitter
BQM includes beam longitudinal stability analysis
  comparison of 8 acquisitions at turn spacing of fraction of synchrotron period
  must make sure it is not the trigger that moves!
instability measurement includes component proportional to ADC trigger offset
  trigger offset is due to free running clock of ADC, different for each acquisition, and <125 ps (ADC is 8 GS/s)
  top plot: stable beam is measured as marginally unstable, proportionally to trigger offset excursion among acquisitions
  bottom plot: if profiles are interpolated according to trigger offset, instability measurement is reduced
for the purposes of longitudinal beam observation, the trigger jitter of the observation systems is negligible
hand-written notes
from my 2009 logbook!
instability [%]
0
instability [%]
10
20
30
0
10
20
30

## Slide 9: added complexity for ion operation
fRF = 4620 frev too low at injection for ions
  e.g. for lead (Pb)
  (cavity bandwidth: 199.5 – 200.4 MHz)
  Df = 0.9%
use Frequency Shift Keying (FSK) and “Amplitude” Modulation (AM)
  FSK: fRF,on and fRF,off in the same turn
  AM: RF off for half of the time
  choose fRF,on as needed for beam, within cavity bandwidth
    at injection: bunch to bucket transfer from injector (CERN Proton Synchrotron), and capture at SPS (h = 4653, fRF,on = 199.9255 MHz)
  fRF,off in the other half of the ring, such that beam is in bucket 1 and with correct phase after a turn
    fRF,avg = 4620 frev = (fRF,on + fRF,off)/2
in addition, Fixed Frequency Acceleration: accelerate with varying h (fRF,cen = 200.222 MHz)
p [GeV] (Pb) | frev [kHz] | fRF [MHz]
17.07 | 42.967 | 198.5094
451.15 | 43.375 | 200.3921
1 turn
fRF,on
fRF,off

## Slide 10: examples of acquisitions with Pb ions
complex RF operation complicates longitudinal observations
  frequency swing from injection to high energy combined with cable delays results in moving acquisition
    e.g. bucket 1 in MR acquisition moves by ~4 buckets
  BQM needs to verify beam pattern: pattern matching depends on time in acquisition, and on phase of FSK modulation
10 s

## Slide 11: triggering scheme with White Rabbit
in 2024, frev and fRF synthesized locally by WR2RF (receives digitally the FTW for the fRF)
  on WR2RF see A. Spierer and G. Hagmann at this workshop
  delay compensation knob: calculate cable delay compensation, at every turn
  FSK offset knob: adjust for counting fRF,on and fRF,off
  trigger unit offset: used for compatibility with previous setup
advantages
  observation does not slip with acceleration
  same bucket 1 reference for different beams
    results also in easier settings management for different users
WR2RF
WR
network
General Machine Timing
Local Timing
Receiver
VME
Trigger Unit
ADC
frev
fRF

## Slide 12: examples of acquisitions with WR2RF - ions
10 s
with standard distribution
10 s
with WR2RF

## Slide 13: present installation
WR2RF
VME
Trigger
Unit
General
Machine
Timing
Local
Timing
Receiver

## Slide 14: conclusions
several systems used at CERN SPS for longitudinal beam observations
  e.g. Mountain Range for visual checks
  e.g. Beam Quality Monitor for automated analysis of beam pattern, stability, … and inhibition of injection into LHC if parameters are out of spec
improvement in longitudinal beam observations thanks to WR2RF
  no observation slippage throughout acceleration ramp
  single bucket 1 reference for different beam types
  easier setting management
WR2RF settings management to be improved
  ideally, user to input delay and azimuth
  results in cumbersome commissioning at present

## Slide 15: references
I. Béjar Alonso, O. Bruning, P. Fessia, M. Lamont, L. Rossi, L. Tavian, M. Zerlauth, "High-Luminosity Large Hadron Collider (HL-LHC): Technical design report", CERN, Geneva, Switzerland, 2020.
J. Coupard et al., "LIU Technical Design Report- Volume I: Protons", CERN, Geneva, Switzerland, Rep. CERN- ACC2014-0337, Dec. 2014.
E. Shaposhnikova, E. Ciapala, E. Montesinos, "Upgrade of the 200 MHz RF system in the CERN SPS", in Proc. 2nd Int. Particle Accelerator Conf. (IPAC’11) IPAC11, San Sebastian, Spain, Sept. 2011, MOPC058.
D. Boussard, T. Bohl, T. Linnecar, U. Wehrle, “Non integer harmonic number acceleration of lead ions in the CERN SPS”, 16th Biennial Particle Accelerator Conference and International Conference on High-Energy Accelerators, Dallas, TX, USA, 1 - 5 May 1995, pp.1506-1508.
information on WR2RF: https://www.white-rabbit.tech/rf-over-wr-cern/
Tomasz Włostowski et al.,“TRIGGER AND RF DISTRIBUTION USING WHITE RABBIT”, ICALEPCS201.

## Slide 16: spares

## Slide 17: more on ion operation
injection: h = 4653 (AM and FSK)
after inj, before ramp: fRF to fRF,cen
  frev constant, h varies, fRF varies
during energy ramp: fRF = fRF,cen
  frev varies, h varies, fRF constant
stop FFA when frev,Pb 4620 = fRF,cen
  continue with standard: fRF = 4620 frev
  stop FSK
1.
2.
3.
4.
Notes: FFA_LSA.py

## Slide 18: abstract
High energy synchrotrons, like the Super-Proton Synchrotron (SPS) and the Large Hadron Collider (LHC) at CERN, require high-precision beam synchronous triggers for longitudinal measurements, e.g. to acquire bunch profiles from a wall current monitor pickup.
The observation triggering scheme is based on the General Machine Timing (GMT) followed by dedicated trigger units counting the revolution and RF frequency clocks to allow synchronisation to the exact RF bucket.
Combined with a programmable fine delay, accurate triggers can be placed at any azimuthal position with a resolution of about 20 ps.
The SPS installation is described in detail, including its additional flexibility for measurements at injection, extraction and bunch rotation.
The performance and limitations of such an implementation are analysed in terms of jitter with respect to the beam, delay variation due to cable lengths between the clock generation and acquisition with a sweeping revolution frequency.
Such varying delays can be compensated with the White Rabbit (WR) technology, and highlights from the recent upgrade in the SPS are presented.