## Slide 1: WA6 Report FEL & Undulators
L. Giannessi (LNF),
on behalf of the WA6 collaboration team
A. Doria, M. Carpanese, F. Nguyen, A. Petralia (ENEA),
I. Balossino, M. Del Franco, M. Galletti, A. Giribono, A. Ghigo, A. Iovine, M. Opromolla, L. Sabbatini, A. Selce, C. Vaccarezza, A. Vannozzi, F. Villa, M. Castellano (Laboratori Nazionali di Frascati),
Vittoria Petrillo (Un. Milano),
Cristian Boffo (FNAL),
Najmeh Mirian (DESY)
Support from ENEA - Holographyc Interferometry & Fibre Optic Sensors (HIFOS) Laboratory (M. Caponero, A. Polimadei)

## Slide 2: Outline
Introduction
Freezing the AQUA undulator geometry: minimum gap – vacuum chamber
AQUA Magnetic design / max field
AQUA Beam acceptance / FEL performances / tuning range
Alignment tolerances
Lessons from the SABINA Undulator: mechanical tolerances/feasibility
Magnetic tolerances
Missing parts

## Slide 3: EUPRAXIA FELs
ARIA
AQUA
Modulator
Dispersive section
Seed
Radiators
  VUV seeded HGHG FEL
  Soft-X ray SASE FEL – optimized for 4 nm
Focus on the AQUA line

## Slide 4: EUPRAXIA AQUA Undulator Model (derived from SABINA)
The total undulator magnetic length considered is 20 m, i.e. 10 modules 2 m each.
Period length: provide sufficient tuning range at fixed energy which allows the FEL to reach carbon and eventually nitrogen K-edge (at higher peak current/beam energy) is 18 mm.
Polarization: variable polarization is an asset as it fits with the requests from the scientific case. Circular polarization ensures higher gain (about 2 m = 1 module)
Apple X type: Substantially higher field at comparable undulator aperture = extended tuning range. Tuning range independent of polarization.
Experience from the SABINA Undulator at LNF (KYMA).
The target photon energy range is extended toward lower photon energies by
  Small gap aperture (thin UV chamber walls – Apple X design)
  High undulator remanent field (high remanent field magnets are assumed – Br=1.35 T)
  Tuning the electron beam energy
AQUA - APPLE-X 1990 mm long modules, period 18 mm, polarization circular left (CL), circular right (CR), linear horizontal (LH), possibly linear vertical (LV).
Fully symmetric (Kmax independent of polarization)
No mechanical or magnetic prototyping will be carried out specifically for the TDR, but feasibility studies for magnetic and
From SABINA Undulator:
Magnetic design
Mechanical deformation analysis

## Slide 5: AQUA UNDULATOR Magnetic design
EUPRAXIA AQUA UM (linear) –
Min gap 6 mm (RADIA)
Modeling parameters:
Remanent field Br = 1.35 T
Undulator period λu = 18 mm
4 blocks / period, NdFeB
# of periods (eff.) N = 110 (Lu=2m)
D5.1: Technologies for the CompactLight Undulator,
F.Nguyen et al., XLS Deliverable
 | LP (h) | CP | LP (v) | units
Ix | 0 | 0 | 0 | G m
Iy | 0.0119 | -0.0095 | 0.4118 | G m
IIx | 0 | -0.0179 | -0.1322 | G m2
IIy | 0 | -0.0001 | 0 | G m2
Field Integrals
Number of periods N = 111.5
Total length of the magnetic array Lund= 1990.4 mm

## Slide 6: Vacuum pipe geometry
5 10-7
Apple X undulator is symmetric, minimal access from sides. Vacuum chamber is a cylinder of diameter d = 5 mm with sustaining blades
Wake fields mimimization requires smooth and regular surface – minimise apertures and other discontinuities. Wake field effects tolerated at d = 5 mm
Vacuum: access ports for pumping available only at the
undulator transitions
pumping stations
Lu = 1990 mm
d
courtesy of A. Liedl
d
Vacuum pipe by extrusion, circular, uniform thickness < 300 um. No coating. Cleaning and long-term heating procedure (V. Lollo).
Pipe ext. diam. (mm) | 5.6
Piper inner diam. d (mm) | 5.0
Wedge cut (mm) | 2.8
φ aperture (mm) | 6.0
B max (T) (in LP) | 0.935
Kmax (in LP) | 1.572
Krms (aw = max in CP) | 1.111
max 𝜆0 (nm) (@ 1 GeV) | 5.25
Tuning range | 

## Slide 7: Vacuum chamber positioning and tensioning
Vacuum chamber tensioned at the two UM extrema + holders along the UM
Tension
Position
vertical
horizontal
Mechanical design required for defining size and tolerances

## Slide 8: Wake field analysis (courtesy of F. Nguyen)
Assuming cylindrical symmetry for the wall geometry, the longitudinal (monopole) wakefield generates an energy loss and an increase in energy spread independent of the beam orbit, while the transverse (dipole) wakefield generates an emittance growth that actually depends on the orbit.
Longitudinal:
The energy loss due to the longitudinal resistive wall wakefields was calculated by M. Migliorati, F. Bosco et al. (Uni La Sapienza – Rome) and plugged into time dependent Genesis 1.3 simulations for EuPRAXIA@SPARC_LAB electron both short and long bunches
The resulting longitudinal RW wakefield introduces energy spread, affecting the FEL gain length and overall performance. Energy loss and FEL power are evaluated with the RW wakefield mode], assuming a copper VC with different inner radii.
The energy loss – and so the average FEL power – for both inner radii is comparable to the case of no wakefields at all.
30 pC
30 pC
300 pC
300 pC
Recall from previous TDR Committee meeting

## Slide 9: Transverse wake field analysis (courtesy of F. Nguyen)
The transverse (dipole) wakefield generates an emittance growth that actually depends on the orbit. Analytical treatment based on K. Bane & G. Stupakov formulae and the relationship between transverse and longitudinal RW impedances are used to estimate the kick angle kT parameter. We assume an orbit offset of 50 μm. The kick scales linearly with the offset (and it is zero on axis).
Transverse:
For a vacuum chamber inner radius of 2.5 mm, the peak current region of the bunch is affected by a potential kick angle per unit length of 5 nrad/m (10 nrad/m in the high charge case), assuming 50 μm of trajectory transverse offset. Larger offsets would suppress FEL lasing for the shift in resonance (see next).
This lets us estimate the required accuracy in the vacuum chamber alignment. A transverse offset of the vacuum chamber with respect to a perfectly aligned trajectory induces a transverse kick.
Assuming an offset of ±150 μm of the vacuum chamber the kick corresponds to inducing an angle of ∽60 nrad
r = 2.5 mm
Charge
30 pC
Charge
300 pC
r = 2.5 mm
kick angle per unit length (mrad/m x 10-6)
beam current profile
Recall from previous TDR Committee meeting

## Slide 10: FEL Parameter acceptance analysis
The undulator is engineered to amplify radiation at 4 nm from a suitable beam. We analyze its performance at 4 nm as well as its tuning range.
We used a (modified) Ming Xie model to analyse the FEL performance vs. the e-beam parameters.
We assume a photon energy of 4 nm = 310 eV at 1 GeV (the highest photon energy)
We assume a gaussian beam (in current energy, energy spread, transverse momenta and spatial distributions)
With a peak current 1.5 kA, duration 5 fs, average beta functions βx= βy =10 m, we also assume εx= εy.

## Slide 11: Performance at 4 nm – circular polarization
emittances (mm-mrad, ex=ey)
emittances (mm-mrad, ex=ey)
energy spread (rel.)
Circular polarization
1.5 kA
4 nm
beta 10 m
energy spread (rel.)
emittances (mm-mrad, ex=ey)
emittances (mm-mrad, ex=ey)
energy spread (rel.)
energy spread (rel.)
parameters from nominal case (14/6/2024)
CHICANE
DOGLEG*
* The "DOGLEG" case is characterised by 3.2 kA peak current (fluctuating between 1 kA to 9 kA)

## Slide 12
emittances (mm-mrad, ex=ey)
Linear polarization
1.5 kA
4 nm
beta 10 m
emittances (mm-mrad, ex=ey)
energy spread (rel.)
emittances (mm-mrad, ex=ey)
emittances (mm-mrad, ex=ey)
energy spread (rel.)
energy spread (rel.)
energy spread (rel.)
Performance at 4 nm – linear polarization

## Slide 13
emittances (mm-mrad, ex=ey)
energy spread (rel.)
Linear polarization
1.2 kA
4 nm
beta 10 m
emittances (mm-mrad, ex=ey)
emittances (mm-mrad, ex=ey)
emittances (mm-mrad, ex=ey)
energy spread (rel.)
energy spread (rel.)
energy spread (rel.)
Performance at 4 nm – linear polarization 1.2 kA

## Slide 14: AQUA tuning range – Linear polarization
Tuning range is calculated assuming the following reference beam parameters
Energy (GeV)
Energy (GeV)
Energy (GeV)
Energy (GeV)
Wavelength (nm)
Wavelength (nm)
Wavelength (nm)
Wavelength (nm)
Nphot/pulse
(x1010)
Sat Length (m) (magnetic)
Peak power (GW)
Pulse energy (μJ)
extended range

## Slide 15: AQUA tuning range – circular polarization
Tuning range is calculated assuming the following reference beam parameters
Energy (GeV)
Energy (GeV)
Energy (GeV)
Energy (GeV)
Wavelength (nm)
Wavelength (nm)
Wavelength (nm)
Wavelength (nm)
Nphot/pulse
(x1010)
Sat Length (m) (magnetic)
Peak power (GW)
Pulse energy (μJ)
extended range
The Apple X undulator provides the same KRMS value in both linear and circular polarizations

## Slide 16: Trajectory, matching
Quadrupole offset errors up to qx,y = 400 μm lead to an off-axis beam wander which can be pre-corrected with a corrector magnet (less than 10 mT if 3.6 cm-long), to ensure FEL amplification.
Ideal correction is when correctors are embedded into the quadrupole (share same iron).
This would pose an upper limit to the orbit correction loop response time. To be investigated.
Examples of FODO matching
Integrated quadrupole field vs. beam energy.

## Slide 17: Sensitivity to transverse offsets (2 mm bunch), no wakes (presented 11/2023)
FEL power reduction in
Circular polarization APPLE-X
FEL power reduction in
Linear polarization APPLE-X
Conclusion
Circular Polarization: 50mm offset gives rise to ~ 67% power decrease
Linear Polarization: the reduction is steeper and 50 mm is probably too much
Courtesy of F. Nguyen
While quadrupole offsets can be compensated by steering the trajectory to force it to stay close to the undulator axis, injection jitters in angle and position cannot be compensated.
Tolerances: trajectory, injection offset 1

## Slide 18
effect of transverse tilts/offsets
Tolerances: trajectory, injection offset 1

## Slide 19: Lessons learned from the SABINA Undulator
Mechanical stability and reproducibility
In collaboraton with the Holographyc Interferometry & Fibre Optic Sensors (HIFOS) Laboratory at ENEA (ref. M. Caponero) we measured the deformations of the undulator guilders
Magnetic error analysis
Indication on the undulator feasibility comparing the SABINA undulator and the ideal RADIA model to reconstruct magnetic dipolar errors along the undulator

## Slide 20
Courtesy of I. Balossino, A. Selce, A. Polimadei, A. Vannozzi, M. Del Franco, L. Sabbatini, M. Caponero
CAD model by KYMA
deformations in μm
Sensors
1
2
3
A diffraction grating is produced by modifying the refraction index of the core of a fiber (FBG Sensors). Rough approximation: the refractive index has a sinusoidal modulation along the axis of the fibre.
The sensor length is 10 mm, temperature and strain sensing at the level 0.1K - 1/106 relative elongation sensitivity
Undulator Mechanical tests on the SABINA undulator FBG measurements

## Slide 21: Undulator Mechanical tests on the SABINA undulator FBG measurements
Undulator tested for
Temperature dependence over a rance of 3 °C
Magnetic forces: gap – phase variations opening
sensors were used in two different ways:
  as strain measurement, by gluing the fiber fully adhered to the surface of the magnet holder-plates;
  as gap measurement devices, by placing the sensors between adjacent plates.
Distribution of sensors

## Slide 22: Brief summary of FBG strain measurements
Temperature dependence:
  max deformation of 0.12 nm over 2.7 °C/15 hours
Mechanical
  by moving the four arrays all together from the minimum gap to the maximum gap, and in small steps from minimum gap to 50 mm of gap opening.
  by shifting the phase at different undulator gaps. In Fig. (right) the effect of a phase shift with the undulator tuned at minimum gap is shown.

## Slide 23: FBG strain measurement conclusions
The wavelength shifts are perfectly reproducible. No hysteresis or values not correlated to a gap macroscopic movement were observed, except for the temperature dependence.
The largest observed wavelength shift is ∼0.2 nm for the gap sensors and a factor 2-5 lower for the strain sensor devices.
Gap sensors, the reference length is the plates separation. The plate sepatation cannot be measured an is virtually zero. In order to estimate an upper limit, we may consider that over an hypothetical 1 mm gap, the variation would be ∽ 150 nm. This has a negligible effect on the undulator field.
Strain sensors, the reference length is the sensor length: the local deformation is ∽300 nm/cm.
These deformation values are compatible or lower than those calculated by finite elements methods and confirm the reliability of the undulator mechanical structure
A finite element model of the long AQUA undulator module should provide a suitable estimate of the expected structure deformation under the effect of magnetic forces.

## Slide 24: Study of tolerances for magnetic field errors
We analyzed the sensitivity of the FEL radiation growth with respect to the magnetic errors by means of a procedure, miming the protocols used by the undulator manufacturers.
We group the hypothetical magnets in 3-5 magnets ensembles, each group is characterised by the magnetic moment corresponding to a single magnet N or S
We assume a truncated gaussian distribution for these magnetic moments, we follow a sorting procedure to generate the magnetic errors corresponding to an entire array of 110x4 magnets, corresponding to the 2.2m undulator.
We use this distribution of magnetic errors to simulate SASE FEL amplification in Genesis1.3
N
S

## Slide 25: Study of tolerances for magnetic field errors
The table (right) summarises the required conditions on field and field integral required (ref. V. Petrillo).
We now link these field /field integrals with those resulting from the field distributions measured from the SABINA undulator. This provides a link between a similar realized device and the specs of the magnets used for the realization
Bmeasured-Bradia,rescaled
ΔBx (T)
ΔBy (T)
z (m)
different δB/B of
the dipoles ensamble
resulting condition
on the field
Difference between the measured field and the model for SABINA UM

## Slide 26: Summary – status of the TDR
WP6 Undulators Design and Physical requirements:
The physical parameters and specification of the AQUA undulator system are established
Most of the sensitivity studies are concluded.
Coherence between the set of parameters presented still need to be improved
The constructive design of the components requires engineering and design support that is not currently available. However, the components that require the most significant effort (the undulators) are those that need to be assigned to industry for development outside the laboratories.
We indicated a technical readiness status at 41%
WP6 Undulators: TDR Writing
The TDR structure (chapters) is ready - the order of the various arguments need to be adjusted
Consistency between different sections has to be improved
The link between the magnetic specs required and the SABINA measurements to be included
We indicated a writing readiness status at 30%

## Slide 27: Supplementary slides

## Slide 28: ARIA
Undulators, seed and tuning range

## Slide 29: ARIA Radiator Undulators
Main features:
variable gap, variable phase for adjustable polarization (EPU) (six motors)
𝛌u = 55.2 mm, Np=42, Lu=2.4 m
working gap: 10 ÷ 32 mm
Modulator
Dispersive section
Seed
Radiators
FERMI FEL-1 Radiator
Courtesy of Bruno Diviacco
Similar to FERMI FEL-1 radiators
built by KYMA in 2009-2010 for FERMI
FEL-1
Main Physical Specifications:
Phase error sF < 5 º rms
Trajectory offset error < 20 mm rms
Trajectory tilt error < 25 mrad rms
Peak-to-peak field error DB/B < 0.5% rms
Integrated Quadrupole (N/S) < 100 G
Integrated Sextupole (N/S) < 100 G/cm

## Slide 30: ARIA Tuning range parameters
FEL
  Max harmonic = 10
  Undulator K-range from FERMI FEL-1:
  Kmax = 3.4 (CR), 4.35 (LV), 5.45 (LH)
Electron beam parameters:
  Energy 1.0 -> 0.7 GeV
  Energy spread 200 keV @ 0.8 kA -> 400 keV@1.5 kA
  e-beam duration:
    > 100 fs (long bunch mode, 200 pC)
    -> 8 fs (short bunch mode, 30 pC)
  beam emittance 2 mm mrad in long bunch mode/ 0.8 mm mrad in short bunch mode - beta function 10 m
Seed laser:
  We assume a minimum seed energy available in the range, of 20 uJ
  The seed spot size (average) is independent on the wavelength and is 0.5 mm^2
  Seed duration 400 fs (long seed) -> 200 fs (short seed), possibly no frequency chirp – i.e. seed spectral width close to FTL (not essential in short bunch mode)

## Slide 31: ARIA Seed laser option
TOPAS-PRIME tuning curves. Pump: 1 mJ, 100 fs, 800 nm. HE version is commercial and E>10 uJ for the entire BW.
https://lightcon.com/product/topas-prime-opa/#performance
A
B
Courtesy of M. Galletti

## Slide 32: Long-bunch long-seed mode Linear Polarization
Beam energy (GeV)
FEL Wavelength (nm)
Pulse energy (μJ)
Pol. LH
h=2
h=3
h=4
h=5
A: Seed range 320-400 nm
High energy range 100-50 nm – higher power
Minimum gap/max K
h=6
h=7
Beam energy (GeV)
FEL Wavelength (nm)
Pulse energy (μJ)
Pol. LH
h=4
h=5
h=6
B: Seed range 600-800 nm
Continuous tuning in the range 60-180 nm
h=7
h=8
An OPA such as the TOPAS can seed the ARIA FEL line covering the spectral range 200-50 nm with a single OPA process 2HG (B). Improved performances below 100 nm can be achieved with the 4th HG process (A)

## Slide 33: ARIA short summary
ARIA operates in High Gain Harmonic Generation and may cover the VUV spectral range down to 50 nm with an undulator similar to the one of FERMI FEL-1. Contrary to FERMI it uses a seed longer than the electron bunch and uses the electron bunch shaping and control capabilities of Eupraxia@SPARCLAB for controlling thethe lught pulse properties.
A commercial laser based on an Optical Parametric Amplifier such as the TOPAS should have the correct pulse energy and overall features to seed ARIA
Two OPA regimes can be used to cover the full spectral range with harmonic order below seven. In case a single OPA regime is used with second harmonic conversion, the full range is covered with harmonic order below 12

## Slide 34: AQUA
  Magnetic design & tuning range -> vacuum chamber geometry
  Longitudinal and transverse wake-fields
  Analysis of SABINA Undulator and first lessons for the AQUA undulator
    Magnetic: field quality, field integrals, trajectory and FEL amplification
    Mechanical: stability and reproducibility tests

## Slide 35: Transverse resistive wall wakefields
Transverse RW wakefields induced inside the cylindrical Cu vacuum chamber of radius a=2… 3 mm affect the electron bunch orbit along the undulator line, depending on the initial transverse offset at entrance.
Analytical treatment based on K. Bane & G. Stupakov formulae and the relationship between transverse and longitudinal RW impedances are used to estimate the kick angle kT parameter
Courtesy of F. Nguyen
Preliminary conclusions
Short bunch: Max kick: 2×10-5 mrad/m but outside the current peak
Long bunch: same order of magnitude, but superimposed to the current profile

## Slide 36
First tolerance study of undulator magnetic field errors for the AQUA beamline using the data from the SABINA undulator measurements. Courtesy of M.Opromolla
E (GeV) | 1 | slice (MeV) | 0.489
Q (pC) | 200 | slice (um) | 0.8
(kA) | 1.26 | (µm) | 60.9, 56
E (GeV) | 1 |  | 0.489
Q (pC) | 200 |  | 0.8
 | 1.26 |  | 60.9, 56
Long beam (60 fs), = 0.94e-3
Considered a simulation in a long bunch case to reduce SASE shot to shot statistical fluctuations
Magnetic field errors reconstructed from the SABINA undulators measurements (3 modules used in random sequence to provide similar field integrals)
Without orbit correction the beam walks out of axis and particles are lost.
Added correctors at the end of each undulator section to zero the second field integral betweenthe undulators (similar to the correction of a trajectory feedback system)
- - - long beam
W. Magnetic
errors
PWA short beam
Ideal
First and second field integrals specs. achieved for the SABINA undulator seems sufficient for the AQUA undulator line
z (m)
<x> (m)
<Y> (m) - - -
corrected trajectory

## Slide 37: Timeline for SCU development at FERMILAB (Courtesy of C. Boffo)
21.11.2023 C. Boffo | EuPRAXIA
Some delay with respect to previous schedule.
New schedule:
Prototype completed (testing after Christmas 23' )
Vacuum vessel in final stages of manufacturing
Thermal shield and MLI in procurement
Assembly will be completed in September 2024
DELAYED 1 YEAR

## Slide 38: AQUA summary after last meeting (Nov. 2023)
Magnetic design is completed for different magnet apertures. The effective aperture depends on the next item
Vacuum chamber design is in progress. Diameter between 5 and 6 mm. The diameter in this range still allows 20% photon energy tuning via gap aperture change
Longitudinal wake fields do not constitute a problem for the pipe radius/beam conditions selected
Transverse wake field calculations were carried out. The figures will be used to define the straightness and alignment tolerances required by the vacuum chamber.
The tolerance on the beam injection indicates that the transverse beam position jitter at the undulator entrance has to be less than 50 um pp. Similar simulations will be carried out for the injection angle jitter.
Similar calculation are in progress for the determination of the maximum field integral from the undulator and from the quadrupoles alignment.
Mechanical stiffness of the SABINA undulator is indicating some unexpected behavior under investigation. The results will be discussed with the producer to explore mitigation strategy for the AQUA undulator.